## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Designing for Reduced Hazard
Image: Wikimedia Commons, Fume Hood , Author: U.S. National Institute for Occupational Safety and Health
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
Hazard and Risk – Past and Present
Toxicology
Assessing Hazards and Exposure
  What Happens When You’re Exposed?
Hazard Minimization Through Molecular Design
QSAR - Quantitative Structure Activity Relationship
Molecular Design Research Network (MoDRN)
Topics To Be Covered

## Slide 3
There are over 100,000 chemicals in global circulation.
700+ chemicals are introduced to the US Market each year.
85% of these chemicals lack experimental data on environmental risk.
There has been unintended biological activity which has led to increased hazard as well as toxic endpoints for humans and the environment.
The Challenge of Environmental Risk
Source: Wikimedia Commons

## Slide 4
The ability to cause adverse consequence.
What types of chemical hazards are there?
  Global Hazards (global warming, acid rain, ozone depletion, security threat)
  Physicochemical Hazards (explosivity, corrosivity, oxidizers/reducers)
  Toxicological
    Environmental (aquatic toxicity, avian toxicity, mammalian toxicity)
    Human (e.g., carcinogenicity, neurotoxicity, hepatotoxicity, dermal toxicity)
Hazard
Notes: Avian Toxicity – toxicity in birds
Hepatotoxicity (from hepatic toxicity) implies chemical-driven liver damage

## Slide 5
Risk = f(Hazard, Exposure)
Environmental risk is resulting from exposure to a potential environmental hazard
Risk can be reduced by in two ways:
If as hazard , exposure needs to be reduced to 0
If hazard = 0, exposure can be
Ultimate goal is to use BENIGN materials = with no hazard
Risk Equation

## Slide 6
Exposure becomes irrelevant
Less dependence on systems which can fail or be sabotaged
Competitive advantage – reduces costs associated with toxic materials
Why Use Benign Materials?
Ultimate goal is to use BENIGN materials = with no hazard

## Slide 7: How have we dealt with chemicals and the environment in the past?
Historical Approach to Hazard Problems

## Slide 8
Waste treatment, control, and disposal; pollutant monitoring; hazardous waste site cleanup.
Development of standards for emissions to air, releases to water, and disposal by land, as well as regulation of these standards.
“Command and Control”
Compensating injured employees
Buying protective equipment
Historical Approach to Hazard Problems

## Slide 9
In U.S., 1.78 million tons of toxic chemicals were released directly to air, water, and land in 2011
Only 650 of toxic chemicals out of 100,000 in commerce are tracked by Toxic Release Inventory
Mihelcic, J. R.; Zimmerman, J. B., Environmental engineering: Fundamentals, sustainability, design. Wiley Global Education: 2014.
Chemicals in the Environment

## Slide 10: Why should we care?

## Slide 11
One of Green Chemistry’s greatest strengths is the ability to design for reduced hazard.
148 xenobiotics in the body
Xenobiotic: synthetic chemical, that is foreign to the body or to an ecological system.
Of the chemicals found:
  76 cause cancer in humans or animals,
  94 are toxic to the brain and nervous system, and
  79 cause birth defects or abnormal development.
The dangers of exposure to these chemicals in combination has never been studied.
Image Source: http://svtc.org/our-work/e-waste/
Body Burden

## Slide 12
The traditional definition of toxicology is "the science of poisons."
A more descriptive definition of toxicology is
"the study of the adverse effects of chemicals or physical agents on living organisms".
What is Toxicology

## Slide 13
What Counts as Toxic
Mihelcic, J. R.; Zimmerman, J. B., Environmental engineering: Fundamentals, sustainability, design. Wiley Global Education: 2014.
Notes: Debilitating – making something weak

## Slide 14
Acute toxicity | Carcinogenicity | Bioconcentration
Subchronic & chronic toxicity | Neurotoxicity | Degradation & transport
Reproductive toxicity | Immunotoxicity | Aquatic toxicity
Developmental toxicity | Genotoxicity | Terrestrial organism toxicity
Molecular weight | Molecular volume | Dipole moment
Hydrophilic surface area | Hydrophobic surface area | Rotatable bonds
Hydrogen bonds | Ionization potential | Electron affinity
Partition coefficients | Acid/base properties | Polarizability
Relating Toxic Endpoints to Molecular Features & Properties
Relationships

## Slide 15
A toxic agent is anything that can produce an adverse biological effect.
It may be chemical, physical, or biological in form.
For example, toxic agents may be
chemical (such as cyanide),
physical (such as radiation), and
biological (such as snake venom)
Definitions

## Slide 16: What is the most important factor in bringing about the adverse biological impact?

## Slide 17
Dose is the amount of a substance administered at given times.
For example:
  650 mg Paracetamol/Tylenol as a single dose
  500 mg Penicillin every 8 hours for 10 days
Dose

## Slide 18
Highly toxic chemicals can be life saving when given in appropriate doses.
An apparently nontoxic chemical can be toxic at high doses. (Too much of a good thing can be bad)
Dose Makes the Poison
Source: Wikimedia Commons

## Slide 19
Source: Marczewski, A.E., and Kamrin, M. Toxicology for the citizen, Retrieved August 17, 2000: www.iet.msu.edu/toxconcepts/toxconcepts.htm.
Approximate Lethal Doses of Common Chemicals (Calculated for a 160 lb. human from data on rats)
Chemical Lethal Dose
Sugar (sucrose) 900 g
Alcohol (ethyl alcohol) 1.5 L
Salt (sodium chloride) 250 g
Herbicide (2, 4-D) 125 mL
Arsenic (arsenic acid) 1-2 teaspoons
Nicotine one half teaspoon
Food poison (botulism) microscopic
Lethal Doses
Notes: 1 Quart = 0.946 lit

## Slide 20: How is toxicity testing done?

## Slide 21
The dose-response relationship is a fundamental and essential concept in toxicology. It correlates exposures and the spectrum of induced effects.
The dose-response relationship is based on observed data from:
experimental animal
Human in vitro cell studies
human clinical (but for drugs only…)
Dose-Response
Notes: In vitro comes from the Latin term "in glass." The term refers to studies of biological properties that are done in a test tube (i.e. in a glass vessel) rather than in a human or animal.In vitro studies are often contrasted to in vivo ("in life") studies which are done inside an organism.

## Slide 22
Knowledge of the dose-response relationship:
  establishes causality that the chemical has in fact induced the observed effects
  establishes the lowest dose where an induced effect occurs - the threshold effect
  determines the rate at which injury builds up - the slope for the dose response.
  LD50, NOAEL, LOAEL, and RfD (see next slide.
Dose-Response

## Slide 23
LD 50- A common dose estimate for acute toxicity is the LD50 (Lethal Dose Response 50%).
This is a statistically derived dose at which 50% of the individuals will be expected to die.
NOAEL - No Observed Adverse Effect Level
Highest data point at which there was no adverse effect.
LOAEL - Low Observed Adverse Effect Level
Lowest data point in your experiment at which there was an adverse effect.
LD 50
UF = Uncertainty factor (10-1000)
UF is bigger when larger uncertainty on experiment
RfD – estimate of a daily oral exposure to the human population, that’s likely to be without risk of an effect
LD50, NOAEL, LOAEL, and RfD
RfD

## Slide 24
0
100
50
40
30
20
10
60
70
80
90
Inhaled Dose (ppm)
% Mortality
Solvent 99-7
Solvent 99-2
0 50 100 150 200 250 300 350
Plotted here are two theoretical curves for the toxicity of solvents used in the cleaning of silicon compounds. Both solvent 99-2 and 99-7 performed equally well against a variety of manufactured silicon compounds. The task at hand for you is to determine which solvent would you pick to be “safer” for use. As you can see from the accompanying data both compounds have an equivalent Lethal dose 50 value (LD50). These are based on average values during a 6 hour exposure period.
In-Class Discussion- Which Solvent Would You Use?

## Slide 25
Solvent 99-7 causes lethality at much lower levels than 99-2 (20ppm versus 150 ppm respectively), and the response is much more predictable (i.e. less population heterogeneity). In case of Solvent 99-2, higher levels can be inhaled before any harmful effects should begin.
0
100
50
40
30
20
10
60
70
80
90
Inhaled Dose (ppm)
% Mortality
Solvent 99-7
Solvent 99-2
0 50 100 150 200 250 300 350
In-Class Discussion- Which Solvent Would You Use?

## Slide 26
Review and analysis of toxicology data and assessing if the substance causes toxic effects
Sources include animal and human studies and computational data
These studies have difficulty with showing causation (if a risk factor lead to disease)
Mihelcic, J. R.; Zimmerman, J. B., Environmental engineering: Fundamentals, sustainability, design. Wiley Global Education: 2014.
Hazard Assessment
Risk = f(Hazard, Exposure)

## Slide 27
Determines the extent and frequency of human exposure to target chemicals.
Guidelines for residential, industrial and commercial sites
For engineers, the knowledge of hazard and exposure provides information whether the site needs to be remediated.
Mihelcic, J. R.; Zimmerman, J. B., Environmental engineering: Fundamentals, sustainability, design. Wiley Global Education: 2014.
Exposure Assessment
Risk = f(Hazard, Exposure)
Example of exposure evaluation: workers touching soil

## Slide 28: Hazard assessment, dose-response & exposure assessment
Risk Characterization

## Slide 29
ChemHAT - easy way to access summarized information on chemical hazards in the workplace
ChemSpider
Protox
Safer Choice - for consumers, businesses, and purchasers to find products that perform and are safer for human health and the environment.
toxicity assessment based on experimental or predicted LD 50
Tools For Hazard Characterization
Notes: Show tools

## Slide 30: What happens once you are exposed to a toxicant?

## Slide 31
ABSORBTION
DISTRIBUTION
METABOLISM
EXCRETION
ADME
http://blog.gyrosproteintechnologies.com/spinblog/adme-of-therapeutic-proteins

## Slide 32
Source: Wang and Skolnik, Chemistry and Biodiversity, 2009
Chemical Processes in ADME
Place where the drug (or chemical) can take effect
Notes: More complex
ADME can be controlled by these parameters

## Slide 33
Dermal
Respiratory
Digestive
Skin is the first barrier to absorption for the chemical. The skin can keep chemicals out of the body, or it can let them in, depending on the physical and chemical properties of the chemical. Absorption of a chemical will result in the chemical circulating inside the body and perhaps causing adverse effects.
As chemicals are inhaled, they may reach the lungs. The lung surface is a poor barrier against the entry of many chemicals into the body, which means that absorption of chemicals into the lung can be rapid and efficient.
If chemicals are swallowed, either intentionally or unintentionally, they enter the gastrointestinal tract (GI). From there, they may either pass through the body or be absorbed into the body.
Absorption

## Slide 34
Dermal
Respiratory
Digestive
Absorption
Parameter | Preferred | Not Preferred
Physical state | solid | liquid
LogP | Less than 0 or greater than 5 | Between 0 and 5
Molecular weight | More than 400 Da | Less than 400 Da
Parameter | Preferred | Not Preferred
Particle size | More than 5 nm | Less than 5 nm
LogP | Less than 0 or greater than 5 | Between 0 and 5
Molecular weight | More than 400 Da | Less than 400 Da
Vapor pressure [mmHg] | Less than 0.001 | More than 0.001
Parameter | Preferred | Not Preferred
Particle size | More than 100 nm | Less than 100 nm
LogP | Less than 0 or greater than 5 | Between 0 and 5
Phase | solid | liquid
Molecular Weight [Da] | More than 500 Da | Less than 400 Da
LogP – measure of partition coefficient of a molecule between aqueous and lipophilic phases.
Notes: LogP – measure of partition coefficient of a molecule between aqueous and lipophilic phases.
Da – Dalton, unit of molar mass, g/mol

## Slide 35
Distribution is the movement of a chemical throughout the bloodstream and into other organs, such as the brain and the bones. Pharmaceuticals such as antibiotics and painkillers are designed to have high distribution rates so they can reach their target organs and have therapeutic effects. For chemicals such as detergents, distribution should be limited.
Distribution depends on many factors such as log P, polar surface area, acidic/basic properties, and molecular weight.
Distribution as opposed to absorption is more difficult to control.
Distribution
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor
Notes: Polar Surface Area of a molecule is defined as the surface sum over all polar atoms, primarily oxygen and nitrogen, also including their attached hydrogen atoms. PSA is a commonly used medicinal chemistry metric for the optimization of a drug's ability to permeate cells.

## Slide 36
As a chemical is distributed through the body, it will most likely undergo metabolism. Metabolism is the body’s way to transform the molecules into metabolites in the liver. This facilitates their excretion (removal) through the kidneys. The rate at which a chemical is metabolized is usually dependent on its accessibility to enzymes.
Metabolism is unpredictable. Metabolism can lead to detoxification or toxification of the organism.
Metabolism
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor

## Slide 37
After the chemical is absorbed, the body can eliminate it by a process called excretion which can occur through the kidneys, the skin, the GI tract, and the lungs. If the chemical is not eliminated from the body, it can accumulate, or stay in the blood, which can lead to disease. Bioaccumulation is favored for lipophilic molecules in fatty tissues.
Excretion as opposed to absorption is more difficult to control.
Elimination
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor

## Slide 38
Pollution
Persistence
Depletion of resources
Flammability
Radioactivity
Risk of Explosion
Chemical Reactivity
Understanding Physicochemical Properties Associated with Reduced Hazard
Chemical and Physical Properties
pKa chain branching log P molecular refractivity mol. wt. hydrolyzable groups
EHOMO ELUMO electronegativity hardness dipole log D7.4 # H-bond accept/donor
DESIGN

## Slide 39
Absorption organs
GI tract
Skin
Lungs
Eyes
Acidic substance
pKa<7
Unionized at pH>pKa
Basic substance
pKa>7
Un-ionized at pH>pKa
Lipid soluble
Absorbed across intestine membrane into blood
Chemical
Property-Based Guidelines for Bioavailability
Notes: Different absorption mechanisms - GI tract has largest SA, respiratory has largest blood flow & thinnest membrane, skin has variable thickness; different requirements for water sol

## Slide 40
molecular size < 400 Da
log Pow 0 - 6
presence of solvents
Ionization (polar, ionized)
molecular size < 500 Da
log Pow 0 - 5
Non-ionization at GI pH
Particle size < 5um
molecular size < 400 Da
vapor pressure < 0.001 mmHg
water solubility
molecular size
vapor pressure < 0.001 mmHg
Voutchkova, A.; Osimitz, T.; Anastas, T. Chem. Rev. 2010, 110, 5845
Property-Based Guidelines for Bioavailability
Absorption organs
GI tract
Skin
Lungs
Eyes

## Slide 41
Educational game based on ADME and scientific data for surfactants to make connection between physico-chemical properties and health.
http://gwiz.yale.edu
Safer Chemical Design Game
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor

## Slide 42: Approaches to Hazard Minimization through Molecular Design

## Slide 43
Bioavailability Structure/Shape Activity Mechanism of Action
Molecular
Weight
Solubility
Electronic
Charge
Volatility
Reactive
Functional
Groups
Bioaccumulation/
Persistence
Particle
size
Receptor
binding
Key events
Shape/
Molar Volume
Toxicokinetics
Toxicodynamics
Chemists can control quite well
Not well understood and relatively complex
That’s what we want to target
Green Chemistry Molecular Design Pyramid

## Slide 44
Elimination of the molecular initiating event that activates pathway
Changing reactive functional groups
Reducing or eliminating bioavailability
Reduction of need for associated hazardous substances
Design for End-of-Use product life
Approaches to Hazard Minimization Through Molecular Design

## Slide 45
Where the mechanistic pathway of action is known, molecular structures can be designed such that the necessary reactions are either impossible or highly disfavored resulting in significant toxicity reduction.
Elimination of the molecular initiating event that activates pathway

## Slide 46
In the absence of specific mechanistic information, chemists can modify structure such that certain reactive functional groups, e.g. cyano, electrophilic, etc, can be minimized or eliminated from the chemical structure where feasible.
B. Changing Reactive Functional Groups

## Slide 47
In order for a chemical to manifest its intrinsic hazard, it must be able to reach the toxicological target, human, animal, environmental or global. Through structural molecular design, properties such as solubility, log Kow, and volatility can adjusted to reduce hazard manifestation.
C. Reducing or Eliminating Bioavailability
Notes: The octanol/water partition coefficient (Kow) is defined as the ratio of a chemical's concentration in the octanol phase to its concentration in the aqueous phase of a two-phase octanol/water system

## Slide 48
Many chemical substances, if not hazardous themselves, require the use of other hazardous substances e.g. paints with VOCs, surfaces requiring specific cleaners, plastics with various additives.
Through molecular design, these associated substances can be eliminated by making the desired properties integral to the product
D. Reduction of Need for Associated Hazardous Substances

## Slide 49
Persistence of chemical in the environment is a problem that can be designed out of molecular structure.
By creating products that degrade to innocuous by-products under designed conditions, e.g., heat, light, time one can reduce or eliminate this hazard.
Design for utilization of waste as a feedstock is an important goal.
E. Design for End-of-Useful Product Life

## Slide 50: By Changing the Molecular Charge: Cephalosporins
Clinical nephrotoxicity was recognized early – damage to proximal tubular epithelia.
Mechanism: the drug is rapidly transported across basolateral membrane via the organic anion transporter, OAT1. Transport out of cell into lumen is less well characterized (involves other OAT, OAT4).
Cephalosporin has a very low affinity for OAT4 due to its zwitterionic character, resulting in considerable intracellular accumulation
Cephaloridine
Cephalothin
In contrast, cephalothin, an anionic analog of the original zwitterionic drug, rapidly moves across the epithelia from blood into urine
Is thus not a neurotoxin
Cephalosporins: Antibiotic molecules used for gram+ bacteria
Notes: Cephalosporins are a type of beta-lacatam antibiotic.
First generation:Cephaloridine

## Slide 51
Diquat
Paraquat
By Manipulating Sterics: Paraquat and Diquat
Diquats and Paraquats are herbicides (plant killer), primarily for weed and grass control
In animal studies, diquat causes mild, reversible injury
Paraquat is not metabolized by the liver. It has life-threatening effects on the gastrointestinal tract, kidney, liver, heart and other organs
Both: Toxic doses are life threatening. Impacts GI tract, kidney lungs, liver, heart, other organs
Registered as a restricted use pesticide
Not registered as a restricted use pesticide
http://npic.orst.edu/RMPP/rmpp_ch12.pdf
Notes: Paraquat is a non-selective contact herbicide of the diphenyl class. It was introduced in the 1960s and became used worldwide. However it was soon recognized that paraquat also cause selective pulmonary toxicity to humans (damage to alveolar cells type I and II, causing edema, inflammation and hermorrhage, lung fibrosis).
Steric effects are nonbonding interactions that influence the shape and reactivity of ions and molecules. Steric effects complement electronic effects, which usually dictate shape and reactivity. Steric effects result from repulsive forces between overlapping electron clouds.

## Slide 52
Acrylate is understood to be carcinogenic because it can readily undergo Michael addition reactions
The addition of a methyl group to form methacrylate decreases the electrophilicity of the b-carbon, and decreases tendency for Michael reactions.
While this does not reduce the commercial efficacy, but whereas acrylate causes cancer is experimental assays, methacrylate does not.
Acrylate
carcinogenic
Methacrylate
non-carcinogenic
By Manipulating Electrophilicity: Acrylates
Notes: Electr

## Slide 53
Benzene is known to cause hematotoxicity and leukemia in humans
This is understood to be due to one of its metabolites, (E,E)-muconaldehyde.
Toluene is comparatively much less toxic, as the methyl group is oxidized more easily than the benzene ring to give benzoic acid
By Facilitating Detoxification: Benzene
hematotoxicity,
leukemia
non-toxic
hepatic oxidation
[detoxification]

## Slide 54
DDT is well known to be environmentally persistent.
DDT analog with Silicon above was synthesized.
While less persistent, the analog turned out to be non-toxic to insects.
This is due to the more readily oxidized (metabolized) Si-H bond compared to C-H and also the larger size of the molecule.
DDT
(Toxic to insects)
Si-DDT Analog
(Non-toxic to insects)
By Isosteric Substitution: Carbon with Silicon

## Slide 55
Even if chemists design one chemical, it has to undergo tests
Designing New Molecules is Not a Trivial Task

## Slide 56
QSAR = classification models used in the chemical and biological sciences and engineering
QSAR-Quantitative Structure Activity Relationship
Wikipedia
potency of the response variable
"predictor" variables
QSAR
Structure, physico-chemical properties, chemical functionalities
Biological activity: toxicology and eco-toxicology
[like LC50 or oxidative stress]
Known data sets
QSAR established relationship
"predictor" variables
New molecules
QSAR uses the learnt rules to predict biology
QSAR
QSAR predicted potency of the response variable

## Slide 57
Not sufficient data on most chemicals
Not all chemicals can be tested
QSAR has been used successfully for over 60 years
Better to predict than have nothing
Why use QSAR?

## Slide 58
Prediction accuracy not higher than 65-70% for non-carcinogenic chemicals.
Lack of validation with up-to-date data.
Application to a narrow range of chemical structures.
Qualitative output.
Current limitations
Examples of Popular Toxicity Prediction Tools

## Slide 59
Next generation: powers of computational Chemistry
Docking software have been able to model very precisely the active site of a target enzyme (target to a drug for instance, or to a toxic).
In drug design such software are used to predict the best molecules for biological activity. Only the best performing are synthesized and tested.
Similar ideas can be used in toxicology
http://www.molfunction.com/software5.htm
Notes: Jakub’s slide

## Slide 60
Create a reliable tool for chemists which will not only predict the toxicity of existing chemicals but will allow a design of future molecules with reduced hazard
What’s the need?

## Slide 61
Toxicology
Chemistry
Molecular Biology
Computational Chemistry
Molecular Design Research Network
Notes: MoDRN is the collaboration between 4 universities Baylor, GW, UWASH and Yale that uses advances in biology, toxicology, computational chemistry and engineering to develop a robust and well validated computer software that will not only predict toxicity of existing compounds but it will serve as a tool to redefine guidelines for the next generation molecules with reduced hazard. The network will employ the newest strategies of computer modeling to build a computer software which will allow to understand what causes toxic endpoints and what can we do to avoid it. Our efforts will not only limit to research. To have the biggest possible impact we will engage educators and students on undergraduate and high school level to by including safer chemical design in students’ lesson plans and by developing interactive and hands-on teaching tools for undergraduate and high school students. Finally we plan to work with our colleagues across academia, colleagues across many industry sectors and policymakers on the government level to further inform and disseminate safe chemical concepts.

## Slide 62
Hazard and Risk – Past and Present
Toxicology
Assessing Hazards and Exposure
  What Happens When You’re Exposed?
Hazard Minimization Through Molecular Design
QSAR - Quantitative Structure Activity Relationship
Molecular Design Research Network (MoDRN)
Topics Covered

## Slide 63
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE