## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Innovation
Image: Wikimedia Commons, Refining Innovation, Author: U.S. Army Photo by Sgt. Aaron Ellerman, 204th Public Affairs Detachment
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
Transformative Innovation
  What is it that we really want?
Nature as Inspiration
  Design Challenges
Biomimicry
  Color
  Adhesives
  Structured materials, architecture
  Self-Cleaning
There is Still More We Can Learn from Nature
Topics To Be Covered

## Slide 3: Another design principle: Function vs molecule
Green Chemistry also needs to rethink the problem de novo. We move from considering the molecule/material to the function.
Thinking about function calls for interdisciplinary research to “think outside the box”
Molecule/materials
  - Bis phenol A/phtalate
  - Epoxy resin
  - Cis platinum
  - Poly ethylene terephthalate (PET)
  - dichloromethane
Function
  - Plasticizing
  - Coating
  - Catalyst
  - Materials which can be molded, does not leak..
  - Solvent

## Slide 4
Consider the function or service and NOT the product
Original product: Telephone Lines
What we really wanted is long distance communication.
Why not have a cellphone?
Key Concepts of Disruptive Innovation
Images: WikiCommons

## Slide 5
Consider the function or service and NOT the product
Key Concepts of Disruptive Innovation
Images: Wikipedia
“We have not invented electricity by improving candles”

## Slide 6
Coffee decaffeination
Coffee beans without caffeine
Original product: Facility to decaffeinate coffee
What we really wanted is decaffeinated coffee.
Why not have coffee beans that don’t have caffeine?
Decaf Coffee Innovation
Images: WikiCommons

## Slide 7
Dye produces various colors, but adds cost and waste issues
Naturally colored cotton
Original product: dye for cotton
What we really wanted is colored cotton
Why not have a naturally colored cotton?
Colored Fabric Innovation
Images: WikiCommons, http://www.knittersreview.com/

## Slide 8
Detergent
Self-cleaning clothes
Original product: detergent
What we really wanted is clean clothes
Why not have self cleaning clothes?
Clean Clothes Innovation
Images: WikiCommons

## Slide 9
Original product: lawn mower
What we really wanted short grass
Why not have a no-mow grass?
Lawn mower
No-mow grass
Grass Innovation
Images: WikiCommons

## Slide 10
Color without “dye”?
Scent without “fragrance”?
Adhesion without “adhesive”?
Disinfection without “disinfectant”?
Solvency without the “solvent”?
Catalysis without the catalyst?
Transformation without reaction?
Look to nature for inspiration
What Does That Mean for the Chemical Industry?

## Slide 11
Nature runs on sunlight
Nature uses only the energy it needs
Nature fits form to function
Nature recycles everything
Nature rewards cooperation
Nature banks on diversity
Nature demands local expertise
Nature curbs excesses from within
Nature taps the power of limits
How Nature Does Things..
Janine Benyus, Biomimicry
Notes: 11

## Slide 12
Biomimicry Is Not New…
Images: FirstAir, WikiCommons, The Biomimicry Institute
Notes: 12

## Slide 13
We can now imitate the nano-scale design features that give many natural materials some of their most interesting properties
… But Now It Is Molecular
Images: Pinterest (The Church – Micro), WikiCommons, GecksinTM
Notes: 13
Now applying its principles to emerging technologies; nature has been working at the nanoscale for billions of years. Technology has finally reached the point where we can manipulate materials as the nanoscale too…..
So we can innovate in new ways, for example adhesion without adhesives: Gecco “sticks” w/out adhesive…. Nano fibers on the feet interact with surface via VdW forces allowing the gecco to move upside down and sideways across surfaces. Scientists trying to mimic this with nanomaterials VIDEO

## Slide 14
    Filter particulates from air
    Filter water
    Create color
    Detect fire
    Retard fire
    Adhere or join
    Destroy macrobiotic pests / microbiotic pests
    Distribute data / information
    Distribute electricity
Some Design Challenges
Notes: 14

## Slide 15
    Fabrication of ceramics by nature
    Thermal insulation
    Cool or heat (buildings, clothing)
    Remediate soil
    Self-assembling materials
    Prevent corrosion
    Prevent mineral build-up
    Prevent biotic build-up
    Generate energy
    Sterile, disposable packaging
“After 3.8 billion years of research and development, failures are fossils, and what surrounds us is the secret of survival.”
- Janine Benyus
Overview of Innovation
Notes: 15

## Slide 16
Made by abalone
3,000x stronger than CaCO3
Ceramics and tough materials
Abalone are effectively ceramics factories:
They produce an extremely tough material at ambient temperature and pressure, no toxics, biodegradable
No waste, sustainable feedstock, no toxic substances, no outside sources of energy
One secret: nanopatterning to give extra robustness
Notes: 16
Ambient temperature and pressure, no toxics, biodegradable.
No waste, sustainable feedstock, no toxic substances, no outside sources of energy
Another example of crystallization from the “bottom up”: “Bell Labs Scientists Create World's First Micro-Patterned Crystals Inspired by Bioengineering Found in Nature” BUSINESS WIRE, Feb. 21, 2003:
About two years ago (2001), Aizenberg and her colleagues made the surprising discovery that thousands of calcite crystals spread throughout the exoskeletons of brittlestars, starfish-like marine invertebrates, collectively form an unusual kind of compound eye for the animals. The brittlestar's calcite microlenses expertly compensate for birefringence and spherical aberration, two common types of distortions in lenses. This led the Bell Labs scientists to attempt to mimic nature's success and design crystals based on the brittlestar model, with the ultimate goal of building complexes arrays of microlenses like the brittlestar's.
Today lenses are typically made using a "top down" approach, in which a piece of glass is ground down to a lens' exact specifications. The brittlestar, on the other hand, makes its microlenses using a "bottom up" approach, in which successive layers of calcite are deposited onto an organic template in intricate patterns to form perfect crystalline lenses at the temperature of seawater.
"This is an excellent example where we can learn from Nature," said Cherry Murray, senior vice president of physical sciences research at Bell Labs. "In this case, a relatively simple organism has a solution to a very complex problem in integrated optics and materials design. By studying the brittlestar, we can learn about low-cost ways of forming single crystals in complex shapes at low temperatures. While many years from commercial use, this understanding could be very important to fabrication of nano-patterned materials."

## Slide 17
Ceramics and tough materials
Industrial gas kiln: to make ceramics
http://bcgneeds.com/wp-content/uploads/2014/03/indoor-gas-kiln.jpg
Harsh temperatures
Sol gels can afford materials without the harsh temp requirements
Notes: 17
GE ceramics factory

## Slide 18
Ceramics and tough materials
Sol gel is also called “soft chemistry”
It gives access to great functionalities
http://tolweb.org/Diatoms/21810 - https://www.labroots.com/trending/microbiology/3886/diatoms-they-re-everywhere
Another inspiration from Nature: diatoms
These are porous materials
Porous materials can be made by sol gel techniques and are widely applied for e.g. for catalysis
Notes: 18
GE ceramics factory

## Slide 19
Nature producing colors
Dye strategy
A molecule that can absorb certain wavelength and scatter others
E.g β carotene
Nanopatterning
Nanopatterning of surfaces means light can interact with it and be scattered differently as a function of wavelength
Image: Flickr (Lisa Ann Yount)
Credit: Fabian Heinemann/Wikipedia
Images: Wikipedia
Mother of pearl
Electron microscopy image of a fractured surface of nacre (arrangements of CaCO3 plates)
Notes: 19
Take the peacock for example….

## Slide 20: Producing colors
Once upon a time, color was for the rich. Dyes had to be painstakingly derived from plants or animals; quality was uneven and rich hues like purple were reserved for royalty.
That all changed in 1856, when 18-year-old chemistry student William Perkin discovered a vivid purple that could be used to dye silk and other fabrics.
In tribute to the Parisian fashion world, he named the first synthetic dye after the French name of a purple plant: mauve.
Image: Wikimedia Commons, Purple dye-bath with fresh Hexaplex trunculus, Author: Kanold

## Slide 21: Producing colors
Perkin's mauve was soon followed by Verguin's fuchine, Manchester brown, Martius yellow, Nicholson's blue, Hofmann's violets, and a synthetic rainbow of other hues.
The market for natural dyes collapsed.
By the time Perkin tried to file the patent for his third dye, BASF beat him by one day.
Image: Wikimedia Commons, Dyed Wool Reels, Author: CSIRO

## Slide 22: Producing colors
Soon everyone knew how to make synthetic dyes.
It didn’t make any difference whether you bought them from Perkin, or Nicholson or Hoffman.
It didn’t make any difference if you bought them in the U.K., or Germany, or the U.S.
Dyes became commodities.
It wasn’t enough to simply make mauve more efficiently.
Image: Wikimedia Commons, Pigments for sale on market stall, Goa, India. Author: Dan Brady

## Slide 23: Producing colors
Many commercial dyes are toxic and release to the environment is causing concerns.
2 million tons of chemicals used for dyes production globally every year
https://bedfordviewedenvalenews.co.za/271705/still-no-solution-regarding-stream-pollution/
https://study.com/academy/lesson/textile-dyes-history-toxicity-pollution.html
A red pigment (pain) flows into the Modderfontein Golf course - Bedfordview & Edenvale News (South Africa)
Azo dyes, a class of synthetic nitrogen-based dyes that produce bright reds, oranges and yellows, are one of the most commonly used groups of dyes. They're cost effective to produce, but some of them can be dangerous and have toxic and carcinogenic effects.
Orange colored azo dyes

## Slide 24: Rethinking dyes
“Our team is designing the best enzymes and fermentation biotechnologies to efficiently transform sugar into renewable and long-lasting colors.” Pili team
They produce inks and dyes for textiles and plastics
In the long term, they look into biomass waste
Guillaume Boissonnat from Pili in their incubator at LeCNAM
Sugars
Fermentation
Biodegradable, non toxic dyes
https://www.pili.bio/

## Slide 25
Innovation inspired by a butterfly which, as blue as it seems, doesn’t have an ounce of dye.
Image: Harvard Radcliff Institute, NISE Network, and The Mirasol Effect
Nature producing colors: Nanopatterning

## Slide 26
Teijin Limited of Japan
Morphotex Fibers
No dyes or pigments
Color based on varying thickness and structure of fibers
Reduced energy consumption and chemical release by eliminating dye processes
Image: asknature
Producing colors: getting inspired by nature
Inspiration from Blue Morpho butterfly patterned wings
Notes: 26
Left - Morphotex structural colored fibers
Right - Morpho Butterfly wings.
Teijin Fibers Limited of Japan produces Morphotex fibers. No dyes or pigments are used. Rather, color is created based on the varying thickness and structure of the fibers. Energy consumption and industrial waste are reduced because no dye process must be used.

## Slide 27
Producing colors from cellulose
M. Kaushik, J.-L. Putaux, C. Fraschini, G. Chauve and A. Moores, “Transmission Electron Microscopy for the Characterization of Cellulose Nanocrystals”, ed. Khan Maaz, Pub. InTech, 2015, p.129-163
wood
cotton
Bamboo
Gluconacetobacter xylinus
Halocynthia papillosa
Glaucocystis
Notes: 27
Take the peacock for example….

## Slide 28
Producing colors from cellulose
M. Kaushik, J.-L. Putaux, C. Fraschini, G. Chauve and A. Moores, “Transmission Electron Microscopy for the Characterization of Cellulose Nanocrystals”, ed. Khan Maaz, Pub. InTech, 2015, p.129-163
Renewable, biodegradable and non-toxic
Commercially available from wood pulp
Celluforce plant can produce at the ton scale per day
High specific surface area (300m2/g)
Excellent mechanical strength
Thermally and chemically stable
Celluforce Plant
Notes: 28
Take the peacock for example….

## Slide 29
Producing colors from cellulose
Aqueous suspension can feature chiral nematic ordered phase
Iridescent and birefringent films
Reinforcing material precursor: CNC are less strong than CTN but more so than Kevlar
J.-F. Revol, H.Bradford, J. Giasson, R.H. Marchessault, D.G. Gray, Int. J. Biol. Macromol., 1992, 14, 170
S. Beck-Candanedo et al., Biomacromolecules, 2005
Ying Xu et al., J. Appl. Polym. Sci. 2008
D. Gray et al., Soft Matter 2008
Y. Shin et al. Mater. Lett. 2007
Notes: 29
Take the peacock for example….

## Slide 30
Producing colors from cellulose
Chirally ordered materials
pH responsive flocculants
Aerogels
Supercapacitors
Composites
K. E. Shopsowitz, H. Qi, W. Y. Hamad, M. J. MacLachlan, Nature 468, 422–425
K. H. M. Kan, J. Li, K. Wijesekera and E. D. Cranston, Biomacromolecules, 2013, 14, 3130-3139.
X. Yang and E. D. Cranston, Chem. Mater., 2014, 26, 6016-6025.
S. Y. Liew, D. A. Walsh and W. Thielemans, RSC Adv., 2013, 3, 9158-9162.
K. M. Z. Hossain, I. Ahmed, A. J. Parsons, C. A. Scotchford, G. S. Walker, W. Thielemans and C. D. Rudd, J. Mater. Chem., 2012, 47, 2675-2686.
Notes: 30
Take the peacock for example….

## Slide 31
Cranston, E. D., & Gray, D. G. (2008). Colloids and Surfaces A: Physicochemical and Engineering Aspects, 325(1-2), 44-51.
Lagerwall, J. P., Schütz, C., Salajkova, M., Noh, J., Park, J. H., Scalia, G., & Bergström, L. (2014). NPG Asia Materials, 6(1), e80.
Producing colors from cellulose
Spin coated cellulose nanocrystals: Order can be seen and explains the iridescence
a Wet suspension of cellulose nanocrystals, b, c and d are dried films.
Currently being developed for cosmetic applications (lipstick)
Notes: 31
Take the peacock for example….

## Slide 32
Blue Morpho butterfly scales
IMOD = InterferometricMODulation
IMOD-based innovation that is bistable (low power consumption) and highly reflective (display can be see in direct sunlight)
Display Technology
Image: mirasolTM
Screen displays can be made along the same principles by activating nanosized features in the screen
Notes: 32
Scales of the blue morpho butterfly inspired new digital display technology.
“Qualcomm’s mirasol display technology is based on a reflective technology called IMOD (InterferometricMODulation), with MEMS structures at its core. This MEMS–based innovation is both bistable, meaning it is both extremely low power, and highly reflective, meaning the display itself can be seen even in direct sunlight.”
MEMs = microelectromechanical systems

## Slide 33
Eastgate Building in Harare, Zimbabwe
90% less energy for ventilation than a comparable conventional building
Architecture
Image: www.morpho-biomimicry.be/
Inspired by: termite mounts
Notes: 33
Eastgate Building in Harare, Zimbabwe
Modeled after termite mound - which can only tolerate a temperature difference of 1 degree day or night.
Uses 90% less energy for ventilation than a comparable conventional building (by utilizing natural air flow through the building rather than relying on traditional HVAC system)

## Slide 34
Architecture
Sea Sponge
Image: WikiCommons
Notes: 34
The Swiss Re headquarters in London, otherwise known as "the gherkin," employs a cylindrical design to aid in ventilation with many engineering similarities to the structure of sea sponges.

## Slide 35
Self-Healing Materials and Systems
Beilstein J. Nanotechnol. 2018, 9, 907–935
Mechanism of bone repair
Nature does it all the time: wounds, bone breaks, immune response, adaptive camouflage, self cleaning in plants…
Mechanism of soft tissue repair (Invertebrates)
Notes: 35

## Slide 36
Self-Healing Materials and Systems
Image: Pixabay, Brinker
Brinker technology developed a way to seal leaks in oil and water pipelines called Platelets.
formula injected into wells/pipes and circulating freely until used
Notes: 36
Brinker technology developed a way to seal leaks in oil and water pipelines called Platelets. The technology works by injecting theformula into wells/pipes, as the platelets flow through the system, they are attracted to leak causing holes due to the pressure change encountered as they flow over them. The platelet fills the hole, preventing further leakage
Mimics human blood clotting.

## Slide 37
Self-Healing Materials and Systems
‘Healing’ material contain capsules within polymers.
When needed, the capsule are released and fill the void. For polymers and now iron/steel
Notes: 37
The concept is also applied to polymer and metal systems
Univ Ill Urbana Champagne researchers working on self healing materials: ‘healing’ material incorporated in capsules within polymers. When ruptured (due to cracking or similar), the material in the capsule is released and fills the void and restore structural integrity. Polymers and now iron/steel (self-healing electronics: restore electrical conductance)

## Slide 38
"I will design a unique, two-sided fastener, one side with stiff hooks like the burrs and the other side with soft loops like the fabric of my pants. I will call my invention 'velcro' a combination of the word velour and crochet. It will rival the zipper in its ability to fasten.”
- George de Mestral, 1945
Velcro
Image: WikiCommons
Inspired by seeds that can attach to animal fur via small hooks
Notes: 38
- hook-by loop fastener was invented in
1945 Swiss engineer George de Mestral who was irritated by the burrs that would cling to his clothing on walks
- inspiration: burdock plant

## Slide 39
Blue Mussel
Adhesives
Inspiration from Nature: the Mussel byssus
Mussel attach to rocks using catechol-based proteins
Mussel
Byssus
Byssus foot
And E. adhesive proteins
Notes: 39
In the event that adhesives are necessary….. Look to nature to determine a biocompatible, harmful chemical and VOC-free option
Columbia's PureBond is a soy-based formaldehyde-free technology used in the construction of hardwood plywood products.
Columbia Forest Products learned about natural adhesives from the blue mussel. This ocean species attaches itself firmly to underwater structures without use of toxic chemicals.

## Slide 40
Inspired by Nature humans have developed an adhesive, based on soy-source to fabricate wood boards.
No formaldehyde used:
Safer workplace
Safer homes (formaldehyde is a in door pollutant)
Adhesives
Notes: 40
In the event that adhesives are necessary….. Look to nature to determine a biocompatible, harmful chemical and VOC-free option
Columbia's PureBond is a soy-based formaldehyde-free technology used in the construction of hardwood plywood products.
Columbia Forest Products learned about natural adhesives from the blue mussel. This ocean species attaches itself firmly to underwater structures without use of toxic chemicals.

## Slide 41
Adhesives
Image: WikiCommons, Geim, A. K. et al. Microfabricated adhesive mimicking gecko foot-hair. Nature Materials
Notes: 41
self-cleaning (doesn’t stick to non-target materials like sand)
reusable
doesn’t use adhesive
a square centimeter can support 4 kg
how does it work?
gecko foot hairs typically have diameters of 200 to 500 nm. Gecko feet are made of keratin, “gecko tape” the experimental material made in 2003 made of a synthetic polymer

## Slide 42
Other uses:
Clothing waterproofing
Teflon alternatives
Glass coating
Lotus Effect
StoCoat Lotusan®
Superhydrophobicity
The surface structure of lotus leafs minimizes adhesion of dirt particles to the surface
Cleaning
Image: StoCorp, WikiCommons
Notes: 42
Avoid use of harsh chemical cleaners or repainting

## Slide 43
Organized Chaos…
Notes: 43
The organized chaos of a blanket of fall leaves inspired InterfaceFLOR designers to create Entropy, a line of carpet tiles with a random pattern. This randomness means that when any tile gets worn, it can be quickly replaced without worrying about mismatching dyes or patterns. This reduces waste and manufacturing costs. Entropy is part of InterfaceFLOR's i2 collection.

## Slide 44
“Pond scum may be a synonym for ‘primitive’, but the tiny organisms that compose it easily beat the human state of the art when it comes to capturing energy from the sun. Some purple bacteria answering to that unflattering description use light energy with almost 95% efficiency – more than four times that of the best man-made solar cells.”
- University of Southern California news release, August 22, 1994
Still More to Be Learned
Images: WikiCommons
Notes: 44
Bioluminescent bacteria, combine chemicals to light up their bodies
Dragonflies out maneuver helicopters
Hummingbirds cross the Gulf of Mexico on less than one tenth an ounce of fuel
Ants carry 100’s lbs equivalent in dead heat

## Slide 45
“If the age of Earth were a calendar year and today were a breath before midnight on New Year’s Eve, we showed up a scant fifteen minutes ago, and all of recorded history has blinked by in the last sixty seconds.”
- Janine Benyus
Still More to Be Learned
Images: WikiCommons
Notes: 45
Bees, turtles and birds navigate w/out maps
penguins dive without scuba gear
Artic fish and frogs freeze solid and then spring back to life, having protected their organs from ice damage
Chameleons and cuttlefish hide without moving by changing patterns in their skin to blend in with their surroundings
How do they do it?!

## Slide 46
Topics To Be Covered
Transformative Innovation
  What is it that we really want?
Nature as Inspiration
  Design Challenges
Biomimicry
  Color
  Adhesives
  Structured materials, architecture
  Self-Cleaning
There is Still More We Can Learn from Nature

## Slide 47
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE