## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
The 12 Principles of Green Chemistry
Image: Wikimedia Commons, Author: Steve Jurvetson
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
Anastas, P. T.; Warner, J.C. Green Chemistry: Theory and Practice, Oxford University Press,1998
The 12 Principles of Green Chemistry

## Slide 3
Anastas, P. T.; Warner, J.C. Green Chemistry: Theory and Practice, Oxford University Press,1998
The 12 Principles of Green Chemistry
The principles address:
  Toxicity
    - Reducing the hazard
  Feedstocks
    - Use of renewable resources
  Designing safer products
    - Non toxic products by design
  Biodegradability
    - Enhancing break down at the end of life
  Energy
    - Reducing the energy needs
  Accidents
    - Eliminating accidents
  Efficiency
    - Shorter processes and synthesis

## Slide 4
Waste Prevention
It is better to prevent waste than to treat or clean up waste after it is formed.
Image: Harshaw Chemical Company discharges waste water into the Cuyahoga river
Source: National Archives and Records Administration

## Slide 5: What is waste?
Waste is anything that is a leftover from the product/process and cannot be re-used.
Waste can be produced in any stage of a process life-cycle:
Origins of feedstock
Manufacturing
Distribution
Use
End of life
When is waste not waste?
When it can be reused, becoming a feedstock.
When it can be reduced or completely eliminated.
Waste Prevention

## Slide 6
Waste generated by different industry segments:
R. A. Sheldon, Chem. Ind., 1992, 903–906
R. A. Sheldon, Chem. Ind., 1997, 12–15
Production of pharmaceuticals produces a lot of waste due making complex molecules with demanding quality standards, often requiring batch processing; there are greater regulatory constraints and often high value and low volume products are manufactured.
Many industry sectors try to decrease waste generation by decreasing the number of synthetic steps to generate the product and by implementing a solvent recovery system.
Waste Prevention

## Slide 7
Waste Prevention
Case study: Sildenafil citrate production
Sildenafil citrate, commonly known as Viagra, is a selective inhibitor of phosphodiesterase 5 (PDE5). This new drug immediately became a major seller, achieving sales of more than $1 billion during its first year on the market. With such a rapid sales take off it was critical that the environmental performance of the synthesis was good from the outset.
Conventional sildenafil citrate synthesis included:
11 step synthesis, which gave a 4.2% overall yield.
Tin chloride, a heavy metal and a major environmental polluter.
The use of stoichiometric quantities of thionyl chloride in a solvent. This has a high environmental impact.
Hydrogen peroxide, which causes burns upon skin contact and is a fire and transportation hazard, especially when in contact with organic materials.
Produced over 1300 L of waste per 1 kg of product.
The amount of organic waste produced by the sildenafil citrate processes at various time points
Dunn, P.J et al Green Chem., 2004, 6, 43-48

## Slide 8
Waste Prevention
Alternative production of sildenafil citrate:
Average yield of last three steps = 97% yield.
Reduction of the ratio of solvent waste/kg product over 17 years from 1300 L/kg to only 7 L/kg by minimizing solvent use, increasing solvent recovery, improving solvent selection, and telescoping steps.
Only the solvents t-butanol, ethyl acetate, 2-butanone, and a trace of toluene still require disposal.
Dunn, P.J et al Green Chem., 2004, 6, 43-48
Case study: Sildenafil citrate production

## Slide 9
Conventional method of obtaining phenols from petroleum:
Petroleum
Phenols (benzene, toluene, xylenes)
The method is not sustainable – it is dependent on depleting resources.
Case study: Phenols
Phenols are widely used in household products and as intermediates for industrial synthesis. They are often referred to as drop-in platform chemicals.
Waste Prevention
Image: Pixabay

## Slide 10
Alternative production of phenols from biomass waste using depolymerization:
This method uses abundant product (waste) as a starting material.
Waste Prevention
Phenols
Biomass
Case study: Phenols
Image: Pixabay

## Slide 11
Waste Prevention
Case study: Production of ethylene oxide
Ethylene oxide is used as an intermediate in the production of several industrial chemicals, the most notable of which is ethylene glycol. It is also used as a fumigant in certain agricultural products and as a sterilant for medical equipment and supplies.
Conventional ethylene oxide synthesis included:
A 2-step synthesis with a chlorohydrin intermediate.
For each kilogram of product, 5 Kg of waste were disposed.

## Slide 12
Alternative production of ethylene oxide:
Waste Prevention
Use of molecular oxygen removes the need for chlorine.
New process generates more than 16 times less waste than the original one, and eliminates the formation of waste water.
Case study: Production of ethylene oxide
Image: Wikimedia Commons, Author: LHcheM

## Slide 13
Waste Prevention
Case study: Revalorization of biofuel byproducts
When byproducts cannot be avoided, other innovative solutions should be considered. One productive solution is to seek an industrial ecology approach where the waste can become a new raw material with significant value for another process as it re-enters the life-cycle. This approach is currently being applied to the production of biofuel.
+
Waste
+
Material
Energy
Waste
Energy
Biofuel
1.
2.

## Slide 14
Atom Economy
Synthetic methods should be designed to maximize the incorporation of all materials used in the process into the final product.
Image: Wikimedia Commons, Author: Astrid 91

## Slide 15
Atom Economy
In 1990 Barry Trost introduced the concept of synthetic efficiency: Atom Economy (AE). It refers to the concept of maximizing the use of raw materials so that the final product contains the maximum number of atoms from the reactants.
The ideal reaction would incorporate all of the atoms of the reactants.
The AE is measured as the ratio of the molecular weight of the desired product over the molecular weights of all reactants used in the reaction.
Additional considerations when designing a green reaction:
Generation of co-products and waste, toxicity of co-products and waste, energy needs, purification steps, solvent and catalyst usage

## Slide 16
Atom Economy
Example: Epoxidation of styrene
Assume 100% yield.
100% of the desired epoxide product is recovered.
100% formation of the co-product: m-chlorobenzoic acid.
A.E. of this reaction is 23%.
77% of the products are waste.
desired epoxide
waste
styrene

## Slide 17
Conventional method of styrene production:
Use of benzene, a known carcinogen, as a starting material.
High temperature (800-950 0C).
Case study: Styrenes
Atom Economy
Styrenes are precursors to polystyrene. Polystyrene is one of the most widely used plastics, the scale of its production being several million tons per year.

## Slide 18
Alternative method of styrene production from butadiene using Diels-Alder reaction:
Diels-Alder reaction = 100% atom economy.
Use of non-toxic starting material.
Case study: Styrenes
Atom Economy

## Slide 19
Conventional synthesis of ibuprofen:
Case study: Ibuprofen
  6 stoichiometric steps.
  <40% atom utilization.
Atom Economy

## Slide 20
Alternative catalytic synthesis of ibuprofen:
  3 catalytic steps.
  80% atom utilization.
  BHC
Case study: Ibuprofen
Atom Economy

## Slide 21
Less Hazardous Chemical Synthesis
Whenever practicable, synthetic methodologies should be designed to use and generate substances that possess little or no toxicity to human health and the environment.
Image: Wikimedia Commons, Center for Biofilm Research Laboratory Montana State University

## Slide 22
Ideally, non-toxic substances are used to synthesize a chemical product.
Less Hazardous Chemical Synthesis

## Slide 23
Organic chemistry’s synthetic toolbox has been significantly improved over the past decade by the innovative work of green chemists and the many new reactions that have been developed.
Cascade, or tandem reactions, such as C–H activation, metathesis, and enzymatic reactions are some excellent examples of the cleaner and more efficient synthetic tools that are now available to organic chemists.
Less Hazardous Chemical Synthesis

## Slide 24
Case study: Synthesis of adipic acid
Adipic acid (AA), also referred to as hexanedioic acid, is one of the most produced commodity chemicals worldwide. With a projected global market size of more than 7 billion US dollars by 2019, AA is a versatile building block for an array of processes in the chemical, pharmaceutical and food industries. Its primary use is as a precursor for the synthesis of the polyamide Nylon-6,6.
Conventional synthesis of adipic acid:
Uses benzene, a known carcinogen, as a starting material.
Involves oxidation with an excess of HNO3, and production of greenhouse gas nitrous oxide (N2O), the latter accounting for approximately 5–8% of the worldwide anthropogenic N2O emissions.
Less Hazardous Chemical Synthesis

## Slide 25
Alternative synthesis of adipic acid:
Development of biocatalytic processes for producing adipic acid and catechol from sugars.
Biocatalytic process using yeast converts sugars to cis,cis-muconic acid, and this intermediate stage allows ready access to catechol and adipic acid.
Uses water as solvent at ambient temperature and pressure.
Less Hazardous Chemical Synthesis
Case study: Synthesis of adipic acid
Raj, K et al. Biocatalytic production of adipic acid from glucose using engineered Saccharomyces cerevisiae. Metabolic Engineering Communications. 6, 2018, 28-32

## Slide 26
Conventional paper bleaching with Chlorine dioxide (ClO2):
Produces unacceptable quantities of chlorinated pollutants.
Many of these pollutants are exceptionally toxic.
Alternative technology for paper bleaching with TAML/H2O2:
Alternative catalytic breakdown of H2O2 provides the oxidative equivalent.
Lower temperature and time requirements.
Case study: Paper Bleaching
Less Hazardous Chemical Synthesis
Image: Wikimedia Commons, Author: Sammutawe

## Slide 27
Designing Safer Chemicals
Chemical products should be designed to preserve efficacy of the function while reducing toxicity.
Image: Wikimedia Commons, Author: Sentryair

## Slide 28: The modern motto of toxicology:
“Everything is toxic. It is simply depends on the dose”
Often otherwise phrased as
“The dose makes the poison.”
Risk = Hazard x Exposure
Green chemistry and engineering focus on reducing risk by reducing hazard.
Designing Safer Chemicals

## Slide 29
Hazard types to avoid:
  Toxicological/Eco-toxicological
    Carcinogenicity
    Reproductive
    Developmental
    Neurological
    Global warming potential
    Ozone depleting potential
    Bioaccumulation
    Persistence
  Physical
    Explosivity
    Flammability
    Corrosivity
Physical/Chemical Properties to consider:
  Water solubility
  Log Kow
  Volatility
  Molar volume
  Aspect ratio
  Radical formation
  Nucleophilicity
  Electrophilicity
  pH/pKa
  Surface area
  Reducing potential
  Oxidizing potential
  Polarizability
Designing Safer Chemicals

## Slide 30
Chemists can design chemicals which have reduced toxicity by:
- Manipulation of chemical bonds, chemical functional groups.
  Reactive functional groups have a greater potential to be toxic. Removing these groups is likely to reduce toxicity.
- Elimination of the molecular initiating event that activates pathway
  While difficult to achieve, if the chemical is modified not to interact with the biological pathway, no biological effect is triggered and the toxicity can be avoided.
- Reducing or eliminating bioavailability.
  If a chemical does not absorb into a body, it cannot cause harm.
Designing Safer Chemicals

## Slide 31
Conventional use of organotin compounds as antifoulants:
TBTO and other organotin antifoulants have long half-lives in the environment (the half-life of TBTO in seawater is over 6 months).
They bioconcentrate in marine organisms (the concentration of TBTO in marine organisms has been found to be up to 104 times greater than in the surrounding water).
Organotin compounds are chronically toxic to marine life and can enter food chain.
They are bioaccumulative.
Tributyltin oxide (TBTO)
Case study: Antifoulants
Designing Safer Chemicals
Antifoulants are generally dispersed in the paint as it is applied to the hull. Organotin compounds such as tributyltin oxide (TBTO) have traditionally been used. TBTO works by gradually leaching from the hull and killing the fouling organisms in the surrounding area.

## Slide 32
Alternative antifoulants:
Sea-Nine® 211 works by maintaining a hostile growing environment for marine organisms. When organisms attach to the hull (treated with DCOI), proteins at the point of attachment with the hull react with the DCOI. This reaction with the DCOI prevents the use of these proteins for other metabolic processes. The organism detaches itself and searches for a more hospitable surface to grow upon.
Only organisms attached to hull of ship are exposed to toxic levels of DCOI.
Readily biodegrades once leached from ship (half-life is less than one hour in sea water).
Case study: Antifoulants
Designing Safer Chemicals

## Slide 33
In 2014, the Solberg Company earned an award for its halogen-free RE-HEALING Foams for use in fighting fires. Traditionally, firefighting foams used fluorinated surfactants, persistent chemicals that have the potential for negative environmental impacts.
The RE-HEALING firefighting foam concentrates use a blend of non-fluorinated surfactants and sugars. This works well and with far less environmental impact.
Control, extinguishing time, and burnback resistance are paramount to the safety of firefighters everywhere, and the new foams have excellent performance in each category. The RE-HEALING Foams also achieve full regulatory compliance with existing fire protection standards.
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-2014-designing-greener-chemicals-award
Designing Safer Chemicals

## Slide 34
Conventional use of agricultural pesticide and a malarial control agent Dichlorodiphenyltrichloroethane (DDT):
DDT
Carcinogenic.
The threat to wildlife - especially birds – has almost led to the extinction of a bald eagle population.
Case study: Pesticides
Image Source: http://www.avoidingregret.com/2014/06/photo-essay-eggs-and-nests-of-bird.html
Designing Safer Chemicals
Notes: DDT was used in the second half of World War II to control malaria and typhus among civilians and troops. After the war, DDT was made available for use as an agricultural insecticide and its production and use duly increased. Müller was awarded the Nobel Prize in Physiology or Medicine "for his discovery of the high efficiency of DDT as a contact poison against several arthropods" in 1948
Unfortunately it’s effect on birds was not tested. Research have shown that for certain species, DDT causes the thinning of eggshells which led almost to species extinction.

## Slide 35
Alternative (and natural) use of Spinosad for insect control:
  Produced by bacteria Saccharopolyspora spinosa.
  Isolated from Caribbean soil samples (sugar mill).
  It selectively targets nervous system of insects.
  Demonstrates high selectivity, low mammalian toxicity, and a good environmental profile.
  Dow AgroSciences
Case study: Pesticides
  Saccharopolyspora spinosa
Toxicity scorecard
Rat: LD50>5000 mg/kg
Duck: LD50>5000 mg/kg
Fish: LC50-96h=30.0 mg/L
Bee: LD50=0.0025 mg/bee
Designing Safer Chemicals

## Slide 36
Safer Solvents and Auxiliaries
The use of auxiliary substances (solvents, separation agents, etc.) should be made unnecessary whenever possible and, when used, innocuous.
Image: Dr. El Sayed Arafat from NAWCAD’s Materials Lab, U.S. Navy

## Slide 37
Solvents account for the vast majority of mass wasted in syntheses and processes. Moreover, many conventional solvents are toxic, flammable, and/or corrosive.
Solvents volatility and solubility have contributed to air, water and land pollution, have increased the risk of workers’ exposure, and have led to serious accidents.
Recovery and reuse, when possible, is often associated with energy-intensive distillation and sometimes cross contamination. In an effort to address all those shortcomings, chemists have started to search for safer solutions.
Safer Solvents and Auxiliaries

## Slide 38
Problematic organic solvents
No Solvent Supercritical fluids
Water solvent Ionic liquids
Avoidance
Environmentally
benign and safe
Easily separable, safe
Zero
Volatility
Greener alternatives
Safer Solvents and Auxiliaries

## Slide 39
Case study: Coffee decaffeination
Conventional method of coffee decaffeination:
Coffee decaffeination was performed in a chlorinated organic solvent, dichloromethane (DCM), exposure to which can lead to headaches, mental confusion, nausea, vomiting, dizziness and fatigue.
Coffee beans were heated with steam and then exposed to DCM for decaffeination.
Safer Solvents and Auxiliaries
Image: Wikimedia Commons, Coffee Mechanical Separator, Aquapulp

## Slide 40
Soaking green coffee beans in water doubles their size, allowing the caffeine to dissolve into water inside the bean.
Caffeine removal occurs in an extraction vessel (70 feet high,10 feet in diameter), suffused with carbon dioxide at roughly 90 °C and 250 atm. Caffeine diffuses into this scCO2. The beans enter at the top of the chamber and move toward the bottom over 5 hours.
Decaffeinated beans at the bottom of the vessel are removed, dried and roasted.
Recovery of dissolved caffeine occurs in an absorption chamber. A shower of water droplets leaches the caffeine out of the supercritical carbon dioxide. The caffeine in this aqueous extract is then often sold to soft-drink manufacturers and drug companies. The purified carbon dioxide is recirculated for further use.
Alternative method for coffee decaffeination:
Zosel, K. Practical Applications of Material Separation with Supercritical Gases. Angew. Chem., Int. Ed. 1978, 17, 702-709
Safer Solvents and Auxiliaries
Case study: Coffee decaffeination

## Slide 41
Delicate biomedical materials such as vaccines and tissues are conventionally sterilized with ethylene oxide - a carcinogenic, mutagenic, toxic, and flammable gas - or with gamma radiation, which is lethal to all cells.
Both methods damage the materials they are sterilizing.
Ethylene oxide persists in tissue.
Case study: Medical sterilization
Conventional medical sterilization:
Safer Solvents and Auxiliaries
Image: Svetlana Pohovey, 359th Medical Group, U.S. Air Force photo/Staff Sgt. Kevin Iinuma

## Slide 42
Development of a supercritical carbon dioxide (scCO2) based method for sterilization of biological material.
NovaSterilis sterilization uses scCO2, peracetic acid, and small amounts of water at low temperatures and modest pressures to achieve rapid sterilization of sensitive biomaterials.
NovaSterilis Inc.
Alternative medical sterilization:
Safer Solvents and Auxiliaries
Case study: Medical sterilization

## Slide 43
Case study: Replacing dichloromethane (DCM) in chromatography
Amgen’s Green Solvents for Chromatography in practice. If a compound suitably elutes in 5% DCM–MeOH, the bar chart predicts that 60% 3 : 1 EtOAc : EtOH in heptanes or 40% i-PrOH in heptanes would be a suitable starting point to evaluate greener solvent alternatives.
Amgen developed a guide to replace DCM with greener alternatives. DCM is known to be associated with respiratory and cardiovascular toxicity in humans, carcinogenicity, and genotoxicity.
The guide on the right compares the eluting power of different greener solvent mixtures with reference to DCM-Methanol.
Safer Solvents and Auxiliaries

## Slide 44
Zoloft® is an anti-depressant and was once one of the best selling pharmaceuticals on the market.
Conventional sertraline synthesis:
Synthesis was a three step process.
Used 4 hazardous solvents (methylene chloride, tetrahydrofuran, toluene, and hexane).
Zoloft®
Safer Solvents and Auxiliaries
Case study: Manufacturing process for sertraline, the active ingredient in the popular drug Zoloft®

## Slide 45
The process was streamlined to a single step that is carried out in ethanol, a much less toxic solvent.
The new process is also catalytic, cutting down on starting materials by 60%, 45%, and 20% for the three components of the reaction.
The combined steps eliminated 310,000 pounds of titanium tetrachloride, 220,000 pounds of 50% sodium hydroxide, 330,000 pounds of 35% hydrochloric acid waste, and 970,000 pounds of solid titanium dioxide waste per year.
Pfizer, Inc
Case study: Manufacturing process for sertraline, the active ingredient in the popular drug Zoloft®
Alternative sertraline synthesis:
Safer Solvents and Auxiliaries
Image: Wikimedia Commons, Author: Ragesoss

## Slide 46
Design for Energy Efficiency
Energy requirements should be recognized for their environmental and economic impacts and should be minimized. Synthetic methods should be conducted at ambient temperature and pressure.
Image: U.S. Air Force photo/Bill Evans

## Slide 47
Most energy is used for heating, cooling, separations and pumping.
Ideally, all reactions are performed at ‘ambient’ conditions – room temperature and atmospheric pressure – in order to minimize energy usage.
Design for Energy Efficiency
Image: Wikimedia Commons, Janicki Omni Processor Pilot Plant in Dakar, Senegal , Author: Janicki Bioenergy

## Slide 48
Atorvastatin, a cholesterol-lowering drug, suffers from an energy-demanding synthesis as a result of two cryogenic reactions at - 70 oC
New biocatalytic synthesis uses enzyme DERA and shortens the process by removing two energy intensive chemical steps.
Case Study: Atorvastatin
Design for Energy Efficiency
Notes: Deoxyribose-5-phosphate Aldolase as a Synthetic Catalyst'

## Slide 49
Sono-, microwave-, and photo-assisted chemistry are known to save energy, improve reaction time, and catalytic activity.
Sonochemistry:
Uses of high frequency (20-100 kHz) sound waves to promote chemical reaction.
The collapse of bubbles formed in a solution generates a very high temperature and a higher pressure than conventional heating.
Used in the production of triglycerides from methyl transesterification.
Microwave:
Uses a high-frequency electric field to heat or cool the local environment with electrical charges.
Avoids unnecessarily prolonged residence time at a given temperature.
Photo-assisted:
Naturally occurring, such as using the sun as a catalyst.
Used in photo-driven acylation for the production of valuable synthetic intermediates and commercial fragrances in bulk.
Used by BASF to develop automotive primer coating, a precursor readily able to be crosslinked under photo irradiation, as opposed to its conventional energy-intensive thermally driven variation.
Design for Energy Efficiency

## Slide 50
Use of Renewable Feedstocks
A raw material or feedstock should be renewable rather than depleting whenever technically and economically practical.
Image: Wikipedia, Pongamia Pinnata Seeds

## Slide 51
Petroleum Products [Hydrocarbons]
Biomaterials [Carbohydrates, Proteins, Lipids]
Highly Functionalized Molecules
Functionalized Compounds [Olefins, Alkylchlorides]
Highly Functionalized Molecules
Use of Renewable Feedstocks

## Slide 52
Chart: Biomass production in nature: 180 billion metric tons/year
| Carbohydrates | Lignin | Fats, proteins, terpenes, etc.
Sales | 75 | 20 | 5
Only about 4% utilized by humans
(food, ethanol, sweeteners)
Nature’s richest source of aromatic carbon. Used in polymers, adhesives, production of phenolic chemicals.
Converted into polymers, lubricants, and detergents.
Building blocks for a diverse chemical platform.
Use of Renewable Feedstocks

## Slide 53: Case study: Producing polymers from renewable resources (PHAs)
The development of microorganisms that produce polyhydroxyalkanoates (PHAs) are from renewable feedstocks such as cornstarch and cellulose hydrolysate.
The microorganisms have proven to be applicable to conventional commercial equipment and can even be recycled using this same equipment.
They can be used in biodegradable products, such as credit cards.
They are comparable with polyolefins - which are made from petroleum feedstocks - in terms of strength, melting point, and can be manufactured with the existing equipment.
Polyhydroxyalkanoates (PHAs) are a broadly useful family of natural, environmentally friendly, and high-performing, bio-based plastics.
Metabolix
Use of Renewable Feedstocks
Image: Alpha Stock Images, Author: Nick Youngson

## Slide 54
Carpet tile backings were usually comprised of bitumen, polyvinyl chloride (PVC), or polyurethane - which are all derived from petroleum.
PVC - the most common base for carpet tile backings - is made from vinyl chloride, a toxic substance which releases toxic dioxins and hydrochloric acid as byproducts upon combustion.
Case study: Carpet tile backings
Conventional synthesis:
Use of Renewable Feedstocks
Image: Wikimedia Commons, Swatches of Carpet, Author: Quadell

## Slide 55
Shaw Industries, Inc
Alternative synthesis:
The development of a new, recoverable carpet backing.
Utilizing a combination of low-toxicity polyolefin resins, the backing can be separated from any fiber and recovered by elutriation, grinding, and air separation.
Collection, transportation, elutriation, and reprocessing is less expensive than using fresh starting material.
Use of Renewable Feedstocks
Case study: Carpet tile backings
Image: Flickr, Author: Emily May

## Slide 56
Conventional synthesis:
Over 400 million pounds of toner are consumed in the U.S. each year.
Conventional petroleum-based resin toners are difficult to remove from paper, making paper recycling more intensive.
Case study: Development and commercialization of toners
Use of Renewable Feedstocks
Image: Wikimedia Commons, Black toner container, Author: Adamantios

## Slide 57
Alternative process:
The development of a novel, bioderived printer toner that is easier to deink from paper.
This technology incorporates functional groups in their toners that are susceptible to chemical degradation for recycling.
These toners are biobased, derived from soybean oil and corn.
At 25% market penetration, this technology could reduce CO2 emissions by 360,000 tons/year.
Battelle
Use of Renewable Feedstocks
Case study: Development and commercialization of toners

## Slide 58
Case study: Production of levulinic acid
Levulinic acid is used as a precursor for pharmaceuticals, plasticizers, and various other additives. It is also widely used as a building block or starting material for a wide number of compounds.
Conventional synthesis:
Obtained by heating hexoses (glucose, fructose) or starch in dilute hydrochloric acid or sulfuric acid.
The yield depends on the nature of the acid, acid concentration, temperature, and pressure.
The reaction also produces hard to remove by-products.
Use of Renewable Feedstocks

## Slide 59
Paper mill
sludge
Levulinic acid
Municipal solid waste
and waste paper
Agricultural
residues,
waste wood
Alternative synthesis:
Levulinic acid can be obtained from paper mill sludge, agricultural and municipal waste and paper.
Utilizes a high-temperature, dilute-acid hydrolysis process that converts cellulosic biomass.
Biofine, Inc
Use of Renewable Feedstocks
Case study: Production of levulinic acid

## Slide 60
Reduce Derivatives
Unnecessary derivatization (blocking group, protection/deprotection, temporary modification of physical/chemical processes) should be avoided whenever possible.
Image: Wikimedia Commons, Center for Biofilm Research Laboratory Montana State University

## Slide 61
Substrate
Product
Substrate
Intermediate A
Intermediate B
Intermediate C
Intermediate D
Intermediate E
Product
Conventional approach
Green Chemistry approach
Reduce Derivatives
Notes: Whenever possible, limit number of steps and unnecessary transformations. Avoid the use of protecting groups as it requires extra reagents and generates more waste.

## Slide 62
Synthesis of 6-aminopenicillanic acid – core moiety of penicillin
Conventional synthesis of 6-aminopenicillanic acid using 3 steps and intermediate products:
Alternative synthesis using enzyme and fewer derivatives:
Case study: 6-aminopenicillanic acid
Reduce Derivatives

## Slide 63
Catalysis
Catalytic reagents (as selective as possible) are superior to stoichiometric reagents.
Image: Flickr, Catalysts, Author: BASF Catalysts

## Slide 64
Catalysts can facilitate complex reactions by:
  Lowering the activation energy of the reaction.
  Reducing temperature necessary to achieve a reaction.
  Controlling the site of the reaction (selectivity enhancement).
Image source: Adobe stock
Catalysis
Notes: Catalysts lower the activation (threshold energy) in the reaction.

## Slide 65: Heterogeneous vs Homogeneous
Distinct solid phase
Readily regenerated & recycled
Readily separated
Rates not as fast
Diffusion limited
Sensitive to poisons
Lower selectivity
Long service life
High energy process
Poor mechanistic understanding
Same phase as rxn medium
Expensive and/or difficult to separate
Difficult to separate
Very high rates
Not diffusion controlled
Robust to poisons
High selectivity
Short service life
Mild conditions
Mechanisms well understood
Catalysis

## Slide 66
Distinct solid phase
Readily regenerated & recycled
Readily separated
Rates not as fast
Diffusion limited
Sensitive to poisons
Lower selectivity
Long service life
High energy process
Poor mechanistic understanding
Green
catalyst
Catalysis
Heterogeneous vs Homogeneous
Same phase as rxn medium
Expensive and/or difficult to separate
Difficult to separate
Very high rates
Not diffusion controlled
Robust to poisons
High selectivity
Short service life
Mild conditions
Mechanisms well understood

## Slide 67
  Dartt and Davis
Case study: Green naproxen synthesis
  97% yield in three steps
Nonsteroidal anti-inflammatory drug (NSAID) of the propionic acid class (the same class as ibuprofen) that relieves pain, fever, swelling, and stiffness; COX inhibitor
Catalysis
Notes: cyclooxygenase

## Slide 68
Polyoxometalate (POM) catalysts
  - non-toxic, inorganic cluster compounds
  - selectively delignify wood
  - utilize only air and water
Allows use of oxygen instead of chlorine as the whitener of paper pulp and water as the solvent
Generates only CO2 and H2O, instead of chlorinated organics
  Hill, Emory University;
  Hill et al, Nature 2001, 414, 191–195
Case study: Paper production
Catalysis
1st step
2nd step
3rd step
4th step

## Slide 69
One of Dow Chemical’s awards is for a green catalyst that reduces the environmental footprint associated with producing propylene oxide, one of the biggest volume industrial chemicals in the world. The Hydrogen Peroxide to Propylene Oxide (HPPO) process, which was developed jointly with BASF, serves as a chemical building block for a vast array of products including detergents, polyurethanes, de-icers, food additives, and personal care items. The new process reduces the production of wastewater by as much as 70–80 percent and reduces the use of energy by 35 percent over conventional technologies.
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-2010-greener-synthetic-pathways-award
Catalysis
propylene oxide molecule
Image: Wikipedia, propylene oxide molecule, Author: Jynto

## Slide 70
A new catalyst developed by pharmaceutical companies Merck and Codexis for the green synthesis of sitagliptin - the active ingredient in the type 2 diabetes treatment Januvia™ - may also be useful in the manufacturing of other drugs. For example, recent clinical trial showed that it may help patients with acute coronary syndrome.
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-2010-greener-reaction-conditions-award
Catalysis
sitagliptin
Image: Wikipedia, sitagliptin, Author: NEUROtiker

## Slide 71
An example of green catalysts with the potential to reduce the pharmaceutical industry’s environmental impact is the powerful series of tetra-amido macrocyclic ligand (TAML) catalysts modelled on natural peroxidase enzymes developed by Terry Collins of Carnegie Mellon University. Collins thinks that using the catalysts at a late stage in the sewage treatment process would allow them to break down a wide variety of chemical residues - including those from Lipitor, Prozac, Zoloft, the contraceptive pill, and more - before they enter the environment.
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-1999-academic-award
Catalysis
Image: Wikicommons, Pipes of the Minsk sewage treatment plant, Author: Homoatrox

## Slide 72
Design for Degradation
Chemical products should be designed so that at the end of their function they do not persist in the environment and instead break down into innocuous degradation products.
Image: Wikicommons, a landfill in Dryden, Ontario, Author: Michelle Arseneault

## Slide 73
Early examples:
  Sulfonated detergents
    Alkylbenzene sulfonates – 1950’s & 60’s
    Foam in sewage plants, rivers, and streams
    Persistence was due to long alkyl chain
    Introduction of an alkene group into the chain increased degradation
  Chlorofluorocarbons (CFCs)
    Do not break down, persist in atmosphere and contribute to destruction of the ozone layer.
  DDT
    Bioaccumulate and cause thinning of egg shells
Design for Degradation

## Slide 74
Conventional plasticizers, such as DiNP, are an additive used to soften plastics:
DiNP exposure has been linked to liver toxicity, endocrine disruption, and carcinogenicity.
The additives persist in the environment.
Case study: Plasticizers
Plasticizers for plastics are additives, most commonly phthalate esters in PVC applications. Almost 90% of plasticizers are used in PVC, giving this material improved flexibility and durability. The majority of PVC is used to produce films and cables.
Design for Degradation

## Slide 75
Alternative plasticizers, such as isosorbide diester, can be derived from starch:
Offers 1 to 1 substitution of DiNP in plastics.
Isosorbide diester is thermally stable and biodegradable.
Design for Degradation
Case study: Plasticizers

## Slide 76
Conventional plastics (PET) are made from petroleum:
PET Plastic persists in the environment
It is made from depleting resources
high temperature
vacuum
catalyst
Petroleum
Case study: Plastics
Design for Degradation

## Slide 77
Synthesis of PolyLactic Acid (PLA) from starch:
The development of a biobased, compostable, and recyclable polylactic acid (PLA) polymer that uses 20–50 percent less fossil fuel resources than comparable petroleum-based polymers.
It is the first family of polymers derived entirely from renewable resources that can compete cost-effectively with traditional fibers and plastic packaging materials.
The manufacturing process consists of three solvent-free steps that lead to the production of lactic acid, lactide, and PLA high polymer with very high yields and internal recycling schemes that reduce waste.
PLA is fully biodegradable or can be readily hydrolyzed into lactic acid for recycling back into the process.
Cargill Dow LLC
Design for Degradation
Case study: Plastics
Alternative process:

## Slide 78
Case study: Fire extinguishers
Conventional approaches:
Chemical additives or alternatives to water for firefighting applications can have negative long-term environmental and health effects.
Halon gases are destructive to the ozone layer.
Aqueous film-forming foams release both toxic hydrofluoric acid and fluorocarbons when used.
Fluorosurfactant compounds are resistant to microbial degradation, often leading to contamination of groundwater supplies and failure of wastewater treatment systems.
Design for Degradation
Image: Wikimedia Commons, Author: Caduser2003

## Slide 79
The development of a fire extinguishing foam that is nontoxic and highly biodegradable.
PYROCOOL F.E.F. (Fire Extinguishing Foam) is an alternative formulation based on a biodegradable surfactant.
PYROCOOL F.E.F. has a low application volume.
Extinguishing an oil tanker fire estimated to take 10 days can be put out in 12.5 minutes.
Alternative production:
Design for Degradation
Case study: Fire extinguishers
Image: Wikimedia Commons, Kyrgyz Republic firefighters, Author: Senior Airman Brett Clashman, U.S. Air Force

## Slide 80
Real-time Analysis for Pollution Prevention
Analytical methodologies need to be further developed to allow for real-time in-process monitoring and control prior to the formation of hazardous substances.
Image: Wikimedia Commons, Author: Hindustanilanguage

## Slide 81
Real time analysis for a chemist is the process of “checking the progress of chemical reactions as it happens”.
Knowing when your product is “done” can save a lot of waste, time, and energy!
Real-time Analysis for Pollution Prevention

## Slide 82: The Role of Analytical Chemistry
Analytical chemistry has been at the heart of the environmental movement since its inception. It’s been used in:
    Identification
    Monitoring
    Measurement
    Characterization
Real-time Analysis for Pollution Prevention

## Slide 83: What Does Green Analytical Chemistry Mean?
Green Chemistry is applicable to all chemical processes, including the methods, protocols and processes of environmental analytical chemistry.
Image: Wikipedia
Real-time Analysis for Pollution Prevention

## Slide 84: Examples of Green Analytical Chemistry Methodologies
Supercritical Fluid Extraction
X-ray fluorescence detection for multi-metal matrix
Solid-phase extraction and micro-extraction
Image Sources: https://www.thermofisher.com, https://www.intechopen.com/books/herbicides-advances-in-research/recent-advances-in-the-extraction-of-triazines-from-water-samples, http://soviethammer.info/thlon/s/supercritical-fluid-extraction-co2/
Real-time Analysis for Pollution Prevention

## Slide 85: Process Analytical Chemistry to Minimize Waste Generation
Through the use of real-time, in-process monitors, sensors, etc., pollution and hazardous waste generation can be prevented rather than simply measured after it is produced.
Solid-acid catalyzed 1-butene/isobutane alkylation process:
  replaces HF and H2SO4 catalysts
  process utilizes supercritical CO2 to prevent coke accumulation in pores of solid catalyst
  on-line GC analysis
Subramaniam, University of Kansas
Ind. Eng. Chem. Res., 2001, 40 (18), pp 3879–3882
Real-time Analysis for Pollution Prevention
Image: Wikimedia Commons, Author: Smokefoot
Notes: Alkylation of isobutane with n-butenes to form highly branched isoparaffins is an important process in gasoline manufacture. This reaction is currently catalyzed using either liquid hydrofluoric acid or sulfuric acid. Although these liquid acids rapidly catalyze the alkylation reaction, there are a number of drawbacks associated with their use. Solid acids have been studied extensively as possible catalysts for alkylation. However, with solid acid catalysts, the catalyst deactivates rapidly with time on stream. It is been hypothesized and shown that when the reaction is carried in supercritical media, the solid acid catalyst deactivation slows down considerably; however, high temperatures are needed to bring the reaction mixture to supercritical conditions, which results in the formation of undesired products. In this study, the effects of using different operation conditions for alkylation on a USY zeolite were investigated. It was observed that the deactivation rate was slower in supercritical-phase alkylation. Carbon dioxide was used as a diluent to lower the critical temperature of the reaction mixture in the ratio 27/9/1 for carbon dioxide/isobutene/1-butene. The use of diluent favored both alkylate selectivity and coke precursor removal.

## Slide 86: Continuous Flow Reactors
Replacing batch reactors on large, medium, and even small scale has distinct advantages:
Image Sources: http://encyclopedia.che.engin.umich.edu/Pages/Reactors/menu.html, https://www.technologynetworks.com/drug-discovery/product-news/automated-compound-library-production-294622
Real-time Analysis for Pollution Prevention
  Precise control of reaction conditions.
  Reproducible reaction outcome (product purity).
  Minimizes waste, and provides increased safety.

## Slide 87
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-2008-greener-reaction-conditions-award
Real-time Analysis for Pollution Prevention
Case study: Real-time analysis in cooling systems
Conventional Cooling Systems:
They consume large amounts of water.
Microbial growth and mineral scale decrease the efficiency and increase energy consumption of heat-exchange.
However, high levels of biocide to prevent microbial growth increases the risk of leaks in the system.
Biocide and metal-byproducts from corrosion are then released into the environment with the waste water.
Image: Wikimedia Commons, Cooling tower and cooling water discharge at a Philippsburg nuclear power plant, Author: Michael Kauffmann

## Slide 88
In 2008 Naclo Company won the EPA Greener Reaction Conditions Award for their innovative 3D TRASAR® Technology.
Real-time Analysis for Pollution Prevention
Case study: Real-time analysis in cooling systems
Alternative Cooling System with 3D TRASAR® Technology:
The 3D TRASAR® System allows for the real-time monitoring of mineral scale buildup.
This system can also utilize poor-quality water.
3D Scale Control prevents mineral scale formation to increase efficiency.
3D Bio-control performs a real-time check for planktonic and sessile bacteria. This reduces the amount of biocide used since biocides are then added only when necessary, rather than on a set schedule.
The 3D TRASAR® System greatly reduces the amount of wastewater discharged from cooling systems.
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-2008-greener-reaction-conditions-award
Image: Wikipedia, A lavender-colored nonpotable water pipeline in Mountain View, California, Author: Grendelkhan

## Slide 89
Inherently Safer Chemistry
for Accident Prevention
Substance and the form of a substance used in a chemical process should be chosen so as to minimize the potential for chemical accidents, including releases, explosions, and fires.
Image: Flickr, Author: sea turtle

## Slide 90
Approaches to design safer chemistry can include the use of solids or low vapor pressure substances in place of volatile liquids.
Other approaches include avoiding the use of molecular halogens in large quantities.
Continuous flow processes can help to minimize chemical hazards.
Inherently Safer Chemistry
for Accident Prevention
Accidents can be avoided by minimizing hazards

## Slide 91
Polyhydroxyamide (PHA):
Can be molded into seats, bins, and wall panels.
It is synthesized under mild conditions.
It decomposes into fire-resistant polybenzoxazole (PBO) and water upon heating.
  Westmoreland, UMass Amherst
Case study: Designing safer polymers for use in airplanes
Image Source: https://videohive.net/item/plane-interior-flying-in-the-clouds/9895121
Inherently Safer Chemistry
for Accident Prevention

## Slide 92
Tragedy in Bhopal, India - 1984
In arguably the worst industrial accident in history, 40 tons of methyl isocyanate were accidentally released when a holding tank overheated at a Union Carbide pesticide plant, located in the heart of the city of Bhopal. 15,000 people died and hundreds of thousands more were injured.
Chemists try to avoid things that explode, light on fire, are air-sensitive, etc.
When these things happen in the “real world”, lives are lost.
Inherently Safer Chemistry
for Accident Prevention
methyl isocyanate
Image: Wikimedia Commons, Bhopal Plant in 2010, Author: Julian Nitzsche

## Slide 93
December 3, 1984 – toxic gas leaked from a Union Carbide factory, killing thousands instantly and injuring many more (many of who died later of exposure). Up to 20,000 people have died as a result of exposure (3-8,000 instantly). More than 120,000 still suffer from ailments caused by exposure
What happened?
Methyl isocyanate - used to make pesticides - was being stored in large quantities on-site at the plant.
Methyl isocyanate is highly reactive, exothermic molecule.
Most safety systems either failed or were inoperative.
Water was released into the tank holding the methyl isocyanate.
The reaction occurred and the methyl isocyanate rapidly boiled, producing large quantities of toxic gas.
Inherently Safer Chemistry
for Accident Prevention
Tragedy in Bhopal, India - 1984

## Slide 94
Inherently Safer Chemistry
for Accident Prevention
Case study: Production of gasoline alkylate with AlkyClean® Technology
In 2016 Albemarle and CB&I won the EPA green chemistry award for their inherently safer AlkyClean® process technology.
AlkyClean® Technology:
The AlkyClean® solid acid alkylation process produces high quality alkylate without using liquid acid catalysts.
The solid acid alkylation process is safer for both people working directly in production and for people in the area surrounding the production facility.
There are also environmental and economic benefits since neither acid-soluble oils nor spent acids are produced.
Conventional alkylate production:
Alkylate is typically produced from the reaction of isobutane and light olefins.
This requires the use of liquid acid catalyzed processes, such as hydrofluoric acid.
Hydrofluoric acid is extremely toxic. When released it forms clouds that can be lethal for up to five miles.

## Slide 95: More examples available
Presidential Green Chemistry Challenge Winners
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-winners
How Industrial Applications in Green Chemistry Are Changing Our World (white paper) by American Chemical Society
Inherently Safer Chemistry
for Accident Prevention

## Slide 96: Synthesis Comparison Exercise
Dihydropyrimidone is a pharmaceutical compound that displays medicinal properties as vasodilatory calcium-channel blockers and anti-viral, anti-bacterial, and anti-inflammatory agents. More than one synthetic schemes have been proposed for its synthesis since the late 1800s. Compare the two synthetic routes and analyze which pathway is greener. In your argument, be sure to consider and compare all aspects of the reaction.
Inherently Safer Chemistry
for Accident Prevention

## Slide 97
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE