## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Waste Prevention
Image: Wikimedia Commons, Anacortes Refinery, Author: Walter Siegmund
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
Waste Prevention
It is better to prevent waste than to treat or clean up waste after it is formed.
Image: Harshaw Chemical Company discharges waste water into the Cuyahoga river
Source: National Archives and Records Administration

## Slide 3
The Waste Treatment Pyramid
Reduced Solvent Use
Waste as a Feedstock
Biodegradation of Waste
Designing Processes to Include Biodegradation of Waste
Topics To Be Covered

## Slide 4: Waste treatment pyramid: The 4 Rs Reduce, Reuse, Recycle, Recover
Reduction
Reuse
Recycling
Energy recovery
Disposal
Most favored option
Least favored option
Prevention
Incineration
Landfill
Recycling
Composting
We need various types of technology to reduce and reuse waste.
Ultimately, the production of waste should be prevented.
Notes: Need for technologies to Reduce and Reuse waste.
Ultimately, the waste production should be Prevented

## Slide 5: Landfills
  Consolidated material is buried with mud and other sealing agents to enable chemical, bacteriological, and physical degradation.
  Semi-anaerobic conditions lead to production of methane and CO2.
  If captured, landfill gas (methane) from decomposing garbage can be used to produce electricity, heat, and fuels.
Reduction
Reuse
Recycling
Energy recovery
Disposal

## Slide 6: Incineration and Pyrolysis
Incineration
  Solid organic waste is combusted.
  Some thermal treatments allow energy capture.
  Solid mass is reduced by 95-96%.
Pyrolysis
  Thermal decomposition at 200-300°C occurring in the absence of oxygen.
  Precursor of both the combustion and gasification processes.
  The products of biomass pyrolysis include biochar, bio-oil, and gases - such as methane, hydrogen, carbon monoxide, and carbon dioxide.
Reduction
Reuse
Recycling
Energy recovery
Disposal

## Slide 7: Recycling and Composting
Recycling
  Converting waste materials into new materials and objects.
  Available for metals, plastic, paper, glass.
Composting
  Organics undergo a biological decomposition to form a material (compost) that is non-toxic to plant growth.
  By-product of the reaction are CO2, water and heat.
Anaerobic conditions and biogas production
  Adopted for farm waste.
  Can reduce greenhouse gas emissions and can provide a cost-effective source of renewable energy.
  Recovered biogas can be an energy source for electricity, heating or transportation fuel.
Cost-benefit of recycling: energy savings
Material | Energy savings
Aluminum | 95%
Cardboard | 24%
Glass | 5-30%
Paper | 40%
Plastics | 70%
Steel | 60%
Reduction
Reuse
Recycling
Energy recovery
Disposal

## Slide 8: Reuse and Repurpose
Gasification:
  Converts organic based materials into CO, H2 and CO2.
  Achieved by reacting the material at high temperatures (>700 °C), without combustion, with a controlled amount of oxygen and/or stem.
  The resulting gas mixture is called syngas.
  Syngas is combustible and often used as a fuel.
Reduction
Reuse
Recycling
Energy recovery
Disposal
Alcohol production (biomass conversion into mixed alcohol fuels):
  Biological/chemical method for converting any biodegradable material into useful chemicals, such as biofuels (e.g., ethanol, propanol, n-butanol, isopropanol, 3-pentanol).
  Made by enzymatic breakdown of biomass into simple sugars, followed by yeast fermentation into alcohols.

## Slide 9: The Reduction and Elimination of Waste
Reduced solvent or solventless processes
Self separation
Process intensification
Material deposition
Use waste as a feedstock
Reduction
Reuse
Recycling
Energy recovery
Disposal

## Slide 10
Reduced Solvent: Sildenafil Citrate Production
Sildenafil citrate, commonly known as Viagra, is a selective inhibitor of phosphodiesterase 5 (PDE5). This new drug has immediately became a major seller, achieving sales of more than $1 billion during its first year on the market. With such a rapid sales take off it was critical that the environmental performance of the synthesis was good from the outset.
Average yield of last three steps = 97% yield.
Reduction of the ratio of solvent waste/kg product over 17 years from 1300 L/kg to only 7 L/kg by minimizing solvent use, increasing solvent recovery, improving solvent selection, and telescoping steps.
Only the solvents t-butanol, ethyl acetate, 2-butanone, and a trace of toluene still require disposal.
Comparison of organic and aqueous waste and vapor emissions for the sildenafil citrate process at three time points
Dunn, P.J et al Green Chem., 2004, 6, 43-48

## Slide 11
A one-pot, three step sequence.
Eliminates the need for several hazardous reagents such as ZnCl2, triphenylphosphine, and solvents such as dimethylformamide and dichloromethane.
E-factor improved by an order of magnitude.
Solvent consumption reduced by 95%, hazardous waste by 65%, preventing 1.5 million tons of hazardous waste per year.
Reduced Solvent: dNTPs
They are the building blocks of both DNA and RNA, which are chains of nucleotides made through the processes of DNA replication and transcription. Nucleoside triphosphates also serve as a source of energy for cellular reactions and are involved in signaling pathways. Nowadays they are synthesized and used in molecular biology.
Notes: dNTPs are essencial feedstock to perform Polymarase Chain Reaction (PCR)

## Slide 12
Reduced Solvent: Production of Ethylene Oxide
Ethylene oxide is used as an intermediate in the production of several industrial chemicals, the most notable of which is ethylene glycol. It is also used as a fumigant in certain agricultural products and as a sterilant for medical equipment and supplies.
Use of molecular oxygen removed the need for chlorine.
New process generated more than 16 times less waste than the original one, eliminating the formation of waste water.

## Slide 13: Solventless Process: Mechanochemistry
Chemistry physically activated
Motion → Friction → Heat → Reaction
Uses High Energy Ball Milling
Vibrating ball mill crushes particles which results in large surface areas.
Mixing of solids allows reaction at surfaces.
Thermal equilibrium is broken – “hot spots”, estimated at 10000 K, – Lasting 10‐7 seconds.
Collisions break crystalline material.
High pressures are generated.
Wilkening, M., Düvel, A., Preishuber-Pflügl, F., et al. (2016). Structure and ion dynamics of mechanosynthesized oxides and fluorides. Zeitschrift für Kristallographie - Crystalline Materials, 232(1-3), pp. 107-127.

## Slide 14: Utilizing Waste as a Feedstock
Some examples:
Waste cooking oil for biodiesel
Crustacean shell waste for chitosan based products
Red mud for bricks
Glycerol for lactic acid using catalyst

## Slide 15: Example: Electrocatalytic Oxidation of Glycerol to Chemical Feedstocks
2011 US bio-diesel production reached 967 million gallons.
  1 Olympic-size swimming = approximately 660,000 gallons.
  Almost 1460 Olympic-sized swimming pools of glycerol.
Current treatment:
  Dispose (sold for $240/ton!).
  Combust as fuel.
Chen, L.; Ren, S.; Ye, X. P., Fuel Processing Technology 2014, 120, 40-47.
T. Werpy, G. Petersen, Top value added chemicals from biomass, Pacific Northwest National Laboratory (PNNL), National Renewable Energy Laboratory (NREL), Office of Biomass Program (EERE), 2004.
Bio-diesel
“Waste”

## Slide 16: Glycerol to Other Chemicals
Polylactic acid
Valuable medicinal product
Sunless tanning product
Anti-freeze
Industrial chemical precursors
Skin exfoliating reagent
Notes: There are just a handful of examples of what we could do with glycerol so BURNING it is definitely not the most efficient way to use the limited resources nature offers.

## Slide 17: Production and Applications of Lactic Acid
90% of lactic acid comes from anaerobic fermentation of hexose sugar (e.g. corn starch).
Compete with food sources.
Slow and requires a lot of purifications.
Dusselier, M.; Van Wouwe, P.; Dewaele, A.; Makshina, E.; Sels, B. F., Energy & Environmental Science 2013, 6 (5), 1415-1442.
  Other applications of Lactic Acid:
  Food preservatives
  Edible pH modifier
  Textile industry
  Cosmetic and pharmaceutical industries

## Slide 18: Water Electrolysis with Earth Abundant Metal Catalyst
2H2O ---> O2 + 4H+ + 4e-
2H+ + 2e- ---> H2
Cathode
Anode
Power
Supply
e-
e-
e-
e-
e-
e-
e-
Cathode:
Any conductive materials
Anode:
Expansive platinum group metals
Cobalt 1,2‐bis(diphenylphosphino)ethane
(Co-DPPE)
Bloomfield, A. J.; Sheehan, S. W.; Collom, S. L.; Crabtree, R. H.; Anastas, P. T., A heterogeneous water oxidation catalyst from dicobalt octacarbonyl and 1,2-bis(diphenylphosphino)ethane. New J. Chem. 2014, 38 (4), 1540-1545.
Notes: Also, this catalyst works well in alkaline environment

## Slide 19: Electrocatalytic Oxidation of Glycerol
2H2O ---> O2 + 4H+ + 4e-
2H+ + 2e- ---> H2
Water-compatible
Atmospheric pressure
Rm temp. or above
Very low current / voltage
Cathode
Anode
Power
Supply
e-
e-
e-
e-
e-
e-
e-

## Slide 20: Example: Neutralization of Red Mud through Energy Efficient Extraction of Sodium Ions
The Bayer Process (Karl Bayer, 1887)
Element | Composition
Fe2O3 | 30-60wt%
Al2O3 | 10-20wt%
SiO2 | 3-50wt%
Na2O | 2-10wt%
CaO | 2-8wt%
TiO2 | trace-25wt%
K, Cr, V, Ni, Ba, Cu, Mn, Pb, Zn, Sc | Traces
NaOH, 170 – 180 °C
1 – 6 atm
Sodium aluminate
Na+ Al(OH)4-
Precipitation
Electrolytic Reduction
Red Mud
Alumina
Al2O3
(~2 tonne)
Aluminum
(~1 tonne)
Bauxites
(4 – 5 tonne)
Source: http://www.aluminiumleader.com/production/aluminum_production
Red mud is a toxic byproduct of the industrial process that refines bauxite, raw aluminum ore, into aluminum oxide, or alumina.
Depending on the origin, quality and composition of the bauxite, the amount of red mud left over from the alumina refining can vary widely. For every ton of alumina produced, the process can leave behind a third of a ton to more than two tons of red mud.
Notes: http://www.aluminiumleader.com/production/aluminum_production/

## Slide 21: Red Mud: Pollution and Accidents
Stade, Germany
Ajka, Hungary
Noranda Alumina plant at Gramercy - located alongside the Mississippi River
Damandjodi, India
The mud also has a high pH because of the sodium hydroxide solution used in the refining process. The base is strong enough to kill plant and animal life, and to cause burns and damage to airways if the fumes are breathed.
Most refineries collect the mud in open ponds to allow some of the water to evaporate. Once it's dry, after several years, the red mud is buried or mixed with soil.
The red mud is kept in reservoirs, so there is the possibility of leaks and floods, as seen in western Hungary.
Notes: http://www.theguardian.com/environment/2014/jan/08/devecser-hungary-eco-town
http://www.theatlantic.com/photo/2011/09/a-flood-of-red-sludge-one-year-later/100158/
http://lacoastpost.com/blog/?p=13160
http://redmud.org/red-mud/disposal/

## Slide 22: Red Mud: Neutralization and Potentials
If it is neutralized to pH 8 – 9:
  Building Materials
    Cement, bricks, tiles, etc.
  Pollution Control
    Removal of toxic heavy metal: Cd, Pb, Cr, etc..
    Removal of aromatic pollutant: dyes, phenols, chlorophenols, boron agents, etc.
Economically Unfeasible Schemes:
  Acid neutralization (from waste plant).
  CO2 pumping.
  Seawater neutralization.
Arch. Environ. Sci. 2012 ,6, 13-33
We can fight pollution with pollution!

## Slide 23: Neutralization of Red Mud through Selective Extraction of Sodium Ions
Red Mud Heterogeneous Basic Aq. Solution
Metal
Co(Dppe)
Na+ Ion Selective Membrane
Na+
Na+
Na+
Na+
Sodium Hydroxide Solution
2H2O ---> 2O2 + 4e- + 4H+
Water oxidized to lower pH and pushes Na+ ions through
4 H2O + 4e− → 2H2 + 4OH−
Generates OH- to facilitate the Na+ passing
*Patent Pending

## Slide 24: Successful Neutralization
Chart: Hours
| 0 | 2.4166666666666621 | 2.9166666666666621 | 3.466666666666665 | 3.5166666666666662 | 4.5999999999999979 | 5.2333333333333396 | 5.7166666666666632 | 6.3666666666666671 | 6.8999999999999986 | 7.583333333333333 | 8.5833333333333304 | 9.1833333333333336 | 9.6833333333333318 | 10.18333333333333 | 10.75 | 11.25 | 11.516666666666669 | 11.96666666666667 | 12.483333333333331 | 22.25 | 23.08333333333325 | 24.08333333333324
Set 1 | 12.89 | 12.65 | 12.68 | 12.61 | 12.61 | 12.59 | 12.58 | 12.44 | 12.38 | 12.3 | 12.23 | 12.13 | 11.98 | 11.77 | 11.59 | 11.16 | 10.35 | 9.95 | 9.28 | 7.17 | 0 | 0 | 0
 | K | Na | Fe | Al | Ca
[Ion]int. (Anode) | 0.3 | 461 | 0.1 | 0.3 | 4.5
6 volt, Room Temperature, 12 hours |  |  |  |  | 
[Ion]hr=12 (Cathode – Trial 1) | 0.1 | 71.6 | - | - | 0.1
[Ion]hr=12 (Cathode – Trial 2) | 0.1 | 71.6 | - | - | 0.2
[Ion]hr=12 (Cathode – Control, no e-) | 0.0 | 0.0 | - | - | 0.0
Using this process, red mud can be neutralized at room temperature in 12 hours.

## Slide 25: Biodegrade the Waste
Biodegradation - "A process by which microbial organisms transform or alter (through metabolic or enzymatic action) the structure of chemicals introduced into the environment." – US EPA, 2009
“Ready” biodegradability – remove 70% of dissolved organic carbon AND achieve 60% theoretical oxygen demand or CO2 production within a 10-day window in a 28-day test. – OECD
“Ultimate” biodegradability – 60-70% of organic carbon converted to CO2 within 28 days.

## Slide 26: Aerobic Versus Anaerobic Digestion
Difference in oxygen supply, organism types, and products formed.

## Slide 27: Aerobic Digestion
Bacteria consume organic matter.
Needs a constant supply of oxygen, pH adjustments, and mixing.
Byproducts: heat, CO2, and H2O.
Frequently used by water treatment plants or in composting.

## Slide 28: Anaerobic Digestion
Bacteria consume organic matter in the absence of oxygen.
Common in fermentation and landfill; produces biogas consisting of methane, ammonia, hydrogen sulfide.
Biogas is considered a renewable energy.

## Slide 29: Digestion versus Chemical Structure
Not all chemicals will biodegrade at the same rate (think plastic vs paper).
The rate of biodegradation depends on the microorganism, but also a chemical structure of the molecule.
Some parts of the molecule are known to be more biodegradable than the others.
There is a publically available software that analyses the chemical structure and predicts whether the molecule will degrade slower (days) or slower (months, years).

## Slide 30: Predicting Biodegradation: EPA, EPISuite
EPI = Estimation Programs Interface http://www.epa.gov/oppt/exposure/pubs/episuitedl.htm

## Slide 31: BIOWIN Models Based on Molecular Fragment Contributions
Six aerobic degradation models
  BIOWIN1&2: qualitative, based on database of 264 chemicals
  BIOWIN3&4: estimation of rate, based on 200 chemicals
  BIOWIN5&6: qualitative, based on database of 884 chemicals
New anaerobic degradation model
  BIOWIN 7: “screening level”, methanogenic bacteria, 169 chemicals

## Slide 32: BIOWIN Demonstration/Exercise
Interface with ChemDraw
Exercise:
  Compare molecules with similar structure
  How do the aerobic (BIOWIN 6) and anaerobic (BIOWIN 7) estimates change?
  Note any parts of the molecule that are not used in the model
  When there is ambiguity, do the BIOWIN1-5 models help reveal any trends?

## Slide 33
TEAM 1

## Slide 34
Increasing number of rings & molecular weight
1.
2.
3.
4.
5.
1>2>4>3>5
Most biodegradable (aerobic)
Least biodegradable
Favors biodegradation
- OH
- Low molecular weight
Disfavors biodegradation
- High molecular weight
- Cl
4>1>2>3>5
Most biodegradable (anaerobic)
Least biodegradable
TEAM 1
Notes: Increasing number of rings

## Slide 35
TEAM 2

## Slide 36
1.
2.
3.
4.
5.
6.
Bisphenol A derivatives: Halogenated and BPS
Poor biodegradation due to high MW
Disfavors biodegradation
- High molecular weight
Tertiary carbon BPA
Halogens, but F better than Cl
Favors biodegradation
- Low molecular weight
1>6>3>4>2>5
Most biodegradable (aerobic)
Least biodegradable
6>2>4=5>3>1
Most biodegradable (anaerobic)
Least biodegradable
TEAM 2

## Slide 37
TEAM 3

## Slide 38
1.
2.
3.
4.
5.
Different plasticizers
Linear and branched;
Two green plasticizers: Reduced ring to cyclo and isosorbide ring
Disfavors biodegradation
Side chains and branching
Ethers
Favors biodegradation
Linear chains
Cyclo
Esters
1>4>2>3>5
Most biodegradable (aerobic)
Least biodegradable
1>5>2>4>3
Most biodegradable (anaerobic)
Least biodegradable
TEAM 3

## Slide 39
TEAM 4

## Slide 40
Explosives (TNT, nitroglycerine)
1.
2.
3.
4.
5.
Favors biodegradation
Small molecular weight
OH
Disfavors biodegradation
CH3
Large MW
NNO2CH3
Degrades faster due to small MW
4>5>1=2=3
Most biodegradable (aerobic)
Least biodegradable
4>5>2>1>3
Most biodegradable (anaerobic)
Least biodegradable
TEAM 4

## Slide 41: Summary of BIOWIN Models
Poorly degraded
Readily degraded

## Slide 42
Design for Biodegradation?
Since we know the chemical moieties, functional groups, and types of bonds which make the molecule biodegradable, can we build-in biodegradability into chemical products?
YES!

## Slide 43
Example: Plasticizers
kills bacteria,
biodegradation halts
complete degradation to CO2 + H2O
Plasticizers are additives in plastic applications. Almost 90% of plasticizers are used in PVC, giving this material improved flexibility and durability.
Di-propylene glycol dibenzoate decomposes into a product which is toxic to bacteria, and therefore stops the biodegradation process.
With slightly changed structure, 1,5-pentanediol dibenzoate biodegrades into CO2 and H2O

## Slide 44
Example: Pesticides
DDT
DDT – Dichlorodiphenyltrichloroethane, which was used as agricultural pesticide, is persistent in the environment.
Not only does it bioaccumulates, but it undergoes a reaction to DDE which is even more toxic than DDT.
DDE
methoxychlor
Methoxychlor shares many insecticidal properties as DDT and it’s potency, but it is not persistent.
It degrades into methoxychlor phenol, which has also low toxicity and it is easily excreted.
Methoxychlor phenol
Toxic
Low toxicity

## Slide 45
Tetrapropylene alkylbenzene sulfonate (TPPS) was used as a surfactant for laundry detergents and accumulated into the water supply due to incomplete degradation.
Water tended to foam when coming out of the tap.
Example: Detergents
TPPS was replaced by linear alkylbenzene sulfonate (LAS).
Replacing the methyl branched chain of TPPS by a linear carbon chain reduces the biopersistence.
Low biodegradation
High biodegradation

## Slide 46
Triclosan is an antibacterial and antifungal agent found in some consumer products, including toothpaste, soaps, detergents, toys, and surgical cleaning treatments.
It persists in the environment.
Example: Antibacterial Products
Chlorophene is a bacteriocide and fungicide in cosmetics.
It is very biodegradable in the media and entirely removeable from the wastewater.
Low biodegradation
High biodegradation

## Slide 47
The Waste Treatment Pyramid
Reduced Solvent Use
Waste as a Feedstock
Biodegradation of Waste
Designing Processes to Include Biodegradation of Waste
Topics Covered

## Slide 48
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE