## Slide 1
From Theory to Practice
Image: NASA Earth Observatory
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE
Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry

## Slide 2
Implementation: Why, What, and How
Understanding Context
  Green Chemistry in the Marketplace
Identifying Opportunities
  Life Cycle and Green Chemistry Principles as a Guide to Finding Opportunity
Delivering Innovation
  Green Chemistry Strategies at All Stages
Green Chemistry Assessment Tool
How to Proceed: Moving Forward
Topics To Be Covered

## Slide 3
Why  What  How
After several hours of listening to lectures, doing exercises, and viewing case studies, how do you go about implementation and/or dissemination of Green Chemistry?
The process can be summarized in 3 words:
What’s Next?

## Slide 4
Why
Understand Context
Business/Market
What
Identify Opportunities
Product/Service
How
Deliver Innovation
Technology

## Slide 5
Reasons may vary:
Reduce cost
Increase margins
Increase sale
Enhance corporate competitiveness
Improve reputation
Why
Understand Context
Business/Market
Potential roadblocks
Resource depletion
Environmental damage
Growing population
Increasing consumption
Societal attitudes
Regulatory landscape

## Slide 6
Why
Understand Context
Business/Market
Political
  Social services
  Consumer protection
  Tax competition
  Knowledge competition
Environmental
  Climate change
  Extinctions
  Water
  Waste
  Resource constrains
Social
  Urbanization
  Demographics
  Population growth
  Fear
Technology
  Nano
  Molecular biology
  Statistics
  Computational science
  Green chemistry
Economic
  Globalization
  High value services
  Income
Understand Trends & Drivers

## Slide 7
Why
Understand Context
Business/Market
Generate a problem statement
If only we could _________, then we could____________
Think of an outcome

## Slide 8
What are we delivering?
What
  Identify Opportunities
    Product/Service
New synthetic route
New catalyst
Alternative solvent
New product
What is the “functional unit”?
Number of reaction runs
Performance (yield or atom economy)
Energy usage per period of time
Kg of parts cleaned

## Slide 9
Use Life Cycle and Green Chemistry Principles as a guide
Image source: Wikipedia
What
  Identify Opportunities
    Product/Service

## Slide 10
What
  Identify Opportunities
    Product/Service
Image source: Wikipedia

## Slide 11
Raw materials extraction
Production of waste and energy consumption during raw material extraction
High impact materials: rare metals, natural extracts (perfume ingredients), bricks, concrete, electronic equipment
How
  Deliver Innovation
  Technology

## Slide 12
Design strategy for raw materials
Reduce the hazard for the materials used: avoid materials that are persistent, bioacummulative, have high toxicity profile
Use renewable materials like carbohydrates, lipids, biopolymers
Use recycled materials or materials from the waste stream
Reduce the number of raw materials used
Minimize transportation (locally sourced, or manufacturing shifted onsite)
Avoid materials that generate a lot of waste or are energy intensive
Avoid materials produced in environmentally damaging way
Use BIOWIN or PBT Profiler (http://www.pbtprofiler.net/default.asp) for persistence/degradation and bioconcentration
Use ChemHAT, Protox, ChemSpider for toxicity profile
EcoSAR (not discussed) for ecotoxicity
How
  Deliver Innovation
  Technology

## Slide 13
Manufacturing
Possibly the greatest impact
Extensive processing that uses energy and produces a large volume of waste
Examples include consumer products and chemicals
How
  Deliver Innovation
  Technology

## Slide 14
Design strategy for manufacturing
Improve energy efficiency of the process
Use technologies which minimize production of waste and emissions
Use renewable energy
Avoid hazardous process and auxiliary materials (use safer solvents)
Recycle process materials (solvents)
Choose disposal to minimize environmental impact
Use waste as a feedstock for another process
Use solvent selection guides for better solvent alternative
Identify chemicals of concern: Toxic Release Inventory (https://www.epa.gov/toxics-release-inventory-tri-program)
Use IRIS (https://www.epa.gov/iris ) to check human health effect from chemical exposure
Atom economy, E-factor for reaction performance
How
  Deliver Innovation
  Technology

## Slide 15
Distribution
Products which are transported over long distances, are heavy and require a lot of packaging
  Example includes fresh out of season vegetables shipped to locations around the world
How
  Deliver Innovation
  Technology

## Slide 16
Design strategy for distribution
Minimize packaging per unit of service
Use returnable packaging
Avoid PVC and use packaging from renewable feedstocks
Manufacture product at the point of use
Use a lower impact transportation
How
  Deliver Innovation
  Technology

## Slide 17
Use
Products with high durability that go through many cycles are found in this category.
  Examples include cars, laser printers and dishwashers
How
  Deliver Innovation
  Technology

## Slide 18
Design strategy for use
Minimize energy efficiency per unit of service
Can the product be made safer for a human and environment?
Can the amount of product be automated to avoid losses of product?
Design out waste and emissions in use or make it environmentally benign
Minimize auxiliary processes and make materials renewable and recyclable
Collect and recycle waste
How
  Deliver Innovation
  Technology

## Slide 19
Disposal (End-of-Life)
Products that are toxic or persistent are hard to dispose
  Example includes batteries
How
  Deliver Innovation
  Technology

## Slide 20
Design strategy for disposal
Design so that manufacturer can recover and reuse the product at end of life
Design for easy disassembly
Can the individual components be recycled at the end of life?
Avoid harmful substances that could be released at end of life
Ensure that a toxic substance can be easily extracted from the product
Design materials that are biodegradable and compostable
Consumer information on recycling streams and means.
How
  Deliver Innovation
  Technology

## Slide 21
Based on the life cycle, assess the overall improvement to the process/technology
Identify if any tradeoffs were made between green chemistry principles
Conclusions

## Slide 22
International Flavors & Fragrances Inc (IFF)
International company employing ~7000 people with manufacturing facilities in 35 countries and current market of $10 billion.
In Vision 2020, they committed to embed sustainability in the company culture and develop a measurable metrics which will support triple bottom line.
As a part of this initiative they developed a Green Chemistry Assessment tool, to track their progress.
How do Others Track Their Success?

## Slide 23
Internal, easy to apply, uniform and standardized method of analyzing safety, health and environmental impact
Distributed and accepted by scientists and staff across the globe
Sharable with technical and non-technical experts, senior managers, customers and other stakeholders within IFF
Green Chemistry Assessment Tool

## Slide 24
Each Green Chemistry principle has a scoring system to improve process, operations and products with the purpose of having a positive impact on TBL
Score for each principle ranges from 0 (worst) to 5 (best)
*Results are presented in the radar chart
Chart: Green Principles Score
| Prevent Waste | Atom Economy | Less Hazardous Synthesis | Design Benign Chemicals | Benign Solvents | Design for Energy Efficiency | Use of Renewable Feedstocks | Reduce Derivatives | Catalyst | Design for Biodegradation | RT Analysis & Polution Prevention | Design for Acciddent Prevention
 | 3 | 3 | 1 | 3 | 3 | 3 | 0 | 5 | 1 | 5 | 5 | 3
* Scoring is relative and specifically developed for IFF products. It is not shared publically.
Scoring

## Slide 25
While IFF uses the scoring system internally, their guidelines may be useful for other companies
  If a process generates hazardous waste, it is assigned 0
  If the process has over 80% atom economy, then it is assigned 5
Scoring
Chart: Green Principles Score
| Prevent Waste | Atom Economy | Less Hazardous Synthesis | Design Benign Chemicals | Benign Solvents | Design for Energy Efficiency | Use of Renewable Feedstocks | Reduce Derivatives | Catalyst | Design for Biodegradation | RT Analysis & Polution Prevention | Design for Acciddent Prevention
 | 3 | 3 | 1 | 3 | 3 | 3 | 0 | 5 | 1 | 5 | 5 | 3

## Slide 26
Fragrance aroma used in perfumery applications such as personal care and fine fragrances.
New synthesis includes:
Environmental Benefits
Improvement in mass efficiency from 25 to 85%
Chemical waste elimination up to 80%
Improved worker safety in reduction of hazardous waste
Economic benefits
94% reduction in energy cost
Greater efficiency leading to lower costs for chemical resources
Reduction for capital cost for equipment
Reduction of technical failures during scale-up
2 reaction steps
Synthesis of Veridan

## Slide 27
Prevent waste (34)
  High, non-hazardous waste was reduced by 50 tons
Atom economy (34)
  Yield increased by 10%
Less hazardous synthesis (14)
  Elimination of safety hazards (not defined)
Design benign chemicals (33)
  No change in score
Benign solvents (33)
  No change in score: same non-hazardous solvents used
Design for energy efficiency (35)
  Increase from 8kg/h*m3 to 100kg/h*m3
Improvements – STEP 1– Grignard Addition
Improvement from assigned value 3 in the traditional reaction to value 4 in the new synthesis

## Slide 28
7. Use of renewable feedstocks (00)
  The process does not use renewable feedstock
8. Reduce derivatives (55)
  No derivatives involved
9. Catalysis (11)
  No catalyst used
10. Design for biodegradation (55)
  No change
11. RT analysis for pollution prevention (55)
  Process monitoring and control present
12. Design for accident prevention (35)
  Process hazards eliminated
Improvements – STEP 1– Grignard Addition

## Slide 29
Chart: STEP1: Grignard Addition
| Prevent Waste | Atom Economy | Less Hazardous Synthesis | Design Benign Chemicals | Benign Solvents | Design for Energy Efficiency | Use of Renewable Feedstocks | Reduce Derivatives | Catalyst | Design for Biodegradation | RT Analysis & Polution Prevention | Design for Acciddent Prevention
Old process | 3 | 3 | 1 | 3 | 3 | 3 | 0 | 5 | 1 | 5 | 5 | 3
New process | 4 | 4 | 4 | 3 | 3 | 5 | 0 | 5 | 1 | 5 | 5 | 5

## Slide 30
Prevent waste (35)
  Waste reduced by 80%, solvent recyclable between batches
Atom economy (15)
  Mass efficiency increased from 25-80%, yield improved by 10%
Less hazardous synthesis (35)
  Aluminium isopropoxide and phosphoric acid oxidation replaced by air and catalyst
Design benign chemicals (33)
  No change in score
Benign solvents (35)
  Acetone replaced by water
Design for energy efficiency (44)
  Reaction run at atmospheric pressure and temperature below 100C
Improvements – STEP 2– Oxidation from alcohol to ketone

## Slide 31
7. Use of renewable feedstocks (05)
  New process uses air
8. Reduce derivatives (55)
  No derivatives involved
9. Catalysis (35)
  Use 5% reusable catalyst in place of 66% aluminum isopropoxide
10. Design for biodegradation (55)
  No change
11. RT analysis for pollution prevention (55)
  Process monitoring and control present
12. Design for accident prevention (35)
  New engineering controls in place
Improvements – STEP 2– Oxidation from alcohol to ketone

## Slide 32
Chart: STEP 2: Oxidation from alcohol to ketone
| Prevent Waste | Atom Economy | Less Hazardous Synthesis | Design Benign Chemicals | Benign Solvents | Design for Energy Efficiency | Use of Renewable Feedstocks | Reduce Derivatives | Catalyst | Design for Biodegradation | RT Analysis & Polution Prevention | Design for Acciddent Prevention
Old process | 3 | 1 | 3 | 3 | 3 | 4 | 0 | 5 | 3 | 5 | 5 | 3
New process | 5 | 5 | 5 | 3 | 5 | 4 | 5 | 5 | 5 | 5 | 5 | 5

## Slide 33
No –
  because metrics have uncertainties and may not apply the same way across disciplines
  They will still be the need for human decision to weight each parameters
But..
  They show greening opportunities (see LCA class)
  It allows a systematic evaluation and serves as a guide
  And it is a good start
Is Green Chemistry Assessment Tool an absolute solution?

## Slide 34
BASF Eco-Efficiency Analysis method
It is a complete suite of tools developed by BASF to be able to articulate their efforts in Green Chemistry, but also sustainability at large.
Impact & Economics

## Slide 35
BASF Eco-Efficiency Analysis method
Eco-efficiency is defined as the ratio of economic creation to ecological destruction from the perspective of the end consumer.
Six impact categories for the ecologic destruction
  Consumption of energy
  Consumption of resources
  Land use
  Emissions into air, water and soil (wastes)
  Toxic potential of used and released substances
  Risk potential

## Slide 36
> Impact of each of these categories is normalized with respect to one another.
> The least favorable alternative, according to a system that is specific
to each category, is given the value 1 and the other alternatives are given values between 0 and 1 depending on their relative impact.
Ecological Footprint

## Slide 37
The ecological footprint is then combined into a standalone score that can be looked against cost.

## Slide 38
BASF Eco-Efficiency Analysis method
Integration of the Social Dimension into the Eco-Efficiency Analysis (the SEECube®)
Weighting
Normalization
working accidents /UB
employees
consumer
locoal &
national community
future
generations
international
community
SEECube®: Now cost, environmental footprint and social acceptability can be seen in one integral graph.

## Slide 39
BASF Eco-Efficiency Analysis method
Benefits for the company
Strategic Decisions
Investment decisions
Technology decisions
Site decisions
Evaluate product portfolio
Marketing, Customers
Demonstration of product advantages
Improved customer relations
Product Differentiation
Better understand competitive
advantages
Research and development
Quantification of the most important factors
Drive sustainable
products and processes
Drive production/process improvements
Stakeholder and Government Dialogue
Communication with authorities
Demonstration of Sustainability
Government “approvals”

## Slide 40
With brilliance and optimism.
  Science and technology has risen to the challenge and it has the creativity and capability to do it again.
How to Proceed?

## Slide 41
Responsibly.
  With power comes responsibility. With all the knowledge, perspective and training you acquire, you also have acquired the ability to impact others – to impact the world. Once you have the power to impact the world, you have the responsibility to impact it for the better.
How to Proceed?

## Slide 42
With conviction, courage and commitment.
Green Chemistry and Green Engineering
  Because we can.
  Because we must
How to Proceed?

## Slide 43
How to Proceed?
In science (and innovation) one needs to be a complete schizophrenic
Sometimes you need to be the wildest dreamer and think completely outside the box
And at other times be the most rigorous analysts and #1 critic of your own ideas and results
The tension between these two attitudes will offer you opportunities for success
Robert H. Crabtree
https://www.knowledgehut.com/blog/business-management/become-certified-business-analyst-professional-cbap
https://blog.wagepoint.com/all-content/how-to-start-a-promising-business-with-a-really-crazy-idea

## Slide 44
Implementation: Why, What, and How
Understanding Context
  Green Chemistry in the Marketplace
Identifying Opportunities
  Life Cycle and Green Chemistry Principles as a Guide to Finding Opportunity
Delivering Innovation
  Green Chemistry Strategies at All Stages
Green Chemistry Assessment Tool
How to Proceed: Moving Forward
Topics To Be Covered

## Slide 45
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE