## Slide 1
Designing for Recycling & Degradation
Lecture #14
Date
Course #

## Slide 2: Principle #1: Waste Prevention
It is better to prevent waste than to treat or clean up waste after it is formed.
Image: Harshaw Chemical Company discharges waste water into the Cuyahoga river
Source: National Archives and Records Administration

## Slide 3
The Waste Treatment Pyramid
Reduced Solvent Use
Waste as a Feedstock
Biodegradation
  Design rules/rules of thumb for biodegradation
Designing Products and/or Waste to Biodegrade
Outline

## Slide 4
The Waste Treatment Pyramid
Reduced Solvent Use
Waste as a Feedstock
Biodegradation
  Design rules/rules of thumb for biodegradation
Designing Products and/or Waste to Biodegrade
Outline

## Slide 5: Waste treatment pyramid: The 4 R’s Reduce, Reuse, Recycle, Recover
Reduction
Reuse
Recycling
Energy recovery
Disposal
Most favored option
Least favored option
Prevention
Incineration
Landfill
Recycling
Composting
We need various types of technology to reduce and reuse waste.
Ultimately, the production of waste should be prevented.
Notes: Need for technologies to Reduce and Reuse waste.
Ultimately, the waste production should be Prevented

## Slide 6: Landfills
  Consolidated material is buried with mud and other sealing agents to enable chemical, bacteriological, and physical degradation.
  Semi-anaerobic conditions lead to production of methane and CO2.
  If captured, landfill gas (methane) from decomposing garbage can be used to produce electricity, heat, and fuels.
Reduction
Reuse
Recycling
Energy recovery
Disposal
Image: Wikipedia

## Slide 7: Incineration and Pyrolysis
Incineration
  Solid organic waste is combusted.
  Some thermal treatments allow energy capture.
  Solid mass is reduced by 95-96%.
Pyrolysis
  Thermal decomposition at 200-300°C occurring in the absence of oxygen.
  Precursor of both the combustion and gasification processes.
  The products of biomass pyrolysis include biochar, bio-oil, and gases - such as methane, hydrogen, carbon monoxide, and carbon dioxide.
Reduction
Reuse
Recycling
Energy recovery
Disposal
Image: Wikipedia

## Slide 8: Recycling and Composting
Recycling
  Converting waste materials into new materials and objects.
  Available for metals, plastic, paper, glass.
Composting
  Organics undergo a biological decomposition to form a material (compost) that is non-toxic to plant growth.
  By-product of the reaction are CO2, water and heat.
Anaerobic conditions and biogas production.
  Adopted for farm waste.
  Can reduce greenhouse gas emissions and can provide a cost-effective source of renewable energy.
  Recovered biogas can be an energy source for electricity, heating or transportation fuel.
Cost-benefit of recycling: energy savings
Material | Energy savings
Aluminum | 95%
Cardboard | 24%
Glass | 5-30%
Paper | 40%
Plastics | 70%
Steel | 60%
Reduction
Reuse
Recycling
Energy recovery
Disposal

## Slide 9: Reuse and Repurpose
Gasification:
  Converts organic based materials into CO, H2 and CO2.
  Achieved by reacting the material at high temperatures (>700 °C), without combustion, with a controlled amount of oxygen and/or stem.
  The resulting gas mixture is called syngas.
  Syngas is combustible and often used as a fuel.
Alcohol production (biomass conversion into mixed alcohol fuels):
  Biological/chemical method for converting any biodegradable material into useful chemicals, such as biofuels (e.g., ethanol, propanol, n-butanol, isopropanol, 3-pentanol).
  Made by enzymatic breakdown of biomass into simple sugars, followed by yeast fermentation into alcohols.
Reduction
Reuse
Recycling
Energy recovery
Disposal

## Slide 10: The Reduction and Elimination of Waste
Reduced solvent or solventless processes
Self separation
Process intensification
Material deposition
Use waste as a feedstock
Reduction
Reuse
Recycling
Energy recovery
Disposal

## Slide 11
The Waste Treatment Pyramid
Reduced Solvent Use
Waste as a Feedstock
Biodegradation
  Design rules/rules of thumb for biodegradation
Designing Products and/or Waste to Biodegrade
Outline

## Slide 12
Reduced Solvent: Sildenafil Citrate Production
Sildenafil citrate, commonly known as Viagra, is a selective inhibitor of phosphodiesterase 5 (PDE5). This new drug has immediately became a major seller, achieving sales of more than $1 billion during its first year on the market. With such a rapid sales take off it was critical that the environmental performance of the synthesis was good from the outset.
Average yield of last three steps = 97% yield.
Reduction of the ratio of solvent waste/kg product over 17 years from 1300 L/kg to only 7 L/kg by minimizing solvent use, increasing solvent recovery, improving solvent selection, and telescoping steps.
Only the solvents t-butanol, ethyl acetate, 2-butanone, and a trace of toluene still require disposal.
Comparison of organic and aqueous waste and vapor emissions for the sildenafil citrate process at three time points
Dunn, P.J et al Green Chem., 2004, 6, 43-48

## Slide 13
A one-pot, three step sequence.
Eliminates the need for several hazardous reagents such as ZnCl2, triphenylphosphine, and solvents such as dimethylformamide and dichloromethane.
E-factor improved by an order of magnitude.
Solvent consumption reduced by 95%, hazardous waste by 65%, preventing 1.5 million tons of hazardous waste per year.
Reduced Solvent: dNTPs
They are the building blocks of both DNA and RNA, which are chains of nucleotides made through the processes of DNA replication and transcription. Nucleoside triphosphates also serve as a source of energy for cellular reactions and are involved in signaling pathways. Nowadays they are synthesized and used in molecular biology.
Notes: dNTPs are essencial feedstock to perform Polymarase Chain Reaction (PCR)

## Slide 14
Reduced Solvent: Production of Ethylene Oxide
Ethylene oxide is used as an intermediate in the production of several industrial chemicals, the most notable of which is ethylene glycol. It is also used as a fumigant in certain agricultural products and as a sterilant for medical equipment and supplies.
Use of molecular oxygen removed the need for chlorine.
New process generated more than 16 times less waste than the original one, eliminating the formation of waste water.
E-Factor = 0.3

## Slide 15: Solventless Process: Mechanochemistry
Chemistry physically activated
  Motion → Friction → Heat → Reaction
Uses High Energy Ball Milling
  Vibrating ball mill crushes particles which results in large surface areas.
  Mixing of solids allows reaction at surfaces.
  Thermal equilibrium is broken – “hot spots”, estimated at 10000 K, – Lasting 10‐7 seconds.
  Collisions break crystalline material.
  High pressures are generated.
Wilkening, M., Düvel, A., Preishuber-Pflügl, F., et al. (2016). Structure and ion dynamics of mechanosynthesized oxides and fluorides. Zeitschrift für Kristallographie - Crystalline Materials, 232(1-3), pp. 107-127.

## Slide 16
The Waste Treatment Pyramid
Reduced Solvent Use
Waste as a Feedstock
Biodegradation
  Design rules/rules of thumb for biodegradation
Designing Products and/or Waste to Biodegrade
Outline

## Slide 17: Utilizing Waste as a Feedstock
Some examples:
Waste cooking oil for biodiesel
Crustacean shell waste for chitosan based products
Red mud for bricks
Glycerol for lactic acid using catalyst
https://www.123rf.com/stock-photo/biodiesel_production.html?&sti=nb1guj45pd99v8lsd8|&mediapopup=70457693

## Slide 18: Example: Electrocatalytic Oxidation of Glycerol to Chemical Feedstocks
2011 US bio-diesel production reached 967 million gallons.
  1 Olympic-size swimming = approx. 660,000 gallons.
  Almost 1460 Olympic-sized swimming pools of glycerol.
Current treatment:
  Dispose (sold for $240/ton!).
  Combust as fuel.
Chen, L.; Ren, S.; Ye, X. P., Fuel Processing Technology 2014, 120, 40-47.
T. Werpy, G. Petersen, Top value added chemicals from biomass, Pacific Northwest National Laboratory (PNNL), National Renewable Energy Laboratory (NREL), Office of Biomass Program (EERE), 2004.
Bio-diesel
“Waste”

## Slide 19: Glycerol to Valuable Platform Chemicals
Polylactic acid
Valuable medicinal product
Sunless tanning product
Anti-freeze
Industrial chemical precursors
Skin exfoliating reagent
Notes: There are just a handful of examples of what we could do with glycerol so BURNING it is definitely not the most efficient way to use the limited resources nature offers.

## Slide 20: Production and Applications of Lactic Acid
90% of lactic acid comes from anaerobic fermentation of hexose sugar (e.g. corn starch).
Compete with food sources.
Slow and requires a lot of purifications.
Dusselier, M.; Van Wouwe, P.; Dewaele, A.; Makshina, E.; Sels, B. F., Energy & Environmental Science 2013, 6 (5), 1415-1442.
  Other applications of Lactic Acid:
  Food preservatives
  Edible pH modifier
  Textile industry
  Cosmetic and pharmaceutical industries

## Slide 21: Water Electrolysis with Earth Abundant Metal Catalyst
2H2O ---> O2 + 4H+ + 4e-
2H+ + 2e- ---> H2
Cathode
Anode
Power
Supply
e-
e-
e-
e-
e-
e-
e-
Cathode:
Any conductive materials
Anode:
Expansive platinum group metals
Cobalt 1,2‐bis(diphenylphosphino)ethane
(Co-DPPE)
Bloomfield, A. J.; Sheehan, S. W.; Collom, S. L.; Crabtree, R. H.; Anastas, P. T., A heterogeneous water oxidation catalyst from dicobalt octacarbonyl and 1,2-bis(diphenylphosphino)ethane. New J. Chem. 2014, 38 (4), 1540-1545.

## Slide 22: Electrocatalytic Oxidation of Glycerol
Bloomfield, A. J.; Sheehan, S. W.; Collom, S. L.; Crabtree, R. H.; Anastas, P. T., A heterogeneous water oxidation catalyst from dicobalt octacarbonyl and 1,2-bis(diphenylphosphino)ethane. New J. Chem. 2014, 38 (4), 1540-1545.
2H2O ---> O2 + 4H+ + 4e-
2H+ + 2e- ---> H2
Water-compatible
Atmospheric pressure
Rm temp. or above
Very low current / voltage
Cathode
Anode
Power
Supply
e-
e-
e-
e-
e-
e-
e-

## Slide 23: Example: Neutralization of Red Mud through Energy Efficient Extraction of Sodium Ions
The Bayer Process (Karl Bayer, 1887)
Element | Composition
Fe2O3 | 30-60wt%
Al2O3 | 10-20wt%
SiO2 | 3-50wt%
Na2O | 2-10wt%
CaO | 2-8wt%
TiO2 | trace-25wt%
K, Cr, V, Ni, Ba, Cu, Mn, Pb, Zn, Sc | Traces
NaOH, 170 – 180 °C
1 – 6 atm
Sodium aluminate
Na+ Al(OH)4-
Precipitation
Electrolytic Reduction
Red Mud
Alumina
Al2O3
(~2 tonne)
Aluminum
(~1 tonne)
Bauxites
(4 – 5 tonne)
Source: http://www.aluminiumleader.com/production/aluminum_production
Red mud is a toxic byproduct of the industrial process that refines bauxite, raw aluminum ore, into aluminum oxide, or alumina.
Depending on the origin, quality and composition of the bauxite, the amount of red mud left over from the alumina refining can vary widely. For every ton of alumina produced, the process can leave behind a third of a ton to more than two tons of red mud.
Notes: http://www.aluminiumleader.com/production/aluminum_production/

## Slide 24: Red Mud: Pollution and Accidents
Stade, Germany
Ajka, Hungary
Noranda Alumina plant at Gramercy - located alongside the Mississippi River
Damandjodi, India
The mud also has a high pH because of the sodium hydroxide solution used in the refining process. The base is strong enough to kill plant and animal life, and to cause burns and damage to airways if the fumes are breathed.
Most refineries collect the mud in open ponds to allow some of the water to evaporate. Once it's dry, after several years, the red mud is buried or mixed with soil.
The red mud is kept in reservoirs, so there is the possibility of leaks and floods, as seen in western Hungary.
Image Source: Wikipedia Commons
Notes: http://www.theguardian.com/environment/2014/jan/08/devecser-hungary-eco-town
http://www.theatlantic.com/photo/2011/09/a-flood-of-red-sludge-one-year-later/100158/
http://lacoastpost.com/blog/?p=13160
http://redmud.org/red-mud/disposal/

## Slide 25: Red Mud: Neutralization and Potentials
If it is neutralized to pH 8 – 9:
  Building Materials
    Cement, bricks, tiles, etc.
  Pollution Control
    Removal of toxic heavy metal: Cd, Pb, Cr, etc..
    Removal of aromatic pollutant: dyes, phenols, chlorophenols, boron agents, etc.
Economically Unfeasible Schemes:
  Acid neutralization (from waste plant).
  CO2 pumping.
  Seawater neutralization.
Arch. Environ. Sci. 2012 ,6, 13-33
We can fight pollution with pollution!

## Slide 26: Neutralization of Red Mud through Selective Extraction of Sodium Ions
Red Mud Heterogeneous Basic Aq. Solution
Metal
Co(Dppe)
Na+ Ion Selective Membrane
Na+
Na+
Na+
Na+
Sodium Hydroxide Solution
2H2O ---> 2O2 + 4e- + 4H+
Water oxidized to lower pH and pushes Na+ ions through
4 H2O + 4e− → 2H2 + 4OH−
Generates OH- to facilitate the Na+ passing
*Patent Pending
Courtesy of Dr. Jason Lam

## Slide 27: Successful Neutralization
 | K | Na | Fe | Al | Ca
[Ion]int. (Anode) | 0.3 | 461 | 0.1 | 0.3 | 4.5
6 volt, Room Temperature, 12 hours |  |  |  |  | 
[Ion]hr=12 (Cathode – Trial 1) | 0.1 | 71.6 | - | - | 0.1
[Ion]hr=12 (Cathode – Trial 2) | 0.1 | 71.6 | - | - | 0.2
[Ion]hr=12 (Cathode – Control, no e-) | 0.0 | 0.0 | - | - | 0.0
Chart: Hours
| 0 | 2.4166666666666621 | 2.9166666666666621 | 3.466666666666665 | 3.5166666666666662 | 4.5999999999999979 | 5.2333333333333396 | 5.7166666666666632 | 6.3666666666666671 | 6.8999999999999986 | 7.583333333333333 | 8.5833333333333304 | 9.1833333333333336 | 9.6833333333333318 | 10.18333333333333 | 10.75 | 11.25 | 11.516666666666669 | 11.96666666666667 | 12.483333333333331 | 22.25 | 23.08333333333325 | 24.08333333333324
Set 1 | 12.89 | 12.65 | 12.68 | 12.61 | 12.61 | 12.59 | 12.58 | 12.44 | 12.38 | 12.3 | 12.23 | 12.13 | 11.98 | 11.77 | 11.59 | 11.16 | 10.35 | 9.95 | 9.28 | 7.17 | 0 | 0 | 0
Using this process, red mud can be neutralized at room temperature in 12 hours.
Courtesy of Dr. Jason Lam

## Slide 28
The Waste Treatment Pyramid
Reduced Solvent Use
Waste as a Feedstock
Biodegradation
  Design rules/rules of thumb for biodegradation
Designing Products and/or Waste to Biodegrade
Outline

## Slide 29: Biodegrade the Waste
Biodegradation - "A process by which microbial organisms transform or alter (through metabolic or enzymatic action) the structure of chemicals introduced into the environment." – US EPA, 2009
“Ready” biodegradability – remove 70% of dissolved organic carbon AND achieve 60% theoretical oxygen demand or CO2 production within a 10-day window in a 28-day test. – OECD
“Ultimate” biodegradability – 60-70% of organic carbon converted to CO2 within 28 days.

## Slide 30: PBT Chemicals: History
Persistent
Bioaccumulative
Toxic
PBT chemicals are of high concern due to their resistance to degradation, high mobility in the environment, and high toxicity.
What makes a chemical structure more Persistent?

## Slide 31: PBT Chemicals: Examples
Synthetic detergents (1950’s – 1960’s)
DDT (1960’s – today)
Plastics (today)

## Slide 32
Example: Pesticides
DDT
DDT – Dichlorodiphenyltrichloroethane
Ideal insecticide:
  Inexpensive to prepare
  Very wide spectrum in activity
  Non-toxic to humans (or so they thought)
  Persistent, negating the requirement for re-treatment
  Inventors awarded Nobel Prize in 1948
1962: Rachel Carson, Silent Spring (https://youtu.be/Ipbc-6IvMQI)
  Linked widespread DDT use to cancer and thinning of bird eggs shells
  Carcinogen, endocrine disruptor, developmental and reproductive effects
Replaced in the developed world with more expensive pesticides, such as organophosphates

## Slide 33: Aerobic Versus Anaerobic Digestion
Difference in oxygen supply, organism types and products formed.

## Slide 34: Aerobic Digestion
Bacteria consume organic matter.
Needs a constant supply of oxygen, pH adjustments, and mixing.
Byproducts: heat, CO2, and H2O.
Frequently used by water treatment plants or in composting.

## Slide 35: Anaerobic Digestion
Bacteria consume organic matter in the absence of oxygen.
Common in fermentation and landfill; produces biogas consisting of methane, ammonia, hydrogen sulfide.
Biogas is considered a renewable energy.

## Slide 36: Digestion versus Chemical Structure
Not all chemicals will biodegrade at the same rate (think plastic vs paper).
The rate of biodegradation depends on the microorganism, but also a chemical structure of the molecule.
Some parts of the molecule are known to be more biodegradable than the others.
There is a publically available software that analyses the chemical structure and predicts whether the molecule will degrade slower (days) or slower (months, years).

## Slide 37
The Waste Treatment Pyramid
Reduced Solvent Use
Waste as a Feedstock
Biodegradation
  Design rules/rules of thumb for biodegradation
Designing Products and/or Waste to Biodegrade
Outline

## Slide 38: Reasons for resistance of a substance to microbial degradation
Appropriate microorganisms do not exist or are not present in the environment
There are inadequate nutrients for the microbial population
The temperature, pH or pO2 is too low or too high; ionic conditions are unsuitable
Concentration of substrate is too high (toxic) or too low
The substrate is adsorbed or covalently attached to clays, humus, etc., or is physically inaccessible
The substrate is not accessible to attack because it is too large and/or insoluble
The substrate:
  Is not transported into the cell
  Is not a substrate for the available enzymes
  Is not an inducer for appropriate enzymes or transport systems
  Does not give rise to products that can integrate into normal metabolism
  Is converted into products that are toxic or interfere with normal metabolism
From: Chem. Reviews, 2007, Vol. 107, No. 6, 2207-2227
Environment
Molecule

## Slide 39: Rules of thumb for biodegradability
Chem. Reviews, 2007, Vol. 107, No. 6, 2207-2227
Feature | Structure
Halogens: Especially chlorine and fluorine and if more than 3 in a molecule | 
Chain branching if extensive: Quaternary C’s are problematic | 
Tertiary amine, nitro, nitroso, azo, and arylamino groups | 
Polycyclic aromatic residues | 
Heterocyclic residues | 
Aliphatic ether bonds (except in ethoxylates) | 
Features that increase resistance to aerobic biodegradation
Notes: The addition of chlorine atom to a phenyl ring makes the ring less susceptible to attack by oxygenase enzymes, which use an electrophilic form of oxygen as the oxidant; strongly electron-withdrawing groups such as chlorine are therefore to be avoided if possible.
Features that increase resistance to aerobic biodegradation:
  Halogens (especially chlorine and fluorine and if more than 3 in a molecule) (Electron withdrawing groups on a phenyl ring makes the ring less susceptible to attack)
  Chain branching if extensive (quaternary C’s problematic)
  Tertiary amine, nitro, nitroso, azo, and arylamino groups
  Polycyclic residues (ex., PAHs) (especially with more than 3 rings)
  Heterocyclic residues (ex., imidazole)
  Aliphatic ether bonds (except in ethoxylates)

## Slide 40: Rules of thumb for biodegradability
Chem. Reviews, 2007, Vol. 107, No. 6, 2207-2227
Feature | Structure
Groups susceptible to enzymatic hydrolysis (esters, including phosphate esters) and amides | 
Oxygen atoms in the form of hydroxyl, aldehyde, or carboxylic acid groups, ketones (not ether, with the exception of ethoxylate groups) | 
Unsubstituted linear alkyl chains (especially  4 carbons) and phenyl rings | 
Molecular features that generally increase aerobic biodegradability:
Notes: The addition of chlorine atom to a phenyl ring makes the ring less susceptible to attack by oxygenase enzymes, which use an electrophilic form of oxygen as the oxidant; strongly electron-withdrawing groups such as chlorine are therefore to be avoided if possible.
Molecular features that generally increase aerobic biodegradability:
Groups susceptible to enzymatic hydrolysis (esters, including phosphate esters) and amides
Oxygen atoms in the form of hydroxyl, aldehyde, or carboxylic acid groups, ketones (not ether, with the exception of ethoxylate groups)
Unsubstituted linear alkyl chains (especially ≥ 4 carbons) and phenyl rings

## Slide 41: Class Exercise Options
  Predicting Biodegradation: U.S. EPA EPISuite tool, BIOWIN
  Design for Biodegradability Discussion Questions

## Slide 42: Exercise #1
Predicting Biodegradation: U.S. EPA EPISuite, BIOWIN

## Slide 43: Predicting Biodegradation: EPA, EPISuite
EPI = Estimation Programs Interface http://www.epa.gov/oppt/exposure/pubs/episuitedl.htm

## Slide 44: BIOWIN Models Based on Molecular Fragment Contributions
Six aerobic degradation models
  BIOWIN1&2: qualitative, based on database of 264 chemicals
  BIOWIN3&4: estimation of rate, based on 200 chemicals
  BIOWIN5&6: qualitative, based on database of 884 chemicals
New anaerobic degradation model
  BIOWIN 7: “screening level”, methanogenic bacteria, 169 chemicals

## Slide 45: BIOWIN Demonstration/Exercise
Interface with ChemDraw
Exercise:
  Compare molecules with similar structure
  How do the aerobic (BIOWIN 6) and anaerobic (BIOWIN 7) estimates change?
  Note any parts of the molecule that are not used in the model
  When there is ambiguity, do the BIOWIN1-5 models help reveal any trends?

## Slide 46
TEAM 1

## Slide 47
Increasing number of rings & molecular weight
1.
2.
3.
4.
5.
1>2>4>3>5
Most biodegradable (aerobic)
Least biodegradable
Favors biodegradation
- OH
- Low molecular weight
Disfavors biodegradation
- High molecular weight
- Cl
4>1>2>3>5
Most biodegradable (anaerobic)
Least biodegradable
TEAM 1
Notes: Increasing number of rings

## Slide 48
TEAM 2

## Slide 49
1.
2.
3.
4.
5.
6.
Bisphenol A derivatives: Halogenated and BPS
Poor biodegradation due to high MW
Disfavors biodegradation
- High molecular weight
Tertiary carbon BPA
Halogens, but F better than Cl
Favors biodegradation
- Low molecular weight
1>6>3>4>2>5
Most biodegradable (aerobic)
Least biodegradable
6>2>4=5>3>1
Most biodegradable (anaerobic)
Least biodegradable
TEAM 2

## Slide 50
TEAM 3

## Slide 51
1.
2.
3.
4.
5.
Different plasticizers
Linear and branched;
Two green plasticizers: Reduced ring to cyclo and isosorbide ring
Disfavors biodegradation
Side chains and branching
Ethers
Favors biodegradation
Linear chains
Cyclo
Esters
1>4>2>3>5
Most biodegradable (aerobic)
Least biodegradable
1>5>2>4>3
Most biodegradable (anaerobic)
Least biodegradable
TEAM 3

## Slide 52
TEAM 4

## Slide 53
Explosives (TNT, nitroglycerine)
1.
2.
3.
4.
5.
Favors biodegradation
Small molecular weight
OH
Disfavors biodegradation
CH3
Large MW
NNO2CH3
Degrades faster due to small MW
4>5>1=2=3
Most biodegradable (aerobic)
Least biodegradable
4>5>2>1>3
Most biodegradable (anaerobic)
Least biodegradable
TEAM 4

## Slide 54: Exercise #2
Designing for Biodegradability Discussion Questions
Notes: Use the “rules of thumb” for increasing and decreasing resistance to aerobic biodegradation (the next two slides) as a reference for students to work through the discussion questions either as a whole group, or in small groups.
This activity is available also as a hand-out. You are welcome to provide the handout to students, have them work through the questions on their own, using the rules of thumb as a guide. And, then lead a group discussion with slides 57-60 to discuss the answers that the students came up with

## Slide 55
Feature | Structure
Halogens: Especially chlorine and fluorine and if more than 3 in a molecule | 
Chain branching if extensive: Quaternary C’s are problematic | 
Tertiary amine, nitro, nitroso, azo, and arylamino groups | 
Polycyclic aromatic residues | 
Heterocyclic residues | 
Aliphatic ether bonds (except in ethoxylates) | 
Features that increase resistance to aerobic biodegradation
Designing for Biodegradability: Discussion Questions
Notes: The addition of chlorine atom to a phenyl ring makes the ring less susceptible to attack by oxygenase enzymes, which use an electrophilic form of oxygen as the oxidant; strongly electron-withdrawing groups such as chlorine are therefore to be avoided if possible.

## Slide 56
Feature | Structure
Groups susceptible to enzymatic hydrolysis (esters, including phosphate esters) and amides | 
Oxygen atoms in the form of hydroxyl, aldehyde, or carboxylic acid groups, ketones (not ether, with the exception of ethoxylate groups) | 
Unsubstituted linear alkyl chains (especially  4 carbons) and phenyl rings | 
Molecular features that generally increase aerobic biodegradability:
Designing for Biodegradability: Discussion Questions

## Slide 57
Triclosan was used extensively as an antimicrobial agent in soaps, detergents and other household products.
In 2016, the U.S. FDA announced that as of September 2017, they would prohibit the sale of consumer antiseptic washes containing triclosan. There are some health concerns linked to triclosan, including it being a possible endocrine disrupting chemical. Based on the structure, would you expect the chemical to persist in aerobic conditions?
Designing for Biodegradability: Discussion Questions
U.S. Food and Drug Administration. September 2, 2016,
https://www.fda.gov/NewsEvents/Newsroom/PressAnnouncements/ucm517478.htm
Notes: Yes, based on the structure this should persist in aerobic conditions. The students should be able to identify the functional groups that will increase the resistance to degradation using the “rules of thumb” slides as a reference – the ether group and the chlorine groups will increase the resistance.

## Slide 58
Name the following alkanes. Identify the isomers.
Rank the alkanes in terms of their biodegradability (based on the design rules). Justify your ranking.
Write condensed and bond-line formulas for three isomers of the alkane C5H12. Based on biodegradability design rules, rank the isomers in terms of biodegradability. Justify your ranking.
Designing for Biodegradability: Discussion Questions
Notes: Depending on the level of the students in your class, you can have them name the alkanes for practice – and, also write the different formulas for the isomers. If you have more advanced students, then focus on the persistence of the alkanes based on the chain branching – quaternary carbons will persist longer than tertiary, followed by secondary – use the “rules of thumb” ppt slides as a reference

## Slide 59
Aerobic biodegradation of a phenyl ring typically proceeds by the electrophilic addition of oxygen to the phenyl ring. The oxygen reactive species can take on different forms, depending on the enzyme and conditions. Propose a simple mechanism for the electrophilic addition in which oxygen is introduced to phenol and compare it to chlorobenzene. Use a simple “E+” to represent the reactive oxygen species. Which do you believe will be more biodegradable under aerobic conditions and why?
Dr. Dalila Kovacs, Grand Valley State University
Designing for Biodegradability: Discussion Questions
Notes: Aerobic biodegradation of a phenyl ring typically proceeds by the electrophilic addition of oxygen to the phenyl ring. The oxygen reactive species can take on different forms, depending on the enzyme and conditions. Propose a simple mechanism for the electrophilic addition of oxygen to phenol and compare it to chlorobenzene. Use a simple “E+” to represent the reactive oxygen species. Which do you believe will be more biodegradable under aerobic conditions and why?
Remember the rule: The addition of chlorine atom to a phenyl ring makes the ring less susceptible to attack by oxygenase enzymes, which use an electrophilic form of oxygen as the oxidant; strongly electron-withdrawing groups such as chlorine are therefore to be avoided if possible.
The students should propose that the phenol should be more biodegradable based on the rules of thumb. The electron donating groups (-OH) allows for oxygen to more readily attack the benzene ring. The strongly electron-withdrawing group (-Cl) will hinder this.

## Slide 60
The aromatic compounds shown are chlorinated derivatives of phenol that are mainly used as fungicides and pesticides, besides a variety of other uses. While their chemical properties protect crops from destructive insects, one problem is their rate of bioaccumulation in the environment and their biodegradability– how long they persist in soil, water, and our bodies. Interestingly, the number and location of the chlorine substituents on the aromatic ring affect the biodegradability of these compounds. Organic chemists currently work to synthesize new polyhalophenols that retain the desired pesticide properties, but are degraded quickly to safe byproducts.
Designing for Biodegradability: Discussion Questions

## Slide 61
Design for Biodegradation?
Since we know the chemical moieties, functional groups, and types of bonds which make the molecule biodegradable, can we build-in biodegradability into chemical products?
YES!

## Slide 62
The Waste Treatment Pyramid
Reduced Solvent Use
Waste as a Feedstock
Biodegradation
  Design rules/rules of thumb for biodegradation
Designing Products and/or Waste to Biodegrade
Outline

## Slide 63
Tetrapropylene alkylbenzene sulfonate (TPPS) was used as a surfactant for laundry detergents and accumulated into the water supply due to incomplete degradation.
Water tended to foam when coming out of the tap.
Example: Detergents
Low biodegradation!!
Tetrapropylene alkylbenzene sulfonate
(TPPS)

## Slide 64
Example: Detergents
High biodegradation!!
linear alkylbenzene sulfonate (LAS).
TPPS was replaced by linear alkylbenzene sulfonate (LAS).
Replacing the methyl branched chain of TPPS by a linear carbon chain reduces the biopersistence.

## Slide 65
Example: Pesticides
DDT
DDT – Dichlorodiphenyltrichloroethane, which was used as agricultural pesticide, is persistent in the environment.
Not only does it bioaccumulates, but it undergoes a reaction to DDE which is even more toxic than DDT.
DDE
methoxychlor
Methoxychlor shares many insecticidal properties as DDT and it’s potency, but it is not persistent.
It degrades into methoxychlor phenol, which has also low toxicity and it is easily excreted.
Methoxychlor phenol
Toxic
Low toxicity

## Slide 66
Example: Plasticizers
kills bacteria,
biodegradation halts
complete degradation
to CO2 + H2O
Plasticizers are additives in plastic applications. Almost 90% of plasticizers are used in PVC, giving this material improved flexibility and durability.
Di-propylene glycol dibenzoate decomposes into a product which is toxic to bacteria, and therefore stops the biodegradation process.
With slightly changed structure, 1,5-pentanediol dibenzoate biodegrades into CO2 and H2O

## Slide 67
Triclosan is an antibacterial and antifungal agent found in some consumer products, including toothpaste, soaps, detergents, toys, and surgical cleaning treatments.
It persists in the environment.
Example: Antibacterial Products
Chlorophene is a bacteriocide and fungicide in cosmetics.
It is very biodegradable in the media and entirely removeable from the wastewater.
Low biodegradation
High biodegradation

## Slide 68
The Waste Treatment Pyramid: Prevention of waste and the reduction in the use of materials is the best way to avoid waste in the first place!
Reduced Solvent Use: Solvents contribute to a large % of the materials used in chemical processes and products; reducing the use of solvents can have a great impact
Waste as a Feedstock: waste can be processed to be a valuable feedstock or platform chemical for use in many industry sectors
Biodegradation: Understanding design rules and rules of thumb for biodegradation can help to predict if a molecule will be persistent
Designing for biodegradation is possible!
Summary

## Slide 69: Homework #3
Estimating Biodegradation of Organic Molecules

## Slide 70
Estimating Biodegradation of Organic Molecules
Calculation of the Biodegradation Index (BI):
BI = 3.199 + a1f1 + a2f2 +a3f3 + …. + anfn + amMW
Variable | Meaning
an | Assigned contribution factor to functional group (see attached table)
fn | # of times/frequency a functional group in a molecule
am | Molecular weight contribution factor (-0.00221)
MW | Molecule weight of molecule
*BI is an indicator of aerobic biodegradation rate. A value to 5 indicates the compound is expected to degrade over HOURS. A value of 4 corresponds to a biodegradation of DAYS. Last, values of 3,2, or 1 correspond to biodegradation in WEEKS, MONTHS, and YEARS respectively. These values of BI should not be viewed as an accurate quantitative predictor of biodegradation. Rather, it should be viewed as a relative ranking of the probability that compound will degrade in the assigned timeframe.
J.W. Raymond et al. / Journal of Hazardous Materials B84 (2001) 189–215
Notes: See enclosed activity – also,