## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Energy delivery in Chemistry
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE
Source: wikipedia

## Slide 2
Role of energy in a chemical process
Microwaves
Flow chemistry
Photochemistry
Electrochemistry
Mechanochemistry
Topics To Be Covered

## Slide 3
Feedstock: renewable
Catalyst: play on the activation energy
Products: safe + biodegradable
Medium + energy
What’s important in a chemical reaction

## Slide 4
Chemical industry energy use in the US
  Chemistry accounts for a large portion of energy use
  E.g. the Haber Bosch process alone (production of ammonia) represents 1% all al energy consumption in the world.
N. Notman, Haber-Bosch power consumption slashed, Chem. World, Oct 2012
https://www.eia.gov/energyexplained/index.php?page=us_energy_industry
Use of energy in the chemical industry

## Slide 5
What do you think?
Why do we need energy in a chemical process?

## Slide 6
Reaction heating (endothermic reaction)
Reaction cooling (exothermic reaction)
Agitation, pumping…
Working up
  Distillation
  Drying
  Filtrations
  …
Use of energy in a chemical process
Synthetic process of acetylsalicylic acid (aspirin)

## Slide 7
During reaction: Activation Energy
  Activation energy = energy barrier for the reaction
During the reaction | At purification step | When things go wrong
  It can be provided by:
    Thermal heating
    Another energy delivery methods
      Electrochemistry
      Photochemistry
      Sonochemistry
      Microwave
      Mechanochemistry
Use of energy: Activation energy

## Slide 8
After reaction
  Heat for distillation to separate and purify or concentrate desired products
  Heat to dry product material
  Energy for waste treatment
Eg: sun vs artificial cocoa bean drying
25% of chemical industry energy input is distillations and drying processes
During the reaction | At purification step | When things go wrong
Use of energy: Purification

## Slide 9
Solutions for energy reduction during purification:
  Tandem reactions (less steps = less purification)
  Heterogeneous catalysis (easy separation)
  Tunable/switchable solvents (easy separation)
  Biphasic medium where the product separate (easy separation)
  Solventless processes (easy separation, no heating of solvent)
During the reaction | At purification step | When things go wrong
Use of energy: Purification

## Slide 10
Apparatus operated below design specification
Bad maintenance (leaks…)
Lack of monitoring
Lack of energy recovery (for heating buildings for instance)
Bad energy source choice
From UK data, the relative energy consumption/t of product have dropped from 170 in 1960 to 60 in 2000
In USA 50% of industry
consumption is chemistry + refinery
During the reaction | At purification step | When things go wrong
Use of energy: Sources of energy wastes

## Slide 11
A green engineering solution: heat recovery
  Eg: a biomass burner to generate energy
https://reich-chemistry.wikispaces.com/Michael+Gautreau+Brett+Fredericks+wiki+project2009?responseToken=9d3531ae35b397f7a71d66ae7f508307
During the reaction | At purification step | When things go wrong
Use of energy: Sources of energy wastes

## Slide 12
During reaction: Activation Energy
  Activation energy = energy barrier for the reaction
During the reaction | At purification step | When things go wrong
  It can be provided by:
    Thermal heating
    Another energy delivery methods
      Electrochemistry
      Photochemistry
      Sonochemistry
      Microwave
      Mechanochemistry
Use of energy: Let’s focus on the reaction

## Slide 13
Thermal heating
  Delivered from natural gas or other fossil fuels
  either using the heat of combustion directly or superheated steam.
  In the lab we use rather electricity with hot plates or heating mantels
Use of energy: Activation reaction

## Slide 14
Thermal heating in batch: limitations:
Use of energy: Activation reaction

## Slide 15
Thermal heating in batch: limitations:
  Solvent needs to be heated to heat the molecule: it’s a loss of energy
  Homogeneity issues: there is a gradient of temperatures in the batch
  Heating of products after reaction… potential degradation
reacted
degraded
Use of energy: Activation reaction

## Slide 16
Thermal heating in batch: limitations:
  Solvent needs to be heated to heat the molecule: it’s a loss of energy
  Green solution: Solventless processes
Advantage | Disadvantage
No solvent heating/distilling | High viscosity/solubility problems
Easy separation | 
Use of energy: Activation reaction

## Slide 17
Thermal heating in batch: limitations:
  Solvent needs to be heated to heat the molecule: it’s a loss of energy
  Green solution: Ways to direct energy better towards the reaction and only the reaction.
    Microwaves (heats up only polar molecules)
    Sonochemistry (localized bursts of energy)
    Electrochemistry (electronic activation)
    Photochemistry (photonic activation)
    Mechanochemistry (to reaction solids together: no solvent heating)
Use of energy: Activation reaction

## Slide 18
Thermal heating in batch: limitations:
  Homogeneity issues:
  Degradation issues:
  Green solution: Flow chemistry
    The reaction can be heated only on a small volume (homogeneous)
    The reaction can be heated only when needed and reacted products don’t need to be overheated
reacted
degraded
Use of energy: Activation reaction

## Slide 19
Principle of microwaves
  Microwaves reactors (and oven) have a fixed frequency at 2.45 GHz (to avoid interferences with telecommunications and cell phones)
  This correspond to a time scale of 10-12 s, which is the time it takes for a molecule to rotate
  Microwaves do not have enough energy to break a bond or to make a molecule vibrate: It is even lower than Brownian motion energy
CHEM 462: 20. Energy input reduction (I)
10-2
Practical Microwave Synthesis for Organic Chemists: Strategies, Instruments, and Protocols, Green Chem., 2004, 6 , 128–141
Microwave

## Slide 20
Principle of microwaves
  Microwaves reactors (and oven) have a fixed frequency at 2.45 GHz (to avoid interferences with telecommunications and cell phones)
  This correspond to a time scale of 10-12 s, which is the time it takes for a molecule to rotate
  Microwaves do not have enough energy to break a bond or to make a molecule vibrate: It is even lower than Brownian motion energy
CHEM 462: 20. Energy input reduction (I)
Practical Microwave Synthesis for Organic Chemists: Strategies, Instruments, and Protocols, Green Chem., 2004, 6 , 128–141
Microwave

## Slide 21
Main mechanism for microwave heating: Dipolar polarization mechanism
Alignment of the molecule with the electric field
Dipole realigns to the field, generating heat through molecular friction/dielectric loss
Microwave: mechanism

## Slide 22
Dipolar polarization mechanism
  Molecules that produce heat under microwaves
    Water
    Ethanol
    DMSO
    DMF
    CH2Cl2
  Bad microwaves solvents are benzene, CCl4 and ethers.
CHEM 462: 20. Energy input reduction (I)
Molecule must be polar
Molecule must be protic or viscous
Molecule produces heat
Microwave: mechanism
Notes: Viscocity of water (1cP), methanol (0.59 CP), DCM (0.44 cP), ether (0.224 cP)

## Slide 23
Solvents may be ranked for their microwave performance
the higher tan δ, the better the microwave heating
Microwave: solvents

## Slide 24
Advantages of microwave heating
  Heating uniformity: (conduction, convection and radiation are secondary)
  Heating speed: Target temperature easier to reach fast especially in small volumes
  Effect of super heating: heating above the boiling point of the solvent
  Selective heating: polar molecules could be heated without solvent heating
  Ohmic heating for metals and magnetic materials: local extreme heatings
CHEM 462: 20. Energy input reduction (I)
Microwave
Notes: Viscocity of water (1cP), methanol (0.59 cP), DCM (0.44 cP), ether (0.224 cP)

## Slide 25
  Devulcanization of rubber (recycling process): advantageous because no solvent needed, good heat repartition
  Dupont process for HCN production: gaseous reaction, so only the solid catalyst is heated. Locally, temperature is 1200°C!
CHEM 462: 20. Energy input reduction (I)
Microwave: industry applications
Al2O3
Pt
Local ohmic heating
Notes: Viscocity of water (1cP), methanol (0.59 cP), DCM (0.44 cP), ether (0.224 cP)

## Slide 26
Chem. Commun., 2011, 47, 4583–4592
Flow chemistry: Chemical method taking place in a tube. The chemical reaction is performed in a continuous fashion.
The volume in which the reaction takes place is small (a few mm3 to cm3)
=> it’s easy to control conditions within this volume (temperature, pressure…)
Flow chemistry

## Slide 27: Continuous Flow Reactors
Replacing batch reactors on large, medium, and even small scale has distinct advantages:
Image Sources: http://encyclopedia.che.engin.umich.edu/Pages/Reactors/menu.html, https://www.technologynetworks.com/drug-discovery/product-news/automated-compound-library-production-294622
Real-time Analysis for Pollution Prevention
  Precise control of reaction conditions.
  Reproducible reaction outcome (product purity).
  Minimizes waste, and provides increased safety.

## Slide 28
Advantages:
  Particular interest in reactions that can not be scaled up.
  Good heat transfer
  Mass transfers
  Continuous production
  Constant quality
  Safety (reactive reagents, better control of dangerous reactions)
  More facile scale up
Can be combined with
  Photochemistry
  Microwave
  Electrochemistry
Flow chemistry
In such systems, high pressure can take place in a very small volume => improved safety

## Slide 29
Flow vs batch: Faster, + selective reactions
Chem. Commun., 2011, 47, 4583–4592
Flow
Batch
Flow chemistry

## Slide 30
Large scale
“This thermal process required very high temperatures to be efficient that were not easily reached in conventional reactors”
bicyclic isoxazolidines: [3 + 2] cycloaddition: oximes generate in situ nitrones (reaction intermediate which is instable)
Rincón, J. A.; Mateos, C.; García-Losada, P.; Mergott, D. J. Org. Process Res. Dev. 2015, 19 (2), 347–351
120 g/h
Flow chemistry: upsacling

## Slide 31
Combining flow with microwave heating
G. Shore, W.-J. Yoo, C.-J. Li and M. G. Organ, Chem.–Eur. J., 2010, 16, 126
NMP
Flow chemistry/microwave

## Slide 32
From glycerol to biofuel
  Glycerol is a by product from the biodiesel industry (abundant)
  Solketal tert-butyl ether (STBE) can be an effective fuel additive
Monbaliu, J.-C. M.; Winter, M.; Chevalier, B.; Schmidt, F.; Jiang, Y.; Hoogendoorn, R.; Kousemaker, M. A.; Stevens, C. V. Bioresour. Technol. 2011, 102 (19), 9304–9307
Flow chemistry: biomass conversion
virtual STBE production of 90 t/y, with less than 4 equivalents of acetone and 1 equivalent of isobutene

## Slide 33
Electrochemistry is the use of electricity to perform chemistry
The principle was discovered Michael Faraday in 1832
At the heart of central technologies
  Water splitting (H2 production)
  Batteries
  Fuel cells
Electrochemistry
Michael Faraday

## Slide 34
For electrolysis to occur, electrons must pass from the anode to the cathode through an external, electrical circuit interconnecting the two electrodes.
There must be a mechanism for charge transport between the electrodes within the cell
There may or may not be a separator
Electrochemistry: principles
Pletcher, D.; Walsh, F. C. Organic electrosynthesis. In Industrial Electrochemistry; Springer Netherlands: Dordrecht, 1993; pp 294–330.

## Slide 35
Industrial electroorganic synthesis: Monsanto hydrodimerization of acrylonitrile to adiponitrile
  A precursor to the diamine used in the synthesis of Nylon-6,6.
  400 000 metric tons of adiponitrile in 2014, or ∼30% of the adiponitrile market
  competitive with the conventional route starting from butadiene.
Dupont process
Pletcher, D.; Walsh, F. C. Organic electrosynthesis. In Industrial Electrochemistry; Springer Netherlands: Dordrecht, 1993; pp 294–330.
Montsanto process
Electrochemistry: Applications

## Slide 36
Industrial electroorganic synthesis: Monsanto hydrodimerization of acrylonitrile to adiponitrile
Monsanto process
Pletcher, D.; Walsh, F. C. Organic electrosynthesis. In Industrial Electrochemistry; Springer Netherlands: Dordrecht, 1993; pp 294–330.
Electrochemistry: Applications

## Slide 37
Modern electrochemistry: merger with biocatalysis: muconic acid production
Working electrode: Pb, Fe, Ni, Sn, and Zn
Bioengineered Saccharomyces cerevisiae
Glucose
bio
electro
Electro step: 94% yield and 100% faradaic efficiency
Matthiesen, J. E.; Suástegui, M.; Wu, Y.; Viswanathan, M.; Qu, Y.; Cao, M.; Rodriguez-Quiroz, N.; Okerlund, A.; Kraus, G.; Raman, D. R.; et al. ACS Sustain. Chem. Eng. 2016, 4 (12), 7098–7109
Electrochemistry: Applications

## Slide 38
Modern electrochemistry: merger with biocatalysis: muconic acid production
Specialty Nylon 6,6 for improved performance
Glucose
bio
electro
Matthiesen, J. E.; Suástegui, M.; Wu, Y.; Viswanathan, M.; Qu, Y.; Cao, M.; Rodriguez-Quiroz, N.; Okerlund, A.; Kraus, G.; Raman, D. R.; et al. ACS Sustain. Chem. Eng. 2016, 4 (12), 7098–7109
Electrochemistry: Applications

## Slide 39
Photochemistry is the use of light to perform chemistry
Advantages for green chemistry
  Energy is directly targeted to the chemical bond to break
  Photons are clean reagents compared to radical initiators
  Because of directed energy input, lower heating are required: better selectivity are achievable
  Photochemical reactions open interesting pathways.
CHEM 462: 20. Energy input reduction (II)
Photochemistry
Source: wikipedia

## Slide 40
Some limitations of photochemistry
  The power of transmitted light is function of the square of the distance to the source: this causes limitations.
  Fouling: Fouling comes from little particles coming from the reactor. Those particles scatter light and render the solution less transparent to light => reduce yield
  Managing the light input: Often the reaction uses only one single wavelength and the lamps used are polychromatic. Lamps also produce heat to some extent => loss of energy
  Lamps and transparent reactors are often expensive
  Cooling: photochemical systems made not be so energy efficient because cooling systems are often need to avoid heating from the lamps.
CHEM 462: 20. Energy input reduction (II)
Photochemistry
Source: wikipedia
The use of flow reactors and LED lamps are leading to rapid growth of photochemical processes

## Slide 41
CHEM 462: 20. Energy input reduction (II)
Photochemistry: the light source
Using solar radiation directly for chemistry
Using solar radiation -> energy -> photochemistry
Seems like a good idea BUT:
The solar spectrum is not focused on the relevant wavelength
Issues with variability in sun availability
Issues with exposing chemical reaction to the outside world: not easy to control cleaning of tubes, fouling…
More controlled conditions.
Makes sense energetically

## Slide 42
5-HMF (Hydroxymethylfurfural) can be produced from biomass. It is inherently unstable
Yet production is taking off as it is increasingly viewed as a key platform molecule: need to convert it to molecule of use
Photochemistry: application
Heugebaert, T. S. A.; Stevens, C. V.; Kappe, C. O. ChemSusChem 2015, 8 (10), 1648–1651
5-HMF
6: 5-hydroxy-5-(hydroxymethyl)-
furan-2(5 H)-one (interesting monomer)
10: 5-hydroxy-4-keto-pentenoic acid (interesting monomer)
Rose bengal
Photocatalyst (dye):

## Slide 43
Titanium dioxide nanoparticles
  At the nanoparticles state, titanium dioxide absorb visible light and creates an electron hole
  Valence electrons
  Conduction electrons
D here can be pollutants: like NO, SO but also organic molecules
Photochemistry: application for depollution

## Slide 44
Photoactive materials
http://cristalactiv.com/ourproducts/
Photochemistry: application for depollution

## Slide 45: Mechanochemistry
Chemistry physically activated. Several mechanisms:
High energy
Friction generated heat
Physical comminution (particle size reduction)
“hot spots”, estimated at 10000 K, lasting 10‐7 seconds: plasma effects
Low energy
Physical mixing in solid state: diffusion aided reaction at interfaces
Shearing forces deliver energy for molecule activation
May be aided by catalytic amounts of solvents (liquid assisted grinding)
Wilkening, M., Düvel, A., Preishuber-Pflügl, F., et al. (2016). Structure and ion dynamics of mechanosynthesized oxides and fluorides. Zeitschrift für Kristallographie - Crystalline Materials, 232(1-3), pp. 107-127.

## Slide 46: Mechanochemistry
High energy
Low energy
Planetary mill with ~100 balls
Vibrational mill with 1-2 balls

## Slide 47
A vibrational mill
Tomislav Friscic, McGill

## Slide 48: Mechanochemistry
Noble metals recycling
Noble metal widely used as catalysts and in electronics
Traditional recycling: aggressive conditions (aqua regia, a mixture of concentrated nitric and hydrochloric acids)
Tomislav Friščić and his team showed they could use mechanochemistry for generating:
Soluble metal salts
Metal complexes (with ligands)
They used:
mild oxidant: Oxone
halide salts
Angew. Chem. Int. Ed. 2018, DOI: 10.1002/anie.201712602
https://cen.acs.org/articles/96/i5/Shaking-gold-palladium.html?utm_source=Newsletter&utm_medium=Newsletter&utm_campaign=CEN
“It’s a remarkable result that illustrates the value of mechanochemistry, it’s a very benign protocol which doubles the solvent savings and offers an alternative to recycle valuable catalysts that are often discarded.” Carsten Bolm
b) (NH4)2PdCl4; c) (NH4)2PdBr4; d) NH4AuCl4; e) NH4AuBr4.
Tomislav Friscic

## Slide 49: Mechanochemistry: nanoparticles synthesis
M. J. Rak, N. Saade, T. Friscic, A. Moores, Green Chem., 2014, 16, 86-89.
Ligand and metal precursor are loaded and milled: no solvent, no additive, no reducer
b. 1.8nm
a. 4.2nm
c. 1.5nm
d. 1.3nm
XPS shows reduced Au(0)

## Slide 50
Role of energy in a chemical process
Microwaves
Flow chemistry
Photochemistry
Electrochemistry
Mechanochemistry
Topics Covered

## Slide 51
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE