## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Renewable Feedstocks for molecules
Image: Wikimedia Commons, Author: R. Möhler
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
Use of Renewable Feedstocks
A raw material or feedstock should be renewable rather than depleting whenever technically and economically practical.
Image: Wikipedia, Pongamia Pinnata Seeds

## Slide 3
What can we make from petroleum (focus on molecules)
The biorefinery
Renewable Feedstocks
  Triglycerides
  Lignocellulosic Feedstocks
  N containing polymers
  Latex polymer
  Small molecule feedstocks
Examples
  From lignin
  Vanillin
  Platform molecules
  Fatty acids
The Advantages and Drawbacks of bio-based molecules
Topics To Be Covered

## Slide 4: What can be made from one barrel of oil?
http://www.visualcapitalist.com/can-made-one-barrel-oil/

## Slide 5
Notes: Today, the list of petroleum based products is even longer.

## Slide 6: The biorefinery
What Is a Biorefinery?
A biorefinery is a facility that integrates biomass conversion processes and equipment to produce fuels, power, and chemicals from BIOMASS. The biorefinery concept is analogous to today's petroleum refineries, which produce multiple fuels and products from petroleum. Industrial biorefineries have been identified as the most promising route to the creation of a new domestic biobased industry.
http://www.nrel.gov/biomass/biorefinery.html

## Slide 7: Renewable feedstocks
Biomass (algae, corn, switchgrass, poplar, willow, sorghum, and bamboo)
Agricultural waste (ex. manure)
Urban waste (garbage, sewage)
CO2
Renewable feedstocks include the following materials:
Source: Adobe Stock

## Slide 8
Organisms have provided a huge share of the materials used by humans throughout their existence.
• Biomass is the leading candidate to replace petroleum as a feedstock for the organic chemicals industry.
• Partially oxidized biomass material avoids expensive, and sometimes difficult oxidation steps in oxidizing petroleum
Biological feedstocks
Biomass: Plant material generated by photosynthesis
Image: Wikimedia Commons, Author: Daniel Schwen

## Slide 9
Chart: Biomass production in nature: 180 billion metric tons/year
| Carbohydrates | Lignin | Fats, proteins, terpenes, etc.
Sales | 75 | 20 | 5
Only about 4% utilized by humans
(food, ethanol, sweeteners)
Nature’s richest source of aromatic carbon. Used in polymers, adhesives, production of phenolic chemicals.
Converted into polymers, lubricants, and detergents.
Building blocks for a diverse chemical platform.
Lignocellulolic feedstock

## Slide 10
Oils (25% of biomass usage): first renewable raw material used towards the chemical industry
-> surfactants, cosmetic products, and lubricants as major products
Triglicerides
Images: Creative commons
Lipid oils can be extracted from the seeds of some plants.
• Volatile solvent n-hexane, C6H14, is used to extract the oils.
• Solvents are distilled off from the extract and recirculated through the process.
Image: Wikimedia Commons, Marula - Sclerocarya birrea – Seeds, Author: Genet

## Slide 11
Nature has evolved plant cell wall structure to prevent easy degradation by chemical attack… hence the challenge
Cellulose
Lignin
Hemicellulose
Lignocellulolic feedstock
Images: Creative commons

## Slide 12
Chitin
Meier, M. A.; Metzger, J. O.; Schubert, U. S., Chem Soc Rev 2007, 36 (11), 1788-1802
G.W. Huber, S. Iborra, A. Corma, Chem. Rev., 2006, 106, 4044−4098
X. Chen, S. L. Chew, F.M. Kerton, N. Yan, Green Chem., 2014, 16, 2204-2212
N containing polymers
Grain seeds can be used as sources of protein.
• Grain seeds are generally used for food.
• They are potentially useful as chemical feedstocks for specialty applications.
• Transgenic plants can be used to make specialty proteins, such as medicinal agents.
Proteins
Image: Wikimedia Commons, Brown Flax Seeds, Author: Sanjay Acharya
Can give access to glucosamine

## Slide 13
Latex rubber
Latex rubber can be collected from rubber tree sap (Hevea tree)
Image: Wikimedia Commons, Rubber trees in Kerala, India, Author: M.arunprasad
Latex rubber

## Slide 14
Small Molecules Feedstocks
Carbohydrates are created in several forms:
• Sucrose sugar, C12H22O11, is squeezed from sugar cane as sap and is extracted from sugar beets and sugar cane with water.
• Starch, a polymer of glucose readily isolated from grains (such as corn) and from potatoes, and is readily broken down by adding water to produce glucose.
• Huge amounts of cellulose, which occur in the woody parts of plants, can be broken down to glucose with cellulase enzymes.
Small molecules arbohydrates can be used as feedstocks for chemical processes

## Slide 15
Vanillin
Meier, M. A.; Metzger, J. O.; Schubert, U. S., Chem Soc Rev 2007, 36 (11), 1788-1802
G.W. Huber, S. Iborra, A. Corma, Chem. Rev., 2006, 106, 4044−4098 – Wikipedia: terpenes
Small molecules feedstocks
conifer resins = source of terpenes
sugars, oligosaccharides, peptides, oligopeptides, alcohols, amines
Steam treatment and distillation are used to extract such molecules => major challenge
Some terpenes
limonene
Α-pinene

## Slide 16
Biomass needs to be reduced to used as fuel.. Or as molecules
Dehydration
Reduction
Redox rearrangements (-CO2)
Fossil vs biomass: the process
Images: Creative commons
Notes: 16

## Slide 17: What can be made from renewable feedstocks?
Defense and aerospace
Adhesives
Coatings
Corrosion, inhibitors
Automotive
Solvents
Polymers
Fuels
Household cleaners
Surfactants
Fragrances
Dyes
Cosmetics
Builders
Chelating agents
Dyes
Agriculture
Pesticides
Fungicides
Fertilizers
Electronics
Solder
Housings
Displays
Pharmaceuticals
Specialty Chemicals
Used in Academic Research Labs

## Slide 18: Companies that make bio-based products
Image: National Research Council. 2015. Industrialization of Biology: A Roadmap to Accelerate the Advanced Manufacturing of Chemicals. Washington, DC: The National Academies Press. https://doi.org/10.17226/19001.

## Slide 19: How are biological feedstocks processed?
?
Images: Creative commons
Conventional chemistry
Microorganisms
(aerobic, anaerobic)
Enzymes
Fermentation

## Slide 20: Example: Enzymatic lignocellulose breakdown
Lignocellulose is a complex polymer obtained from plant cell walls. It has many aromatic subunits.
Images: Creative commons

## Slide 21: Main Industries for Lignocellulose
Retains applied nitrogen longer in the plants’ root zone, optimizing crop utilization and yield, and reducing nutrient run-off.
Retains applied nitrogen longer in the plants’ root zone, optimizing crop utilization and yield, and reducing nutrient run-off.
PAPER INDUSTRY
BIOETHANOL INDUSTRY
Lignin powder
Bioethanol
Burnt or Discarded
Images: Creative commons

## Slide 22: Lignin: A Source of Renewable ‘Drop-in’ Platform Chemicals
A Need of New Technology:
Economical
Sustainable
Selective
Efficient
phenol
The lignin structure includes aromatic (ring) structures.
If it is broken down selectively, it can be a source of drop-in platform chemicals such as phenol.

## Slide 23: A Depolymerization Strategy for the Valorization of Lignin
With the addition of hydrogen and a selective catalyst, lignin can be broken down into phenols.
Lignin
Phenols

## Slide 24: The story of vanillin
Vanilla has been extracted and used, for instance for making chocolate drinks by the Aztecs
Vanillin can be found in many plants. The highest natural concentrations, 1–3% and sometimes higher, are found in the properly cured pods of the “vanilla bean”
M. B. Hocking, J. Chem. Ed., 1997, 1055-59

## Slide 25: The story of vanillin
In 1874–75, synthetic vanillin could be prepared from eugenol (clove oil), it was competitive with naturally extracted vanillin and became the main source of vanillin until the 1920s
The next phase was to produce it from lignin
M. B. Hocking, J. Chem. Ed., 1997, 1055-59
Clove oil (eugenol)

## Slide 26: The story of vanillin
The conversion of lignin (waste pulping process) to vanillin was first suggested at the end of the XIXth century
Some of the research was done at McGill (1930s) with G.H. Tomlinson. Yields up to 10% with O2 and 3-% with nitrobenzene where obtained
Tomlinson, G. H., II; Hibbert, H. J. Am. Chem. Soc. 1936, 58, 345–348.

## Slide 27: The story of vanillin
M. B. Hocking, J. Chem. Ed., 1997, 1055-59
The vanillin production of Ontario Pulp and Paper became such a valuable component of their operations that the scale was gradually expanded to 3.4 million kilograms per year by 1981, sufficient to supply 60% of the then current world market. This also began to subtly affect the pulping component of their business”
Paper mill, Thorold, ON

## Slide 28: The story of vanillin
Since the 1970 it become more competitive and more environmentally friendly to produce vanillin from petro chemicals. Via guaiacol. This is a process developed by Rhodia.
M. B. Hocking, J. Chem. Ed., 1997, 1055-59

## Slide 29: The story of vanillin
From 2000, Rhodia developed a biosynthesis of vanillin. With yeast, ferulic acid extracted from rice bran can be turned into vanillin. It’s not competitive with petro based vanillin, but it can be labeled “natural Vanillin”
Source: Wikipedia: Vanillin
M.J. Gasson, Y. Kitamura, W. R. McLauchlan et al., J. Biol. Chem., 1998, 273, 4163-4170.

## Slide 30: Example: Penicillin production using fermentation
Penicillin antibiotics were among the first medications to be effective against many bacterial infections caused by staphylococci and streptococci. They are still widely used today, though many types of bacteria have developed resistance due to the extensive use.
The secondary metabolite of a fungus - Penicillium chrysogenum - grows using a carbon source of glucose and lactose.
Once the fungus reaches a stationary phase, it starts producing the antibiotic.
Images: Creative commons

## Slide 31
The idea is to depolymerize cellulose (or ideally lignocellulose) and form a molecule that could further be derived in many more. E.g : 5-hydroxymethylfurfural (HMF)
H. B. Zhao, J. E. Holladay, H. Brown and Z. C. Zhang, Science, 2007, 316, 1597–1600
The platform strategy

## Slide 32
5-hydroxymethylfurfural (HMF) as a building block
A. A. Rosatella, S.P. Simeonov, R. F. M. Fradea, C.A.M. Alfonso Green Chemistry 13.4 (2011): 754-793.
FDA: replacement monomer for terephthalic acid
polyurethane foams
biofuel and fuel additive
The platform strategy

## Slide 33: The Top 10 Chemical Targets (platform chemicals from bio-feedstocks)

## Slide 34
Fatty acids are obtained from triglycerides extracted from vegetable or algea oil
  100 million tonnes of oils and fats are produced annually, 25% from soya
  14% of it is used for chemicals manufacture
  The rest is used for food and for making biodiesel
  25% of all the biomass used for molecules is from fatty acids
  Problems associated with the usage of vegetable oil:
    Mix of several acids in the oil
    Low concentration of a given acid
    =>genetic engineering was used:
      E.g. rapeseed can have an erucic acid concentration varying from 0- 50%
      E.g. rapeseed can have a lauric acid concentration varying from 0- 37%
      E.g. sunflower oil can contain up to 92% of oleic acid
CHEM 462: 24.Chemicals from renewable feedstock
Green Chemistry: An Introductory Text, M. Lancaster, RSC Publishing, Cambridge, 2012
Fatty acid as feedstock

## Slide 35
Use of fatty acids: surfactant
  3 Mt/a of surfactants produced in Europe only (mostly for household detergents)
  About a 1/6 of it comes from renewable material
Synthetic surfactant
Fatty acid as feedstock

## Slide 36
Major use of fatty acids: surfactant
  soap
Ionic surfactants
Green Chemistry: An Introductory Text, M. Lancaster, RSC Publishing, Cambridge, 2012
Fatty acid as feedstock

## Slide 37
Use of fatty acids: lubricant
  Lubricant represents 2% of the non-food, non-fuel use of fatty acids
    Fatty acids have a higher viscosity
    Their properties are more stable with temperature
    Lower evaporation loss
    Lower toxicity
    Better biodegradability
  Vegetable oils can also be used
    Rape seed
    Canola
    Soyabean
    They all contains mixture of esters of fatty acids (16:0, 18:0, 18:1, 18:2, 18:3, 22:1)
Green Chemistry: An Introductory Text, M. Lancaster, RSC Publishing, Cambridge, 2012
Fatty acid as feedstock

## Slide 38
Further chemical transformation via oxidation
  Doing this with recyclable catalyst selectively is the big challenge
Fatty acid as feedstock

## Slide 39
These are great examples, but some compete with food.
Idea: using waste from the food industry?
Idea: using urban waste
Fatty acid as feedstock
Images: Creative commons

## Slide 40: Recent development: biomass waste
From cashew nut shell waste: David Cole Hamilton
CHEM 462: 24.Chemicals from renewable feedstock
David Cole-Hamilton (St Andrews, UK) Eur. J. Lipid Sci. Technol. 2012, 114, 1183 Mubofu, Egid B. Pure App. Chem. 88.1-2 (2016): 17-27
  byproduct of the cashew nut processing industry available at about 300 000 tonnes/year worldwide
  5: tsetse fly pheromone 6: detergent
  7: plasticizer 8: precursor to chemicals
the top five producers being
- Vietnam (1.1 million tons)
Nigeria (0.95 million tons)
India (0.75 million tons)
Cote d’Ivoire (0.45 million tons%)
Brazil (0.11 million tons)
Notes: 40

## Slide 41: Avoiding competing with food: biomass waste
Orange peels: James Clark (York, UK)
  Global agriculture produces about 15.6 million tons of orange and other citrus waste annually in the form of discarded peels
    biofuels
    bio-based solvents
    Fragrances
    water purifiers
CHEM 462: 24.Chemicals from renewable feedstock
http://cleantechnica.com/2012/07/07/opec-uses-orange-peel-for-biofuel-and-other-biobased-products/
low temperature microwaves
+ cellulose
Notes: 41

## Slide 42: Why use renewable feedstocks?
Economic reasons:
  The inherent long-term tendency for petroleum price increases.
  A fluctuation of a few cents in the price of crude oil can result in massive price swings for downstream products.
  The constant decrease in cost of renewable resources.
Scientific reasons:
  The constant improvement in quality of renewable feedstocks.
  Modern plant breeding.
  Genetic manipulation.
  Breakthroughs in catalysis (enzymes, etc.).
Environmental reasons:
  Biological compatibility (to an extent).
  The use of waste streams (wood pulping, agriculture, etc.).
  Mitigate CO2 emissions

## Slide 43: Some Potential Challenges of Using Renewable Feedstocks
Feedstock cultivation
  Competition with food supply
  Land demand
  Nutritional needs
  Diseases
  Initial investment
Harvesting method to maximise yields and minimise degradation of product
Post harvest processing
Product extraction and purification
Product standardization
Complexity
Product storage, packing, and distribution
New methodologies for alternative feedstocks

## Slide 44
What can we make from petroleum (focus on molecules)
The biorefinery
Renewable Feedstocks
  Triglycerides
  Lignocellulosic Feedstocks
  N containing polymers
  Latex polymer
  Small molecule feedstocks
Examples
  From lignin
  Vanillin
  Platform molecules
  Fatty acids
The Advantages and Drawbacks of bio-based molecules
Topics To Be Covered

## Slide 45
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE