## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Renewable Feedstocks for energy
Image: Wikimedia Commons, Author: R. Möhler
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
Use of Renewable Feedstocks
A raw material or feedstock should be renewable rather than depleting whenever technically and economically practical.
Image: Wikipedia, Pongamia Pinnata Seeds

## Slide 3
Where does things come from
Fossil carbon
  Gas
  Oil
  Coal
First, Second, and Third Generation Feedstocks
  Bioethanol
  Ethanol from cellulose
  Biodiesel
  Biofuel from algea
The Advantages and Drawbacks of Biofuel
Topics To Be Covered

## Slide 4: Where does stuff come?
Fimiston Open Pit (Gold mine, Australia)
Brine pools (Lithium mine, Soquimich, Atacama, Chile)
vs
Biomass
Mined materials
CHEM 512: Heterogeneous catalysis

## Slide 5: Where does stuff come?
vs
Biomass
Mined materials
CHEM 512: Heterogeneous catalysis
C
For carbon

## Slide 6: Renewable vs. Fossil Feedstocks
Feedstock:
A raw material to supply or fuel or industrial process.
Renewable or Depleting is a question of time:
A renewable resource is determined to be renewable if it can be replenished in a relevant amount of time.
Fossil fuels are depleting because they cannot be replenished in a practical timeframe from vegetation.
Image: Wikimedia Commons, Author: Johnlacrosse

## Slide 7: Fossil carbon timeline
Fossil carbon is formed over 300 million years ago
    CO2
Absorption
Death
Decomposition 99,99%
Sequestration 0.01%
Fossil fuel: gas, oil, char…
Millions of years
Source: DOE

## Slide 8: How is petroleum generated and used?
Petroleum Products [Hydrocarbons – highly reduced state]
Biomaterials [Carbohydrates, Proteins, Lipids]
Highly Functionalized Molecules
Functionalized Compounds [Olefins, Alkylchlorides]
Highly Functionalized Molecules
1. High temperature, and pressure; natural process of oil creation
2. Oil extraction and processing
3. Separation and oxidation, high energy input
4. Further functionalization, replacing reactive groups with functional groups of interest
Over millennia

## Slide 9: Fossil carbon
Formation of fossil fuels: what happens during sequestration?
  Transformation under high temperature and pressure of cellulose, lignin, lipids, chitin, proteins…
    into kerogen and bitumen (high molecular weigh, viscous material). Kerogen from an oil shale deposit of western USA: C215H330O12N5S
    Then cracking of this material into lower molecular weight material: crude oil and natural gas.
    Reforming can also afford coal
      Oil shale containing kerogen
Image: Wikimedia Commons

## Slide 10: Where does energy come from?
Fossil fuels provide a significant part of our energy supply (almost three quarter):
  oil + coal + gas
    Sources of world energy
The graph includes a prediction for year 2035, where the projected energy consumption will reach 770 quadrillion British Thermal Unit [BTU].
Source: U.S. Energy Information Administration [U.S. EIA].
Increasing world energy consumption since 1990.
http://www.eia.gov/todayinenergy/detail.cfm?id=11951

## Slide 11: Carbon peak?
The oil peak may actually not happen soon… or at all
M. King Hubbert, was an oil geologist of developed the theory of the ‘ultimately recoverable reserve’. He predicted that oil production in the USA would peak at about 1970
“The peak concept is not valid for modelling mineral resource depletion”
Critical Metals Handbook, First Edition. Edited by Gus Gunn, 2014 John Wiley & Sons,
A peak in resource science is defined as a moment when production peaks before it drops continuously.

## Slide 12: Gas from fracking
Zhiltsov, S. S.; Semenov, A. V. In Shale Gas: Ecology, Politics, Economy; Springer International Publishing, 2016; pp 9–16.
Gas production by fracking as exploded over the past 10 years

## Slide 13: Gas from fracking
Gas production by fracking as exploded over the past 10 years
http://www.eia.gov/todayinenergy/detail.cfm?id=11951

## Slide 14: Crude oil in the world
CHEM 512: Heterogeneous catalysis

## Slide 15
Only ~ 3.5 % of all crude oil processed ends up in petrochemicals
The rest is called the paraffins
  70 % is used as fuel
  25% is asphalt, coke, bitumen, wax, etc.
chemicals are worth as much as the fuel !
Source: New Scientist 2007
Source: www.fas.org
CHEM 512: Heterogeneous catalysis
Use & Cost of Crude Oil (USA)

## Slide 16: How are petroleum products made?
By using a fractionation column.
By oxidation (typically by a powerful oxidizing agent like chloride) and adding numerous additives.

## Slide 17: What is petroleum used for?

## Slide 18: The South African context
CHEM 512: Heterogeneous catalysis
South Africa has no oil
  Apartheid: South Africa under embargo between the 1960s and 1990s
  South Africa has a lot of mining ressources: Gold, Nickel, Chromium, Copper, Platinum…and coal. But no oil.
  Sasol company (Suid Afrikaanse Steenkool en Olie) makes most of current diesel fuel used in SA by Fisher Trosph process
http://www.fischer-tropsch.org/

## Slide 19: The South African context
CHEM 512: Heterogeneous catalysis
South Africa has no oil
Catalysis, From principles to Applications, by M. Beller, A. Renken, R.A. van Santen, Wiley-VCH 2012.
.
High energy input
High energy input

## Slide 20: Fisher Tropsch
Future of Fischer-Tropsch
  Turn biomass into fuels… and waste too!
CO
H2

## Slide 21: Fisher Tropsch
Type: commercial Status: initiated production and commercial operations (biomethanol)
Feedstock: post-sorted municipal solid waste (after recycling and composting) Products: methanol, ethanol Capacity: 38 million litres / 10 million gallons per year - Source: Enerkem website
Fischer-Tropsch to methanol
  Enerkem, Quebec company founded by Prof. Esteban Chornet (U. Sherbrooke)
Edmonton plant

## Slide 22: What about energy from renewable resources?
Source: Adobe Stock

## Slide 23
World energy consumption by source as reported in 2013.
While the use of fossil fuels is still predominant, by 2013 there was an increase in the use of renewable sources of energy. Most renewable energy comes from biomass.
Source: REN21 Renewables 2014 Global Status Report.
Energy Feedstocks Sources

## Slide 24: Renewable feedstocks
Biomass (algae, corn, switchgrass, poplar, willow, sorghum, and bamboo)
Agricultural waste (ex. manure)
Urban waste (garbage, sewage)
CO2
Renewable feedstocks include the following materials:
Source: Adobe Stock

## Slide 25: Environmental Issues
Bioenergy can have positive impacts:
• Green house gas reduction (through fossil-fuel substitution).
• More agrobiodiversity, soil carbon increase, less erosion.
But these impacts can also be negative:
• Green house gas from cultivation, soil carbon, life-cycle, direct and indirect land-use changes.
• Loss of biodiversity from land-use changes, water use, agrochemicals, erosion.
Competition with food

## Slide 26
First Generation Biofuels
Oils for diesel
Grains are used to produce ethanol
Food versus fuel
Second Generation Biofuels
Using agricultural wastes  lignocellulosics
Lignocellulosics from agrowaste
Grasses
These crops were not domesticated for use as biofuels
Third Generation Biofuels (looking to the future)
Algae
Types of Biofuel

## Slide 27
The first Diesel engin was exhibited to function with vegetable oil
In 1900 a small Diesel engine was exhibited by the Otto company which, on the suggestion of the French Government, was run on Arachide oil, and operated so well that very few people were aware of the fact. The motor was built for ordinary oils, and without any modification was run on vegetable oil. Rudolf Diesel
Rudolf Diesel
Chalkley, Alfred Philip (1912), Diesel engines for land and marine work (2nd ed.), New York, New York, USA: D. Van Nostrand, p. 3
Biodiesel

## Slide 28
Biodiesel refers to vegetable oil or animal fat-based diesel fuel consisting of long-chain esters. The main component of vegetable oil is triglycerides, which require transesterification prior to usage as a fuel. Transesterification is essential to get a good fuel.
BIODIESEL
Biodiesel

## Slide 29: Advantages of Biodiesel
40% reduction in global warming potential compared to conventional diesel
8% reduction in sulfur oxides. The release of sulfur oxides can lead to acid rain.
3% reduction in methane.
32% reduction in particulate matter (PM10 68%).
83.6% reduction in particulate matter soot.
79% reduction in wastewater.
96% reduction in hazardous waste, but double the non-hazardous waste.
By using spent oil, diesel can be turned from a first to second generation fuel
Compared to conventional diesel processing, biodiesel requires additional processing and has a lower overall energy return. Energy return is one of the important parameters that enables engineers to evaluate the efficiency and viability of a process. Energy return describes the amount one can gain from the production verses the amount of energy input. Biodiesel lags far behind conventional diesel processing in this regard.
Source: National Biodiesel Board,” Lifecycle Summary,” available at http://www.nbb.org/pdf_files/fuelfactsheets/LifeCycle_Summary.PDF
Notes: Source: National Biodiesel Board,” Lifecycle Summary,” available at http://www.nbb.org/pdf_files/fuelfactsheets/LifeCycle_Summary.PDF

## Slide 30: Steps Required to Produce Biofuel from Soybeans
Retrieved: nancymeyersdesign.com

## Slide 31: First Generation bioethanol
Grind up the feedstock so it can be easily and quickly processed.
Sugar is dissolved out of the material.
The sugar is fed to microbes that use it for food, producing ethanol and carbon dioxide in the process.
Purify the ethanol to desired concentration.
Images: Wikipedia Commons, Corncobs, Author: Sam Fentress; Wikimedia Commons, Biofuel Pumps, Author: Mario Roberto Duran Ortiz
Notes: Source: Department of Energy, Alternative Fuels Data Center, “How is Ethanol Made?”, available at http://www.eere.energy.gov/afdc/altfuel/eth_made.html

## Slide 32: First Generation bioethanol
This biofuel can be generated from:
  Sugar cane -> Sugar
  Corn -> Starch
  Lignocellulosic materials (waste or grasses) -> Cellulose
http://www.cropenergies.com/en/Bioethanol/Markt/Dynamisches_Wachstum/
https://marketresearch.biz/report/bioethanol-market/

## Slide 33: Bioethanol: the Brazilian case – from sugar
  Canes are crushed -> sugar juice
  For ethanol the sugar juice is diluted into 20% solution and fermented (yeast) for 8 hours: 6-10% ethanol solution. The yeast is removed and either recycled or dried and used as animal feed.
  The fibrous material left from the crusher is then used and burnt to provide electricity.
  From that 95 or 100% ethanol can be obtained by distillation (or membrane-filtration).
  For sugar production. the syrup can be filtered, condensed and sugar is recrystallized.
Fibrous remains of processed sugarcane, called bagasse, are burned in Brazil to generate electricity

## Slide 34: Bioethanol: the Brazilian case – from sugar
  A fermentation process
    In the example below, Nozoyme introduces a new enzyme able to prevent foaming (no more surfactant use)
https://www.novozymes.com/en/news/news-archive/2016/11/launch-of-worlds-first-biological-foam-control-for-sugarcane-ethanol

## Slide 35: Bioethanol: the Brazilian case – from sugar
Ethanol can be used directly as a liquid fuel:
  Either mixed with normal gasoline: a blend can have up to 25% of ethanol (US)
  Another strategy is to use 100% ethanol: it requires a special engine: 12.6% of transportation energy is made up with ethanol in Brazil (flex fuel technology)
Source: Wikipedia, Ethanol fuel in Brazil - Fuel Ethanol Market Analysis 2018 – 2025, Grand view research 2017.
Petrobras gas station at São Paulo with dual fuel service, marked A for alcohol (ethanol) and G for gasoline
Global fuel ethanol market volume by application, 2016 (%)

## Slide 36: Bioethanol: the Brazilian case – from sugar
Ethanol can be used directly as a liquid fuel:
  Either mixed with normal gasoline: a blend can have up to 25% of ethanol (US)
  Another strategy is to use 100% ethanol: it requires a special engine: 12.6% of transportation energy is made up with ethanol in Brazil (flex fuel technology)
  The country has reduced CO2 emissions by more than 350 million tons since the introduction of flex-fuel vehicles that can run on any combination of ethanol and gasoline. There are more than 26 million such vehicles in Brazil.
Source: Novozyme

## Slide 37: Bioethanol: the US case – from starch
  Ethanol is produced from cornstarch
  Cornstarch need to be converted into glucose by enzymes: the process is less efficient
From Novozyme
Cornstarch
Sugar
Ethanol

## Slide 38: Bioethanol: the US case – from starch
  To provide energy for the USA society, the surface necessary to plant with corn is… the whole surface of the USA.
  Bioethanol from corn is controversial: scientists (Pimentel and others) claim that bioethanol from corn costs more energy to produce than the energy it delivers… Is it really worth then?
  Since 2004/5, George Bush has launched a program dedicated to bioethanol from corn.

## Slide 39: Bioethanol: the US case – from starch
Bioethanol pushed the demand for U.S. corn
Million tonnes/year
Fuel Ethanol Market Analysis 2018 – 2025, Grand view research 2017.

## Slide 40: Environmental Consequences per Unit Energy
Greenhouse Gas Emissions per Unit Energy
Soybean biodiesel needs less fertilizer and pesticide than corn ethanol.
Soybean biodiesel produces significantly less green house gas.
Comparing corn bioethanol and biodiesel
Data of Lee et al. and Muir et al, collated in Gressel“Genetic Glass Ceilings, Hopkins, 2007

## Slide 41
To fill up an average 25 gallon SUV gas tank with ethanol requires the same amount of grain as it takes to feed 1 person for 1 year.
Every person in the U.S. uses 500 gallons of gasoline per year.
That means that each year, every person in the U.S. would use enough gasoline to feed 20 people for one year.
There are 300 million people in the U.S. – if each person was using enough food to feed 20 people to run their cars, that alone would require enough grain to feed 6 billion people.
Food verses Biofuel: The Math
Notes: Source: Sharon Astyk, “Ethics of Biofuels” Energy Bulletin (Dec. 28 2006), available at http://www.energybulletin.net/24169.html

## Slide 42: Ethanol Supply: The Effect on Corn Supply and on Gasoline Supply

## Slide 43
First Generation Biofuels
Oils for diesel
Grains are used to produce ethanol
Food versus fuel
Second Generation Biofuels
Using agricultural wastes  lignocellulosics
Lignocellulosics from agrowaste
Grasses
These crops were not domesticated for use as biofuels
Third Generation Biofuels (looking to the future)
Algae
Types of Biofuel

## Slide 44: Second Generation Biofuels: Cellulosic Feedstock
Switchgrass
Wheat Straw
Hybrid Poplar
Corn Stalks
Image, Wikimedia Commons, Author: David Hawgood

## Slide 45: Second Generation Biofuels
  To qualify as second generation, a feedstock must not be suitable for human consumption and meet the following criteria:
    Should grow on marginal (non-agricultural) land.
    Should not require large amounts of water or fertilizer.
    Certain food products can become second generation fuels when they are no longer useful for consumption:
        Waste vegetable oil (2nd generation feedstock).
        Virgin vegetable oil (1st generation feedstock).

## Slide 46
Data of Lee et al. and Muir et al, collated in Gressel,
“Genetic Glass Ceilings, Hopkins, 2007
Switchgrass still needs water and fertilizer to grow.
kg ha-1 yr-1 | Corn | Switchgrass
N | 148 | 0
P | 23 | 4
K | 50 | 6
Nutrients needed:
corn versus switchgrass.
Nitrogen fertilizer
Water
Switchgrass as a Feedstock

## Slide 47
First Generation Biofuels
Oils for diesel
Grains are used to produce ethanol
Food versus fuel
Second Generation Biofuels
Using agricultural wastes  lignocellulosics
Lignocellulosics from agrowaste
Grasses
These crops were not domesticated for use as biofuels
Third Generation Biofuels (looking to the future)
Algae
Types of Biofuel

## Slide 48
Third Generation Biofuels: Algae Feedstock
Source: wikipedia

## Slide 49: Biodiesel from algae
“It has more oil per pound than corn and soybeans, does not divert crops from the food supply and can potentially be grown in sewage water and seawater without impacting the freshwater supply.” J. Zimmerman
http://www.csa.com/discoveryguides/biofuel/review7.php

## Slide 50: Biodiesel from algae
Adaptable to large scale
  On a larger scale, Solix has built a pilot-scale demonstration facility with three-quarters of an acre of photosynthetic area forecasted to generate 1,500–2,000 gallons/year of biocrude, or an estimated several tons of biomass per year if the solids are included (2011)
  Note: Solix today seems focused on the specialty nutrition products from algea
“The ideal location is in a dry, sunny, flat desert, with a carbon dioxide source such as a coal-fired power plant and a significant wastewater source"Bryan McCarty, Solix Biofuels' vice president of engineering
https://www.asme.org/engineering-topics/articles/bioengineering/scaling-algae-growth-for-biofuels

## Slide 51: Is Algae “Green Gold”?
Currently being developed.
30 times more oil per acre than current crops that are being used.
No sulfur.
Non-toxic
Highly biodegradable,
Not subject to a commodity risk like crude oil, corn, and soybeans are.
Notes: Source: EcoFriend Article, “Algae BioFuels: PetroSun’s Subsidiary to Develop Bio-diesel Form Algae” India (2006), available at http://www.ecofriend.org/entry/algae-biofuels-petrosuns-subsidiary-to-develop-bio-diesel-form-algae/

## Slide 52: Pros
Versatility in growth methods
Versatility in uses
Speed of production
Potential for huge production levels
CO2 reduction
Cons
Energy intensive
Not competitive against foreign oil (yet)
Needs funding
Technology not ready (yet)
Algae: The Pros and Cons

## Slide 53: How to Overcome the Technical Roadblocks to Low-Cost Advanced Biofuel Production
Make all of the components of biomass available for biofuel and co-product production:
Use the appropriate parts of specific plants.
Improve the efficiency of biomass to biofuel conversion:
Do it faster, cheaper, and sustainably.
Minimize the cost of biomass transportation.
Move more for less.

## Slide 54: Biofuels as an Alternative
Biofuels are not THE answer to sustainable energy, but biofuels may be part of the answer.
Biofuels may offer environmental and economic advantages over fossil fuels, but the magnitude of these advantages depends on how a biofuel crop is grown and converted into a usable fuel.

## Slide 55
Where does things come from
Fossil carbon
  Gas
  Oil
  Coal
First, Second, and Third Generation Feedstocks
  Bioethanol
  Ethanol from cellulose
  Biodiesel
  Biofuel from algae
The Advantages and Drawbacks of Biofuel
Topics To Be Covered

## Slide 56
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE