## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Renewable Feedstocks for molecules
Image: Wikimedia Commons, Author: R. Möhler
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
Use of Renewable Feedstocks
A raw material or feedstock should be renewable rather than depleting whenever technically and economically practical.
Image: Wikipedia, Pongamia Pinnata Seeds

## Slide 3
What can we make from petroleum (focus on molecules)
The biorefinery
Renewable Feedstocks
  Triglycerides
  Lignocellulosic Feedstocks
  N containing polymers
  Latex polymer
  Small molecule feedstocks
Examples
  From lignin
  Vanillin
  Platform molecules
  Fatty acids
The Advantages and Drawbacks of bio-based molecules
Topics To Be Covered

## Slide 4: What can be made from one barrel of oil?
http://www.visualcapitalist.com/can-made-one-barrel-oil/
low value
high volume
high value
low volume

## Slide 5
Notes: Today, the list of petroleum based products is even longer.

## Slide 6: The biorefinery
What is a Biorefinery?
A biorefinery is a facility that integrates biomass conversion processes and equipment to produce fuels, power, and chemicals from BIOMASS. The biorefinery concept is analogous to today's petroleum refineries, which produce multiple fuels and products from petroleum. Industrial biorefineries have been identified as the most promising route to the creation of a new domestic biobased industry.
http://www.nrel.gov/biomass/biorefinery.html

## Slide 7: How do we get chemicals from biomass?
1. Extraction of desired compound
Linolenic acid
Notes: Flax -> linseed oil -> Linolenic acid (47-55% of linseed oil).
Drying agent in paints, varnishes, inks.

## Slide 8: How do we get chemicals from biomass?
1. Extraction of desired compound
Linolenic acid
2. Extraction of precursor
Erucic acid
Erucamide
Notes: Modified rape seed -> erucic acid (60,000 tpa in Europe) -> erucamide (slip agent for polyethylene bags)

## Slide 9: How do we get chemicals from biomass?
1. Extraction of desired compound
Linolenic acid
3. Hydrolysis
2. Extraction of precursor
Erucic acid
Erucamide
Notes: Waste from pulp mills -> -> levulinic acid (70% yield) and from there to many products.
DALA (delta-aminolevulinic acid), a biodegradable herbicide.

## Slide 10: How do we get chemicals from biomass?
4. Pyrolysis
350-
500 ˚C
oil + char
Notes: Pyrolysis. Heat it up to 350-500 ˚C, obtain gas, liquid (pyrolysis oil) and solid (char) products. The pyrolysis oil is the most valuable, as a source of chemicals and as a fuel. The char, if very pure, can be valuable, but often it is not pure.
Gasification. Solves problem of variable quality feedstocks. Gasify at 400-600 ˚C. Get CO, H2, char and unfortunately tars and hydrocarbons. Tar can be combusted at high temperature to make CO2, water, and cracked tar compounds.The CO2 and C (charcoal) are reacted to make CO in the “reduction” step.

## Slide 11: How do we get chemicals from biomass?
5. Gasification to syngas
drying
4. Pyrolysis
350-
500 ˚C
oil + char
H2 + CO + charcoal + tar
400-600 ˚C
1200 ˚C combustion
CO2
synthesis
gas
polyethylene
fuels &
solvents
CH4
CH3OH
Ru
Fe
Ni
Cu
Fischer-Tropsch chemistry
Notes: Pyrolysis. Heat it up to 350-500 ˚C, obtain gas, liquid (pyrolysis oil) and solid (char) products. The pyrolysis oil is the most valuable, as a source of chemicals and as a fuel. The char, if very pure, can be valuable, but often it is not pure.
Gasification. Solves problem of variable quality feedstocks. Gasify at 400-600 ˚C. Get CO, H2, char and unfortunately tars and hydrocarbons. Tar can be combusted at high temperature to make CO2, water, and cracked tar compounds.
The CO2 and C (charcoal) are reacted to make CO in the “reduction” step.

## Slide 12
Chart: Biomass production in nature: 180 billion metric tons/year
| Carbohydrates | Lignin | Fats, proteins, terpenes, etc.
Sales | 75 | 20 | 5
Only about 4% utilized by humans
(food, ethanol, sweeteners)
Nature’s richest source of aromatic carbon. Used in polymers, adhesives, production of phenolic chemicals.
Converted into polymers, lubricants, and detergents.
Building blocks for a diverse chemical platform.
Biomass feedstock

## Slide 13
Nature has evolved plant cell wall structure to prevent easy degradation by chemical attack… hence the challenge
Cellulose
Lignin
Hemicellulose
Lignocellulosic feedstock
Images: Creative commons

## Slide 14
Cellulose
Lignocellulosic feedstock
image from PNG All
syngas
Notes: images from Wikipedia except lab coat from http://www.pngall.com/lab-coat-png

## Slide 15
Lignocellulosic feedstock
Hemicellulose
syngas
Notes: Xylitol photo by PG Jessop.

## Slide 16
Lignin
Lignocellulosic feedstock
Liquid
Smoke
artificial vanillin
Paper Mill, Thorold, ON

## Slide 17
Carbohydrate Feedstocks
Carbohydrates are created in several forms:
• Sucrose sugar, C12H22O11, is squeezed from sugar cane as sap and is extracted from sugar beets and sugar cane with water.
• Starch, a polymer of glucose readily isolated from grains (such as corn) and from potatoes, and is readily broken down by adding water to produce glucose.
• Huge amounts of cellulose, which occur in the woody parts of plants, can be broken down to glucose with cellulase enzymes.
Carbohydrates can be used as feedstocks for chemical processes.

## Slide 18
Carbohydrate Feedstocks
Starch
MSG

## Slide 19
Oils (25% of biomass usage): first renewable raw material used towards the chemical industry
-> surfactants, cosmetic products, and lubricants as major products
Triglycerides Feedstock
Images: Creative commons
Lipid oils can be extracted from the seeds of some plants.
• Volatile solvent n-hexane, C6H14, is used to extract the oils.
• Solvents are distilled off from the extract and recirculated through the process.
Image: Wikimedia Commons, Marula - Sclerocarya birrea – Seeds, Author: Genet

## Slide 20
Triglycerides Feedstock

## Slide 21
Fatty acids are obtained from triglycerides extracted from vegetable or algae oil:
  100 million tonnes of oils and fats are produced annually, 25% from soya
  14% of it is used for chemicals manufacture
  The rest is used for food and for making biodiesel
  25% of all the biomass used for molecules is from fatty acids
  Problems associated with the usage of vegetable oil:
    Mix of several acids in the oil
    Low concentration of a given acid
    =>genetic engineering was used:
      E.g. rapeseed can have an erucic acid concentration varying from 0- 50%
      E.g. rapeseed can have a lauric acid concentration varying from 0- 37%
      E.g. sunflower oil can contain up to 92% of oleic acid
Green Chemistry: An Introductory Text, M. Lancaster, RSC Publishing, Cambridge, 2012
Triglycerides Feedstock

## Slide 22
Triglycerides Feedstock
Credit: Ulet Ifansasti/Greenpeace

## Slide 23
Chitin
Meier, M. A.; Metzger, J. O.; Schubert, U. S., Chem Soc Rev 2007, 36 (11), 1788-1802
G.W. Huber, S. Iborra, A. Corma, Chem. Rev., 2006, 106, 4044−4098
X. Chen, S. L. Chew, F.M. Kerton, N. Yan, Green Chem., 2014, 16, 2204-2212
N containing polymers
Grain seeds can be used as sources of protein.
• Grain seeds are generally used for food.
• They are potentially useful as chemical feedstocks for specialty applications.
• Transgenic plants can be used to make specialty proteins, such as medicinal agents.
Proteins
Image: Wikimedia Commons, Brown Flax Seeds, Author: Sanjay Acharya
Can give access to glucosamine

## Slide 24
Terpenes
Image: Wikimedia Commons, Rubber trees in Kerala, India, Author: M. Arunprasad
Latex rubber
Hydrocarbon terpenes can be tapped from rubber trees as a latex suspension in tree sap.
Steam treatment and distillation are used to extract terpenes from sources such as pine or citrus tree biomass.

## Slide 25
Dehydration
Reduction
Redox rearrangements (-CO2)
Fossil vs biomass: the differences
Images: Creative commons
Oxidation
Petroleum & natural gas
Biomass (other than triglycerides & terpenes)
Notes: 25

## Slide 26
Fossil vs biomass: the differences
Adapted from: Basu, Biomass Gasification and Pyrolysis: Practical Design and Theory
Crude Oil
ethylene, PE, propylene, PP
acrylonitrile
& styrene
1
caprolactam
cumene
ethylene glycol
ethylene oxide
phenol
xylene
terephthalic acid
vinyl chloride
toluene
methanol
Triglycerides
Biomass
ratio
Notes: 26

## Slide 27
Fossil vs biomass: the differences
Resources
Primary
Feedstock
Second
Feedstock
High value compound
Technology Roadmap: Energy and GHG Reductions in the Chemical Industry via Catalytic Processes, Int. Energy Agency, 2013.
Notes: 27

## Slide 28
Fossil vs biomass: the differences
Resources
Primary
Feedstock
Second
Feedstock
High value compound
Technology Roadmap: Energy and GHG Reductions in the Chemical Industry via Catalytic Processes, Int. Energy Agency, 2013.
MTO
gasification
then FT
farming
removal of water is here
lowering O/C ratio is here
Notes: 28

## Slide 29
Fossil vs biomass: the differences
Resources
Primary
Feedstock
Second
Feedstock
High value compound
Technology Roadmap: Energy and GHG Reductions in the Chemical Industry via Catalytic Processes, Int. Energy Agency, 2013.
dehydration
fermentation
drying
farming
removal of water is here
lowering O/C ratio is here
Notes: 29

## Slide 30
Fossil vs biomass: the differences
Resources
Primary
Feedstock
Second
Feedstock
High value compound
Technology Roadmap: Energy and GHG Reductions in the Chemical Industry via Catalytic Processes, Int. Energy Agency, 2013.
cracking
distillation
oil
production
no removal of water required
Notes: 30

## Slide 31: Companies that make bio-based products
Image: National Research Council. 2015. Industrialization of Biology: A Roadmap to Accelerate the Advanced Manufacturing of Chemicals. Washington, DC: The National Academies Press. https://doi.org/10.17226/19001.

## Slide 32
The idea is to depolymerize cellulose (or ideally lignocellulose) and form a molecule that could further be derived in to many more.
E.g : 5-hydroxymethylfurfural (HMF)
H. B. Zhao, J. E. Holladay, H. Brown and Z. C. Zhang, Science, 2007, 316, 1597–1600
The platform strategy

## Slide 33
5-hydroxymethylfurfural (HMF) as a building block
A. A. Rosatella, S.P. Simeonov, R. F. M. Fradea, C.A.M. Alfonso Green Chemistry 13.4 (2011): 754-793.
FDA: replacement monomer for terephthalic acid
polyurethane foams
biofuel and fuel additive
The platform strategy

## Slide 34: The Top 10 Chemical Targets (platform chemicals from saccharide feedstocks)

## Slide 35
These are great examples, but some compete with food.
Idea: using waste from the food industry?
Idea: using urban waste
Images: Creative commons
Avoiding competing with food

## Slide 36
From cashew nut shell waste: David Cole Hamilton
CHEM 462: 24.Chemicals from renewable feedstock
David Cole-Hamilton (St Andrews, UK) Eur. J. Lipid Sci. Technol. 2012, 114, 1183 Mubofu, Egid B. Pure App. Chem. 88.1-2 (2016): 17-27
  byproduct of the cashew nut processing industry available at about 300 000 tonnes/year worldwide
  5: tsetse fly pheromone 6: detergent
  7: plasticizer 8: precursor to chemicals
the top five producers being
- Vietnam (1.1 million tons)
Nigeria (0.95 million tons)
India (0.75 million tons)
Cote d’Ivoire (0.45 million tons%)
Brazil (0.11 million tons)
Avoiding competing with food: biomass waste
Notes: 36

## Slide 37
Orange peels: James Clark (York, UK)
  Global agriculture produces about 15.6 million tons of orange and other citrus waste annually in the form of discarded peels
    biofuels
    bio-based solvents
    Fragrances
    water purifiers
CHEM 462: 24.Chemicals from renewable feedstock
http://cleantechnica.com/2012/07/07/opec-uses-orange-peel-for-biofuel-and-other-biobased-products/
low temperature microwaves
+ cellulose
Avoiding competing with food: biomass waste
Notes: 37

## Slide 38: Why use renewable feedstocks?
Economic reasons:
  The inherent long-term tendency for petroleum price to increase.
  A fluctuation of a few cents in the price of crude oil can result in massive price swings for downstream products.
  The constant decrease in cost of renewable resources.
Scientific reasons:
  The constant improvement in quality of renewable feedstocks.
  Modern plant breeding.
  Genetic manipulation.
  Breakthroughs in catalysis (enzymes, etc.).
Environmental reasons:
  Biological compatibility (to an extent).
  The use of waste streams (wood pulping, agriculture, etc.).
  Mitigate CO2 emissions

## Slide 39: Some Potential Challenges of Using Renewable Feedstocks
Feedstock cultivation
  Competition with food supply
  Land demand
  Nutritional needs
  Diseases
  Initial investment
Harvesting method to maximise yields and minimise degradation of product
Post harvest processing
Product extraction and purification
Product standardization
Complexity
Product storage, packing, and distribution
New methodologies for alternative feedstocks

## Slide 40
What can we make from petroleum (focus on molecules)
The biorefinery
Renewable Feedstocks
  Triglycerides
  Lignocellulosic Feedstocks
  N containing polymers
  Latex polymer
  Small molecule feedstocks
Examples
  From lignin
  Vanillin
  Platform molecules
  Fatty acids
The Advantages and Drawbacks of bio-based molecules
Topics Covered

## Slide 41
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE