## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Designing for Reduced Hazard
Image: Wikimedia Commons, Fume Hood , Author: U.S. National Institute for Occupational Safety and Health
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
Dermal
Respiratory
Digestive
Skin is the first barrier to absorption for the chemical. The skin can keep chemicals out of the body, or it can let them in, depending on the physical and chemical properties of the chemical. Absorption of a chemical will result in the chemical circulating inside the body and perhaps causing adverse effects.
As chemicals are inhaled, they may reach the lungs. The lung surface is a poor barrier against the entry of many chemicals into the body, which means that absorption of chemicals into the lung can be rapid and efficient.
If chemicals are swallowed, either intentionally or unintentionally, they enter the gastrointestinal tract (GI). From there, they may either pass through the body or be absorbed into the body.
Absorption

## Slide 3
Understanding Physicochemical Properties Associated with Reduced Hazard
Chemical and Physical Properties
pKa chain branching log P molecular refractivity mol. wt. hydrolyzable groups
EHOMO ELUMO electronegativity hardness dipole log D7.4 # H-bond accept/donor
DESIGN

## Slide 4
Dermal
Respiratory
Digestive
Parameter | Preferred | Not Preferred
Physical state | solid | liquid
LogP | Less than 0 or greater than 5 | Between 0 and 5
Molecular weight | More than 400 Da | Less than 400 Da
Parameter | Preferred | Not Preferred
Particle size | More than 5 nm | Less than 5 nm
LogP | Less than 0 or greater than 5 | Between 0 and 5
Molecular weight | More than 400 Da | Less than 400 Da
Vapor pressure [mmHg] | Less than 0.001 | More than 0.001
Parameter | Preferred | Not Preferred
Particle size | More than 100 nm | Less than 100 nm
LogP | Less than 0 or greater than 5 | Between 0 and 5
Phase | solid | liquid
Molecular Weight [Da] | More than 500 Da | Less than 400 Da
LogP – measure of partition coefficient of a molecule between aqueous and lipophilic phases.
Property-Based Guidelines for Bioavailability
Notes: LogP – measure of partition coefficient of a molecule between aqueous and lipophilic phases.
Da – Dalton, unit of molar mass, g/mol

## Slide 5
Educational game based on ADME and scientific data for surfactants to make connection between physico-chemical properties and health.
http://gwiz.yale.edu
Safer Chemical Design Game
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor

## Slide 6: Approaches to Hazard Minimization through Molecular Design

## Slide 7
Bioavailability Structure/Shape Activity Mechanism of Action
Molecular
Weight
Solubility
Electronic
Charge
Volatility
Reactive
Functional
Groups
Bioaccumulation/
Persistence
Particle
size
Receptor
binding
Key events
Shape/
Molar Volume
Toxicokinetics
Toxicodynamics
Chemists can control quite well
Not well understood and relatively complex
That’s what we want to target
Green Chemistry Molecular Design Pyramid

## Slide 8
Elimination of the molecular initiating event that activates pathway
Changing reactive functional groups
Reducing or eliminating bioavailability
Reduction of need for associated hazardous substances
Design for End-of-Use product life
Approaches to Hazard Minimization Through Molecular Design

## Slide 9
Where the mechanistic pathway of action is known, molecular structures can be designed such that the necessary reactions are either impossible or highly disfavored resulting in significant toxicity reduction.
Elimination of the molecular initiating event that activates pathway

## Slide 10
In the absence of specific mechanistic information, chemists can modify structure such that certain reactive functional groups, e.g. cyano, electrophilic, etc, can be minimized or eliminated from the chemical structure where feasible.
B. Changing Reactive Functional Groups

## Slide 11
In order for a chemical to manifest its intrinsic hazard, it must be able to reach the toxicological target, human, animal, environmental or global. Through structural molecular design, properties such as solubility, log Kow, and volatility can adjusted to reduce hazard manifestation.
C. Reducing or Eliminating Bioavailability
Notes: The octanol/water partition coefficient (Kow) is defined as the ratio of a chemical's concentration in the octanol phase to its concentration in the aqueous phase of a two-phase octanol/water system

## Slide 12
Many chemical substances, if not hazardous themselves, require the use of other hazardous substances e.g. paints with VOCs, surfaces requiring specific cleaners, plastics with various additives.
Through molecular design, these associated substances can be eliminated by making the desired properties integral to the product
D. Reduction of Need for Associated Hazardous Substances

## Slide 13
Persistence of chemical in the environment is a problem that can be designed out of molecular structure.
By creating products that degrade to innocuous by-products under designed conditions, e.g., heat, light, time one can reduce or eliminate this hazard.
Design for utilization of waste as a feedstock is an important goal.
E. Design for End-of-Useful Product Life

## Slide 14: By Changing the Molecular Charge: Cephalosporins
Clinical nephrotoxicity was recognized early – damage to proximal tubular epithelia.
Mechanism: the drug is rapidly transported across basolateral membrane via the organic anion transporter, OAT1. Transport out of cell into lumen is less well characterized (involves other OAT, OAT4).
Cephalosporin has a very low affinity for OAT4 due to its zwitterionic character, resulting in considerable intracellular accumulation
Cephaloridine
Cephalothin
In contrast, cephalothin, an anionic analog of the original zwitterionic drug, rapidly moves across the epithelia from blood into urine
Is thus not a neurotoxin
Cephalosporins: Antibiotic molecules used for gram+ bacteria
Notes: Cephalosporins are a type of beta-lacatam antibiotic.
First generation:Cephaloridine

## Slide 15
Diquat
Paraquat
By Manipulating Sterics: Paraquat and Diquat
Diquats and Paraquats are herbicides (plant killer), primarily for weed and grass control
In animal studies, diquat causes mild, reversible injury
Paraquat is not metabolized by the liver. It has life-threatening effects on the gastrointestinal tract, kidney, liver, heart and other organs
Both: Toxic doses are life threatening. Impacts GI tract, kidney lungs, liver, heart, other organs
Registered as a restricted use pesticide
Not registered as a restricted use pesticide
http://npic.orst.edu/RMPP/rmpp_ch12.pdf
Notes: Paraquat is a non-selective contact herbicide of the diphenyl class. It was introduced in the 1960s and became used worldwide. However it was soon recognized that paraquat also cause selective pulmonary toxicity to humans (damage to alveolar cells type I and II, causing edema, inflammation and hermorrhage, lung fibrosis).
Steric effects are nonbonding interactions that influence the shape and reactivity of ions and molecules. Steric effects complement electronic effects, which usually dictate shape and reactivity. Steric effects result from repulsive forces between overlapping electron clouds.

## Slide 16
Acrylate is understood to be carcinogenic because it can readily undergo Michael addition reactions
The addition of a methyl group to form methacrylate decreases the electrophilicity of the b-carbon, and decreases tendency for Michael reactions.
While this does not reduce the commercial efficacy, but whereas acrylate causes cancer is experimental assays, methacrylate does not.
Acrylate
carcinogenic
Methacrylate
non-carcinogenic
By Manipulating Electrophilicity: Acrylates
Notes: Electr

## Slide 17
Benzene is known to cause hematotoxicity and leukemia in humans
This is understood to be due to one of its metabolites, (E,E)-muconaldehyde.
Toluene is comparatively much less toxic, as the methyl group is oxidized more easily than the benzene ring to give benzoic acid
By Facilitating Detoxification: Benzene
hematotoxicity,
leukemia
non-toxic
hepatic oxidation
[detoxification]

## Slide 18
DDT is well known to be environmentally persistent.
DDT analog with Silicon above was synthesized.
While less persistent, the analog turned out to be non-toxic to insects.
This is due to the more readily oxidized (metabolized) Si-H bond compared to C-H and also the larger size of the molecule.
DDT
(Toxic to insects)
Si-DDT Analog
(Non-toxic to insects)
By Isosteric Substitution: Carbon with Silicon

## Slide 19
Even if chemists design one chemical, it has to undergo tests
Designing New Molecules is Not a Trivial Task

## Slide 20
QSAR = classification models used in the chemical and biological sciences and engineering
QSAR-Quantitative Structure Activity Relationship
Wikipedia
potency of the response variable
"predictor" variables
QSAR
Structure, physico-chemical properties, chemical functionalities
Biological activity: toxicology and eco-toxicology
[like LC50 or oxidative stress]
Known data sets
QSAR established relationship
"predictor" variables
New molecules
QSAR uses the learnt rules to predict biology
QSAR
QSAR predicted potency of the response variable

## Slide 21
Not sufficient data on most chemicals
Not all chemicals can be tested
QSAR has been used successfully for over 60 years
Better to predict than have nothing
Why use QSAR?

## Slide 22
Prediction accuracy not higher than 65-70% for non-carcinogenic chemicals.
Lack of validation with up-to-date data.
Application to a narrow range of chemical structures.
Qualitative output.
Current limitations
Examples of Popular Toxicity Prediction Tools

## Slide 23
Next generation: powers of computational Chemistry
Docking software have been able to model very precisely the active site of a target enzyme (target to a drug for instance, or to a toxic).
In drug design such software are used to predict the best molecules for biological activity. Only the best performing are synthesized and tested.
Similar ideas can be used in toxicology
http://www.molfunction.com/software5.htm
Notes: Jakub’s slide

## Slide 24
Create a reliable tool for chemists which will not only predict the toxicity of existing chemicals but will allow a design of future molecules with reduced hazard
What’s the need?

## Slide 25
Toxicology
Chemistry
Molecular Biology
Computational Chemistry
Molecular Design Research Network
Notes: MoDRN is the collaboration between 4 universities Baylor, GW, UWASH and Yale that uses advances in biology, toxicology, computational chemistry and engineering to develop a robust and well validated computer software that will not only predict toxicity of existing compounds but it will serve as a tool to redefine guidelines for the next generation molecules with reduced hazard. The network will employ the newest strategies of computer modeling to build a computer software which will allow to understand what causes toxic endpoints and what can we do to avoid it. Our efforts will not only limit to research. To have the biggest possible impact we will engage educators and students on undergraduate and high school level to by including safer chemical design in students’ lesson plans and by developing interactive and hands-on teaching tools for undergraduate and high school students. Finally we plan to work with our colleagues across academia, colleagues across many industry sectors and policymakers on the government level to further inform and disseminate safe chemical concepts.

## Slide 26
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE