## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Catalysis
Image: Flickr, Catalysts, Author: BASF Catalysts
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
What is a Catalyst?
Catalytic Cycle
Types of Catalysts
Catalysts and Sustainability
Important Improvements Using Catalysts
Enzymatic Reactions
Examples and Considerations
Topics To Be Covered

## Slide 3
Catalysis
Catalytic reagents (as selective as possible) are superior to stoichiometric reagents.
Source: Wikipedia

## Slide 4
What is catalyst?
The catalyst is not a reagent or a product as it is not consumed: it’s noted above the equation arrow
The catalyst participates in the kinetic equations but not in the equilibrium constant
A catalyst is a substance that increases the rate at which a chemical reaction approaches equilibrium, but is not consumed in the process.
A + Cat → ACat (1)
B + ACat → ABCat (2)
ABCat → CatP (3)
CatP → Cat + P (4)
A + B → P
A + B → P
Cat
Overall reaction

## Slide 5
Nobel Prizes for catalysis
Ostwald, 1909, Catalysis (Ostwald Process)
Sabatier (together with Grignard), 1912, Heterogeneous Catalytic Hydrogenation
Haber, 1918, Ammonia Synthesis
Harden-Euler-Chelpin, 1929, Fermentation of Sugar by Enzymes
Bergius, Bosch, 1931, Catalytic High Pressure Chemistry
Ziegler, Natta, 1963, Alkene Polymerization
Fischer, Wilkinson, 1973, Organometallic Sandwich Complexes
Noyori, Sharpless and Knowles, 2001, Enantioselective Catalysis
Chauvin, Grubbs, Schrock, 2005, Metathesis
Ertl, 2007, Heterogeneous Catalysis
Suzuki, Heck, Negishi, 2010, Coupling reactions
Arnold, 2018, directed evolution (-> biocatalysis)

## Slide 6
The catalytic cycle
Catalysis can be viewed as a cyclic event: A catalytic cycle is defined as the succession of chemical changes undergone by the catalyst until it recovers its initial state.
I. Chorkendorff, J. W. Niemantsverdriet, Concepts of Modern Catalysis and Kinetics, Wiley-VCH, 2003
The catalyst remains reusable at the end of the process to go for a new cycle
If at any point the cycle breaks, catalysis stops!
A stoichiometric reaction can be view as a catalytic reaction going through 1 cycle

## Slide 7
Any reaction needs some energy to happen: the activation energy: Ea
When using a catalyst, an alternative path is created for a reaction, more complex, but energetically much more favorable.
Smaller activation energy for catalytic reaction => larger reaction rate
Catalysis = kinetic phenomenon
Catalysis can be viewed as a cyclic event: A catalytic cycle is defined as the succession of chemical changes undergone by the catalyst until it recovers its initial state.
I. Chorkendorff, J. W. Niemantsverdriet, Concepts of Modern Catalysis and Kinetics, Wiley-VCH, 2003
Ea < Ea
Reaction rate > reaction rate
Ea
Ea

## Slide 8
Examples of catalysts
Many molecules/enzymes/materials can be catalysts:
Catalysis, Concepts and green applications, by Gadi Rothenberg, Wiley-VCH 2008.
copper-zinc crystallites on silica
zeolite (crystalline aluminosilicate)
enzyme (biocatalyst)

## Slide 9
Catalyst | Reactions catalyzed
Iron oxide | Ammonia from nitrogen and hydrogen
Chromium-Molybdenum Alloy Nickel-Molybdenum Alloy Zeolite (Porous Aluminum and Silica Oxide) | Petroleum Industry
Acid (HCl, H2SO4, HNO3) | Many organic reactions
Enzymes | Starch into sugars and sugars to ethanol
Catalysts are widely used by industry and by nature

## Slide 10
Haber Bosch Process
The Haber-Bosch process, which allows fertilizer production, is facilitated by a catalyst.
The invention of the process led to a global increase in human population.
Consumes 1% of the total human energy use on the planet
Source: Wikipedia
Fritz Haber
(1868-1934)
Nobel Prize 1918
Carl Bosch
(1874-1940)
Nobel Prize 1931
The Haber-Bosch process accounts for ~ 40 % of the overall N2 fixation on earth and the only source of NH3 for the subsequent synthesis of all nitrogen containing man-made materials

## Slide 11
A kinetic process
At room temperature the reaction is thermodynamically driven:
G= –16.4 kJ mol–1; H°=–45.9 kJ mol–1
But: very high Ea:
heating required!
Chorkendorff & Niemantsverdriet, Concepts of Modern Catalysis and Kinetics, Wiley-VCH (2003)
NH3
N2 + H2
At 800 K
thermo: no
kinetics: no
At 298 K
thermo: yes
kinetics: no
At 700 K
thermo: no
But “Le Chatelier” can push with high pressure
kinetics: yes – catalyst!
“Le Chatelier” allows us to shift an equilibrium to the side that we would like to favor.
Kinetics= the rate of reaction and how fast equilibrium is reached
Thermodynamics= whether reaction is favorable (lower free energy)
Lower free energy
(more stable)

## Slide 12
Terminology: Types of Catalysts
 | Homogeneous | Heterogeneous | Biocatalysis
Form | Soluble metal complexes, usually mononuclear | Metals, usually supported, or metal oxides | Enzymes (polypeptides), many with a metal based active site
Active site | Well-defined, discrete molecules | Poorly defined | Well defined
Temperature | Low (<250oC) | High (250 – 500°C) | 25°C mostly Up to 100°C
Selectivity | High | Low | High
Product separation | Generally problematic on large scale | Easy | From yeasts or bacteria. Amenable to large scale
Green? | Less Green | More Green Separation, Recycle/Regeneration | Very green

## Slide 13
Criteria to design a Green Catalyst?
 | Homogeneous | Heterogeneous | Biocatalysis
Form | Soluble metal complexes, usually mononuclear | Metals, usually supported, or metal oxides | Enzymes (polypeptides), many with a metal based active site
Active site | Well-defined, discrete molecules | Poorly defined | Well defined
Temperature | Low (<250oC) | High (250 – 500°C) | 25°C mostly Up to 100°C
Selectivity | High | Low | High
Product separation | Generally problematic on large scale | Easy | From yeasts or bacteria. Amenable to large scale
Green? | Less Green | More Green Separation, Recycle/Regeneration | Very green
An ideal green catalyst would have a preferred parameters from each type.
Notes: After click text turns green – what are the criteria to design a green catalyst?

## Slide 14
Homogeneous catalysis
Biocatalysis
metal crystallite
oxide support
Heterogeneous catalysis
Catalysis, Concepts and green applications, by Gadi Rothenberg, Wiley-VCH 2008. - http://bio1151.nicerweb.com/Locked/media/ch08/catalytic.html
Terminology: Types of Catalysts
Still, all types of catalysts relies on the same principle and go through a catalytic cycle.

## Slide 15
Catalysts are not eternal! The important question is how many cycles can they achieve on average and how fast
Terminology
  Turn over number (TON) = total number of cycles
  Turn over frequency (TOF) = number of cycles/time
  TOF = TON / time
Catalysts evaluation: TON, TOF, selectivity
 | Inorganic Catalyzed Reaction | Enzymatic Reactions
TOF | 0.01 – 10000 s-1 (Very slow) | 100 up to 40 million s-1 (Extremely fast)
Selectivity | Medium to good selectivity | Excellent selectivity

## Slide 16
Biocatalysis relies on the use of yeast and bacteria to perform chemistry
Fast growing market in many sectors
Homogeneous catalysis
Biocatalysis
Heterogeneous catalysis
Catalysis, Concepts and green applications, by Gadi Rothenberg, Wiley-VCH 2008 - K. H. Shaughnessy, Chem. Rev. 2009, 109, 643-710. Source: Novozyme
Catalysis in Industry
Over 90 vol% of the chemicals worldwide are manufactured with the aid of solid catalysts
800 000 tons of solid catalysts are prepared each year
Heterogeneous catalysts allow continuous processes or flow reactors
Recovery is a real challenge
For processes for which heterogeneous is not good
DKK 12.46 billion = $1.94 billion

## Slide 17
Catalysis Drives the Chemical Industry
Source: Wikipedia
Pharmaceuticals
Fine chemicals
Consumer Products
Catalytic processes contribute to more than 35% of global GDP.
Petroleum

## Slide 18: Important Heterogeneous Catalytic Processes
Haber-Bosch process:
  N2 + 3 H2 → 2 NH3
  Fe/Ru catalysts, high pressure and temperature.
  Critical for fertilizer & nitric acid production.
Fischer-Tropsch chemistry:
  n CO + 2n H2 → (CH2)n + n H2O , syn gas to liquid fuels.
  Fe/Co catalysts.
  Source of fuel for Axis in WWII.
.
Automotive three-way catalysis:
  NOx/CO/HC → N2/CO2/H2O
  Pt/Rh/Pd supported on ceria/alumina.
  Makes exhaust 99% cleaner.
set of chemical reactions that changes a mixture of carbon monoxide gas and hydrogen gas into liquid hydrocarbons (like gasoline or kerosene)

## Slide 19: Designing a Green Catalyst
http://www.rsc.org/chemistryworld/Issues/2011/January/CriticalThinking.asp
Not all catalysts are created equal. Chemists need to consider various factors when deciding on a catalyst.
Many metals which are used as catalysts are quickly depleting.
Is the catalyst non-toxic?
Is it actually used in sub-stoichiometric amounts?
Does it require special conditions (sensitivity to solvent, moisture, oxygen)?
Is it derived from abundant/renewable resources?
Can it be reused?
Can it be separated from the products?
Might it lead to dangerous conditions (Runaway/chain reactions)?

## Slide 20: Metal scarcity
Source: Wikipedia

## Slide 21: Use a lifecycle as a guide
Material Extraction
  Abundance?
Processing/Manufacturing
  Energy?
  Waste?
  Toxicity of materials?
Use
  Selectivity?
  Turnover number?
  Safety?
End-of-life
  Reusability?
  Ease of separation?
Source: Wikipedia

## Slide 22: The Need to Develop More Sustainable Catalysts
European Commission Press Release, June 2010
Raw materials (e.g. rare precious metals) are dispersed around the world and access to them is frequently political.
To gain economic and environmental independence, we must design catalysts which are locally sourced and abundant.

## Slide 23: Current Trends in Catalyst Design
Reduce Loading
High Surface Area Support
Atomic Layer deposition
Earth Abundant Alternatives
Abundant metal
Alloy - Synergistic Effect
Adjust other parameters
  - Solvents
  - Surfactants

## Slide 24: Increased Surface Area
High surface area porous support:
<50 cm2 g-1
50 – 4000 cm2 g-1

## Slide 25: Example: The Haber-Bosch Process
Originally Fritz Haber discovered this reaction using an osmium (Os) based catalyst
  Os metal is rare, toxic and too expensive: it could not be made industrial.
Rapidly alternatives with either iron (Fe) or ruthenium (Ru) were developed
Today’s catalysts: finely divided Ru on a solid support of Fe3O4/Fe2O3/Al2O3/K2O/CaO
Improving the Haber-Bosch process by using an iron catalyst:
Notes: Beware: Osmiun has never been a “traditional” catalysts for HB. It was the first catalyst discovered by F. Haber, but it was only commercialized with Ru or Fe based calasysts. I corrected it. AHM

## Slide 26: Example: Cross coupling reaction
Cross Coupling Reactions:
   Connecting two separate organic molecules together with high selectivity and high yield.
 | USD mol-1
Ni | $1.20
Pd | $1,500
New chemistry innovations allowed the replacement of expensive palladium catalysts with nickel.
These reactions were awarded Nobel Prizes.
Notes: Pd is used catalytically, in small amount, to carry out the reaction. In some cases, Pd needs NOT to be purified

## Slide 27: Eliminate More Reactions: Minimizing functionalization-defunctionalization A Simple Dream
Ideally:

## Slide 29
All are possible!

## Slide 30
The Ultimate CDC Reaction
Non-oxidative conversion of methane to benzene
(McGill Patent Applied, 2013) Li, L.; Fan, S.; Mu, X.; Mi, Z.; Li, C.-J.
J. Am. Chem. Soc. 2014, 136, 7793 (highlighted in Chem. & Eng. News, June 9, 2014)
Angew. Chem. Int. Ed. 2014
Notes: Natural gas is a mixture of small alkanes, such as methane and ethane. It is very plenty on earth and exists in different forms. Shale gas is one source of natural gas which is trapped within shale formations. Over the past decade, shale gas is increasing rapidly and becomes an important clean fuel. At the end of 2012, the price of shale gas is only half of oil in USA.
Obviously, if we can use shale gas instead of the oil as a new carbon source, the future chemical industry will be largely changed. Our recent work is focusing on the production of aromatic compounds directly from shale gas, which is one of the seven basic building blocks in chemical industry

## Slide 31: Example: replacing palladium by iron in hydrogenation
Hydrogenation:
  Usually with expensive, rare metals: Pd, Rh, Ru, Pt
  or toxic, Ni
  iron (Fe) is abundant and non toxic
synthesized
in EtOH
synthesized
in EtOH and water (99:1)
synthesized
in EtOH and water (1:1)
industrial
in EtOH
The iron oxide shell protects Fe(0) from oxidation with water, while allowing interesting reactivity
R. Hudson, A. Rivière, C. M. Cirtiu, K. L. Luska, A. Moores, Chem.Comm. 2012, 48, 3360-3362.
Notes: Pd is used catalytically, in small amount, to carry out the reaction. In some cases, Pd needs NOT to be purified

## Slide 32: Automotive Emissions Control System
“Three-way” Catalyst
CO  CO2
HC  CO2 + H2O
NOx  N2
Pt, Rh, Pd Alumina, ceria, lanthana, etc.
Most widely deployed heterogeneous catalyst in the world.
You probably own one!
Monolith reactor
Notes: HYDROCARBONS

## Slide 33: Enzymatic Reactions
Enzymatically driven reactions that occur in nature are often highly specific and compartmentalized.
Many of these reactions occur in ambient temperature and pressure with a water solvent.
Today, over 5000 of enzymatic reactions types have been identified, and that number continues to grow.
Image: Wikimedia Commons, Penicillium notatum, Author: Crulina 98

## Slide 34: Enzymatic Reactions
Enzymes are biological catalysts and are used in industry, agriculture, and by nature.

## Slide 35: Enzymatic Reactions
This is a general representation of enzymatic reactions – the lock and key mechanism.
The substrate (reactant) binds with the enzyme and forms the Enzyme-substrate complex and is transformed into products A and B, which are released from the active site upon reaction completion.

## Slide 36: Examples on Enzymatic Catalysis
Conventional manufacturing of 6-aminopenicillanic acid (6-APA) - a key raw material for semi-synthetic penicillin and cephalosporin involved the use of environmentally unattractive reagents – requires a chlorinated hydrocarbon solvent and a reaction temperature of –40°C.
In contrast, enzymatic cleavage of penicillin G is performed in water at 37°C and the only reagent used is to adjust the pH.
The enzymatic process currently accounts for the majority of the several thousand tons of 6-APA produced annually on a world-wide basis.
Notes: An illustrative example of the benefits to be gained by replacing conventional chemistry by biocatalysis is provided by the manufacture of 6-aminopenicillanic
acid (6-APA), a key raw material for semi-synthetic penicillin and cephalosporin antibiotics, by hydrolysis of penicillin G [115]. Up until the mid-1980s a chemical
procedure was used for this hydrolysis (Fig. 1.37). It involved the use of environmentally unattractive reagents, a chlorinated hydrocarbon solvent (CH2Cl2)
and a reaction temperature of –40C. Thus, 0.6 kg Me3SiCl, 1.2 kg PCl5, 1.6 kg PhNMe2, 0.2 kg NH3, 8.41 kg of n-BuOH and 8.41 kg of CH2Cl2 were required
to produce 1 kg of 6-APA [116].
In contrast, enzymatic cleavage of penicillin G (Fig. 1.37) is performed in water at 37C and the only reagent used is NH3 (0.9 kg per kg of 6-APA), to adjust
the pH. The enzymatic process currently accounts for the majority of the several thousand tons of 6-APA produced annually on a world-wide basis.
30 1 Introduction: Green Chemistry and Catalysis Fig. 1.37

## Slide 37: Case Study
Sitagliptin, the active ingredient in Merck's Januvia.
Sitagliptin is Merck's top-selling diabetes drug.
It brought $1.9 billion in sales in 2009.
Traditional synthesis used high pressure and a heavy metal – rhodium.
The new improved synthesis with enzymes allows for 99.95% selectivity to the desired product and eliminates all heavy metal wastes.
http://www.rsc.org/chemistryworld/News/2010/June/17061002.asp (Accessed on 4/1/2016)
Savile, C. K.; Janey, J. M.; Mundorff, E. C.; Moore, J. C.; Tam, S.; Jarvis, W. R.; Colbeck, J. C.; Krebber, A.; Fleitz, F. J.; Brands, J.; Devine, P. N.; Huisman, G. W.; Hughes, G. J., Biocatalytic Asymmetric Synthesis of Chiral Amines from Ketones Applied to Sitagliptin Manufacture. Science 2010, 329 (5989), 305-309.
Sitagliptin – Rhodium to Enzyme
Notes: http://www.rsc.org/chemistryworld/News/2010/June/17061002.asp

## Slide 38: Enzymatic catalysis for energy
Bacteria have been used to turn CO2 into methane
http://www.electrochaea.com/about/ - Video: http://www.electrochaea.com/technology/
Notes: http://www.rsc.org/chemistryworld/News/2010/June/17061002.asp

## Slide 39: Enzymatic catalysis for plastic degradation
With specific mutations a PETase properties were improved to degrade plastics. Bacterium in question: Ideonella sakaiensis 201-F6
Austin, H. P.; Allen, M. D.; Donohoe, B. S.; Rorrer, N. A.; Kearns, F. L.; Silveira, R. L.; Pollard, B. C.; Dominick, G.; Duman, R.; El Omari, K.; et al. Proc. Natl. Acad. Sci. U. S. A. 2018, 115 (19), E4350–E4357.
PET films
A. No enzyme B. wild-type PETase C. mutant type PETase
Notes: http://www.rsc.org/chemistryworld/News/2010/June/17061002.asp

## Slide 40: The Pros and Cons of Enzymatic Reactions
  Separations are often complicated.
  They can be expensive to produce.
  Some people might experience allergic reactions to some enzymes.
Pros:
  Mild conditions.
  Aqueous environment.
  Atmospheric conditions.
  A very specific and high reaction rate.
Cons:

## Slide 41
What is a Catalyst?
Catalytic Cycle
Types of Catalysts
Catalysts and Sustainability
Important Improvements Using Catalysts
Enzymatic Reactions
Examples and Considerations
Topics Covered

## Slide 42
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE