## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Solvents
Image: Flikr, Solvents used during the Tamper Evident Seals Workshop, Author: Dennis van Zuijlekom
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
Safer Solvents and Auxiliaries
The use of auxiliary substances (solvents, separation agents, etc.) should be made unnecessary whenever possible and, when used, innocuous.
Image: thoughtco.com, Author: unknown

## Slide 3
The problems with solvents
Minimizing solvent use
Selecting greener conventional solvents
Using unconventional solvents
Topics To Be Covered

## Slide 4: What is a solvent?
A solvent is any substance that dissolves another substance(s) so that the resulting mixture is a homogenous solution.
Also conveys energy:
endothermic: brings energy to molecules
exothermic: heat sink

## Slide 5: When are solvents used?
During manufacturing:
  - To facilitate intermolecular chemical reactions via solute molecules & ions.
During processing:
  - To aid in manipulation of chemicals, but not as an integral part of the molecule itself.
During extraction/separation:
  - To separate or purify the chemical products from co-products, byproducts and impurities.
During cleaning:
  - To remove oil, grease and silica from mechanical parts.
During product formulation:
  - To design a product and process (quantities, raw materials, mixture design and testing)
Solvents are used in all stages of a product’s life-cycle:

## Slide 6: Solvent Usage by Sector
Source: Int. J. Mol. Sci. 2015, 16(8), 17101-17159; doi:10.3390/ijms160817101

## Slide 7: Waste in a “Typical” Pharmaceutical Synthesis

## Slide 8: Life Cycle Analysis of a Pharmaceutical
Basis: 1 kg of active pharmaceutical ingredient (API).
Process studied has 7 stages.
26 API materials are directly used in the process.
These 26 API materials are made from 125 commercially available raw materials.
LCA includes:
  Process:
    Materials
    Energy
    Transportation
  Treatment:
    Wastewater treatment
    Incineration
    Landfill

## Slide 9: Key Findings of the Life Cycle Analysis (LCA) of a Pharmaceutical
Solvent use (excluding incineration) is a major contributor to:
  Energy (ca. 75%)
  Resource utilization (about 80%)
  Photochemical ozone creation potential (ca. 70%)
  Greenhouse gases (about 50%)
Solvent-related energy use alone contributes to:
  30% of the materials
  70% of resource depletion
  90% of the greenhouse gas emissions
Notes: Photochemical Ozone Creation Potential measures the production of ozone from a VOC emission through computer modelling of a complex series of chemical reactions in the atmosphere.

## Slide 10: Conventional Solvents
Volatile Organic Compounds
  Chloroform, carbon tetrachloride, methylene chloride, perchloroethylene (PERC)
  Benzene, Toluene, Xylene (BTX)
  Acetone, Ethylene Glycol, methylethyl ketone (MEK)
Notes: VOCs have been linked to atmospheric ozone generation, commonly known as smog.
PERC is used in dry cleaning.
CFCs deplete an ozone layer which results in severe environmental effects

## Slide 11: What are the concerns for solvents?
Inherent Toxicity
  Methylene chloride, chloroform, carbon tetra chloride and other halogenated solvents are suspected human carcinogens.
Flammability
  Because of their physicochemical properties (low flash point and autoignition temperatures), solvents are flammable.
Explosivity
  They can explode, and since they are used in large volumes, the explosion can be disastrous.
Stratospheric Ozone Depletion
  They reduce the ozone layer which protects the earth from the radiation.
Global Warming Potential
Notes: In a typical chemical reactions, solvent accounts the majority of the reaction weight and therefore, post-processing solvent removal, which is typically achieved through distillation or vacuum evaporation (Video: solvent distillation) , is a very energy costly procedure for large scale synthesis. Moreover, products that are sensitive to impurities may requires extra cycles of distillations. This contributes to another (expensive) problem to deal with waste. Careless disposal of solvents are also known to pose great threat to the environment since many of which are toxic even at low concentration. To make matters worse, most organic solvents are volatile, possibly explosive and moderately toxic upon exposure, these qualities pose great concerns to any individuals who are involved in handling solvent.

## Slide 12: What are the concerns for solvents?
Transportation emissions in the United States and Europe have declined rapidly
The use of volatile chemical products (VCPs)—including pesticides, coatings, printing inks, adhesives, cleaning agents, and personal care products—now constitutes half of fossil fuel VOC emissions in industrialized cities.
McDonald et al., Science 2018 359, 760–764
Total VOC emission factors for end uses of petrochemical sources considered in his study, including from mobile sources and volatile chemical products.

## Slide 13: Minimizing solvent use
Murphy’s Law of Solvents
“The best solvent for any process step is bad for the subsequent step.”
polar
aprotic
nonpolar
aprotic
polar
aprotic
polar
protic
1st step
2nd step
3rd step
4th step

## Slide 14: Minimizing solvent use: Compromise Solvents
• 4 solvents for 3 steps
• 60,000 gallons per y
• 1 solvent for 3 steps
• 6,000 gallons per y
• saved 45% of starting material

## Slide 15: Minimizing solvent use: Switchable Solvents
Nature (2005) 436, 1102
Ind Eng Chem Res (2008) 47, 539
CO2
N2 or Ar
low polarity solvent
high polarity solvent

## Slide 16: Minimizing solvent use: Switchable Solvents
1.0 mL styrene 4.5 mL DBU/PrOH
45 mg initiator
75 ˚C
6 h
CO2
filter or centrifuge
+
Mn = 412,000
PDI = 1.57
N2
Nature (2005) 436, 1102
Ind Eng Chem Res (2008) 47, 539

## Slide 17: Minimizing Solvent Use: Don’t add a solvent
Two options:
Advantages:
  Solvent concerns eliminated.
  Solvent costs eliminated.
  Lots of research on this field: it works!
Disadvantages:
  Exothermic reactions can be dangerous on large scale
  High viscosity (option 1) or no mass transfer at all (option 2)
  need close collaboration with chemical engineers to overcome above problems.
  Efficient mixing can be a problem, particularly for solventless conditions.
  Solvents still often required for extraction, separation and purification of products.
Reactions between solids… can be done by mechanochemistry
Use a liquid reagent as the solvent
Solventless (no liquid at all)

## Slide 18
The problems with solvents
Minimizing solvent use
Selecting greener conventional solvents
Using unconventional solvents
Topics To Be Covered

## Slide 19: What is a greener solvent?
What is a green solvent?
solvent #1
solvent #2
solvent #3
A green solvent is the solvent that makes a product or process have the least environmental impact over its entire life cycle.

## Slide 20
How is DMF made?
How is hexane made?
oil
hexane
distillation
Environmental impact during solvent manufacture
Environmental impact during solvent use
Solvent performance during use
Environmental impact after solvent use

## Slide 21
Chart: MJ/kg
| Ethanol | Hexane | Acetone | Toluene | DMF | EtOAc | THF
MJ/kg | 50.1 | 64.4 | 74.6 | 80 | 91.1 | 95.6 | 270.8
Capello et al., Green Chem (2007) 9, 927
Environmental impact during solvent manufacture
Environmental impact during solvent use
Solvent performance during use
Environmental impact after solvent use

## Slide 22
Environmental impact during solvent manufacture
Environmental impact during solvent use
Solvent performance during use
Environmental impact after solvent use
data from: Isoni, Green Chem. (2016) 18, 6564
Chart: 
| Heptane | Toluene | Ethyl acetate | THF | ethanol | bio-ethanol | NMP
Global warming | 0.71429 | 1 | 0.93168 | 3.3416 | 1.2919 | 3.0559 | 2.9814
Acidification | 0.83721 | 1 | 0.4186 | 3.7674 | 0.97674 | 10.4651 | 3.7674
Eutrophication | 3.6 | 1 | 5 | 3.4 | 1.2 | 10.2 | 4.2
Human toxicity | 0.5 | 1 | 1.25 | 15.75 | 1.25 | 5.75 | 9.75
Impact per kg (relative to 1 kg of toluene)

## Slide 23: GSK solvent selection guide ranking
Solvent selection guide in practice. Each solvent is ranked from 1-10 and color-coded for convenience (1 being the worst, 10 being the best, across 6 different categories.
http://solventguide.gsk.com/
Environmental impact during solvent manufacture
Environmental impact during solvent use
Solvent performance during use
Environmental impact after solvent use

## Slide 24
Notes: Another view of the solvent selection guide: Green and yellow indicate a preferred solvent. Red suggests major heath or environmental issues.

## Slide 25
For green-ness
boiling point / energy to distill
flash point
cumulative energy demand
life cycle analysis
For utility
π* polarity/polarizability
β basicity / hydrogen-bond accepting ability
α acidity / hydrogen-bond donating ability
viscosity
α, β, and π* are Kamlet-Taft solvent parameters
Environmental impact during solvent manufacture
Environmental impact during solvent use
Solvent performance during use
Environmental impact after solvent use

## Slide 26
Chart: π*
| 0 | 0.27 | 0.55000000000000004 | 0.57999999999999996 | 0.55000000000000004 | 0.88 | 0.88 | 0.92 | 0.16 | 0.14000000000000001 | 1 | 0.72 | 1.01 | 0.9 | 0.87 | 0.53 | 0.43 | 0.73 | 0.83 | 0.98 | 0.87 | 0.71 | 0.67 | 0.75 | 0.85 | 0.82 | 0.57999999999999996 | 0.27 | 0.53 | 0.87 | 0.74 | 0.6 | 0.62 | 0.47 | 0.61 | 0.83 | 0.49 | 0.84 | 0.8 | 0.92 | 0.59 | 0.71 | 0.79 | 0.28000000000000003 | 0.53 | 0.81 | 0.28000000000000003
aprotic | 0 | 0.47 | 0.37 | 0.55 | 0.45 | 0.76 | 0.69 | 0.77 | 0.62 | 0.71 | 0.76 | 0.77 | 0.39 | 0.41 | 0.64 | 0.11 | 0.12 | 0.32 | 0.4 | 0.39 | 1.05 | 0.48 | 0.48 | 0.31 | 0.06 | 0 | 0 | 0.46 | 0.41 | 0.49 | 0.41 | 0.42 | 0.37 | 0.42 | 0.25 | 0.8 | 0.57 | 0.64 | 0.67 | 0.64 | 0.1 | 0.07 | 0.06 | 0 | 0 | 0 | 0
protic
High polarity
Low polarity
High basicity
Low basicity
cyclohexane, hexane, heptane
Et2O
dioxane
THF
EtOAc
DMA
DMF
NMP
NEt3
DMSO
OP(OEt)3
PhNO2
PhCN
pyridine
toluene
p-xylene
anisole
propylene
carbonate
sulfolane
HMPA
acetone
MeCN
MeNO2
CH2Cl2
CHCl3
NBu3
MEK
CCl4 &
Cl2C=CCl2
Cl2C=CClH
PhCl
PhBr
EtO2CEt
BzNMe2
EtO2CCl3
butyrolactone
Me2py
4-Mepy
ClC2H4Cl
benzene
quinoline
tetramethyl-urea
MeO2CH
MeOAc
EtO2CPh
MeOC2H4OMe
Pr2O
Jessop, Green Chem (2012) 14, 1245
The aprotic solvents
(α < 0.5)
Environmental impact during solvent manufacture
Environmental impact during solvent use
Solvent performance during use
Environmental impact after solvent use

## Slide 27
Jessop, Green Chem (2012) 14, 1245
The aprotic solvents
(α < 0.5)
Chart: π*
| 0.55000000000000004 | 0.83 | 0.71 | 0.67 | 0 | 0.5 | 0.45 | 0.93 | 0.65 | 0.432 | 0.17699999999999999 | 0.83 | 0.55000000000000004
 | 0.45 | 0.4 | 0.48 | 0.48 | 0 | 0.4 | 0.4 | 0.72 | 0.61 | 0.6 | 0.56

High polarity
Low polarity
High basicity
Low basicity
heptane
EtOAc
propylene
carbonate
acetone
MEK
(EtO)2CO
iPrOAc
PEG
PPG
γ-valerolactone
2-MeTHF
Environmental impact during solvent manufacture
Environmental impact during solvent use
Solvent performance during use
Environmental impact after solvent use

## Slide 28
Chart: π*
| 0.98 | 0.41 | 0.97 | 0.48 | 0.5 | 0.4 | 0.52 | 0.47 | 0.4 | 0.54 | 0.92 | 0.64 | 1.0900000000000001 | 1 | 0.52 | 0.73 | 0.72 | 0.6 | 0.65
 | 0.52 | 1.01 | 0.48 | 0.95 | 0 | 0.81 | 0.9 | 0.88 | 0.84 | 0.77 | 0.52 | 0.45 | 0.18 | 0.51 | 0.45 | 0 | 0.3 | 0.62 | 0
High basicity
Low basicity
PhCH2OH
tBuOH
formamide
iPrOH
octanol
butanol
hexanol
ethanol
ethylene glycol
acetic acid
water
glycerol
hexanoic acid
CF3CH2OH
phenol
methanol
(CF3)2CHOH
High polarity
Low polarity
1-propanol
CF3CO2H
glycerol
Jessop, Green Chem (2012) 14, 1245
The protic solvents
(α > 0.5)
Environmental impact during solvent manufacture
Environmental impact during solvent use
Solvent performance during use
Environmental impact after solvent use

## Slide 29
Jessop, Green Chem (2012) 14, 1245
The protic solvents
(α > 0.5)
Chart: π*
| 0.41 | 0.48 | 0.52 | 0.47 | 0.54 | 1.0900000000000001 | 1 | 0.6 | 0.98 | 0.7 | 0.33 | 0.82 | 0.86 | 0.73 | 0.37 | 0.28999999999999998 | 0.34 | 0.35 | 0.44 | 0.37
 | 1.01 | 0.95 | 0.9 | 0.88 | 0.77 | 0.18 | 0.51 | 0.62 | 0.52 | 0.48 | 0.45

High basicity
Low basicity
tBuOH
iPrOH
butanol
ethanol
ethyl lactate
water
glycerol
methanol
High polarity
Low polarity
1-propanol
Environmental impact during solvent manufacture
Environmental impact during solvent use
Solvent performance during use
Environmental impact after solvent use

## Slide 30
Environmental impact during solvent manufacture
Environmental impact during solvent use
Solvent performance during use
Environmental impact after solvent use
Contained system
Direct to sewage
Direct to environment
Water is probably NOT a green solvent
Water probably IS a green solvent
Water probably IS a green solvent

## Slide 31: Which solvent is greener?
DIfferent types of comparisons
• solvent impact during use
• solvent impact during manufacture and use
• LCA of the entire process
solvent #1
solvent #2
solvent #3
A green solvent is the solvent that makes a product or process have the least environmental impact over its entire life cycle.

## Slide 32
CATEGORY | RATING (RED-YELLOW-GREEN)
Incineration | 
Recycle | 
Biotreatability | 
VOC emmision | 
Environmental impact to water | 
Environmental impact to air | 
Health hazard | 
Exposure hazard | 
Safety hazard | 
Solvent Exercise: Solvent Ratings in 9 Criteria
Give ratings (Green Yellow or Red) in the 9 provided categories based on solvent physicochemical properties.
Notes: Goal: To give the participants an understanding of how the physicochemical and hazardous properties of solvents effect safety and environmental impact.
This activity uses published solvent selection guides generated by a major pharmaceutical company, which uses them to evaluate solvents used in their large-scale process chemistry. The company has rated each solvent according to nine criteria on a “red-yellow-green”/traffic light scale, based on the physicochemical and hazardous properties.

## Slide 33: Solvent Exercise
Molecular weight | 60.05
Boiling point [C] | 118 C
Melting point [C] | 17C
Flash Point [C] | 39C
Auto Ignition Temperature [C] | 426C
Solubility [g/L] | miscable
Vapor Pressure [mm] | 15.5 mm
Percent Volatile | 100
Exposure Limits [ACGIH: TWA] | 10 ppm
Evaporation Rate | 0.97 BuAc
Toxicological data Oral Rat LD50: Skin Rabbit LD50: Inhalation Rat LC50: | 3.31 g/kg 1060 mg/kg 11.4 mg/L 4H
Ecotoxicology data EC50 Water flea (Daphnia magna): LC50 Bluegill (Lepomis macrochirus): | 65 mg/L 48 H 75 mg/L 96 H
Ozone creation potential | 16
Heat of combustion [Btu/lb] | 5645 Btu/lb
Persistence and Degradability: | biodegradable
Azeotropes | Multiple present
Molecular weight | 82.4
Boiling point [C] | 81 C
Melting point [C] | 7 C
Flash Point [C] | -20 C
Auto Ignition Temperature [C] | 245
Solubility [g/L] | 0.06 g/L
Vapor Pressure [mm] | 98 mm
Percent Volatile | 100
Exposure Limits [ACGIH: TWA] | 300 ppm
Evaporation Rate | not known
Toxicological data Oral Rat LD50: | 12.705 g/kg
Ecotoxicology data EC50 algae | 3.8 mg/L
Ozone creation potential | 60
Heat of combustion [Btu/lb] | 18684 Btu/lb
Persistence and Degradability: | Slow biodegradation
Azeotropes | Some present
SOLVENT 1
SOLVENT 2
Notes: Participants should be divided into groups of 4-5 and provided with the solvent cards for acetic acid and cyclohexene, without the names of the solvents and the “red-yellow-green” ratings left blank.
The solvent card would contain categories like:
1. Incineration
2. Recycle
3. VOC emmision
4. Environmental impact to water
5. Environmental impact to air
6. Health hazard
7. Exposure hazard
8. Safety hazard
The groups should be given approximately 20 minutes to discuss the chemical data provided on the cards and provide their own ratings in each of the eight categories. The solvent identities are left blank to avoid biasing the evaluation.
The debriefing will also take approximately 20 minutes. The groups will be asked to report which criteria received a green light and which criteria received a red light and the results will then be tabulated. Then the solvent identities and actual red-yellow-green ratings from the pharmaceutical industry scientists should be revealed. This is likely to result in some “what were they thinking?” comments from the participants.

## Slide 34
Vapor Pressure (mm) - an indication of a liquid's evaporation rate; High vapor pressure = volatile
Solubility in Water (gm/L) – an indication if the solvent can be easily separated
Odor Threshold (ppm) - the lowest concentration of a certain odor compound that is perceivable by the human sense of smell; Strong odors = lower value
Log Kow - octanol/water partition coefficient (Kow) - ratio of a chemical's concentration in the octanol phase to its concentration in the aqueous phase; Higher log kow = more lipophilic
EC50 - concentration of a compound where 50% of its maximal effect (mortality) is observed; Low EC50 = more toxic
Ozone Creation Potential POCP - an indicator of the ability of a VOC to contribute to ozone formation. A measure of the reactivity of an organic compound with hydroxyl radicals & subsequent formation of ozone. High value = more potential
Exposure Limit 8hr TWA (ppm) – a legal limit for exposure of an employee to a chemical substance during 8 hours. Lower value = more harmful
Flash point - the lowest temperature at which vapors of a volatile material will ignite; Lower value = more flammable
Heat of Combustion - energy released as heat when a substance undergoes complete combustion with oxygen under standard conditions; High = easier to burn
Dielectric constant - A measure of a substance's ability to insulate charges from each other. Higher value = more insulation
Autoignition temperature - lowest temperature at which substance spontaneously ignites. Lower value = more flammable

## Slide 35: Solvent Exercise – Solvent 1
major issues have been identified; appropriate control procedures need to be in place.
issues have been identified; the need for control procedures should be considered
no major issues have been identified area
Acetic Acid

## Slide 36: Solvent Exercise – Solvent 2
major issues have been identified; appropriate control procedures need to be in place.
issues have been identified; the need for control procedures should be considered
no major issues have been identified area
Cyclohexane

## Slide 37: Solvent Exercise
Acetic acid (glacial)
  Used in chemical industry to produce photographic film, wood glue, and synthetic fibers.
  Used in food industry as additive.
  Demand: 6.5 million metric tons/year.
Cyclohexane
  Used in chemical industry as precursor for nylon.
  Known organic solvent.
  Global cyclohexane market valued at $5.8 billion in 2013.
Notes: Issues and answers:
1. How much the ratings change depending on the way the solvent is used in industry (i.e., compare a situation where a worker is cleaning the inside of a tank with a situation where solvent is part of an effluent that is being released into a river). The answer - a lot.
2. Is it possible that either of these solvents will ever receive all “green lights” in every category? The answer - almost certainly not. This can function as a segue into a discussion of alternative solvents being developed by green chemists.

## Slide 38: Unconventional Solvents
supercritical CO2
CO2-expanded liquid
ionic liquid
liquid polymer
switchable solvent
water

## Slide 39: Water as a solvent
Advantages:
  Innocuous.
  Well characterized.
  Versatility among applications.
  One of the most obvious alternatives to VOCs.
  Cheap, readily available, and plentiful
  In some cases faster reaction (‘on water’ reactions)
  Useful in biphasic processes in conjunction with other solvents.
Disadvantages:
Low solubility of organic substrates
Incompatibility with many reagents
Removal of water is energy intensive.
Clean up of aqueous waste difficult.
Water based solvents with generalized applications.
Notes: Water, the most popular choice for nature, is undoubtedly the most benign solvent there is. It is easily accessible and cheap to employ, and has the lowest toxicity to the environment. Not only it is non-flammable and non-explosive, but it also has a high heat capacity. With addition of surfactants or other miscible organic co-solvent, water emerges as a new choice in chemical synthesis including oxidations, reductions, nucleophilic substitutions, and electrochemical synthesis. However, water is not perfect and its cons should be considered before it is used in large scale synthesis. Aside from its poor compatibility of organic molecules, distillation of water from reagent requires more demanding condition relatively to other solvents such as methanol. Removal of water, even in vacuum, is more energy intensive (thus less economically viable) than conventional organic solvent. Therefore each solvent selection or replacement needs to be discussed on a case-by-case basis. Replacement of organic solvents to water may be done at least for safety reasons

## Slide 40: Water: Solving the incompatibility problem
Li, 1995
http://students.washington.edu/~haoli/photo_gallery/archives/olympic/
RMgBr reacts with water more than carbonyls
Notes: Water, the most popular choice for nature, is undoubtedly the most benign solvent there is. It is easily accessible and cheap to employ, and has the lowest toxicity to the environment. Not only it is non-flammable and non-explosive, but it also has a high heat capacity. With addition of surfactants or other miscible organic co-solvent, water emerges as a new choice in chemical synthesis including oxidations, reductions, nucleophilic substitutions, and electrochemical synthesis. However, water is not perfect and its cons should be considered before it is used in large scale synthesis. Aside from its poor compatibility of organic molecules, distillation of water from reagent requires more demanding condition relatively to other solvents such as methanol. Removal of water, even in vacuum, is more energy intensive (thus less economically viable) than conventional organic solvent. Therefore each solvent selection or replacement needs to be discussed on a case-by-case basis. Replacement of organic solvents to water may be done at least for safety reasons

## Slide 41
Using safe, nontoxic, and inexpensive surfactants, micelles can be formed in water.
Micelles have hydrophilic exteriors and hydrophobic interiors, allowing for the encapsulation (and reaction) of organic molecules in aqueous environments.
increasing effective concentration increases reaction rates.
Recycling of the surfactant is very efficient.
Image: Bruce H. Lipshutz (Wkipedia)
Water: Solving the solubility problem
Bruce Lipschultz
Shu Kobayashi

## Slide 42: Solvent Usage by Sector
Source: Int. J. Mol. Sci. 2015, 16(8), 17101-17159; doi:10.3390/ijms160817101

## Slide 43
Oil-based paint
organic solvent
soluble polymer
vapour emissions
flammability
smog
inhalation hazards
higher Tg polymer
Water-based paint
water as solvent
insoluble polymer (latex)
no vapour emissions
no flammability
no smog
no inhalation hazards
lower Tg polymer
solvent vapours
solvent vapours
water vapour
water vapour
Water for Oil-Based Paints

## Slide 44
Water for Oil-Based Paints
Oil-based paint
organic solvent
soluble polymer
vapour emissions
flammability
smog
inhalation hazards
higher Tg polymer
Water-based paint
water as solvent
insoluble polymer (latex)
no vapour emissions
no flammability
no smog
no inhalation hazards
lower Tg polymer
We need a paint that is water-soluble while in the can, but water-insoluble once it has dried.

## Slide 45
Switchable paint
carbonated water as solvent
soluble polymer
no vapour emissions
no flammability
no smog
no inhalation hazards
higher Tg polymer
in the can
as dried on the surface
water + CO2
water + CO2
hydrophobic
hydrophilic
Jessop, Green Chem (2018) 20, 1899
Water for Oil-Based Paints

## Slide 46: Supercritical Fluids: CO2
Small molecules (e.g., CO2, H2O) used under conditions of elevated pressure and temperature to form a fluid that is neither liquid nor gas.
Advantages:
Similar advantages to water
  Natural, inert, non-flammable, cheap, plentiful.
  Easily available commercially in > 99.9% pure form.
  By-product of brewing, ammonia synthesis, combustion.
Already being adopted in a variety of commercial processes (see later).
Non-toxic and properties well understood.
Easily removed and recycled, and can be disposed of with no net increase in global CO2.
  Simple product isolation, by evaporation to 100% dryness.
Potential for product processing (extraction, particle micronozation, chromatography, textile dyeing, etc.).
Disadvantages:
  High pressure required.
  May have poor solvency for polar molecules.
  May require Surfactants.
Notes: scCO2 is very attractive as a solvent because it can be removed easily by simply decreasing the pressure in the reaction vessels. This eliminates the need of solvent distillation, which is an energy intensive process, while leaving behind a product with high purity. Besides its’ non-toxic profile, scCO2 is often readily available as an industrial by-product and can be obtained without burning fossil fuels. Several companies offer CO2 recovery, and turn this industrial by-product into a profitable reagent. Such recovery is especially popular in breweries, distilleries, ammonia or ethylene oxide productions.

## Slide 47: Supercritical CO2
scCO2 moves like a gas and dissolves things like a liquid

## Slide 48: Supercritical Fluid Extraction
A novel separation process.
It can be used for:
  Separation and purification of oils, flavours and medicinal components.
  Removal of greasy material.
  Conversion of azeotropic water-ethanol mixture to an anhydrous ethanol.
  Fractionation and purification of polymers.
  Decaffeination of coffee beans
FDA: CO2 “not a solvent”

## Slide 49: Textile Dyeing with scCO2 (waterless Dyeing)
More Efficient Process Developed and Patented by Dr. Swapneshu Baser, Deven Supercriticals Pvt. Ltd., India
Process:
Dissolution of Dye in SC CO2
Swelling of Textile Material by SC CO2
Efficient Diffusion of Dye in Textile Matrix
Depressurise to Entrap Dye in Textile Matrix
Advantages:
No Water Usage
Zero Discharge process
No ETP requirement
Re-use of unused Dye collected in Separator
Lower overall cost of Dyeing

## Slide 50: Limitation of using scCO2
High pressures required:
  Standard HPLC apparatus used in lab, reactors made of stainless steel, many commercially available.
  Higher initial investment for large scale work.
Weak solvent:
  Relatively non-polar, with high quadrupole moment.
  For polar molecules, require use of co-solvents (MeOH, MeCN, THF, toluene).
  Simple modification of reagents to improve solubility.
Energy considerations:
  Compression, Liquification of CO2 requires energy.
  Energy consumption reduced minimal decompression and recycling.
Reacts in the presence of good nucleophiles:
  Often reversible, can be exploited synthetically.

## Slide 51: Reactions in Supercritical Fluids
scC2H4 polymerization (ICI in 1937)
Olefin hydration (Shell, BP, Erdöl, Hibernia, ICI, VEBA…)
N2 hydrogenation (Haber-Bosch Process, BASF 1913)
Idemitsu Petrochemical

## Slide 52: CO2-Expanded Liquids
CO2-expanded NEt3 (Jessop, 1996)
Volumetric expansion of aprotic solvents by CO2
at 40˚C (Kordikowski, 1995)
Review paper: Chem. Rev. 2007, 107, 2666

## Slide 53: CO2-Expanded Liquids
Charged substance mixtures that form a liquid at ambient temperatures.
“Salts whose crystal structure has been perturbed so they are a liquid at room temperature.”
Advantages:
Less organic content than conventional solvents
Variable solvent properties
Highly adjustable polarity
Lowered melting point
Viscosity drops greatly
Excellent mass transfer rates
Improved solubility of reagent gases
Better solvent strength than scCO2
Lower pressure than scCO2
Disadvantages:
  Still requires some pressure
  Still requires some organic solvent
  Doesn’t work with water
Viscosity of CO2-expanded crude oil at 49 ˚C
J. Petrol. Technol. (1965) 102.
Notes: Ionic liquids have been found useful for a wide range of chemical reactions and processes, including hydrogenation reactions, biocatalysis reactions such as transesterification and perhydrolysis, and electrochemical applications such as battery electrolytes
Another use for ionic liquids is as a medium for separation of biologically produced feedstocks from a fermentation broth, such as acetone, ethanol, or butanol

## Slide 54: Ionic Liquids
A salt: A cation and an anion
It has to be liquid below 100°C
Wide chemical variability => adapted to applications
http://www.rtil.eu/pmwiki/pmwiki.php/About/IonicLiquids

## Slide 55: Ionic Liquids
Charged substance mixtures that form a liquid at ambient temperatures.
“Salts whose crystal structure has been perturbed so they are a liquid at room temperature.”
Advantages:
Very low vapour pressure – attractive alternative to VOCs.
Good solvents for a wide range of organic, inorganic and polymeric compounds.
Anion and cation can be fine tuned to give a wide range of solvent properties (e.g. hydrophilic, hydrophobic) which can be exploited.
Wide range of reactions already demonstrated in this medium.
Can be used in conjunction with other alternative solvents (particularly CO2).
Claimed to be recyclable (essential for widespread use) although there may be regulatory problems with this.
Effectively, properties similar to many other high boiling, polar solvents.
Disadvantages:
  Expensive compared to other solvents although cheaper versions are appearing.
  Have to be prepared:
    Usually involves use of other solvents.
  Work-up to separate/extract products usually involves other solvents.
  Recycling also usually involves other solvents to extract unwanted residues.
  Questionable toxicity – some certainly are toxic and have been shown to have a detrimental effect on aquatic life – problem as not VOC so will tend to persist in local environment, on land/sea etc.
  Still requires disposal at end of life (incineration?).
  Always POLAR
Notes: Ionic liquids have been found useful for a wide range of chemical reactions and processes, including hydrogenation reactions, biocatalysis reactions such as transesterification and perhydrolysis, and electrochemical applications such as battery electrolytes
Another use for ionic liquids is as a medium for separation of biologically produced feedstocks from a fermentation broth, such as acetone, ethanol, or butanol

## Slide 56: Ionic Liquids
Organic transformations in IL
Diels-Alder reactions
Alkylation reactions
Hydroformylation reactions
Friedel Crafts reactions
Pd-mediated C-C bond formation
Alkene polymerisation
Biotransformations
T. Welton, Chem. Rev., 1999, 99, 2071. http://www.researchinschools.org/projects/ionic_liquids.html

## Slide 57: Ionic Liquids: Are they green?
Zhang, Env. Sci. Tech., 2008, 42, 1724

## Slide 58: Ionic Liquids: Are they green?
Zhang, Env. Sci. Tech., 2008, 42, 1724
Jessop, Green Chem (2011) 13, 1391

## Slide 59: Alternatives to Ionic Liquids
Deep eutectic solvent
Abbott, Chem. Commun., 2003, 70
choline chloride
(mp 302 ˚C)
urea
(mp 134 ˚C)
+
Liquid polymers

## Slide 60
The problems with solvents
Minimizing solvent use
Selecting greener conventional solvents
Using unconventional solvents
Topics Covered

## Slide 61
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE