## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Green Chemistry: Principles and Metrics
Image: Wikipedia, Biodegradation of nanocellulose, Author: Shaohui Li, Pooi See Lee
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
Green Chemistry
is the design of chemical products and processes that reduce or eliminate the use and/or generation of hazardous substances.

## Slide 3
12. Inherently Safer Chemistry for Accident Prevention. Substance and the form of a substance used in a chemical process should be chosen to minimize the potential for chemical accidents, including releases, explosions, and fires.
The Twelve Principles of Green Chemistry
11. Real-time Analysis for Pollution Prevention. Analytical methodologies need to be further developed to allow for real-time in-process monitoring and control prior to the formation of hazardous substances.
10. Design for Degradation. Chemical products should be designed so that at the end of their function they do not persist in the environment and instead break down into innocuous degradation products.
9. Catalysis. Catalytic reagents (as selective as possible) are superior to stoichiometric reagents.
8. Reduce Derivatives. Unnecessary derivatization (blocking group, protection/deprotection, temporary modification of physical/chemical processes) should be avoided whenever possible .
7. Use of Renewable Feedstocks. A raw material or feedstock should be renewable rather than depleting whenever technically and economically practical.
6. Design for Energy Efficiency. Energy requirements should be recognized for their environmental and economic impacts and should be minimized. Synthetic methods should be conducted at ambient temperature and pressure.
5. Safer Solvents and Auxiliaries. The use of auxiliary substances (solvents, separation agents, etc.) should be made unnecessary whenever possible and, when used, innocuous.
4. Designing Safer Chemicals. Chemical products should be designed to preserve efficacy of the function while reducing toxicity.
3. Less Hazardous Chemical Synthesis. Whenever practicable, synthetic methodologies should be designed to use and generate substances that possess little or no toxicity to human health and the environment.
2. Atom Economy. Synthetic methods should be designed to maximize the incorporation of all materials used in the process into the final product.
1. Prevention. It is better to prevent waste than to treat or clean up waste after it is formed.

## Slide 4
Prevention
It is better to prevent waste than to treat or clean up waste after it is formed.

## Slide 5
Source Reduction
The Pollution Prevention Act of 1990
Disposal
Recycling
Treatment
Pollution Prevention

## Slide 6
Storage
Transportation
Treatment
Disposal
Regulatory Costs
Liability
Worker Health and Safety
Corporate Reputation
Community Relations
New Employee Recruitment
The Cost of Using Hazardous Materials

## Slide 7
Industry spent $115 billion in 1992 on waste treatment, control, and disposal..
Environmental Costs (1992 Perspective)
It was estimated at that time that it would cost as much as $700 billion to clean up existing hazardous waste sites. risen significantly.
These costs, and the costs associated with regulatory compliance, have risen significantly.

## Slide 8
Inventory controls
Approaches to Pollution Prevention
Process controls
In-process recycling
Green Chemistry
Housekeeping changes

## Slide 9
Atom Economy
Synthetic methods should be designed to maximize the incorporation of all materials used in the process into the final product.

## Slide 10
Balancing Reactions

## Slide 11
Atom Economy
Feedstock(s)
Product
Theoretical Yield = 82 g
54 g
28 g
82 g

## Slide 12
Atom Economy
Feedstock(s)
Product
unreacted feedstock(s)
Theoretical Yield = 82 g
54 g
28 g
69.7 g
8.1 g
4.2 g
Actual Yield = 69.7 g
Percent Yield = 69.7/82 = 0.85
85% Yield

## Slide 13
Atom Economy
Feedstock(s)
Product
Co-Product(s)
+
Unreacted feedstock(s)
106 g
352 g
180 g
278 g
Theoretical Yield = 180 g
Actual Yield = 180 g
100% Yield !
E-Factor = mass of nonproducts (waste) / mass of products
278 g / 180 g = 1.54 E-Factor

## Slide 14
Roger Sheldon
Environmental Impact Factor (E-factor)
E-factor = mass waste/ mass product
Sheldon, R. A. Chem Ind (London), 1992, 903..
Environmental Impact Factor
Industry Sector
Oil Refining
Bulk Chemicals
Fine Chemicals
Pharmaceuticals
E-Factor
< 0.1
1 - 5
5 - 50
25 - 100
Production Volume (Tonnage)
1,000,000 – 100,000,000
10,000 – 1,000,000
100 – 10,000
10 – 1,000

## Slide 15
Atom Economy
Barry Trost
Atom Economy
Atom Economy = mass of desired product / mass of feedstocks
106 g
352 g
180 g
278 g
Atom Economy = mass of desired product / mass of feedstocks
180 g / 458 g = 0.393 = 39.3%
Trost, B. M.; Science 1991, (254), pp 1471-1477.

## Slide 16
Atom Economy
Feedstock(s)
Product
Co-Product(s)
+
+
Byproduct(s)
Unreacted feedstock(s)
68 g
56 g
73.16 g
50.84 g
119.04 g
4.96 g
59% Selectivity
96% Selectivity
Condition #1:
Condition #2:

## Slide 17
Atom Economy
Feedstock(s)
Product
Co-Product(s)
+
+
Byproduct(s)
Unreacted feedstock(s)
Decomposed
Feedstocks
Decomposed
Products
Decomposed
Co-Products
Decomposed
Biproducts
minor byproducts
subsequent reactions of components present

## Slide 18
Less Hazardous Chemical Synthesis
Whenever practicable, synthetic methodologies should be designed to use and generate substances that possess little or no toxicity to human health and the environment.

## Slide 19
1-Naphthyl Methylcarbamate
+
Methylisocyanate
1-Naphthol
Less Hazardous Synthesis
The worst industrial accident in history.
40 tons of methyl isocyanate were accidentally released when a holding tank overheated at a pesticide plant, located in the city of Bhopal.
Over 500,000 people were exposed.
Over 3,000 immediate deaths.
Estimates range from 8,000-16,000 subsequent deaths
Bhopal Disaster December 2, 1984
+
Phosgene
Methylamine

## Slide 20
1-Naphthyl Methylcarbamate
+
+
Methylisocyanate
1-Naphthol
+
Phosgene
Methylamine
Less Hazardous Synthesis
+

## Slide 21
Case study: Synthesis of adipic acid
 one of the most produced commodity chemicals worldwide
 projected global market size >US$ 7 billion by 2019
 versatile building block in chemical, pharmaceutical and food industries
 precursor for the synthesis of the polyamide Nylon-6,6.
Conventional synthesis:
 benzene, a known carcinogen, is a starting material
 oxidation with excess of HNO3, production of nitrous oxide (N2O) a GHG (5–8% of worldwide anthropogenic N2O emissions).
Less Hazardous Chemical Synthesis

## Slide 22
Alternative synthesis of adipic acid:
Less Hazardous Chemical Synthesis
Check out: Raj et al. “Biocatalytic production of adipic acid from glucose using engineered Saccharomyces cerevisiae” Metabolic Engineering Communications. 2018, 6, 28-32.
 development of biocatalytic processes for producing adipic acid and catechol from sugars.
 biocatalytic process using yeast converts sugars to cis,cis-muconic acid, and this intermediate stage allows ready access to catechol and adipic acid.
 uses water as solvent at ambient temperature and pressure.

## Slide 23
Designing Safer Chemicals
Chemical products should be designed to preserve efficacy of the function while reducing toxicity.

## Slide 24
“The Incorporation of Hazard Reduction as a Chemical Design Criterion in Green Chemistry”
Anastas, Nicholas; Warner, John C. J. Chem. Health and Safety 2005, 12(2), 9-13.
Designing Safer Chemicals

## Slide 25
“Everything is toxic. It is simply depends on the dose”
Often otherwise phrased as
“The dose makes the poison.”
Risk = Hazard x Exposure
Designing Safer Chemicals
Green chemistry and engineering focus on reducing risk by reducing hazard.

## Slide 26
Hazard types to avoid:
  Toxicological/Eco-toxicological
    Carcinogenicity
    Reproductive
    Developmental
    Neurological
    Global warming potential
    Ozone depleting potential
    Bioaccumulation
    Persistence
  Physical
    Explosivity
    Flammability
    Corrosivity
Physical/Chemical Properties to consider:
  Water solubility
  Log Kow
  Volatility
  Molar volume
  Aspect ratio
  Radical formation
  Nucleophilicity
  Electrophilicity
  pH/pKa
  Surface area
  Reducing potential
  Oxidizing potential
  Polarizability
Designing Safer Chemicals

## Slide 27
Conventional use of organotin compounds as antifoulants:
 TBTO and related antifoulants have long half-lives in the environment (the half-life of TBTO in seawater is >6 months).
 they bioconcentrate in marine organisms (the concentration of TBTO in marine organisms has been found to be up to 104 times greater than in the surrounding water).
 organotin compounds are chronically toxic to marine life and can enter food chain. Extreme neurological hazard.
 bioaccumulative
tributyltin oxide (TBTO)
Case study: Antifoulants
Designing Safer Chemicals
Antifoulants are generally dispersed in the paint as it is applied to the hull. Organotin compounds such as tributyltin oxide (TBTO) have traditionally been used: gradually leaches from the hull, killing the fouling organisms in the surrounding

## Slide 28
Alternative antifoulants (Dow Chemicals):
 Sea-Nine® 211 (DCOI) works by maintaining a hostile growing environment for marine organisms
 when organisms attach to the hull treated with DCOI, proteins at the point of attachment react with the DCOI
 reaction with DCOI prevents the use of these proteins for other metabolic processes: organism detaches itself and searches for a more hospitable surface to grow upon.
 Only organisms attached to hull of ship are exposed to toxic levels of DCOI.
 readily biodegrades once leached from ship (half-life is less than one hour in sea water).
Case study: Antifoulants
Designing Safer Chemicals
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-1996-designing-greener-chemicals-award
Awardee in 1996

## Slide 29
Safer Solvents and Auxiliaries
The use of auxiliary substances (solvents, separation agents, etc.) should be made unnecessary whenever possible and, when used, innocuous.

## Slide 30
Solvents
Feedstock(s)
Product
Co-Product(s)
+
+
Byproduct(s)
Unreacted feedstock(s)
Decomposed
Feedstocks
Decomposed
Products
Decomposed
Co-Products
Decomposed
Biproducts
minor byproducts
subsequent reactions of components present
Solvents
Solvents
Purification

## Slide 31
Usefulness in reaction (performance)
Ease of recycle
Price
Safety (flash point, flammability)
Criteria for Use of Solvents

## Slide 32
Problematic organic solvents
avoidance
environmentally
benign and safe
easily separable, safe
zero
volatility
greener alternatives
Safer Solvents and Auxiliaries
no solvent
supercritical fluids
ionic liquids
water solvent

## Slide 33
Preferred | Useable | Undesirable
Water | Cyclohexane | Pentane
Acetone | Heptane | Hexane(s)
Ethanol | Toluene | Di-isopropyl ether
2-Propanol | Methylcyclohexane | Diethyl ether
1-Propanol | Methyl t-butyl ether | Dichloromethane
Ethyl acetate | Isooctane | Dichloroethane
Isopropyl acetate | Acetonitrile | Chloroform
Methanol | 2-MethylTHF | Dimethyl formamide
Methyl ethyl ketone | Tetrahydrofuran | N-Methylpyrrolidinone
1-Butanol | Xylenes | Pyridine
t-Butanol | Dimethyl sulfoxide | Dimethyl acetate
 | Acetic acid | Dioxane
 | Ethylene glycol | Dimethoxyethane
 |  | Benzene
 |  | Carbon tetrachloride
Dunn and Perry, et. al., Green Chem., 2008, 10, 31-36
Solvent Selection Guides

## Slide 34
Li, C.-J. Acc. Chem. Res. 2002, 35, 533
Li, C.-J. Tetrahedron, 1996, 52, 5643
Water as a Solvent

## Slide 35
Unique properties
  High ionic conductivity
  Non-volatility
  Non-flammable
  High thermal stability
  Liquid over a wide temp range
  Highly solvating, yet non-coordinating
Melting point*
Density*
Viscosity*
Miscibility with water*
Ionic Liquids

## Slide 36
Supercritical CO2

## Slide 37
Zoloft® is an anti-depressant; once one of the best selling pharmaceuticals on the market.
Conventional sertraline synthesis:
 synthesis was a three step process.
 used 4 hazardous solvents (methylene chloride, tetrahydrofuran, toluene, and hexane).
Zoloft®
Safer Solvents and Auxiliaries
Case study: Manufacturing process for sertraline, the active ingredient in the popular drug Zoloft®

## Slide 38
 process was streamlined to a single step, carried out in ethanol, a much less toxic solvent.
 new process is catalytic, cutting down on starting materials by 60%, 45%, and 20% for the three reaction components.
 combined steps eliminated 180 tons of TiCl4, 150 tons of 50% NaOH, 180 tons of 35% HCl waste, and 600 tons of solid TiO2.
Pfizer, Inc
Case study: Manufacturing process for sertraline, the active ingredient in the popular drug Zoloft®
Alternative sertraline synthesis:
Safer Solvents and Auxiliaries
Image: Wikimedia Commons, Author: Ragesoss

## Slide 39
Design for Energy Efficiency
Energy requirements should be recognized for their environmental and economic impacts and should be minimized. Synthetic methods should be conducted at ambient temperature and pressure.

## Slide 40
Thermal (electric)
Cooling (water condensers, water circulators)
Distillation
Equipment (lab hood)
Photo
Microwave
Source of energy:
Power plant – coal, oil, natural gas
Energy in a Chemical Process

## Slide 41
Monitoring, control and maintenance
Loss prevention
Waste heat recovery
Matching energy sources to requirements
Conservation of Thermal Energy

## Slide 42
Energy Usage
Chemicals and petroleum industries account for 50% of industrial energy usage.
~1/4 of the energy used is consumed in distillation and drying processes.

## Slide 43
Photochemical Reactions
Microwave Reactions
Solid State Chemistry (mechanochemistry)
Alternative Forms of Energy

## Slide 44
Atorvastatin, a cholesterol-lowering drug (Lipitor), suffers from an energy-demanding synthesis as a result of two cryogenic reactions at - 70 oC
New biocatalytic synthesis uses enzyme DERA and shortens the process by removing two energy intensive chemical steps.
Case Study: Atorvastatin
Design for Energy Efficiency
DERA: deoxyribose-5-phosphate aldolase
CBzNH
CBzNH
DERA

## Slide 45
Use of Renewable Feedstocks
A raw material or feedstock should be renewable rather than depleting whenever technically and economically practical.

## Slide 46
Biomaterials
Petroleum Products [Hydrocarbons]
Biomaterials [Carbohydrates, Proteins, Lipids]
Highly Functionalized Molecules
Singly Functionalized Compounds [Olefins, Alkylchlorides]
Highly Functionalized Molecules

## Slide 48
Biomaterials
Petroleum Products [Hydrocarbons]
Biomaterials [Carbohydrates, Proteins, Lipids]
Highly Functionalized Molecules
Singly Functionalized Compounds [Olefins, Alkylchlorides]
Highly Functionalized Molecules

## Slide 49
Polyhydroxyalkanoates (PHAs)
Polylactic acid
Polymers from Renewable Resources

## Slide 50
Case study: Production of levulinic acid
 precursor for pharmaceuticals, plasticizers, and various other additives
 widely used as a building block/starting material
Conventional synthesis:
 made by heating hexoses (glucose, fructose) or starch in dilute HCl or H2SO4
 yield depends on acid, its concentration, temperature, pressure
 reaction also produces hard to remove by-products.
Use of Renewable Feedstocks
fructose
hydroxymethylfurfural (HMF)
formic acid
levulinic acid

## Slide 51
paper mill
sludge
levulinic acid
municipal solid waste
and waste paper
agricultural
residues,
waste wood
Alternative synthesis:
 levulinic acid can be obtained from paper mill sludge, agricultural and municipal waste and paper.
 uses a high-temperature, dilute-acid hydrolysis process that converts cellulosic biomass.
Biofine, Inc
Use of Renewable Feedstocks
Case study: Production of levulinic acid
hydrolysis

## Slide 52
DALA (-amino levulinic acid)
(non-toxic, biodegradable herbicide)
Diphenolic acid
Acrylic acid
Succinic acid
THF
MTHF
(fuel additive)
butanediol
gamma
butyrolactone
The Biofine Process – Levulinic Acid Family

## Slide 53
Reduce Derivatives
Unnecessary derivatization (blocking group, protection/deprotectio, temporary modification of physical/chemical processes) should be avoided whenever possible.

## Slide 54
R. B. Woodward’s Synthesis of
RESERPINE
R. B. Woodward’s Synthesis of
RESERPINE

## Slide 55
Protecting Groups
[H]
Protection
Deprotection
[H]

## Slide 56
Noncovalent Derivatization

## Slide 57
Solid State Reactions
+
Extremely low yield in solution

## Slide 58
Solid State Reactions
+

## Slide 59
Solid State Reactions

## Slide 60
Solid State Reactions

## Slide 61
6-APA: core moiety of penicillin
Conventional synthesis of 6-aminopenicillanic acid using 3 steps and intermediates:
Alternative synthesis using enzyme and fewer derivatives:
Case study: 6-aminopenicillanic acid (6-APA)
Reduce Derivatives

## Slide 62
Catalysis
Catalytic reagents (as selective as possible) are superior to stoichiometric reagents.

## Slide 63
Catalysts can facilitate complex reactions by:
lowering the activation energy (Ea) of the reaction.
 reducing temperature necessary to achieve a reaction.
 controlling the site of the reaction (selectivity enhancement).
 catalysis is a cyclic event
Image source: Adobe stock
Catalysis
I. Chorkendorff, J. W. Niemantsverdriet, Concepts of Modern Catalysis and Kinetics, Wiley-VCH, 2003
Notes: Catalysts lower the activation (threshold energy) in the reaction.

## Slide 64
Reduce energy requirements of a reaction
Reduce amount of material used
Increase atom economy
Ability to be reused
Why are Catalysts Considered Green?

## Slide 65
Is the catalyst used in stoichiometric or sub-stoichiometric amounts?
Can the catalyst be reused?
  How many times can it be reused?
  Will the activity of the catalyst decrease as it is reused?
Is the catalyst non-toxic?
Is the catalyst expensive?
Does the catalyst require special conditions?
  Air sensitive?
Questions to Ask?

## Slide 66
Many molecules/enzymes/materials can be catalysts
Catalysis
Catalysis, Concepts and green applications, by Gadi Rothenberg, Wiley-VCH 2008.
copper-zinc crystallites on silica
zeolite (crystalline alumosilicate)
enzyme (biocatalyst)

## Slide 67
  Dartt and Davis
  97% yield in three steps
Nonsteroidal anti-inflammatory drug (NSAID) of the propionic acid class (the same class as ibuprofen) that relieves pain, fever, swelling, and stiffness; COX inhibitor
Catalysis: Green Naproxen Synthesis
Notes: cyclooxygenase

## Slide 68
Enzymes or whole-cell microorganisms
Benefits
  Fast rxns due to correct orientations
  Orientation of site gives high stereospecificity
  Substrate specificity
  Water soluble
  Naturally occurring
  Moderate conditions
  Possibility for tandem rxns (one-pot)
Biocatalysis

## Slide 69
Design for Degradation
Chemical products should be designed so that at the end of their function they do not persist in the environment and instead break down into innocuous degradation products.

## Slide 70
Persistent
Bioaccumulative
Toxic
EPA’s PBT list:
https://www.epa.gov/toxics-release-inventory-tri-program/persistent-bioaccumulative-toxic-pbt-chemicals-covered-tri
PBTs

## Slide 71
Synthetic detergents
1950’s and 60’s – high level of foam in sewage plants and in rivers & streams
  Inefficient operation of sewage plants (and washing machines)
  Branched alkyl structures resulted in persistence issue
  Moved to linear alkyl chains
  First time that structure was linked to performance/function (persistence)
Cheer: https://www.youtube.com/watch?v=lMxlAIeI8QI
Dash: https://www.youtube.com/watch?v=F1YTHr4mTQA
Early Examples of Persistence

## Slide 72
Pesticides: DDT
Ideal insecticide:
  Inexpensive to prepare
  Very wide spectrum in activity
  Non-toxic to humans (or so they thought)
  Persistent, negating the requirement for re-treatment
  Inventors awarded Nobel Prize in 1948
1962: Rachel Carson, Silent Spring (https://youtu.be/Ipbc-6IvMQI)
  Linked widespread DDT use to cancer and thinning of bird eggs shells
  Carcinogen, endocrine disruptor, developmental and reproductive effects
Replaced in the developed world with more expensive pesticides, such as organophosphates
Early Examples of Persistence

## Slide 73
Plastics
Increased production and use in the 20th century:
  Low cost, ease of manufacture, versatility, resistance to water
Parley for the Oceans: http://www.parley.tv/#fortheoceans
Current Examples of Persistence

## Slide 74
Conventional plastics (e.g. PET) are made from petroleum:
 PET Plastic persists in the environment
 made from depleting resources
high temperature
vacuum
catalyst
petroleum product
Design for Degradation: PLASTICS

## Slide 75
Synthesis of PolyLactic Acid (PLA) from starch:
 a biobased, compostable, and recyclable PLA polymer that uses 20–50 percent less fossil fuel resources than comparable petroleum-based polymers.
 the first family of polymers derived entirely from renewable resources that can compete cost-effectively with traditional fibers and plastic packaging materials.
 manufacturing process consists of three solvent-free steps that lead to the production of lactic acid, lactide, and PLA high polymer with very high yields and internal recycling schemes that reduce waste.
 PLA can be biodegraded under industrial compositing conditions - does not degrade though in the environment
Cargill Dow LLC
Design for Degradation: PLASTICS
Alternative process:

## Slide 76
Real-time Analysis
Analytical methodologies need to be further developed to allow for real-time in-process monitoring and control prior to the formation of hazardous substances.

## Slide 77
Jennifer Young
Liz Gron
Lawrence Keith
Chem. Rev. 2007 107, 2695-2706
Green Analytical Methodologies

## Slide 78
Gains in quality, safety and/or efficiency will vary depending on the product and are likely to come from:
  Reducing production cycle times by using on-, in-, and/or at-line measurements and controls. Energy reduction
  Preventing rejects, scrap, and re-processing. Waste reduction
  Considering the possibility of real time release.
  Increasing automation to improve operator safety and reduce human error. Safety
  Facilitating continuous processing to improve efficiency and manage variability
    Using small-scale equipment (to eliminate certain scale-up issues) and dedicated manufacturing facilities. Process Intensification
    Improving energy and material use and increasing capacity. Energy
Relationship to Green Chemistry

## Slide 79
Real time analysis for a chemist is the process of “checking the progress of chemical reactions as it happens”.
Knowing when your product is “done” can save a lot of waste, time, and energy!
Image: Wikimedia Commons
Real-time Analysis for Pollution Prevention

## Slide 80: What Does Green Analytical Chemistry Mean?
Green Chemistry is applicable to all chemical processes, including the methods, protocols and processes of analytical chemistry.
Image: Wikipedia
Real-time Analysis for Pollution Prevention

## Slide 81: Examples of Green Analytical Chemistry Methodologies
X-ray fluorescence detection for multi-metal matrix
Image Sources: https://www.thermofisher.com, https://www.intechopen.com/books/herbicides-advances-in-research/recent-advances-in-the-extraction-of-triazines-from-water-samples, J. P. McMullen, M. T. Stone, S. L. Buchwald and K. F. Jensen, Angew. Chem., 2010, 39, 7230
Desired product
In-line HPLC analyzer, on flow
Real-time adaptation of addition of 1 and 2 to max. 3
Real-time Analysis for Pollution Prevention

## Slide 82
In 2008 Naclo Company won the EPA Greener Reaction Conditions Award for their innovative 3D TRASAR® Technology.
Case study: Real-time analysis in cooling systems
Alternative Cooling System with 3D TRASAR® Technology:
3D TRASAR® System allows for the real-time monitoring of mineral scale buildup.
system can also utilize poor-quality water.
3D Scale Control prevents mineral scale formation to increase efficiency.
3D Bio-control performs a real-time check for planktonic and sessile bacteria. This reduces the amount of biocide used since biocides are then added only when necessary, rather than on a set schedule.
3D TRASAR® System greatly reduces the amount of wastewater discharged from cooling systems.
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-2008-greener-reaction-conditions-award
Image: Wikipedia, A lavender-colored nonpotable water pipeline in Mountain View, California, Author: Grendelkhan
Real-time Analysis for Pollution Prevention
Notes: The system monitors antiscalant levels using a fluorescent-tagged, scale-dispersant polymer and responds quickly when conditions favor scale formation. In addition, 3D Bio-control, also part of the 3D TRASAR® system, is the only online, real-time test for measuring planktonic and sessile bacteria. It uses resazurin, another fluorescent molecule, which changes its fluorescent signature when it interacts with respiring microbes. By adding an oxidizing biocide in response to microbial activity, 3D Bio-control generally reduces the use of biocide and also prevents biofilm from building up on surfaces, maintaining efficient heat transfer.

## Slide 83
Inherently Safer Chemistry
Substance and the form of a substance used in a chemical process should be chosen so as to minimize the potential for chemical accidents, including releases, explosions, and fires.

## Slide 84
approaches to design safer chemistry can include the use of solids or low vapor pressure substances in place of volatile liquids.
 other approaches include avoiding the use of molecular halogens in large quantities.
 continuous flow processes can help to minimize chemical hazards.
Accidents can be avoided by minimizing hazards
Inherently Safer Chemistry
for Accident Prevention

## Slide 85
Case study: Production of gasoline alkylate with AlkyClean® Technology
In 2016 Albemarle and CB&I won the EPA Green Chemistry Award for their inherently safer AlkyClean® process technology.
AlkyClean® Technology:
 AlkyClean® solid acid alkylation process produces high quality alkylate without using liquid acid catalysts.
 solid acid alkylation process is safer for both people working directly in production and for people in the area surrounding the facility.
 environmental and economic benefits since no acid-soluble oils or spent acids are produced.
Conventional alkylate production:
 alkylate is typically produced from the reaction of isobutane and light olefins.
 requires the liquid acid-catalyzed processes, such as hydrofluoric acid.
 hydrofluoric acid is extremely toxic, upon release it forms clouds that can be lethal for up to five miles.
Inherently Safer Chemistry
for Accident Prevention

## Slide 86
The United States Presidential Green Chemistry Challenge

## Slide 87
US Presidential Green Chemistry Challenge
The Presidential Green Chemistry Challenge Awards promote the environmental and economic benefits of developing and using novel green chemistry. These prestigious annual awards recognize chemical technologies that incorporate the principles of green chemistry into chemical design, manufacture, and use.

## Slide 88
Engelhard Co
Shaw Industries
CSI
PPG
Dow AgroSciences
Dow AgroSciences
Rohm and Haas
Albright
and Wilson
Rohm and Haas
Designing Safer Chemicals
Buckmann Laboratories
DuPont
Cargill Dow
Novozymes
Bayer Corporation
Nalco Chemical Company
Argonne National Labs
Imation
Dow
Solvents and Reaction Conditions
Bristol-Myers Squibb Co
Sud-Chemie
Pfizer
Bayer Corporation
Roche Colorado
Lilly Research Laboratories
Flexsys America
BHC Company
Pharmacia
Synthetic Pathways
Jeneil Biosurfactants
AgraQuest
SC Fluids
Eden Bioscience
RevTech
Biofine
PYROCOOL Technologies
Legacy Systems
Donlar Corporation
Small Business
Charles Eckert
&
Charles Liotta
Richard Gross
Eric Beckman
C.-J. Li
Chi Hue Wong
Terry Collins
Barry Trost, Karen Draths & John Frost
Joseph DeSimone
Mark Holzapple
Academic
2004
2003
2002
2001
2000
1999
1998
1997
1996
Archer Daniels Midland
BASF
Archer Daniels Midland & Merck
Metabolix
Robin Rogers
2005
SC Johnson
Codexis
Merck
Akron Cons.
&
Nupro Tech.
Galen Suppes
2006
Designing Safer Chemicals
Solvents and Reaction Conditions
Synthetic Pathways
Small Business
Academic
Cargill
Headwaters Technology
Columbia Forest
Hercules
NovaSterilis
Michael Krische
2007
DOW AgroScience
Nalco
Battelle
SIGNa
RobertMaleczka &
Milton Smith
2008
P&G
&
Cook
CEM
Eastman
Virent Energy
Krzysztof Matyiaszewski
2009
Clarke
Merck
Codexis
Dow
BASF
James Liao
2010
LS9, Inc
Sherwin Williams
Krayton Performance Polymers
Genomatica
BioAmber
Bruce Lipshutz
2011
Buckman
Cytec
Codexis
Robert Waymouth
&
Geoffrey Coates
2012
Elevance
Cargill
Dow
Life Technologies
Richard Wool
2013
Faraday Technology
The Solberg Co.
QD Vision
Solazyme
Shannon Stahl
2014
Amyris
Hybrid Coatings Technologies
Soltex
LanzaTech
Eugene Y.-X. Chen
2015
Renmatix
Newlight Technologies
Dow
AgroSciences
CBI &
Albemarle
Paul Chiric
2016
Verdezyne
2017
US Presidential Green Chemistry Challenge
Dow
Papierfabrik August Koehler
Amgen & Bachem
Merck & Co
Eric Schelter
UniEnergy Technologies

## Slide 89: More examples available!
Presidential Green Chemistry Challenge Winners
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-winners
How Industrial Applications in Green Chemistry Are Changing Our World (white paper) by American Chemical Society

## Slide 90
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE