## Slide 1: 12 Principles of Green Chemistry
Lecture #3
Date:
Course #

## Slide 2: Outline: 12 Principles of Green Chemistry
1. Waste Prevention
2. Atom Economy
3. Less Hazardous Chemical Synthesis.
4. Designing Safer Chemicals.
5. Safer Solvents and Auxiliaries.
6. Design for Energy Efficiency.
7. Use of Renewable Feedstocks.
8. Reduce Derivatives.
9. Catalysis.
10. Design for Degradation.
11. Real-time Analysis for Pollution Prevention.
12. Inherently Safer Chemistry for Accident Prevention.
Anastas, P. T.; Warner, J.C. Green Chemistry: Theory and Practice, Oxford University Press,1998

## Slide 3: 12 Principles of Green Chemistry
Anastas, P. T.; Warner, J.C. Green Chemistry: Theory and Practice, Oxford University Press,1998
The principles address:
  Toxicity
    - Reducing the hazard
  Feedstocks
    - Use of renewable resources
  Designing safer products
    - Non toxic products by design
  Biodegradability
    - Enhancing breaking down at the end of life
  Energy
    - Reducing the energy needs
  Accidents
    - Eliminating accidents
  Efficiency
    - Shorter processes and synthesis

## Slide 4: Isn’t This How It’s Done Now?
Entire industries are geared toward cleaning up after wasteful chemical syntheses
Today’s scientific literature is filled with synthetic pathways that are inefficient in terms of design
Reagents are seldom selected with regard to hazard
Industrial chemicals do not have minimal hazard as a performance criterion
Persistence of chemicals in the biosphere and in our bodies is a major global health issue (250 chemicals are still present since 1945)
The vast majority of organic chemicals are made by depleting (non-renewable) feedstocks
Our chemical industry deals with safety through engineering and security through barricades.
Currently:

## Slide 5: Benefits of Green Chemistry?
The environment:
Human health:
The economy:
For sustainability:
For science:
  Products which will biodegrade and won’t persist in the environment
  Products with won’t cause toxicity to humans
  Novel products which boost competitiveness
Products made from renewable resources
  Fundamental new insights

## Slide 6: Benefits of Green Chemistry?
Defense and aerospace
Adhesives
Coatings
Corrosion, inhibitors
Automotive
Solvents
Polymers
Fuels
Household cleaners
Surfactants
Fragrances
Dyes
Cosmetics
Builders
Chelating agents
Dyes
Agriculture
Pesticides
Fungicides
Fertilizers
Electronics
Solder
Housings
Displays
Pharmaceuticals
Specialty Chemicals
Academic Research Labs
Maybe even your
chemistry lab
Notes: Add examples in lesson plan for products in each industry.

## Slide 7: Benefits of Green Chemistry?
A fundamental change of thinking
Green Chemistry moves our consideration of how to deal with environmental problems from the circumstantial to the intrinsic.
Hazard must be recognized as a flaw in the designing process.
Circumstantial
  - Use
  - Exposure
  - Handling
  - Treatment
  - Protection
  - Recycling
  - Costly
Intrinsic
  - Molecular design for reduced toxicity
  - Reduced ability to manifest hazard
  - Inherent safety from accidents or terrorism
  - Increased potential profitability

## Slide 8: Benefits of Green Chemistry?
Green chemistry focuses on reducing risk by reducing hazard.
- If there is no hazard, exposure becomes irrelevant.
The traditional approach to hazards focuses on reducing risk by minimizing exposure.
- For example, wearing personal protective equipment or space ventilation if the chemical is volatile.
Risk = Hazard x Exposure
Green chemistry and engineering focus on reducing risk by reducing hazard.
Notes: You will always be exposed to materials in some fashion, however, we can try control the hazards associated to it.

## Slide 9
The 12 Principles
of
Green Chemistry

## Slide 10: Waste Prevention
It is better to prevent waste than to treat or clean up waste after it is formed.
A + B
P + W
Ways to prevent waste?
Avoid the generation of W.
Find alternatives to A & B to improved overall efficiency of a reaction.
Incorporate better catalysts to push the reaction to full completion

## Slide 11: Waste Prevention
Industry sector | Annual production (t) | E-factor | Waste produced (t)
Oil refining | 106-108 | Ca. 0.1 | 105 – 107
Bulk chemicals | 104-106 | <1–5 | 104 – 5 × 106
Fine chemicals | 102−104 | 5–50 | 5 × 102 − 5 × 105
Pharmaceuticals | 10–103 | 25–100 | 2.5 × 102 − 105
Environmental Factor (E-Factor) among the scientific community
Sheldon, R. Chem Tech, 1994, 24, 38

## Slide 12: Waste Prevention
Case study: Sildenafil citrate production
Sildenafil citrate, commonly known as Viagra, is a selective inhibitor of phosphodiesterase 5 (PDE5). This new drug immediately became a major seller, achieving sales of more than $1 billion during its first year on the market. With such a rapid sales take off it was critical that the environmental performance of the synthesis was good from the outset.
Conventional sildenafil citrate synthesis included:
11 step synthesis, which gave a 4.2% overall yield.
Tin chloride, a heavy metal and a major environmental polluter.
The use of stoichiometric quantities of thionyl chloride in a solvent. This has a high environmental impact.
Hydrogen peroxide, which causes burns upon skin contact and is a fire and transportation hazard, especially when in contact with organic materials.
Produced over 1300 L of waste per 1 kg of product.
The amount of organic waste produced by the sildenafil citrate processes at various time points
Dunn, P.J et al Green Chem., 2004, 6, 43-48

## Slide 13: Waste Prevention
Alternative production of sildenafil citrate:
Average yield of last three steps = 97% yield.
Reduction of the ratio of solvent waste/kg product over 17 years from 1300 L/kg to only 7 L/kg by minimizing solvent use, increasing solvent recovery, improving solvent selection, and telescoping steps.
Only the solvents t-butanol, ethyl acetate, 2-butanone, and a trace of toluene still require disposal.
Dunn, P.J et al Green Chem., 2004, 6, 43-48
Case study: Sildenafil citrate production

## Slide 14: Waste Prevention
Conventional method of obtaining phenols from petroleum:
Petroleum
Phenols (benzene, toluene, xylenes)
The method is not sustainable – it is dependent on depleting resources.
Case study: Phenols
Phenols are widely used in household products and as intermediates for industrial synthesis. They are often referred to as drop-in platform chemicals.
Image: Pixabay

## Slide 15: Waste Prevention
Alternative production of phenols from biomass waste using depolymerization:
This method uses abundant product (waste) as a starting material.
Phenols
Biomass
Case study: Phenols
Image: Pixabay

## Slide 16: Waste Prevention
Case study: Production of ethylene oxide
Ethylene oxide is used as an intermediate in the production of several industrial chemicals, the most notable of which is ethylene glycol. It is also used as a fumigant in certain agricultural products and as a sterilant for medical equipment and supplies.
Conventional ethylene oxide synthesis included:
A 2-step synthesis with a chlorohydrin intermediate.
For each kilogram of product, 5 Kg of waste were disposed.

## Slide 17: Waste Prevention
Alternative production of ethylene oxide:
Use of molecular oxygen removes the need for chlorine.
New process generates more than 16 times less waste than the original one, and eliminates the formation of waste water.
Case study: Production of ethylene oxide
Image: Wikimedia Commons, Author: LHcheM

## Slide 18: Waste Prevention
Case study: Revalorization of biofuel byproducts
When byproducts cannot be avoided, other innovative solutions should be considered. One productive solution is to seek an industrial ecology approach where the waste can become a new raw material with significant value for another process as it re-enters the life-cycle. This approach is currently being applied to the production of biofuel.
+
Waste
+
Material
Energy
Waste
Energy
Biofuel
1.
2.

## Slide 19: Atom Economy
Synthetic methods should be designed to maximize the incorporation of all materials used in the process into the final product.

## Slide 20: Atom Economy
More Simply…
Ideally all atoms from the reagents are incorporated into a final product.
  High atom economy ↔ less waste production
There are no co-products or byproducts in the reaction.
The molecular waste is therefore reduced.

## Slide 21: Atom Economy
Example: Epoxidation of styrene
Assume 100% yield.
100% of the desired epoxide product is recovered.
100% formation of the co-product: m-chlorobenzoic acid.
A.E. of this reaction is 23%.
77% of the products are waste.
desired epoxide
waste
styrene

## Slide 22: Atom Economy
Conventional method of styrene production:
Use of benzene, a known carcinogen, as a starting material.
High temperature (800-950 0C).
Case study: Styrenes
Styrenes are precursors to polystyrene. Polystyrene is one of the most widely used plastics, the scale of its production being several million tons per year.

## Slide 23: Atom Economy
Alternative method of styrene production from butadiene using Diels-Alder reaction:
Diels-Alder reaction = 100% atom economy.
Use of non-toxic starting material.
Case study: Styrenes

## Slide 24: Atom Economy
Traditional synthesis of
ibuprofen was inefficient:
6 stoichiometric steps
<40% atom utilization
Case study: Ibuprofen

## Slide 25: Atom Economy
Catalytic synthesis of ibuprofen using Green Chemistry:
3 catalytic steps
80% atom utilization (99% with recovered acetic acid)
Case study: Ibuprofen

## Slide 26: Less Hazardous Chemical Synthesis
Whenever practicable, synthetic methodologies should be designed to use and generate substances that possess little or no toxicity to human health and the environment.

## Slide 27: Less Hazardous Chemical Synthesis
Ideally, non-toxic substances are used to synthesize a chemical product.

## Slide 28: Less Hazardous Chemical Synthesis
Organic chemistry’s synthetic toolbox has been significantly improved over the past decade by the innovative work of green chemists and the many new reactions that have been developed.
Cascade, or tandem reactions, such as C–H activation, metathesis, and enzymatic reactions are some excellent examples of the cleaner and more efficient synthetic tools that are now available to organic chemists.

## Slide 29: Less Hazardous Chemical Synthesis
Case study: Synthesis of adipic acid
Adipic acid (AA), also referred to as hexanedioic acid, is one of the most produced commodity chemicals worldwide. With a projected global market size of more than 7 billion US dollars by 2019, AA is a versatile building block for an array of processes in the chemical, pharmaceutical and food industries. Its primary use is as a precursor for the synthesis of the polyamide Nylon-6,6.
Conventional synthesis of adipic acid:
Uses benzene, a known carcinogen, as a starting material.
Involves oxidation with an excess of HNO3, and production of greenhouse gas nitrous oxide (N2O), the latter accounting for approximately 5–8% of the worldwide anthropogenic N2O emissions.

## Slide 30: Less Hazardous Chemical Synthesis
Alternative synthesis of adipic acid:
Development of biocatalytic processes for producing adipic acid and catechol from sugars.
Biocatalytic process using yeast converts sugars to cis,cis-muconic acid, and this intermediate stage allows ready access to catechol and adipic acid.
Uses water as solvent at ambient temperature and pressure.
Case study: Synthesis of adipic acid
Raj, K et al. Biocatalytic production of adipic acid from glucose using engineered Saccharomyces cerevisiae. Metabolic Engineering Communications. 6, 2018, 28-32

## Slide 31
Conventional paper bleaching with Chlorine dioxide (ClO2):
Produces unacceptable quantities of chlorinated pollutants.
Many of these pollutants are exceptionally toxic.
Alternative technology for paper bleaching with TAML/H2O2:
Alternative catalytic breakdown of H2O2 provides the oxidative equivalent.
Lower temperature and time requirements.
Case study: Paper Bleaching
Image: Wikimedia Commons, Author: Sammutawe
Less Hazardous Chemical Synthesis

## Slide 32
Designing Safer Chemicals
Chemical products should be designed to preserve efficacy of the function while reducing toxicity.

## Slide 33: The modern motto of toxicology:
“Everything is toxic. It is simply depends on the dose”
Often otherwise phrased as
“The dose makes the poison.”
Designing Safer Chemicals
Risk = Hazard x Exposure
Green chemistry and engineering focus on reducing risk by reducing hazard.

## Slide 34
Hazard types to avoid:
  Toxicological/Eco-toxicological
    Carcinogenicity
    Reproductive
    Developmental
    Neurological
    Global warming potential
    Ozone depleting potential
    Bioaccumulation
    Persistence
  Physical
    Explosivity
    Flammability
    Corrosivity
Physical/Chemical Properties to consider:
  Water solubility
  Log Kow
  Volatility
  Molar volume
  Aspect ratio
  Radical formation
  Nucleophilicity
  Electrophilicity
  pH/pKa
  Surface area
  Reducing potential
  Oxidizing potential
  Polarizability
Designing Safer Chemicals

## Slide 35
Chemists can design chemicals which have reduced toxicity by:
Manipulation of chemical bonds, chemical functional groups.
  Reactive functional groups have a greater potential to be toxic. Removing these groups is likely to reduce toxicity.
Elimination of the molecular initiating event that activates pathway.
  While difficult to achieve, if the chemical is modified not to interact with the biological pathway, no biological effect is triggered and the toxicity can be avoided.
Reducing or eliminating bioavailability.
  If a chemical does not absorb into a body, it cannot cause harm.
Designing Safer Chemicals

## Slide 36
Conventional use of organotin compounds as antifoulants:
TBTO and other organotin antifoulants have long half-lives in the environment (the half-life of TBTO in seawater is over 6 months).
They bioconcentrate in marine organisms (the concentration of TBTO in marine organisms has been found to be up to 104 times greater than in the surrounding water).
Organotin compounds are chronically toxic to marine life and can enter food chain.
They are bioaccumulative.
Tributyltin oxide (TBTO)
Case study: Antifoulants
Antifoulants are generally dispersed in the paint as it is applied to the hull of a ship. Organotin compounds such as tributyltin oxide (TBTO) have traditionally been used. TBTO works by gradually leaching from the hull and killing the fouling organisms in the surrounding area.
Designing Safer Chemicals

## Slide 37
Alternative antifoulants:
Sea-Nine® 211 works by maintaining a hostile growing environment for marine organisms. When organisms attach to the hull (treated with DCOI), proteins at the point of attachment with the hull react with the DCOI. This reaction with the DCOI prevents the use of these proteins for other metabolic processes. The organism detaches itself and searches for a more hospitable surface to grow upon.
Only organisms attached to hull of ship are exposed to toxic levels of DCOI.
Readily biodegrades once leached from ship (half-life is less than one hour in sea water).
Designing Safer Chemicals
Case study: Antifoulants

## Slide 38
In 2014, the Solberg Company earned an award for its halogen-free RE-HEALING Foams for use in fighting fires. Traditionally, firefighting foams used fluorinated surfactants, persistent chemicals that have the potential for negative environmental impacts.
The RE-HEALING firefighting foam concentrates use a blend of non-fluorinated surfactants and sugars. This works well and with far less environmental impact.
Control, extinguishing time, and burnback resistance are paramount to the safety of firefighters everywhere, and the new foams have excellent performance in each category. The RE-HEALING Foams also achieve full regulatory compliance with existing fire protection standards.
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-2014-designing-greener-chemicals-award
Designing Safer Chemicals

## Slide 39
Conventional use of agricultural pesticide and a malarial control agent Dichlorodiphenyltrichloroethane (DDT):
DDT
Carcinogenic.
The threat to wildlife - especially birds – has almost led to the extinction of a bald eagle population.
Case study: Pesticides
Image Source: http://www.avoidingregret.com/2014/06/photo-essay-eggs-and-nests-of-bird.html
Designing Safer Chemicals
Notes: DDT was used in the second half of World War II to control malaria and typhus among civilians and troops. After the war, DDT was made available for use as an agricultural insecticide and its production and use duly increased. Müller was awarded the Nobel Prize in Physiology or Medicine "for his discovery of the high efficiency of DDT as a contact poison against several arthropods" in 1948
Unfortunately it’s effect on birds was not tested. Research have shown that for certain species, DDT causes the thinning of eggshells which led almost to species extinction.

## Slide 40
Alternative (and natural) use of Spinosad for insect control:
  Produced by bacteria Saccharopolyspora spinosa.
  Isolated from Caribbean soil samples (sugar mill).
  It selectively targets nervous system of insects.
  Demonstrates high selectivity, low mammalian toxicity, and a good environmental profile.
  Dow AgroSciences
  Saccharopolyspora spinosa
Toxicity scorecard
Rat: LD50>5000 mg/kg
Duck: LD50>5000 mg/kg
Fish: LC50-96h=30.0 mg/L
Bee: LD50=0.0025 mg/bee
Designing Safer Chemicals
Case study: Pesticides

## Slide 41
Safer Solvents and Auxiliaries
The use of auxiliary substances (solvents, separation agents, etc.) should be made unnecessary whenever possible and, when used, innocuous.

## Slide 42
Solvents account for the vast majority of mass wasted in syntheses and processes. Moreover, many conventional solvents are toxic, flammable, and/or corrosive.
Solvents volatility and solubility have contributed to air, water and land pollution, have increased the risk of worker exposure, and have led to serious accidents.
Recovery and reuse, when possible, is often associated with energy-intensive distillation and sometimes cross contamination. In an effort to address all those shortcomings, chemists have started to search for safer solutions.
Safer Solvents and Auxiliaries
Image: Adobe Stock

## Slide 43
Problematic organic solvents
No Solvent Supercritical fluids
Water solvent Ionic liquids
Avoidance
Environmentally
benign and safe
Easily separable, safe
Zero
Volatility
Greener alternatives
Safer Solvents and Auxiliaries

## Slide 44
Case study: Coffee decaffeination
Conventional method of coffee decaffeination:
Coffee decaffeination was performed in a chlorinated organic solvent, dichloromethane (DCM), exposure to which can lead to headaches, mental confusion, nausea, vomiting, dizziness and fatigue.
Coffee beans were heated with steam and then exposed to DCM for decaffeination.
Image: Wikimedia Commons, Coffee Mechanical Separator, Aquapulp
Safer Solvents and Auxiliaries

## Slide 45
Soaking green coffee beans in water doubles their size, allowing the caffeine to dissolve into water inside the bean.
Caffeine removal occurs in an extraction vessel (70 feet high,10 feet in diameter), suffused with carbon dioxide at roughly 90 °C and 250 atm. Caffeine diffuses into this scCO2. The beans enter at the top of the chamber and move toward the bottom over 5 hours.
Decaffeinated beans at the bottom of the vessel are removed, dried and roasted.
Recovery of dissolved caffeine occurs in an absorption chamber. A shower of water droplets leaches the caffeine out of the supercritical carbon dioxide. The caffeine in this aqueous extract is then often sold to soft-drink manufacturers and drug companies. The purified carbon dioxide is recirculated for further use.
Alternative method for coffee decaffeination:
Zosel, K. Practical Applications of Material Separation with Supercritical Gases. Angew. Chem., Int. Ed. 1978, 17, 702-709
Safer Solvents and Auxiliaries
Case study: Coffee decaffeination

## Slide 46
Delicate biomedical materials such as vaccines and tissues are conventionally sterilized with ethylene oxide - a carcinogenic, mutagenic, toxic, and flammable gas - or with gamma radiation, which is lethal to all cells.
Both methods damage the materials they are sterilizing.
Ethylene oxide persists in tissue.
Case study: Medical sterilization
Conventional medical sterilization:
Image: Svetlana Pohovey, 359th Medical Group, U.S. Air Force photo/Staff Sgt. Kevin Iinuma
Safer Solvents and Auxiliaries

## Slide 47
Development of a supercritical carbon dioxide (scCO2) based method for sterilization of biological material.
NovaSterilis sterilization uses scCO2, peracetic acid, and small amounts of water at low temperatures and modest pressure to achieve rapid sterilization of sensitive biomaterials.
NovaSterilis Inc.
Alternative medical sterilization:
Safer Solvents and Auxiliaries
Case study: Medical sterilization

## Slide 48
Case study: Replacing dichloromethane (DCM) in chromatography
Amgen’s Green Solvents for Chromatography in practice. If a compound suitably elutes in 5% DCM–MeOH, the bar chart predicts that 60% 3 : 1 EtOAc : EtOH in heptanes or 40% i-PrOH in heptanes would be a suitable starting point to evaluate greener solvent alternatives.
Amgen developed a guide to replace DCM with greener alternatives. DCM is known to be associated with respiratory and cardiovascular toxicity in humans, carcinogenicity, and genotoxicity.
The guide on the right compares the eluting power of different greener solvent mixtures with reference to DCM-Methanol.
Safer Solvents and Auxiliaries
Notes: A convenient guide to help select replacement solvents for dichloromethane in chromatography, Joshua P. Taygerly, Larry M. Miller, Alicia Yee and Emily A. Peterson, Green Chem., 2012, DOI: 10.1039/C2GC36064K

## Slide 49
Zoloft® is an anti-depressant and was once one of the best selling pharmaceuticals on the market.
Conventional sertraline synthesis:
Synthesis was a three step process.
Used 4 hazardous solvents (methylene chloride, tetrahydrofuran, toluene, and hexane).
Zoloft®
Case study: Manufacturing process for sertraline, the active ingredient in the popular drug Zoloft®
Safer Solvents and Auxiliaries

## Slide 50
The process was streamlined to a single step that is carried out in ethanol, a much less toxic solvent.
The new process is also catalytic, cutting down on starting materials by 60%, 45%, and 20% for the three components of the reaction.
The combined steps eliminated 310,000 pounds of titanium tetrachloride, 220,000 pounds of 50% sodium hydroxide, 330,000 pounds of 35% hydrochloric acid waste, and 970,000 pounds of solid titanium dioxide waste per year.
Pfizer, Inc
Alternative sertraline synthesis:
Image: Wikimedia Commons, Author: Ragesoss
Safer Solvents and Auxiliaries
Case study: Manufacturing process for sertraline, the active ingredient in the popular drug Zoloft®

## Slide 51
Design for Energy Efficiency
Energy requirements should be recognized for their environmental and economic impacts and should be minimized. Synthetic methods should be conducted at ambient temperature and pressure.

## Slide 52
Most energy is used for heating, cooling, separations and pumping.
Ideally, all reactions are performed at ‘ambient’ conditions – room temperature and atmospheric pressure – in order to minimize energy usage.
Image: Wikimedia Commons, Janicki Omni Processor Pilot Plant in Dakar, Senegal, Author: Janicki Bioenergy
Design for Energy Efficiency

## Slide 53
Atorvastatin, a cholesterol-lowering drug, suffers from an energy-demanding synthesis as a result of two cryogenic reactions at - 70 oC.
New biocatalytic synthesis uses enzyme DERA and shortens the process by removing two energy intensive chemical steps.
Case Study: Atorvastatin
Design for Energy Efficiency
Notes: Deoxyribose-5-phosphate Aldolase as a Synthetic Catalyst'

## Slide 54
Sono-, microwave-, and photo-assisted chemistry are known to save energy, improve reaction time, and catalytic activity.
Sonochemistry:
Uses of high frequency (20-100 kHz) sound waves to promote chemical reaction.
The collapse of bubbles formed in a solution generates a very high temperature and a higher pressure than conventional heating.
Used in the production of triglycerides from methyl transesterification.
Microwave:
Uses a high-frequency electric field to heat or cool the local environment with electrical charges.
Avoids unnecessarily prolonged residence time at a given temperature.
Photo-assisted:
Naturally occurring, such as using the sun as a catalyst.
Used in photo-driven acylation for the production of valuable synthetic intermediates and commercial fragrances in bulk.
Used by BASF to develop automotive primer coating, a precursor readily able to be crosslinked under photo irradiation, as opposed to its conventional energy-intensive thermally driven variation.
Design for Energy Efficiency

## Slide 55
Use of Renewable Feedstocks
A raw material or feedstock should be renewable rather than depleting whenever technically and economically practical.

## Slide 56
Petroleum Products [Hydrocarbons]
Biomaterials [Carbohydrates, Proteins, Lipids]
Highly Functionalized Molecules
Functionalized Compounds [Olefins, Alkylchlorides]
Highly Functionalized Molecules
Use of Renewable Feedstocks

## Slide 57
Chart: Biomass production in nature: 180 billion metric tons/year
| Carbohydrates | Lignin | Fats, proteins, terpenes, etc.
Sales | 75 | 20 | 5
Only about 4% utilized by humans
(food, ethanol, sweeteners)
Nature’s richest source of aromatic carbon. Used in polymers, adhesives, production of phenolic chemicals.
Converted into polymers, lubricants, and detergents.
Building blocks for a diverse chemical platform.
Use of Renewable Feedstocks

## Slide 58: Case study: Producing polymers from renewable resources (PHAs)
The development of microorganisms that produce polyhydroxyalkanoates (PHAs) are from renewable feedstocks such as cornstarch and cellulose hydrolysate.
The microorganisms have proven to be applicable to conventional commercial equipment and can even be recycled using this same equipment.
They can be used in biodegradable products, such as credit cards.
They are comparable with polyolefins - which are made from petroleum feedstocks - in terms of strength, melting point, and can be manufactured with the existing equipment.
Polyhydroxyalkanoates (PHAs) are a broadly useful family of natural, environmentally friendly, and high-performing, bio-based plastics.
Metabolix
Image: Alpha Stock Images, Author: Nick Youngson
Use of Renewable Feedstocks

## Slide 59
Carpet tile backings were usually comprised of bitumen, polyvinyl chloride (PVC), or polyurethane - which are all derived from petroleum.
PVC - the most common base for carpet tile backings - is made from vinyl chloride, a toxic substance which releases toxic dioxins and hydrochloric acid as byproducts upon combustion.
Case study: Carpet tile backings
Conventional synthesis:
Image: Wikimedia Commons, Swatches of Carpet, Author: Quadell
Use of Renewable Feedstocks

## Slide 60
Shaw Industries, Inc
Alternative synthesis:
The development of a new, recoverable carpet backing.
Utilizing a combination of low-toxicity polyolefin resins, the backing can be separated from any fiber and recovered by elutriation, grinding, and air separation.
Collection, transportation, elutriation, and reprocessing is less expensive than using fresh starting material.
Image: Flickr, Author: Emily May
Use of Renewable Feedstocks
Case study: Carpet tile backings

## Slide 61
Conventional synthesis:
Over 400 million pounds of toner are consumed in the U.S. each year.
Conventional petroleum-based resin toners are difficult to remove from paper, making paper recycling more intensive.
Case study: Development and commercialization of toners
Image: Wikimedia Commons, Black toner container, Author: Adamantios
Use of Renewable Feedstocks

## Slide 62
Alternative process:
The development of a novel, bioderived printer toner that is easier to deink from paper.
This technology incorporates functional groups in their toners that are susceptible to chemical degradation for recycling.
These toners are biobased, derived from soybean oil and corn.
At 25% market penetration, this technology could reduce CO2 emissions by 360,000 tons/year.
Battelle
Use of Renewable Feedstocks
Case study: Development and commercialization of toners

## Slide 63
Case study: Production of levulinic acid
Levulinic acid is used as a precursor for pharmaceuticals, plasticizers, and various other additives. It is also widely used as a building block or starting material for a wide number of compounds.
Conventional synthesis:
Obtained by heating hexoses (glucose, fructose) or starch in dilute hydrochloric acid or sulfuric acid.
The yield depends on the nature of the acid, acid concentration, temperature, and pressure.
The reaction also produces hard to remove by-products.
Use of Renewable Feedstocks

## Slide 64
Paper mill
sludge
Levulinic acid
Municipal solid waste
and waste paper
Agricultural
residues,
waste wood
Alternative synthesis:
Levulinic acid can be obtained from paper mill sludge, agricultural and municipal waste and paper.
Utilizes a high-temperature, dilute-acid hydrolysis process that converts cellulosic biomass.
Use of Renewable Feedstocks
Case study: Production of levulinic acid (Biofine, Inc)
Image Source: Masx Pixel, Pixbay, Flickr
Notes: Image Sources: https://www.maxpixel.net/Manure-Wheelbarrow-Wheelbarrows-Waste-Agriculture-2168726
https://pixabay.com/en/files-paper-office-paperwork-stack-1614223/
https://www.flickr.com/photos/pnnl/3365375855

## Slide 65
Reduce Derivatives
Unnecessary derivatization (blocking group, protection/deprotection, temporary modification of physical/chemical processes) should be avoided whenever possible.

## Slide 66
Substrate
Product
Substrate
Intermediate A
Intermediate B
Intermediate C
Intermediate D
Intermediate E
Product
Conventional approach
Green Chemistry approach
Reduce Derivatives
Notes: Whenever possible, limit number of steps and unnecessary transformations. Avoid the use of protecting groups as it requires extra reagents and generates more waste.

## Slide 67
Synthesis of 6-aminopenicillanic acid – core moiety of penicillin
Conventional synthesis of 6-aminopenicillanic acid using 3 steps and intermediate products:
Alternative synthesis using enzyme and fewer derivatives:
Case study: 6-aminopenicillanic acid
Reduce Derivatives

## Slide 68
Catalysis
Catalytic reagents (as selective as possible) are superior to stoichiometric reagents.

## Slide 69
Catalysts can facilitate complex reactions by:
  Lowering the activation energy of the reaction.
  Reducing temperature necessary to achieve a reaction.
  Controlling the site of the reaction (selectivity enhancement).
Image source: Adobe stock
Catalysis
Notes: Catalysts lower the activation (threshold energy) in the reaction.

## Slide 70: Heterogeneous vs Homogeneous
Catalysis
Distinct solid phase
Readily regenerated & recycled
Readily separated
Rates not as fast
Diffusion limited
Sensitive to poisons
Lower selectivity
Long service life
High energy process
Poor mechanistic understanding
Same phase as rxn medium
Expensive and/or difficult to separate
Difficult to separate
Very high rates
Not diffusion controlled
Robust to poisons
High selectivity
Short service life
Mild conditions
Mechanisms well understood

## Slide 71: Heterogeneous vs Homogeneous
Distinct solid phase
Readily regenerated & recycled
Readily separated
Rates not as fast
Diffusion limited
Sensitive to poisons
Lower selectivity
Long service life
High energy process
Poor mechanistic understanding
Green
catalyst
Same phase as rxn medium
Expensive and/or difficult to separate
Difficult to separate
Very high rates
Not diffusion controlled
Robust to poisons
High selectivity
Short service life
Mild conditions
Mechanisms well understood
Catalysis

## Slide 72
  Dartt and Davis
Case study: Green naproxen synthesis
  97% yield in three steps
Nonsteroidal anti-inflammatory drug (NSAID) of the propionic acid class (the same class as ibuprofen) that relieves pain, fever, swelling, and stiffness; COX inhibitor
Catalysis
Notes: cyclooxygenase

## Slide 73
Polyoxometalate (POM) catalysts
  - non-toxic, inorganic cluster compounds
  - selectively delignify wood
  - utilize only air and water
Allows use of oxygen instead of chlorine as the whitener of paper pulp and water as the solvent
Generates only CO2 and H2O, instead of chlorinated organics
  Hill, Emory University;
  Hill et al, Nature 2001, 414, 191–195
Case study: Paper production
1st step
2nd step
3rd step
4th step
Catalysis

## Slide 74
One of Dow Chemical’s awards is for a green catalyst that reduces the environmental footprint associated with producing propylene oxide, one of the biggest volume industrial chemicals in the world. The Hydrogen Peroxide to Propylene Oxide (HPPO) process, which was developed jointly with BASF, serves as a chemical building block for a vast array of products including detergents, polyurethanes, de-icers, food additives, and personal care items. The new process reduces the production of wastewater by as much as 70–80 percent and reduces the use of energy by 35 percent over conventional technologies.
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-2010-greener-synthetic-pathways-award
propylene oxide molecule
Image: Wikipedia, propylene oxide molecule, Author: Jynto
Catalysis

## Slide 75
A new catalyst developed by pharmaceutical companies Merck and Codexis for the green synthesis of sitagliptin - the active ingredient in the type 2 diabetes treatment Januvia™ - may also be useful in the manufacturing of other drugs. For example, recent clinical trial showed that it may help patients with acute coronary syndrome.
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-2010-greener-reaction-conditions-award
sitagliptin
Image: Wikipedia, sitagliptin, Author: NEUROtiker
Catalysis

## Slide 76
An example of green catalysts with the potential to reduce the pharmaceutical industry’s environmental impact is the powerful series of tetra-amido macrocyclic ligand (TAML) catalysts modelled on natural peroxidase enzymes developed by Terry Collins of Carnegie Mellon University. Collins thinks that using the catalysts at a late stage in the sewage treatment process would allow them to break down a wide variety of chemical residues - including those from Lipitor, Prozac, Zoloft, the contraceptive pill, and more - before they enter the environment.
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-1999-academic-award
Image: Wikicommons, Pipes of the Minsk sewage treatment plant, Author: Homoatrox
Catalysis

## Slide 77
Design for Degradation
Chemical products should be designed so that at the end of their function they do not persist in the environment and instead break down into innocuous degradation products.

## Slide 78
Early examples:
  Sulfonated detergents
    Alkylbenzene sulfonates – 1950’s & 60’s
    Foam in sewage plants, rivers, and streams
    Persistence was due to long alkyl chain
    Introduction of an alkene group into the chain increased degradation
  Chlorofluorocarbons (CFCs)
    Do not break down, persist in atmosphere and contribute to destruction of the ozone layer.
  DDT
    Bioaccumulate and cause thinning of egg shells
Design for Degradation

## Slide 79
Conventional plasticizers, such as DiNP, are an additive used to soften plastics:
DiNP exposure has been linked to liver toxicity, endocrine disruption, and carcinogenicity.
The additives persist in the environment.
Case study: Plasticizers
Plasticizers for plastics are additives, most commonly phthalate esters in PVC applications. Almost 90% of plasticizers are used in PVC, giving this material improved flexibility and durability. The majority of PVC is used to produce films and cables.
Design for Degradation

## Slide 80
Alternative plasticizers, such as isosorbide diester, can be derived from starch:
Offers 1 to 1 substitution of DiNP in plastics.
Isosorbide diester is thermally stable and biodegradable.
Design for Degradation
Case study: Plasticizers

## Slide 81
Conventional plastics (PET) are made from petroleum:
PET Plastic persists in the environment
It is made from depleting resources
high temperature
vacuum
catalyst
Petroleum
Case study: Plastics
Design for Degradation

## Slide 82
Synthesis of PolyLactic Acid (PLA) from starch:
The development of a biobased, compostable, and recyclable polylactic acid (PLA) polymer that uses 20–50 percent less fossil fuel resources than comparable petroleum-based polymers.
It is the first family of polymers derived entirely from renewable resources that can compete cost-effectively with traditional fibers and plastic packaging materials.
The manufacturing process consists of three solvent-free steps that lead to the production of lactic acid, lactide, and PLA high polymer with very high yields and internal recycling schemes that reduce waste.
PLA is fully biodegradable or can be readily hydrolyzed into lactic acid for recycling back into the process.
Cargill Dow LLC
Alternative process:
Design for Degradation
Case study: Plastics

## Slide 83
Case study: Fire extinguishers
Conventional approaches:
Chemical additives or alternatives to water for firefighting applications can have negative long-term environmental and health effects.
Halon gases are destructive to the ozone layer.
Aqueous film-forming foams release both toxic hydrofluoric acid and fluorocarbons when used.
Fluorosurfactant compounds are resistant to microbial degradation, often leading to contamination of groundwater supplies and failure of wastewater treatment systems.
Image: Wikimedia Commons, Author: Caduser2003
Design for Degradation

## Slide 84
The development of a fire extinguishing foam that is nontoxic and highly biodegradable.
PYROCOOL F.E.F. (Fire Extinguishing Foam) is an alternative formulation based on a biodegradable surfactant.
PYROCOOL F.E.F. has a low application volume.
Extinguishing an oil tanker fire estimated to take 10 days can be put out in 12.5 minutes.
Alternative production:
Image: Wikimedia Commons, Kyrgyz Republic firefighters, Author: Senior Airman Brett Clashman, U.S. Air Force
Design for Degradation
Case study: Fire extinguishers

## Slide 85
Real-time Analysis for Pollution Prevention
Analytical methodologies need to be further developed to allow for real-time in-process monitoring and control prior to the formation of hazardous substances.

## Slide 86
Real time analysis for a chemist is the process of “checking the progress of chemical reactions as it happens”.
Knowing when your product is “done” can save a lot of waste, time, and energy.
Real-time Analysis for Pollution Prevention
Image sources: Flickr
Notes: Image Sources: https://www.flickr.com/photos/tuchodi/4003359098
https://www.flickr.com/photos/uclmaps/9420857015

## Slide 87: The Role of Analytical Chemistry
Analytical chemistry has been at the heart of the environmental movement since its inception. It’s been used in:
    Identification
    Monitoring
    Measurement
    Characterization
Real-time Analysis for Pollution Prevention

## Slide 88: What Does Green Analytical Chemistry Mean?
Green Chemistry is applicable to all chemical processes, including the methods, protocols and processes of environmental analytical chemistry.
Image: Wikipedia
Real-time Analysis for Pollution Prevention

## Slide 89: Examples of Green Analytical Chemistry Methodologies
Supercritical Fluid Extraction
X-ray fluorescence detection for multi-metal matrix
Solid-phase extraction and micro-extraction
Image Sources: https://www.thermofisher.com, https://www.intechopen.com/books/herbicides-advances-in-research/recent-advances-in-the-extraction-of-triazines-from-water-samples, http://soviethammer.info/thlon/s/supercritical-fluid-extraction-co2/
Real-time Analysis for Pollution Prevention

## Slide 90: Process Analytical Chemistry to Minimize Waste Generation
Through the use of real-time, in-process monitors, sensors, etc., pollution and hazardous waste generation can be prevented rather than simply measured after it is produced.
Solid-acid catalyzed 1-butene/isobutane alkylation process:
  replaces HF and H2SO4 catalysts
  process utilizes supercritical CO2 to prevent coke accumulation in pores of solid catalyst
  on-line GC analysis
Subramaniam, University of Kansas
Ind. Eng. Chem. Res., 2001, 40 (18), pp 3879–3882
Real-time Analysis for Pollution Prevention
Notes: Alkylation of isobutane with n-butenes to form highly branched isoparaffins is an important process in gasoline manufacture. This reaction is currently catalyzed using either liquid hydrofluoric acid or sulfuric acid. Although these liquid acids rapidly catalyze the alkylation reaction, there are a number of drawbacks associated with their use. Solid acids have been studied extensively as possible catalysts for alkylation. However, with solid acid catalysts, the catalyst deactivates rapidly with time on stream. It is been hypothesized and shown that when the reaction is carried in supercritical media, the solid acid catalyst deactivation slows down considerably; however, high temperatures are needed to bring the reaction mixture to supercritical conditions, which results in the formation of undesired products. In this study, the effects of using different operation conditions for alkylation on a USY zeolite were investigated. It was observed that the deactivation rate was slower in supercritical-phase alkylation. Carbon dioxide was used as a diluent to lower the critical temperature of the reaction mixture in the ratio 27/9/1 for carbon dioxide/isobutene/1-butene. The use of diluent favored both alkylate selectivity and coke precursor removal.

## Slide 91: Continuous Flow Reactors
Replacing batch reactors on large, medium, and even small scale has distinct advantages:
Image Sources: http://encyclopedia.che.engin.umich.edu/Pages/Reactors/menu.html, https://www.technologynetworks.com/drug-discovery/product-news/automated-compound-library-production-294622
  Precise control of reaction conditions.
  Reproducible reaction outcome (product purity).
  Minimizes waste, and provides increased safety.
Real-time Analysis for Pollution Prevention

## Slide 92
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-2008-greener-reaction-conditions-award
Case study: Real-time analysis in cooling systems
Conventional Cooling Systems:
They consume large amounts of water.
Microbial growth and mineral scale decrease the efficiency and increase energy consumption of heat-exchange.
However, high levels of biocide to prevent microbial growth increases the risk of leaks in the system.
Biocide and metal-byproducts from corrosion are then released into the environment with the waste water.
Image: Wikimedia Commons, Cooling tower and cooling water discharge at a Philippsburg nuclear power plant, Author: Michael Kauffmann
Real-time Analysis for Pollution Prevention

## Slide 93
In 2008 Naclo Company won the EPA Greener Reaction Conditions Award for their innovative 3D TRASAR® Technology.
Alternative Cooling System with 3D TRASAR® Technology:
The 3D TRASAR® System allows for the real-time monitoring of mineral scale buildup.
This system can also utilize poor-quality water.
3D Scale Control prevents mineral scale formation to increase efficiency.
3D Bio-control performs a real-time check for planktonic and sessile bacteria. This reduces the amount of biocide used since biocides are then added only when necessary, rather than on a set schedule.
The 3D TRASAR® System greatly reduces the amount of wastewater discharged from cooling systems.
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-2008-greener-reaction-conditions-award
Image: Wikipedia, A lavender-colored nonpotable water pipeline in Mountain View, California, Author: Grendelkhan
Real-time Analysis for Pollution Prevention
Case study: Real-time analysis in cooling systems

## Slide 94
Inherently Safer Chemistry for Accident Prevention
Substance and the form of a substance used in a chemical process should be chosen so as to minimize the potential for chemical accidents, including releases, explosions, and fires.

## Slide 95
Approaches to design safer chemistry can include the use of solids or low vapor pressure substances in place of volatile liquids.
Other approaches include avoiding the use of molecular halogens in large quantities.
Continuous flow processes can help to minimize chemical hazards.
Accidents can be avoided by minimizing hazards
Inherently Safer Chemistry for Accident Prevention

## Slide 96
Polyhydroxyamide (PHA):
Can be molded into seats, bins, and wall panels.
It is synthesized under mild conditions.
It decomposes into fire-resistant polybenzoxazole (PBO) and water upon heating.
  Westmoreland, UMass Amherst
Case study: Designing safer polymers for use in airplanes
Image Source: https://videohive.net/item/plane-interior-flying-in-the-clouds/9895121
Inherently Safer Chemistry for Accident Prevention

## Slide 97
Case study: Production of gasoline alkylate with AlkyClean® Technology
In 2016 Albemarle and CB&I won the EPA green chemistry award for their inherently safer AlkyClean® process technology.
AlkyClean® Technology:
The AlkyClean® solid acid alkylation process produces high quality alkylate without using liquid acid catalysts.
The solid acid alkylation process is safer for both people working directly in production and for people in the area surrounding the production facility.
There are also environmental and economic benefits since neither acid-soluble oils nor spent acids are produced.
Conventional alkylate production:
Alkylate is typically produced from the reaction of isobutane and light olefins.
This requires the use of liquid acid catalyzed processes, such as hydrofluoric acid.
Hydrofluoric acid is extremely toxic. When released it forms clouds that can be lethal for up to five miles.
Inherently Safer Chemistry for Accident Prevention

## Slide 98: More examples available
Presidential Green Chemistry Challenge Winners
https://www.epa.gov/greenchemistry/presidential-green-chemistry-challenge-winners
How Industrial Applications in Green Chemistry Are Changing Our World (white paper) by American Chemical Society
Inherently Safer Chemistry for Accident Prevention

## Slide 99: Synthesis Comparison Exercise
Dihydropyrimidone is a pharmaceutical compound that displays medicinal properties as vasodilatory calcium-channel blockers and anti-viral, anti-bacterial, and anti-inflammatory agents. More than one synthetic schemes have been proposed for its synthesis since the late 1800s. Compare the two synthetic routes and analyze which pathway is greener. In your argument, be sure to consider and compare all aspects of the reaction.
Inherently Safer Chemistry for Accident Prevention

## Slide 100: Summary: 12 Principles of Green Chemistry
1. Waste Prevention
2. Atom Economy
3. Less Hazardous Chemical Synthesis.
4. Designing Safer Chemicals.
5. Safer Solvents and Auxiliaries.
6. Design for Energy Efficiency.
7. Use of Renewable Feedstocks.
8. Reduce Derivatives.
9. Catalysis.
10. Design for Degradation.
11. Real-time Analysis for Pollution Prevention.
12. Inherently Safer Chemistry for Accident Prevention.
Anastas, P. T.; Warner, J.C. Green Chemistry: Theory and Practice, Oxford University Press,1998