## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Designing for Reduced Hazard
Image: Wikimedia Commons, Fume Hood , Author: U.S. National Institute for Occupational Safety and Health
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE
Notes: Problems: 17/18, 36

## Slide 2
Toxicology
Assessing Hazards and Exposure
  What Happens When You’re Exposed?
Hazard Minimization Through Molecular Design
QSAR - Quantitative Structure Activity Relationship
Molecular Design Research Network (MoDRN)
Topics To Be Covered

## Slide 3
In U.S., 1.78 million tons of toxic chemicals were released directly to air, water, and land in 2011
Only 650 of toxic chemicals out of 100,000 in commerce are tracked by Toxic Release Inventory
Mihelcic, J. R.; Zimmerman, J. B., Environmental engineering: Fundamentals, sustainability, design. Wiley Global Education: 2014.
Chemicals in the Environment

## Slide 4
One of Green Chemistry’s greatest strengths is the ability to design for reduced hazard.
148 xenobiotics in the body
Xenobiotic: synthetic chemical, that is foreign to the body or to an ecological system.
Of the chemicals found:
  76 cause cancer in humans or animals,
  94 are toxic to the brain and nervous system, and
  79 cause birth defects or abnormal development.
The dangers of exposure to these chemicals in combination has never been studied.
Image Source: http://svtc.org/our-work/e-waste/
Body Burden

## Slide 5
The traditional definition of toxicology is "the science of poisons."
A more descriptive definition of toxicology is
"the study of the adverse effects of chemicals or physical agents on living organisms".
What is Toxicology

## Slide 6
What Counts as Toxic
Mihelcic, J. R.; Zimmerman, J. B., Environmental engineering: Fundamentals, sustainability, design. Wiley Global Education: 2014.
Notes: Debilitating – making something weak

## Slide 7
Acute toxicity | Carcinogenicity | Bioconcentration
Subchronic & chronic toxicity | Neurotoxicity | Degradation & transport
Reproductive toxicity | Immunotoxicity | Aquatic toxicity
Developmental toxicity | Genotoxicity | Terrestrial organism toxicity
Molecular weight | Molecular volume | Dipole moment
Hydrophilic surface area | Hydrophobic surface area | Rotatable bonds
Hydrogen bonds | Ionization potential | Electron affinity
Partition coefficients | Acid/base properties | Polarizability
Relating Toxic Endpoints to Molecular Features & Properties
Relationships

## Slide 8
A toxic agent is anything that can produce an adverse biological effect.
It may be chemical, physical, or biological in form.
For example, toxic agents may be
chemical (such as cyanide),
physical (such as radiation), and
biological (such as snake venom)
Definitions

## Slide 9
Definitions
P = Kow =
[solute]octanol
[solute]water
1-octanol
water
-1
1
3
5
7
0
2
4
6
8
9
HCO2H
-0.5
methanol
-0.74
toluene
2.73
NEt3
1.45
hexane
4.0
decane
6.3
stearic acid
8.2
octane
5.2
THF
0.5
1-hexanol
2.0
(C6Cl5)2O
8.3
C6Cl6
5.5
1-decanol
4.6
1-butanol
0.8
hydrophobic
hydrophilic
lipophilic
lipophobic
logKow
Compound | Kow | logKow
methanol | 0.18 | -0.74
benzene | 148 | 2.17
toluene | 537 | 2.73
decachloro-biphenyl | 182,000 | 8.26

## Slide 10: What is the most important factor in bringing about the adverse biological impact?

## Slide 11
Dose is the amount of a substance administered at given times.
For example:
  650 mg Paracetamol/Tylenol as a single dose
  500 mg Penicillin every 8 hours for 10 days
Dose

## Slide 12
Highly toxic chemicals can be life saving when given in appropriate doses.
An apparently nontoxic chemical can be toxic at high doses. (Too much of a good thing can be bad)
Dose Makes the Poison
All things are poison, and nothing is without poison, the dosage alone makes it so a thing is not a poison.
Paracelsus 1494-1541

## Slide 13
Lethal Doses
water
HgCl2
NaCN
ethanol
caffeine
Notes: 1 Quart = 0.946 lit

## Slide 14
Source: Marczewski, A.E., and Kamrin, M. Toxicology for the citizen, Retrieved August 17, 2000: www.iet.msu.edu/toxconcepts/toxconcepts.htm.
Approximate Lethal Doses of Common Chemicals (Calculated for a 160 lb. human from data on rats)
Chemical Lethal Dose
Sugar (sucrose) 900 g
Alcohol (ethyl alcohol) 1.5 L
Salt (sodium chloride) 250 g
Herbicide (2, 4-D) 125 mL
Arsenic (arsenic acid) 1-2 teaspoons
Nicotine one half teaspoon
Food poison (botulism) microscopic
Lethal Doses
Notes: 1 Quart = 0.946 lit

## Slide 15: How is toxicity testing done?

## Slide 16
The dose-response relationship is a fundamental and essential concept in toxicology. It correlates exposures and the spectrum of induced effects.
The dose-response relationship is based on observed data from:
experimental animal
Human in vitro cell studies
human clinical (but for drugs only…)
Dose-Response
Notes: In vitro comes from the Latin term "in glass." The term refers to studies of biological properties that are done in a test tube (i.e. in a glass vessel) rather than in a human or animal.In vitro studies are often contrasted to in vivo ("in life") studies which are done inside an organism.

## Slide 17
Knowledge of the dose-response relationship:
  establishes causality that the chemical has in fact induced the observed effects
  establishes the lowest dose where an induced effect occurs - the threshold effect
  determines the rate at which injury builds up - the slope for the dose response.
Dose-Response
log(dose)

## Slide 18
LD50- A common dose estimate for acute toxicity is the LD50 (Lethal Dose Response 50%).
This is a statistically derived dose at which 50% of the individuals will be expected to die.
NOAEL - No Observed Adverse Effect Level
Highest data point at which there was no adverse effect.
LOAEL - Low Observed Adverse Effect Level
Lowest data point in your experiment at which there was an adverse effect.
LD 50
UF = Uncertainty factor (10-1000)
UF is bigger when larger uncertainty on experiment
RfD – estimate of the maximum daily oral exposure to humans, that’s likely to be without risk of an effect
LD50, NOAEL, LOAEL, and RfD
RfD
log(dose)
Notes: RfD = reference dose

## Slide 19
0
100
50
40
30
20
10
60
70
80
90
Inhaled Dose (ppm)
% Mortality
Solvent 99-7
Solvent 99-2
0 50 100 150 200 250 300 350
Plotted here are two theoretical curves for the toxicity of solvents used in the cleaning of silicon compounds. Both solvent 99-2 and 99-7 performed equally well against a variety of manufactured silicon compounds. The task at hand for you is to determine which solvent would you pick to be “safer” for use. As you can see from the accompanying data both compounds have an equivalent Lethal dose 50 value (LD50). These are based on average values during a 6 hour exposure period.
In-Class Discussion- Which Solvent Would You Use?

## Slide 20
Solvent 99-7 causes lethality at much lower levels than 99-2 (20ppm versus 150 ppm respectively), and the response is much more predictable (i.e. less population heterogeneity). In case of Solvent 99-2, higher levels can be inhaled before any harmful effects should begin.
0
100
50
40
30
20
10
60
70
80
90
Inhaled Dose (ppm)
% Mortality
Solvent 99-7
Solvent 99-2
0 50 100 150 200 250 300 350
In-Class Discussion- Which Solvent Would You Use?

## Slide 21
Review and analysis of toxicology data and assessing if the substance causes toxic effects
Sources include animal and human studies and computational data
These studies have difficulty with showing causation (if a risk factor lead to disease)
Mihelcic, J. R.; Zimmerman, J. B., Environmental engineering: Fundamentals, sustainability, design. Wiley Global Education: 2014.
Hazard Assessment
Risk = f(Hazard, Exposure)

## Slide 22
Determines the extent and frequency of human exposure to target chemicals.
Guidelines for residential, industrial and commercial sites
For engineers, the knowledge of hazard and exposure provides information whether the site needs to be remediated.
Mihelcic, J. R.; Zimmerman, J. B., Environmental engineering: Fundamentals, sustainability, design. Wiley Global Education: 2014.
Exposure Assessment
Risk = f(Hazard, Exposure)
Example of exposure evaluation: workers touching soil

## Slide 23: Hazard assessment, dose-response & exposure assessment
Risk Characterization

## Slide 24
ChemHAT - easy way to access summarized information on chemical hazards in the workplace
ChemSpider
Protox
Safer Choice - for consumers, businesses, and purchasers to find products that perform and are safer for human health and the environment.
toxicity assessment based on experimental or predicted LD50
Tools For Hazard Characterization
Notes: Show tools

## Slide 25: What happens once you are exposed to a toxicant?

## Slide 26
ABSORBTION
DISTRIBUTION
METABOLISM
EXCRETION
ADME
http://blog.gyrosproteintechnologies.com/spinblog/adme-of-therapeutic-proteins

## Slide 27
Source: Wang and Skolnik, Chemistry and Biodiversity, 2009
Chemical Processes in ADME
Place where the drug (or chemical) can take effect
Notes: More complex
ADME can be controlled by these parameters

## Slide 28
Dermal
Respiratory
Digestive
Skin is the first barrier to absorption for the chemical. The skin can keep chemicals out of the body, or it can let them in, depending on the physical and chemical properties of the chemical. Absorption of a chemical will result in the chemical circulating inside the body and perhaps causing adverse effects.
As chemicals are inhaled, they may reach the lungs. The lung surface is a poor barrier against the entry of many chemicals into the body, which means that absorption of chemicals into the lung can be rapid and efficient.
If chemicals are swallowed, either intentionally or unintentionally, they enter the gastrointestinal tract (GI). From there, they may either pass through the body or be absorbed into the body.
Absorption

## Slide 29
Dermal
Respiratory
Digestive
Absorption
Parameter | Preferred | Not Preferred
Physical state | solid | liquid
LogP | Less than 0 or greater than 5 | Between 0 and 5
Molecular weight | More than 400 Da | Less than 400 Da
Parameter | Preferred | Not Preferred
Particle size | More than 5 nm | Less than 5 nm
LogP | Less than 0 or greater than 5 | Between 0 and 5
Molecular weight | More than 400 Da | Less than 400 Da
Vapor pressure [mmHg] | Less than 0.001 | More than 0.001
Parameter | Preferred | Not Preferred
Particle size | More than 100 nm | Less than 100 nm
LogP | Less than 0 or greater than 5 | Between 0 and 5
Phase | solid | liquid
Molecular Weight [Da] | More than 500 Da | Less than 400 Da
LogP – measure of partition coefficient of a molecule between aqueous and lipophilic phases.
Notes: LogP – measure of partition coefficient of a molecule between aqueous and lipophilic phases.
Da – Dalton, unit of molar mass, g/mol

## Slide 30
Distribution is the movement of a chemical throughout the bloodstream and into other organs, such as the brain and the bones. Pharmaceuticals such as antibiotics and painkillers are designed to have high distribution rates so they can reach their target organs and have therapeutic effects. For chemicals such as detergents, distribution should be limited.
Distribution depends on many factors such as log P, polar surface area, acidic/basic properties, and molecular weight.
Distribution as opposed to absorption is more difficult to control.
Distribution
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor
Notes: Polar Surface Area of a molecule is defined as the surface sum over all polar atoms, primarily oxygen and nitrogen, also including their attached hydrogen atoms. PSA is a commonly used medicinal chemistry metric for the optimization of a drug's ability to permeate cells.

## Slide 31
As a chemical is distributed through the body, it will most likely undergo metabolism. Metabolism is the body’s way to transform the molecules into metabolites in the liver. This facilitates their excretion (removal) through the kidneys. The rate at which a chemical is metabolized is usually dependent on its accessibility to enzymes.
Metabolism is unpredictable. Metabolism can lead to detoxification or toxification of the organism.
Metabolism
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor

## Slide 32
After the chemical is absorbed, the body can eliminate it by a process called excretion which can occur through the kidneys, the skin, the GI tract, and the lungs. If the chemical is not eliminated from the body, it can accumulate, or stay in the blood, which can lead to disease. Bioaccumulation is favored for lipophilic molecules in fatty tissues.
Excretion as opposed to absorption is more difficult to control.
Elimination
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor

## Slide 33
Pollution
Persistence
Depletion of resources
Flammability
Radioactivity
Risk of Explosion
Chemical Reactivity
Understanding Physicochemical Properties Associated with Reduced Hazard
Chemical and Physical Properties
pKa chain branching log P molecular refractivity mol. wt. hydrolyzable groups
EHOMO ELUMO electronegativity hardness dipole log D7.4 # H-bond accept/donor
DESIGN

## Slide 34
Absorption organs
GI tract
Skin
Lungs
Eyes
Acidic substance
pKa<7
Unionized at pH>pKa
Basic substance
pKa>7
Un-ionized at pH>pKa
Lipid soluble
Absorbed across intestine membrane into blood
Chemical
Property-Based Guidelines for Bioavailability
Notes: Different absorption mechanisms - GI tract has largest SA, respiratory has largest blood flow & thinnest membrane, skin has variable thickness; different requirements for water sol

## Slide 35
molecular size < 400 Da
log Pow 0 - 6
presence of solvents
Ionization (polar, ionized)
molecular size < 500 Da
log Pow 0 - 5
Non-ionization at GI pH
Particle size < 5um
molecular size < 400 Da
vapor pressure < 0.001 mmHg
water solubility
molecular size
vapor pressure < 0.001 mmHg
Voutchkova, A.; Osimitz, T.; Anastas, T. Chem. Rev. 2010, 110, 5845
Property-Based Guidelines for Bioavailability
Absorption organs
GI tract
Skin
Lungs
Eyes

## Slide 36
Educational game based on ADME and scientific data for surfactants to make connection between physico-chemical properties and health.
http://gwiz.yale.edu
Safer Chemical Design Game
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor

## Slide 37: Approaches to Hazard Minimization through Molecular Design

## Slide 38
Bioavailability Structure/Shape Activity Mechanism of Action
Molecular
Weight
Solubility
Electronic
Charge
Volatility
Reactive
Functional
Groups
Bioaccumulation/
Persistence
Particle
size
Receptor
binding
Key events
Shape/
Molar Volume
Toxicokinetics
Toxicodynamics
Chemists can control quite well
Not well understood and relatively complex
That’s what we want to target
Green Chemistry Molecular Design Pyramid

## Slide 39
Hazard Minimization Through Molecular Design
Strategy #1. Use high MW compounds.
High MW compounds can’t be absorbed through membranes (skin, lung, intestine, etc.).

## Slide 40
Hazard Minimization Through Molecular Design
Cros, Thesis “Action of Amyl Alcohol on Organisms”, U of Strasbourg, 1863
Alcohol | Solubility in water | Toxicity
Methanol | miscible | Low
Pentanol | 22 g/L | Medium
Camphor | 1.2 g/L | High
1-Hexadecanol | 1x10-5 g/L | None
Strategy #2. Make the compound very water-soluble or very water-insoluble.
Notes: Cros tested dogs, pigeons, rabbits, by oral, inhalation, dermal and intravenous. Found that aquatic toxicity doesn’t correlate to water solubility. Toxicity increases with DECREASING solubility until there is no solubility and then the compound isn’t toxic anymore. Making the alcohol chain longer therefore increases toxicity up to a point. Why is there a cutoff? If the solubility is TOO low, then not enough of the compound dissolves to have any effect.
Because plants are less sensitive than animals, they require exposure to a higher concentration to cause narcosis.
Therefore a chemical may be too insoluble to affect plants but may still affect animals.
Some chemicals may be so insoluble that they affect neither.
How to do this?

## Slide 41
Hazard Minimization Through Molecular Design
Lazarev, Neelektrolity, Voennomorskaya Medicinskaya Akademiya, 1944
log(1/C) = a•logP - b
log(1/MLD) = 1.065•logP – 0.425
log(1/MLD) = 0.881•logP – 0.989
log(1/LD100) = 1.06•logP – 1.368
log(1/LD50) = 0.618•logP – 2.863
log(1/C) = 0.681•logP – 3.04
Yeast cells
Goldfish
Cat
Grain weevil
Tomato plant
Hansch and Dunn, J. Pharm. Sci. 1972, 61, 1-19
C = concentration required to observe an adverse effect (higher C means less toxic)
1/C = toxicity
Notes: If the toxicity of a compound is caused solely by narcosis, then the toxicity is related to the logP.
Higher logP means more toxic, but there is a cutoff. E.g. equations given. MLD = median lethal dose

## Slide 42
Hazard Minimization Through Molecular Design
Chart: logKow
| -0.66 | -0.16 | 0.34 | 0.88 | 1.4 | 2.0299999999999998 | 253 | 3.03 | 3.53 | 4.03 | 0.23 | 0.73 | 1.23 | 1.73 | 2.23 | 3.23
ROH | -0.24 | -0.04 | 0.44 | 0.87 | 1.38 | 1.83 | 2.32 | 2.86 | 3.18 | 3.57
CH3CO2R | 0.59 | 0.8 | 1.23 | 1.69 | 2.15 | 2.6
hydrophobic
hydrophilic
Less toxic
More toxic
Hansch and Dunn, J. Pharm. Sci. 1972, 61, 1-19
Irpex lacteus
http://www.herbarium.iastate.edu/fungi/fungispecies.php?sp=Irpex+lacteus+(Fr.)+Fr
Strategy #3.
Design the compound to have a low logP.
Notes: C is the minimum toxic dose for madison 517 fungus (irpex lacteus)

## Slide 43
Hazard Minimization Through Molecular Design
von der Ohe, Chem. Res. Toxicol. (2005) 18, 536.
0
2
4
6
8
10
Log (1/LC50)
excess toxicity = Te =
Cpred
Cobs
Strategy #4. Avoid functional groups that cause specific effects (i.e. toxicophores).
Te = 1066
Could be:
• increased acute toxicity (lower LD50 or LC50)
• increased chronic toxicity (not evident in LD50 or LC50)
Notes: The prediction of toxicity by QSAR equations using logP is fine for giving a baseline (narcosis) toxicity, and is usually right if the compound exhibits no specific effects, meaning it doesn’t have a functional group that reacts with a specific enzyme for example.
Tpred = concentration predicted to cause toxic response by using the logP calculation.
Tobs = the (lower) concentration that actually causes toxic response
For example, the Te of divinylsulfone for rat oral LD50 is 1066. It’s 1066 times more toxic than one would expect by narcosis alone. Why? It does a Michael addition.
The graph shows LC50 for daphnia magna for compounds that are known to cause only narcosis (filled circles) and for anilines (hollow circles). Clearly some of the anilines show excess toxicity.
Keep in mind that it’s the Cobs that is important. The observed toxicity. Excess toxicity isn’t as important, but it does help us to design safer chemicals. In o
Daphnia picture from Wikipedia.

## Slide 44
Hazard Minimization Through Molecular Design
C6F5CHO
Te = 51
CH3CHO
Te = 131
Lipnick, Sci. Total Environ. (1991) 109/110, 131.
Which has more excess toxicity?
or
Strategy #4a. Avoid ketones and aldehydes that are prone to imine formation.
Notes: If the toxicity of a compound is caused solely by narcosis, then the toxicity is related to the logP.
Higher logP means more toxic, but there is a cutoff. E.g. equations given. MLD = median lethal dose

## Slide 45
Hazard Minimization Through Molecular Design
Te = 35
Te = >490
Te = >490
Te = 1884
Lipnick, Sci. Total Environ. (1991) 109/110, 131.
SN1
Factors that promote this reaction:
• electron-withdrawing groups or atoms (SN2)
• resonance stabilization of carbocation (SN1)
• good leaving group I, Br > Cl >> F
SN2
Strategy #4b. Avoid allylic/propargylic/benzylic halides.
Notes: If the toxicity of a compound is caused solely by narcosis, then the toxicity is related to the logP.
Higher logP means more toxic, but there is a cutoff. E.g. equations given. MLD = median lethal dose

## Slide 46
Hazard Minimization Through Molecular Design
Michael addition
Te = >81,000
Te = 180
Te = 68
Te = >3,800
Lipnick, Sci. Total Environ. (1991) 109/110, 131.
Which is safer?
logP = 0.98
0.99
or
Strategy #4c. Avoid Michael acceptors.
Notes: If the toxicity of a compound is caused solely by narcosis, then the toxicity is related to the logP.
Higher logP means more toxic, but there is a cutoff. E.g. equations given. MLD = median lethal dose

## Slide 47
Hazard Minimization Through Molecular Design
tubocurare
Strychnos toxifera
Strategy #4d. Avoid acetylcholine mimics (cationic centres with 2 or more small R groups).
where at least two R = small
acetylcholine
Note: such structures don’t have a lower oral LD50. Why?
oral mouse LD50 – 150 mg/kg
intravenous mouse LD50 – 0.13 mg/kg
Notes: Some cationic electrophiles cause neurotoxicity. e.g. NR4+, if 2 or more R’s are small, will cause neuromuscular blocking (curare effect) by binding in the nicotinic acetylcholine receptor. That receptor is the signal recipient in muscles that causes the muscles to contract when the signal (acetylcholine) is received. Prevents muscles from contracting. Tubocurarine from tropical hanging vines is used in arrow poisons and in surgery.(vol 9, p 78 of Handbook of GC).
Note that this doesn’t affect ingestion toxicity because cationic compounds don’t generally pass through the stomach walls. Only dangerous in the bloodstream.

## Slide 48
Hazard Minimization Through Molecular Design
estradiol
a nonylphenol
bisphenol A
Strategy #5. Avoid functional groups that mimic hormone structures.
Notes: Some cationic electrophiles cause neurotoxicity. e.g. NR4+, if 2 or more R’s are small, will cause neuromuscular blocking (curare effect) by binding in the nicotinic acetylcholine receptor. That receptor is the signal recipient in muscles that causes the muscles to contract when the signal (acetylcholine) is received. Prevents muscles from contracting. Tubocurarine from tropical hanging vines is used in arrow poisons and in surgery.(vol 9, p 78 of Handbook of GC).
Note that this doesn’t affect ingestion toxicity because cationic compounds don’t generally pass through the stomach walls. Only dangerous in the bloodstream.

## Slide 49
Elimination of the molecular initiating event that activates pathway
Changing reactive functional groups
Reducing or eliminating bioavailability
Reduction of need for associated hazardous substances
Design for End-of-Use product life
Hazard Minimization Through Molecular Design
More strategies for minimizing hazard

## Slide 50
Where the mechanistic pathway of action is known, molecular structures can be designed such that the necessary reactions are either impossible or highly disfavored resulting in significant toxicity reduction.
Elimination of the molecular initiating event that activates pathway

## Slide 51
In the absence of specific mechanistic information, chemists can modify structure such that certain reactive functional groups, e.g. cyano, electrophilic, etc, can be minimized or eliminated from the chemical structure where feasible.
B. Changing Reactive Functional Groups

## Slide 52
In order for a chemical to manifest its intrinsic hazard, it must be able to reach the toxicological target, human, animal, environmental or global. Through structural molecular design, properties such as solubility, log Kow, and volatility can adjusted to reduce hazard manifestation.
C. Reducing or Eliminating Bioavailability
Notes: The octanol/water partition coefficient (Kow) is defined as the ratio of a chemical's concentration in the octanol phase to its concentration in the aqueous phase of a two-phase octanol/water system

## Slide 53
Many chemical substances, if not hazardous themselves, require the use of other hazardous substances e.g. paints with VOCs, surfaces requiring specific cleaners, plastics with various additives.
Through molecular design, these associated substances can be eliminated by making the desired properties integral to the product
D. Avoid Associated Hazardous Substances

## Slide 54
Persistence of chemical in the environment is a problem that can be designed out of molecular structure.
By creating products that degrade to innocuous by-products under designed conditions, e.g., heat, light, time one can reduce or eliminate this hazard.
E. Design for End-of-Useful Product Life

## Slide 55: By Changing the Molecular Charge: Cephalosporins
Clinical nephrotoxicity was recognized early – damage to proximal tubular epithelia.
Mechanism: the drug is rapidly transported across basolateral membrane via the organic anion transporter, OAT1. Transport out of cell into lumen is less well characterized (involves other OAT, OAT4).
Cephalosporin has a very low affinity for OAT4 due to its zwitterionic character, resulting in considerable intracellular accumulation
Cephaloridine
Cephalothin
In contrast, cephalothin, an anionic analog of the original zwitterionic drug, rapidly moves across the epithelia from blood into urine
Is thus not a neurotoxin
Cephalosporins: Antibiotic molecules used for gram+ bacteria
Notes: Cephalosporins are a type of beta-lacatam antibiotic.
First generation:Cephaloridine
Nephrotoxicity - kidneys

## Slide 56
Diquat
Paraquat
By Manipulating Sterics: Paraquat and Diquat
Diquats and Paraquats are herbicides (plant killer), primarily for weed and grass control
In animal studies, diquat causes mild, reversible injury
Paraquat is not metabolized by the liver. It has life-threatening effects on the gastrointestinal tract, kidney, liver, heart and other organs
Both: Toxic doses are life threatening. Impacts GI tract, kidney lungs, liver, heart, other organs
Registered as a restricted use pesticide
Not registered as a restricted use pesticide
http://npic.orst.edu/RMPP/rmpp_ch12.pdf
Notes: Paraquat is a non-selective contact herbicide of the diphenyl class. It was introduced in the 1960s and became used worldwide. However it was soon recognized that paraquat also cause selective pulmonary toxicity to humans (damage to alveolar cells type I and II, causing edema, inflammation and hermorrhage, lung fibrosis).
Steric effects are nonbonding interactions that influence the shape and reactivity of ions and molecules. Steric effects complement electronic effects, which usually dictate shape and reactivity. Steric effects result from repulsive forces between overlapping electron clouds.

## Slide 57
Acrylate is understood to be carcinogenic because it can readily undergo Michael addition reactions
The addition of a methyl group to form methacrylate decreases the electrophilicity of the β-carbon, and decreases tendency for Michael reactions.
Whereas acrylate causes cancer in experimental assays, methacrylate does not.
Acrylate
carcinogenic
Methacrylate
non-carcinogenic
By Manipulating Electrophilicity: Acrylates
Notes: Electr

## Slide 58
Benzene is known to cause hematotoxicity and leukemia in humans
This is understood to be due to one of its metabolites, (E,E)-muconaldehyde.
Toluene is comparatively much less toxic, as the methyl group is oxidized more easily than the benzene ring to give benzoic acid
By Facilitating Detoxification: Benzene
hematotoxicity,
leukemia
less toxic
hepatic oxidation
[detoxification]

## Slide 59
DDT is well known to be environmentally persistent.
DDT analog with Silicon above was synthesized.
While less persistent, the analog turned out to be non-toxic to insects.
This is due to the more readily oxidized (metabolized) Si-H bond compared to C-H and also the larger size of the molecule.
DDT
(Toxic to insects)
Si-DDT Analog
(Non-toxic to insects)
By Isosteric Substitution: Carbon with Silicon

## Slide 60
Even if chemists design one chemical, it has to undergo tests
Designing New Molecules is Not a Trivial Task

## Slide 61
QSAR = classification models used in the chemical and biological sciences and engineering
QSAR-Quantitative Structure Activity Relationship
Wikipedia
potency of the response variable
"predictor" variables
QSAR
Structure, physico-chemical properties, chemical functionalities
Biological activity: toxicology and eco-toxicology
[like LC50 or oxidative stress]
Known data sets
QSAR established relationship
"predictor" variables
New molecules
QSAR uses the learnt rules to predict biology
QSAR
QSAR predicted potency of the response variable

## Slide 62
Not sufficient data on most chemicals
Not all chemicals can be tested
Allows rapid screening of candidate structures
Why use QSAR?

## Slide 63
Prediction accuracy not higher than 65-70% for non-carcinogenic chemicals.
Lack of validation with up-to-date data.
Application to a narrow range of chemical structures.
Qualitative output.
Current limitations
Examples of Popular Toxicity Prediction Tools

## Slide 64
Next generation: powers of computational Chemistry
Docking software have been able to model very precisely the active site of a target enzyme (target to a drug for instance, or to a toxic).
In drug design such software are used to predict the best molecules for biological activity. Only the best performing are synthesized and tested.
Similar ideas can be used in toxicology
http://www.molfunction.com/software5.htm
Notes: Jakub’s slide

## Slide 65
What’s the need?
Traditional organic solvents Low toxicity Volatile
Ionic liquids Nonvolatile Difficult to remove
Not acutely toxic Hydrolytically unstable
Not hazardous to skin Acutely toxic
Easy to remove Hazardous to skin

## Slide 66
Virtual screening
all possible compounds
compounds that will do the job
green compounds that will do the job
Performance
logKow
pKaH
melting point
vapour pressure
solubility in water
Safety, Health and Environment
flash point
vapour pressure
toxicity to mammals
toxicity to fish
toxicity to insects
eutrophication of surface waters
bioaccumulation potential

## Slide 67
Virtual screening
Procedure (Virtual Screening)
Randomly generate thousands of structures
Predict properties (physical, chemical, health, environment) using QSAR
Reject those that don’t score well for performance criteria.
Consider only those that score well for EH&S criteria.

## Slide 68
Virtual screening

## Slide 69
Virtual screening
ChemT (structure generator)

## Slide 70
Virtual screening
TEST (Toxicity Estimation Software Tool)
https://www.epa.gov/chemical-research/toxicity-estimation-software-tool-test
Draw structure
”Copy SMILES to clipboard”
“Generate from SMILES on clipboard”
Choose endpoint
Choose “consensus”
Calculate
Find the generated data in a “ToxRuns” folder.
Open the file “Prediction Results Consensus.html”
1
2,3
4
5
6

## Slide 71
Virtual screening
false
negatives
false
positives
false negatives
false
positives

## Slide 72
Virtual screening
Raw output (best 12 structures)

## Slide 73
Virtual screening

## Slide 74
Virtual screening
A company needs a basic tertiary amine for a product that would be used outdoors. They are worried about impact on aquatic life. Find the amine that would fit the company’s requirements while being the safest for daphnia magna.
Their requirements are:
• it must be a tertiary amine
• at least one R group on the nitrogen must be n-butyl
• the other two substituents on the N must consist of only C, H, O and/or N.
• the boiling point must be greater than 160 ˚C

## Slide 75
Virtual screening: SMILES structures
• H’s are not usually shown. Normal number of H’s is assumed.
• Single bonds are not shown. Double bonds (=), triple bonds (#) and quadruple bonds ($) are shown.
• B,C,N,O,P,S,F,Cl,Br,I do not need square brackets if they are uncharged & achiral.
water
diethyl ether
O
CCOCC
acrylonitrile
C=CC#N
hydrogen chloride
Cl
• Use square brackets and show H’s if: chiral centre, charged, other element, or unusual # of H’s.
• Use a period to indicate no bond.
propylammonium chloride
CCC[NH3+].[Cl-]
sodium sulfide
[Na+][Na+].[S-2]
• Use parentheses to indicate branching.
O=C(C)C
O=C([H])[H]
CCC(=O)O
FC(F)(F)c(cc1)ccc1C#N
• Use numbers to indicate points of closure for rings (cut the rings to make a linear sequence)
• Use lower case letters to indicate atoms in aromatic rings (or use alternating double and single bonds).
BrC1CCCCC1
O1CCOCC1
c1ccncc1
C1CCCC2C1CCCC2
C1=CC=NC=C1
1
2

## Slide 76
Hazard and Risk – Past and Present
Toxicology
Assessing Hazards and Exposure
  What Happens When You’re Exposed?
Hazard Minimization Through Molecular Design
QSAR - Quantitative Structure Activity Relationship
Molecular Design Research Network (MoDRN)
Topics Covered

## Slide 77
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE