## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Waste Prevention
Image: Wikimedia Commons, Anacortes Refinery, Author: Walter Siegmund
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
Waste Prevention
It is better to prevent waste than to treat or clean up waste after it is formed.
Image: Harshaw Chemical Company discharges waste water into the Cuyahoga river
Source: National Archives and Records Administration

## Slide 3
The Waste Treatment Pyramid
Reduced Solvent Use
Waste as a Feedstock
Biodegradation of Waste
Designing Processes to Include Biodegradation of Waste
Topics To Be Covered

## Slide 4: Waste treatment pyramid: The 4 Rs Reduce, Reuse, Recycle, Recover
Reduction
Reuse
Recycling
Energy recovery
Disposal
Most favored option
Least favored option
Prevention
Incineration
Landfill
Recycling
Composting
We need various types of technology to reduce and reuse waste.
Ultimately, the production of waste should be prevented.
Notes: Need for technologies to Reduce and Reuse waste. Ultimately, the waste production should be Prevented

## Slide 5: Landfills
  Consolidated material is buried with mud and other sealing agents to enable chemical, bacteriological, and physical degradation.
  Semi-anaerobic conditions lead to production of methane and CO2.
  If captured, landfill gas (methane) from decomposing garbage can be used to produce electricity, heat, and fuels.
Reduction
Reuse
Recycling
Energy recovery
Disposal
Image: Wikimedia Commons

## Slide 6: Incineration
Thermal decomposition of wastes through Combustion (in presence of oxygen)
Better than landfills
Reduces solid waste mass by 95 - 96%
Converts wastes in to:
    Heat – (Use: electricity, steam)
    Flue Gas – (Use: indirect heating)
    Ash – (cement, etc)
Disadvantages
    Releases gases such as CO2
    Emits hazardous end products
    No recycling possible
Reduction
Reuse
Recycling
Energy recovery
Disposal
Image: Wikimedia Commons

## Slide 7: Recycling and Composting
Reduction
Reuse
Recycling
Energy recovery
Disposal
Gasification:
  Converts organic based materials into CO, H2 and CO2.
  Achieved by reacting the material at high temperatures (>700 °C), without combustion, with a controlled amount of oxygen and/or steam.
  The resulting gas mixture is called syngas.
  Syngas is combustible and often used as a fuel.
Pyrolysis:
  Thermal decomposition at 200-300°C occurring in the absence of oxygen.
  Precursor of both the combustion and gasification processes.
  The products of biomass pyrolysis include biochar, bio-oil, and gases - such as methane, hydrogen, carbon monoxide, and carbon dioxide.

## Slide 8: Recycling and Composting
Composting
  Organics undergo a biological decomposition to form a material (compost) that is non-toxic to plant growth.
  By-product of the reaction are CO2, water and heat.
.
Reduction
Reuse
Recycling
Energy recovery
Disposal

## Slide 9: Reuse & Recycle
Reduction
Reuse
Recycling
Energy recovery
Disposal
Reuse and Recycle
  Converting waste materials into new materials and objects.
  Available for metals, plastic, paper, glass.
  E.g. PET reuse and repurposing
http://www.packagingtoday.co.uk/news/newsgermans-recycle-more-and-more-effectively-success-in-pet-bottle-recycling-according-to-study-5699219
Cost-benefit of recycling: energy savings
Material | Energy savings
Aluminum | 95%
Cardboard | 24%
Glass | 5-30%
Paper | 40%
Plastics | 70%
Steel | 60%

## Slide 10: The Reduction and Elimination of Waste
Reduced solvent or solventless processes
Process intensification (smaller, cleaner and more energy efficient)
Self-separation (precipitation)
Use waste as a feedstock
Reduction
Reuse
Recycling
Energy recovery
Disposal
Notes: Process Intensification - simple definition of Stankiewicz and Moulijn (2000), PI is ‘Any chemical engineering development that leads to a substantially smaller, cleaner, safer, and more energy efficient technology.
Material Deposition – deposition of powder-sized materials on various surfaces

## Slide 11
Reduced Solvent: Sildenafil Citrate Production
Sildenafil citrate, is a selective inhibitor of phosphodiesterase 5 (PDE5). This new drug has immediately became a major seller, achieving sales of more than $1 billion during its first year on the market. With such a rapid sales take off it was critical that the environmental performance of the synthesis was good from the outset.
Average yield of last three steps = 97% yield.
Reduction of the ratio of solvent waste/kg product over 17 years from 1300 L/kg to only 7 L/kg by minimizing solvent use, increasing solvent recovery, improving solvent selection, and telescoping steps.
Only the solvents t-butanol, ethyl acetate, 2-butanone, and a trace of toluene still require disposal.
Dunn, P.J et al Green Chem., 2004, 6, 43-48
The amount of organic waste produced by the sildenafil citrate processes at various time points

## Slide 12: Utilizing Waste as a Feedstock – Industrial Ecology
Kalundborg, Denmark provides currently best known example of industrial symbiosis in action.
An oil refinery, a power station, gypsum board manufacturer, a pharma company, a cement company, etc – they share ground water, surface water, waste water, steam, and fuel and exchange a variety of byproducts that become in other processes.
http://www.ehrn.co.za/publications/download/09.pdf

## Slide 13: Utilizing Waste as a Feedstock – Industrial Ecology
Some examples:
Waste cooking oil for biodiesel
Glycerol for lactic acid using catalyst
Red mud for bricks
Crustacean (crab, lobster, shrimp, etc) shell waste for chitosan based products

## Slide 14: Example: Used oils as biofuel source
Bio-diesel
Leung, D. Y. C., & Guo, Y. (2006). Transesterification of neat and used frying oil: optimization for biodiesel production. Fuel processing technology, 87(10), 883-890.
Used frying oil
Biodiesel from virgin vegetable oil is considered first generation biofuel because it competes with food
=> Turning to waste can offer a solution: frying oil can be used instead.
“Waste”
Current treatment:
  Dispose / Combust as fuel.

## Slide 15: Glycerol: a waste of biodiesel
Polylactic acid
Valuable medicinal product
Sunless tanning product
Anti-freeze
Industrial chemical precursors
Skin exfoliating reagent
Notes: There are just a handful of examples of what we could do with glycerol so BURNING it is definitely not the most efficient way to use the limited resources nature offers.

## Slide 16: Production and Applications of Lactic Acid- Conventional process
90% of lactic acid comes from anaerobic fermentation of hexose sugar (e.g. corn starch).
Compete with food sources.
Slow and requires a lot of purifications.
Dusselier, M.; Van Wouwe, P.; Dewaele, A.; Makshina, E.; Sels, B. F., Energy & Environmental Science 2013, 6 (5), 1415-1442.
  Other applications of Lactic Acid:
  Food preservatives
  Edible pH modifier
  Textile industry
  Cosmetic and pharmaceutical industries

## Slide 17: Electrocatalytic Oxidation of Glycerol
2H2O ---> O2 + 4H+ + 4e-
2H+ + 2e- ---> H2
Water-compatible
Atmospheric pressure
Room temp. or above
Very low current / voltage
Cathode
Anode
Power
Supply
e-
e-
e-
e-
e-
e-
e-

## Slide 18: Water Electrolysis with Earth Abundant Metal Catalyst
2H2O ---> O2 + 4H+ + 4e-
2H+ + 2e- ---> H2
Cathode
Anode
Power
Supply
e-
e-
e-
e-
e-
e-
e-
Cathode:
Any conductive materials
Anode:
Expensive platinum group metals
Cobalt 1,2‐bis(diphenylphosphino)ethane
(Co-DPPE)
Bloomfield, A. J.; Sheehan, S. W.; Collom, S. L.; Crabtree, R. H.; Anastas, P. T., A heterogeneous water oxidation catalyst from dicobalt octacarbonyl and 1,2-bis(diphenylphosphino)ethane. New J. Chem. 2014, 38 (4), 1540-1545.
Notes: Also, this catalyst works well in alkaline environment

## Slide 19: Example: Neutralization of Red Mud through generation of biofuels
The Bayer Process (Karl Bayer, 1887)
Element | Composition
Fe2O3 | 30-60wt%
Al2O3 | 10-20wt%
SiO2 | 3-50wt%
Na2O | 2-10wt%
CaO | 2-8wt%
TiO2 | trace-25wt%
K, Cr, V, Ni, Ba, Cu, Mn, Pb, Zn, Sc | Traces
NaOH, 170 – 180 °C
1 – 6 atm
Sodium aluminate
Na+ Al(OH)4-
Precipitation
Electrolytic Reduction
Red Mud
Alumina
Al2O3
(~2 tonne)
Aluminum
(~1 tonne)
Bauxites
(4 – 5 tonne)
Source: http://www.aluminiumleader.com/production/aluminum_production
Red mud
toxic sludge (highly basic pH=14)
byproduct of Bayer process
1 ton of Al2O3 => 1/3 to 2 tons of red mud.
Bayer Process: industrial process that refines bauxite, raw aluminum ore, into aluminum oxide, or alumina.
Notes: http://www.aluminiumleader.com/production/aluminum_production/

## Slide 20: Red Mud: Pollution and Accidents
Stade, Germany
Kolontar, Hungary
Noranda Alumina plant at Gramercy - located alongside the Mississippi River
Damandjodi, India
The red mud is kept in reservoirs
Oct. 4, 2010: A hungarian village, Kolontar, is flooded with toxic red mud.
one million cubic metres of red mud
Ten people died, and 150 people were injured
About 40 square kilometres (15 sq mi) of land affected
3 days later the spill reached the Danude
The base is strong enough to kill plant and animal life, and to cause burns and damage to airways if the fumes are breathed.
Notes: http://www.theguardian.com/environment/2014/jan/08/devecser-hungary-eco-town
http://www.theatlantic.com/photo/2011/09/a-flood-of-red-sludge-one-year-later/100158/
http://lacoastpost.com/blog/?p=13160
http://redmud.org/red-mud/disposal/

## Slide 21: Example: Neutralization of Red Mud through generation of biofuels
Pyrolysis of biomass
Pyrolysis of biomass (500°C) affords a mixture of solid, liquid and gas carbonaceous materials
See class on renewable feedstock
Gas (10-20 %)
→ Energy
CO/H2/CO2
Bio-coal (15-20 %)
→ Soil improvement
Bio-crude (60-75%)
→ Fuel
500°C
Further treatments are needed for fuel production => highly acidic (pH 2)
Notes: http://www.aluminiumleader.com/production/aluminum_production/

## Slide 22: Example: Neutralization of Red Mud through generation of biofuels
Prof. Marcel Schlaf, University of Guelph mixed the two waste streams
Neutralization takes place by mixing the waste streams together
Metals present in the red mud catalyze the reduction of the biofuels to obtain higher quality fuel
Bio-crude: biowaste
Red mud: industrial waste
Fuel
Karimi, E.; Gomez, A.; Kycia, S. W.; Schlaf, M. Energy & Fuels 2010, 24, 2747.
Neutral, magnetic powder could be used to make cement.
pH 2
pH 14
H2
C source
Source of metals for catalytic reduction

## Slide 23: Example: Extracting chitin with an ionic liquid
Robin Rogers and Mari Signum Mid-Atlantic, LLC, are commercializing a safe, environmentally friendly, low energy-demanding and overall less costly process to produce chitin from seafood waste.
Chitin is used in a variety of applications, such as food processing, biodegradable plastics and biomedical applications.
Dr. Connelly (ACS), Robin Rogers, Julia Shamshina and John Keyes (awardees)
https://communities.acs.org/community/science/sustainability/green-chemistry-nexus-blog/blog/2018/10/18/american-chemical-society-announces-2018-green-chemistry-challenge-award-winners
chitin
Ionic liquid
Conventional process to manufacture Chitin – Demineralization of Shells using HCl in huge quantity of water, then treating demineralized shells with NaOH solution to extract all the proteins. The Chitin/deproteinized shells are removed & dried. Huge quantity of HCl and NaOH containing wastes. Chitin obtained still not of very high purity.
Notes: Conventional process to manufacture Chitin – Demineralization of Shells using HCl in huge quantity of water, then treating demineralized shells with NaOH solution to extract all the proteins. The Chitin/deproteinized shells are removed & dried. Huge quantity of HCl and NaOH containing wastes. Chitin obtained still not of very high purity.

## Slide 24: Biodegrade the Waste
Biodegradation - "A process by which microbial organisms transform or alter (through metabolic or enzymatic action) the structure of chemicals introduced into the environment." – US EPA, 2009
“Ready” biodegradability – remove 70% of dissolved organic carbon AND achieve 60% theoretical oxygen demand or CO2 production within a 10-day window in a 28-day test. – OECD

## Slide 25: Aerobic Versus Anaerobic Digestion
Difference in oxygen supply, organism types, and products formed.

## Slide 26: Aerobic Digestion
Bacteria consume organic matter.
Needs a constant supply of oxygen, pH adjustments, and mixing.
Byproducts: heat, CO2, and H2O.
Frequently used by water treatment plants or in composting.

## Slide 27: Anaerobic Digestion
Bacteria consume organic matter in the absence of oxygen.
Common in fermentation and landfill; produces biogas consisting of methane, ammonia, hydrogen sulfide.
Biogas is considered a renewable energy.

## Slide 28: Digestion versus Chemical Structure
Not all chemicals will biodegrade at the same rate (think plastic vs paper).
The rate of biodegradation depends on the microorganism, but also a chemical structure of the molecule.
Some parts of the molecule are known to be more biodegradable than the others.
There is a publically available software that analyses the chemical structure and predicts whether the molecule will degrade slower (days) or slower (months, years).

## Slide 29: Some chemical structures favor biodegradation
Favors biodegradation
OH
Linear chains
Cyclo
Esters
- Low molecular weight
Disfavors biodegradation
- High molecular weight
Halogens (F, Cl)
Tertiary carbon
Side chains and branching
Ethers
Poorly degraded
Readily degraded
Tertiary amine
Aromatic NO2
Aliphatic ether
Pyridine
Aromatic Cl
Aliphatic Cl
Aromatic Br
ketone
nitrile
Aromatic ether
phenyl
Aromatic OH
Aliphatic OH
Aromatic acid
Aliphatic Acid
Aldehyde
Ester

## Slide 30: Predicting Biodegradation: EPA, EPISuite
EPI = Estimation Programs Interface http://www.epa.gov/oppt/exposure/pubs/episuitedl.htm

## Slide 31: BIOWIN Models Based on Molecular Fragment Contributions
Aerobic degradation models
Anaerobic degradation model
The program analyses the chemical structure of each molecule within the group, and assesses its biodegradation potential based on the molecule fragment and functional groups. The result is presented as a probability for degradation. If the number is greater or equal to 0.5, then the molecule will degrade faster. In contrast, values less than 0.5 indicate persistence and low biodegradation potential.

## Slide 32
Increasing number of rings & molecular weight
1.
2.
3.
4.
5.
Favors biodegradation
- OH
- Low molecular weight
Disfavors biodegradation
- High molecular weight
- Cl
Ring structures
Notes: Increasing number of rings

## Slide 33
Increasing number of rings & molecular weight
1.
2.
3.
4.
5.
1>2>4>3>5
Most biodegradable (aerobic)
Least biodegradable
Favors biodegradation
- OH
- Low molecular weight
Disfavors biodegradation
- High molecular weight
- Cl
4>1>2>3>5
Most biodegradable (anaerobic)
Least biodegradable
Ring structures
Aerobic: 0.4468
Anaerobic: -0.1909
Aerobic: 0.0677
Anaerobic: -0.3091
Aerobic: 0.0213
Anaerobic: -0.4999
Aerobic: 0.0102
Anaerobic: 0.9093
Aerobic: 0.000
Anaerobic: -2.9547
Notes: Increasing number of rings

## Slide 34
1.
2.
3.
4.
5.
6.
Bisphenol A derivatives: Halogenated and BPS
Disfavors biodegradation
- High molecular weight
Tertiary carbon
Halogens, but Cl better than F
Favors biodegradation
- Low molecular weight
Bisphenol A derivatives

## Slide 35
1.
2.
3.
4.
5.
6.
Bisphenol A derivatives: Halogenated and BPS
Poor biodegradation due to high MW
Disfavors biodegradation
- High molecular weight
Tertiary carbon
Halogens, but Cl better than F
Favors biodegradation
- Low molecular weight
1>6>3>4>2>5
Most biodegradable (aerobic)
Least biodegradable
6>2>4=5>3>1
Most biodegradable (anaerobic)
Least biodegradable
Bisphenol A derivatives
Aerobic: 0.1559
Anaerobic: -0.2593
Aerobic: 0.000
Anaerobic: 0.1224
Aerobic: 0.0009
Anaerobic: -1.4867
Aerobic: 0.0051
Anaerobic: 0.1224
Aerobic: 0.000
Anaerobic: 0.1224
Aerobic: 0.0594
Anaerobic: 0.2341

## Slide 36
1.
2.
3.
4.
5.
Different plasticizers
Linear and branched;
Two green plasticizers: Reduced ring to cyclo and isosorbide ring
Disfavors biodegradation
Side chains and branching
Ethers
arenes
Favors biodegradation
Linear chains
Saturated cyclo
Esters
Plasticizers

## Slide 37
1.
2.
3.
4.
5.
Different plasticizers
Linear and branched;
Two green plasticizers: Reduced ring to cyclo and isosorbide ring
Disfavors biodegradation
Side chains and branching
Ethers
arenes
Favors biodegradation
Linear chains
Saturated cyclo
Esters
1>4>2>3
Most biodegradable (aerobic)
Least biodegradable
1>2>4>3
Most biodegradable (anaerobic)
Least biodegradable
Plasticizers
Aerobic: 0.9355
Anaerobic: 0.3673
Aerobic: 0.6892
Anaerobic: -0.2275
Aerobic: 0.3258
Anaerobic: -1.2826
Aerobic: 0.6960
Anaerobic: -0.2469
Aerobic: 0.2626
Anaerobic: 0.1410

## Slide 39
Design for Biodegradation?
Since we know the chemical moieties, functional groups, and types of bonds which make the molecule biodegradable, can we build-in biodegradability into chemical products?
YES!

## Slide 40
Example: Plasticizers
kills bacteria,
biodegradation halts
complete degradation to CO2 + H2O
Plasticizers are additives in plastic applications. Almost 90% of plasticizers are used in PVC, giving this material improved flexibility and durability.
Di-propylene glycol dibenzoate decomposes into a product which is toxic to bacteria, and therefore stops the biodegradation process.
With slightly changed structure, 1,5-pentanediol dibenzoate biodegrades into CO2 and H2O

## Slide 41
Example: Pesticides
DDT
DDT – Dichlorodiphenyltrichloroethane, which was used as agricultural pesticide, is persistent in the environment.
Not only does it bioaccumulates, but it undergoes a reaction to DDE which is even more toxic than DDT.
DDE
methoxychlor
Methoxychlor shares many insecticidal properties as DDT and it’s potency, but it is not persistent.
It degrades into methoxychlor phenol, which has also low toxicity and it is easily excreted.
Methoxychlor phenol
Slow degradation
Fast degradation

## Slide 42
Tetrapropylene alkylbenzene sulfonate (TPPS) was used as a surfactant for laundry detergents and accumulated into the water supply due to incomplete degradation.
Water tended to foam when coming out of the tap.
Example: Detergents
TPPS was replaced by linear alkylbenzene sulfonate (LAS).
Replacing the methyl branched chain of TPPS by a linear carbon chain reduces the biopersistence.
Low biodegradation
High biodegradation

## Slide 43
Triclosan is an antibacterial and antifungal agent found in some consumer products, including toothpaste, soaps, detergents, toys, and surgical cleaning treatments.
It persists in the environment.
Example: Antibacterial Products
Chlorophene is a bacteriocide and fungicide in cosmetics.
It is very biodegradable in the media and entirely removeable from the wastewater.
Low biodegradation
High biodegradation

## Slide 44
Approaches to deal with Environmental Challenges
The Waste Treatment Pyramid
Reduced Solvent Use
Waste as a Feedstock
Biodegradation of Waste
Designing Processes to Include Biodegradation of Waste
Topics Covered

## Slide 45
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE