## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Metrics
Image: Wikimedia Commons, Life Cycle Thinking, Author:The National Institute of Standards and Technology (NIST)
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
Why do we need metrics in green chemistry?
Established Metrics in Green Chemistry
  Atom Economy
  Environmental (E) Factor
  Atom Utilization
  Reaction Mass Efficiency
Additional Metrics Used in Green Chemistry
  Process Mass Intensity
  Life Cycle Assessment
  Ecological Indicator/Ecological Footprint
Topics To Be Covered

## Slide 3: Conventional Metrics: Percent Yield
Percent yield: % yield = (actual yield/theoretical yield) x 100
What is missing?
What co-products are made?
How much waste is generated?
Is the waste benign waste?
How much energy is required?
Are purification steps needed?
What solvents are used? (are they benign and/or reusable?)
Is the “catalyst” truly a catalyst? (stoichiometric vs. catalytic)

## Slide 4: Established Green Chemistry Metrics
1. Atom economy (atom efficiency)
*including the stoichiometric coefficient
2. Environmental (E) factor
  E-factor = total waste (g) / product (g)
3. Atom utilization (variation of atom economy)
% Atom Utilization = (MW of desired product/MW of all products) X 100
4. Reaction mass efficiency (RME)
(mass of product C/(mass of A + mass of B)) X 100

## Slide 5: Additional Metrics Used in Green Chemistry
5. Process Mass Intensity (PMI)
  The total mass of materials to the mass of the isolated product.
6. Life Cycle Assessment (LCA)
An assessment of environmental impacts associated with all of the stages of a product's life.

## Slide 6: Atom Economy
Atom-Economy is a calculation based on the overall balanced chemical equation. It is simply the mass of desired product divided by the total mass of products.
Or, since the mass of products equals the mass of reactants in a balanced chemical equation, atom economy is the mass of desired product divided by the total mass of reactants.
Barry M. Trost
Stanford University

## Slide 7: Atom Economy – the process
Single Stage Process:
A + B C

## Slide 8: Atom Economy
(1) A + B C
(2) C + D E
(3) E + F G
Multi-Stage Process:

## Slide 9: Atom Economy: Example One
Reagent | MW (g mol-1)
1 (Reactant) | 74.12
2 (Reactant) | 102.91
3 (Reactant) | 98.08
4 (Desired Product) | 137
CH3CH2CH2CH2OH + NaBr + H2SO4  CH3CH2CH2CH2Br + NaHSO4 + H2O
1 2 3 4 5 6 (Desired Product)
275.11 g mol-1
*including the stoichiometric coefficient
Notes: Reaction type??
137 / 275.11
49.8%

## Slide 10: Atom Economy Example Two: Ibuprofen Synthesis
- from Cann, M.C.; and Connelly, M.E. Real World Cases in Green Chemistry, American Chemical Society: Washington, DC, 2000
The Problem:
The traditional industrial synthesis of ibuprofen was developed and patented by the Boots Company of England in the 1960s (U.S. Patent 3,385,886). This synthesis is a six-step process and results in large quantities of unwanted waste chemical byproducts that must be disposed of or otherwise managed. Much of the waste that is generated is a result of many of the atoms of the reactants not being incorporated into the desired product (ibuprofen) but into unwanted byproducts (poor atom economy/atom utilization). The process also uses a variety of solvents, and catalysts (if any) are not used in stoichiometric amounts.
The Solution:
The BHC Company has developed and implemented a new greener industrial synthesis of ibuprofen that is only three steps (U.S. Patents 4,981,995 and 5,068,448, both issued in 1991). In this process, most of the atoms of the reactants are incorporated into the desired product (ibuprofen). This results in only small amounts of unwanted byproducts (very good atom economy/atom utilization) thus lessening the need for disposal and mediation of waste products. There are other environmental advantages to the green synthesis versus the brown synthesis, including solvents and catalyst.

## Slide 11
Ibuprofen
Synthesis

## Slide 12: Atom Economy – Convergent Arm Synthesis
(1) A + B C (1) F + G H
(2) C + D E (2) H + I J
E + J P

## Slide 13: Exercise: Calculate AE of the Greener Synthesis of Ibuprofen

## Slide 14: Exercise: Calculate AE of the Greener Synthesis of Ibuprofen

## Slide 15: Exercise: Calculate AE of the Greener Synthesis of Ibuprofen

## Slide 16: Exercise: Calculate AE of the Greener Synthesis of Ibuprofen

## Slide 17: The Brown Synthesis of Ibuprofen

## Slide 18: “Inherent” Atom Economy of Reaction Classes
Some Atom Economic Reactions | Some Atom Un-Economic Reactions
Rearrangement | Substitution
Addition | Elimination
Diels-Alder | Wittig
Other concerted reactions | Grignard

## Slide 19: Environmental Factor (E-Factor)
Depends on the definition of waste
  Non-recoverable starting materials, solvent, catalysts.
  Undesired side products.
Smaller E-factor means closer to zero waste
E-factor can be used to estimate/calculate the total waste generated:
  Amount of Waste = Amount of Product x E-factor
Industry sector | Annual production (t) | E-factor | Waste produced (t)
Oil refining | 106-108 | Ca. 0.1 | 105 – 107
Bulk chemicals | 104-106 | <1–5 | 104 – 5 × 106
Fine chemicals | 102−104 | 5–50 | 5 × 102 − 5 × 105
Pharmaceuticals | 10–103 | 25–100 | 2.5 × 102 − 105
  E-factor = total waste (g) / product (g)
Notes: Different types of processes have different range of E-factor

## Slide 20: E-Factor Example
Friedel-Craft Alkylation (Substitution)
All numbers represent the mass of the chemical after the reaction.
Phenol | Chloroethane | Catalyst | Solvent | 4-Ethylphenol | 2-Ethylphenol | E-Factor | *3-ton scale
10 | 20 | 5 | 1200 | 80 | 200 | 6.575 | 19.725
  E-factor = total waste (g) / product (g)
Industrial reactions are run on the big scale, so assuming 3 tons of product, this is the new atom economy
Notes: (10+20+5+1200+80) / 200 = 6.575
0.020 / 0.007 / 0

## Slide 21: Reaction Mass Efficiency (RME)
For the generic reaction A + B  C
.

## Slide 22: Comparison of Atom Economy and Reaction Mass Efficiency for 28 Different Chemical Reactions
Chemistry Type/Reagents | Atom Economy (%) | Reaction Mass Efficiency (%) | Chemistry Type | Atom Economy (%) | Reaction Mass Efficiency (%)
Resolution | 40% | 31% | Epoxidation | 83% | 58%
N-Dealkylation | 64% | 27% | Bromination | 84% | 63%
Elimination | 72% | 45% | Hydrogenation | 84% | 74%
N-Alkylation | 73% | 60% | S-Alkylation | 84% | 61%
Chlorination | 74% | 46% | O-Arylation | 85% | 58%
Borohydride | 75% | 58% | N-Acylation | 86% | 62%
Lithal | 76% | 52% | Amination | 87% | 54%
Grignard | 76% | 42% | C-Alkylation | 88% | 61%
Hydrolysis (Acid) | 76% | 50% | Iodination | 89% | 56%
Cyclisation | 77% | 56% | Knoevenagel | 89% | 66%
Cyanation | 77% | 65% | Sulphonation | 89% | 69%
Decarboxylation | 77% | 68% | Esterification | 91% | 67%
C-Acylation | 81% | 51% | Base salt | 100% | 80%
Hydrolysis (Base) | 81% | 52% | Acid Salt | 100% | 83%

## Slide 23: Process Mass Intensity (PMI)
PMI =
PMI accounts for yield, reaction and reagent stoichiometry, catalysts and solvents.
This includes everything that you put into the flask, but usually excludes water.
Ideal PMI = low values (~1)

## Slide 24: Green Chemistry-Related Metrics Used in Chemical Manufacturing
Chemical manufacturer responses (n = 18) to the 2012 Roundtable survey question “What green chemistry and engineering related metrics does your company use? Select all that apply.”
Percentage of respondents indicating one or more metrics surveyed in use computed as the ratio of [total responses – (not sure + none)]/(total responses). PMI = process mass intensity = (mass of raw materials)/(mass of final product).E-factor = (mass of waste)/mass of final product).LCA = life cycle assessment.
Implementing Green Chemistry in Chemical Manufacturing: A Survey Report Robert J. Giraud, Paul A. Williams, Amit Sehgal, Ettigounder Ponnusamy, Alan K. Phillips, and Julie B. Manley
ACS Sustainable Chemistry & Engineering 2014 2 (10), 2237-2242

## Slide 25
Why do we need metrics in green chemistry?
Established Metrics in Green Chemistry
  Atom Economy
  Environmental (E) Factor
  Atom Utilization
  Reaction Mass Efficiency
Additional Metrics Used in Green Chemistry
  Process Mass Intensity
  Life Cycle Assessment
  Ecological Indicator/Ecological Footprint
Topics Covered

## Slide 26
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 27: Atom Economic Reactions
The “Good”

## Slide 28: Addition
  Adding something to a molecule
    A + B ---> C
    Hydrogenation
    Chlorination or Bromination on alkene
    Hydration
Notes: Double bond is like a slot for a pair of atoms
Triple bond is like 2 slots for two pairs of atoms
Atom Economy? Good?

## Slide 29: Diels Alder Reactions
An excellent way of forming 2 C-C bonds simultaneously.
Concerted mechanism; highly regio- and stereoselective.
Some reactions can be carried out in water or ionic liquids, which may also act as catalyst.

## Slide 30: Low atom economy reactions
The “Bad”

## Slide 31: Wittig Reactions
A versatile method of preparing alkenes with an unambiguously placed double bond - gives high yields and takes place under mild conditions. Used for manufacture of vitamins and pharmaceuticals.
Expensive because of poor atom economy, which is due to production of triphenylphosphine oxide (MWt 278).

## Slide 32: Substitution
  Trading some parts of the molecule with another molecule
    AB + CD ---> AC +BD
Friedel-Craft Reaction
(Electrophilic Aromatic Substitution)

## Slide 33: Elimination
  Taking part of a molecule out
    A ---> B + C or more
    Dehydrogenation
    Dehydroxylation
    Dehalogenation