## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Energy delivery in Chemistry
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE
Source: wikipedia

## Slide 2
Role of energy in a chemical process
Microwaves
Flow chemistry
Photochemistry
Electrochemistry
Mechanochemistry
Topics To Be Covered

## Slide 3
Chemical industry energy use in the US
  Chemistry accounts for a large portion of energy use
  E.g. the Haber Bosch process alone (production of ammonia) represents 1% all al energy consumption in the world.
N. Notman, Haber-Bosch power consumption slashed, Chem. World, Oct 2012
https://www.eia.gov/energyexplained/index.php?page=us_energy_industry
Use of energy in the chemical industry

## Slide 4
reaction heating (if endothermic)
reaction cooling (if exothermic)
agitation, pumping…
work-up
  distillation
  drying
  filtrations
  etc…
Use of energy in a chemical process

## Slide 5
Use of energy: Activation reaction
Thermal heating
  Delivered from natural gas or other fossil fuel
  either using the heat of combustion directly or superheated steam.
  in the lab: electricity with hot plates or mantles
http://www.medicalexpo.com/prod/electrothermal/product-80796-510114.html

## Slide 6
Thermal heating in batch: limitations:
  Solvent needs to be heated to activate the molecules: it’s a loss of energy
  Homogeneity issues: there is a gradient of temperatures in the batch
  Heating of products after reaction… potential degradation
reacted
degraded
Use of energy: Activation reaction

## Slide 7
Thermal heating in batch: limitations:
  Solvent needs to be heated to heat the molecule: it’s a loss of energy
  Green solution: a solventless processes
Advantage | Disadvantage
no solvent heating/distilling | high viscosity/solubility problems
easy separation | thermal runaway risk
Use of energy: Activation reaction

## Slide 8
Thermal heating in batch: limitations:
  Solvent needs to be heated to heat the molecule: it’s a loss of energy
  Green solution: direct energy better towards the reaction and only the reaction.
     Microwaves (heats up only polar molecules)
     Sonochemistry (localized bursts of energy)
     Electrochemistry (electronic activation)
     Photochemistry (photonic activation)
     Mechanochemistry (to reaction solids together: no solvent heating)
Use of energy: Activation reaction

## Slide 9
Thermal heating in batch: limitations:
  Homogeneity issues:
  Degradation issues:
  Green solution: Flow chemistry
   The reaction can be heated only on a small volume (homogeneous)
   The reaction can be heated only when needed, avoiding overheating of products
reacted
degraded
Use of energy: Activation reaction

## Slide 10
Principal mechanism for microwave heating: Dipolar Polarization Mechanism
Alignment of the molecule with the electric field...
Dipole realigns to the field, generating heat through molecular friction/dielectric loss...
Microwave Heating: Mechanism
Dipole again realigns to the field, generating heat through molecular friction/dielectric loss... etc
Molecule must be polar
Molecule must be protic or viscous
    water; ethanol
    DMSO; DMF
    CH2Cl2
Bad MW reaction solvents:
benzene, CCl4 and ethers.

## Slide 11
Solvents may be ranked for their microwave performance
the higher tan δ, the better the microwave heating
Solvents for MW Reactions

## Slide 12
  Advantages of microwave heating:
     Heating uniformity: (conduction, convection and radiation are secondary)
     Heating speed: Target temperature easier to reach fast, especially in small volumes
     Effect of super-heating: heating above the boiling point of the solvent
     Selective heating: polar molecules could be heated without solvent heating
     Ohmic heating for metals and magnetic materials: local extreme heatings
CHEM 462: 20. Energy input reduction (I)
MW Reactions
Notes: Viscocity of water (1cP), methanol (0.59 cP), DCM (0.44 cP), ether (0.224 cP)

## Slide 13
  Devulcanization of rubber (recycling process): advantageous because no solvent needed, good heat repartition
  Dupont process for HCN production: gaseous reaction, so only the solid catalyst is heated. Locally, temperature is 1200°C!
CHEM 462: 20. Energy input reduction (I)
Microwave: industry applications
Al2O3
Pt
Local Ohmic heating
Notes: Viscocity of water (1cP), methanol (0.59 cP), DCM (0.44 cP), ether (0.224 cP)

## Slide 14
Chem. Commun., 2011, 47, 4583–4592
Flow chemistry: Chemical method taking place in a flow tube. The chemical reaction is performed in a continuous fashion.
The volume in which the reaction takes place is small (a few mm3 to cm3)
=> it’s easy to monitor reactions and control conditions within this volume (temperature, pressure…)
Flow chemistry

## Slide 15
Advantages of flow methodology:
   reactions that can not be scaled up.
   good heat transfer
   mass transfers
   continuous production
   constant quality
   safety (reactive reagents, better control of dangerous reactions)
   easier scale-up
Can be combined with:
   Photochemistry
   Microwave
   Electrochemistry
Flow chemistry
In such systems, high pressure can take place in a very small volume => improved safety

## Slide 16
Combining flow with microwave heating
Shore et al. Chem.–Eur. J. 2010, 16, 126.
NMP
Flow chemistry/microwave
Example of an A3 coupling
(amine, aldehyde, alkyne)

## Slide 17
 for electrolysis to occur, electrons must pass from the anode to the cathode through an external, electrical circuit interconnecting the two electrodes.
 there must be a mechanism for charge transport between the electrodes within the cell
There may or may not be a separator
Electrochemistry: principles
Pletcher & Walsh “Organic electrosynthesis” in: Industrial Electrochemistry; Springer Netherlands: Dordrecht (1993) pp 294–330.
Michael Faraday

## Slide 18
Industrial electroorganic synthesis: Monsanto hydrodimerization of acrylonitrile to adiponitrile
  A precursor to the diamine used in the synthesis of Nylon-6,6.
  400 000 metric tons of adiponitrile in 2014, or ∼30% of the adiponitrile market
  competitive with the conventional route starting from butadiene.
Dupont process
See: Pletcher & Walsh, Organic electrosynthesis. In Industrial Electrochemistry; Springer Netherlands: Dordrecht (1993); pp 294–330.
Monsanto process
Electrochemistry: Applications

## Slide 19
Merging electrochemistry with biocatalysis for muconic acid production
Bioengineered Saccharomyces cerevisiae
Glucose
Electro step: 94% yield and 100% faradaic efficiency
Matthiesen et al ACS Sustain. Chem. Eng. 2016, 4, 7098–7109
Electrochemistry: Applications
electro
bio

## Slide 20
Specialty Nylon 6,6 for improved performance
Electrochemistry: Applications
Matthiesen et al ACS Sustain. Chem. Eng. 2016, 4, 7098–7109

## Slide 21: Facilitating Chemical Reactions
catalyst
Harvest sun light?
Use light to activate reactions?

## Slide 22
“On the arid lands there will spring up industrial colonies without smoke and without smokestacks; forests of glass tubes will extend over the plains and glass buildings will rise everywhere; inside of these will take place the photochemical processes that hitherto have been the guarded secret of the plants, but that will have been mastered by human industry which will know how to make them bear even more abundant fruit than nature, for nature is not in a hurry and mankind is. And if in a distant future the supply of coal becomes completely exhausted, civilization will not be checked by that, for life and civilization will continue as long as the sun shines.” (Sciences, 1912)
  -Giacomo Luigi Ciamician

## Slide 23
Approaches to the Generation of CF3 Radicals from Sodium Triflinate
L. Li, X. Mu, W. Liu, Y. Wang, Z. Mi and C. -J. Li, J. Am. Chem. Soc., 2016, 138, 5809.

## Slide 24
Substrate Scope (UV Light)
L. Li, X. Mu, W. Liu, Y. Wang, Z. Mi and C. -J. Li, J. Am. Chem. Soc., 2016, 138, 5809.

## Slide 25
From UV to Visible Light
Control Experiment
L. Li, X. Mu, W. Liu, Y. Wang, Z. Mi and C. -J. Li, J. Am. Chem. Soc., 2016, 138, 5809.

## Slide 26
Titanium dioxide nanoparticles
  Nanoparticles of TiO2 absorb visible light, resulting in electron-hole separation
  Valence electrons
  Conduction electrons
D here can be a pollutant
Photochemistry: application for depollution

## Slide 27
Photoactive materials
http://cristalactiv.com/ourproducts/
Photochemistry: application for depollution

## Slide 28: Mechanochemistry
Planetary Mill
Vibrational (Shaker) Mill

## Slide 29
“shaker” or “mixer mill
planetary mill: a benchtop version of an industrial gravity-based mill

## Slide 30
Michael Brand (University of Cardiff) & Jean-Louis Do (McGill University)

## Slide 31
Role of energy in a chemical process
Microwaves
Flow chemistry
Photochemistry
Electrochemistry
Mechanochemistry
Topics Covered

## Slide 32
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE