## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Waste Prevention
Image: Wikimedia Commons, Anacortes Refinery, Author: Walter Siegmund
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
Waste Prevention
It is better to prevent waste than to treat or clean up waste after it is formed.
Image: Harshaw Chemical Company discharges waste water into the Cuyahoga river
Source: National Archives and Records Administration

## Slide 3
The Waste Treatment Pyramid
Reduced Solvent Use
Waste as a Feedstock
Biodegradation of Waste
Designing Processes to Include Biodegradation of Waste
Topics To Be Covered

## Slide 4: Waste treatment pyramid: The 4 Rs Reduce, Reuse, Recycle, Recover
Reduction
Reuse
Recycling
Energy recovery
Disposal
Most favored option
Least favored option
Prevention
Incineration
Landfill
Recycling
Composting
We need various types of technology to reduce and reuse waste.
Ultimately, the production of waste should be prevented.
Notes: Need for technologies to Reduce and Reuse waste.
Ultimately, the waste production should be Prevented

## Slide 5: Landfills
  Consolidated material is buried with mud and other sealing agents to enable chemical, bacteriological, and physical degradation.
  Semi-anaerobic conditions lead to production of methane and CO2.
  If captured, landfill gas (methane) from decomposing garbage can be used to produce electricity, heat, and fuels.
Reduction
Reuse
Recycling
Energy recovery
Disposal
Image: Wikimedia Commons

## Slide 6: Incineration and Pyrolysis
Incineration
  Solid organic waste is combusted.
  Some thermal treatments allow energy capture.
  Solid mass is reduced by 95-96%.
Reduction
Reuse
Recycling
Energy recovery
Disposal
Image: Wikimedia Commons
Material | Energy from burning
biomass | 14-17 GJ.ton-1
Oil | 45 GJ.ton-1
Natural gas | 55 GJ.ton-1

## Slide 7: Recycling and Composting
Reduction
Reuse
Recycling
Energy recovery
Disposal
Gasification:
  Converts organic based materials into CO, H2 and CO2.
  Achieved by reacting the material at high temperatures (>700 °C), without combustion, with a controlled amount of oxygen and/or stem.
  The resulting gas mixture is called syngas.
  Syngas is combustible and often used as a fuel.
Pyrolysis
  Thermal decomposition at 200-300°C occurring in the absence of oxygen.
  Precursor of both the combustion and gasification processes.
  The products of biomass pyrolysis include biochar, bio-oil, and gases - such as methane, hydrogen, carbon monoxide, and carbon dioxide.

## Slide 8: Recycling and Composting
Composting
  Organics undergo a biological decomposition to form a material (compost) that is non-toxic to plant growth.
  By-product of the reaction are CO2, water and heat.
Anaerobic conditions and biogas production
  Adopted for farm waste.
  Can reduce greenhouse gas emissions and can provide a cost-effective source of renewable energy.
  Recovered biogas can be an energy source for electricity, heating or transportation fuel.
Reduction
Reuse
Recycling
Energy recovery
Disposal

## Slide 9: Reuse and Repurpose
Reduction
Reuse
Recycling
Energy recovery
Disposal
Recycling
  Converting waste materials into new materials and objects.
  Available for metals, plastic, paper, glass.
  E.g. PET reuse and repurposing
http://www.packagingtoday.co.uk/news/newsgermans-recycle-more-and-more-effectively-success-in-pet-bottle-recycling-according-to-study-5699219
Cost-benefit of recycling: energy savings
Material | Energy savings
Aluminum | 95%
Cardboard | 24%
Glass | 5-30%
Paper | 40%
Plastics | 70%
Steel | 60%

## Slide 10: The Reduction and Elimination of Waste
Reduced solvent or solventless processes
Self separation
Process intensification
Material deposition
Use waste as a feedstock
Reduction
Reuse
Recycling
Energy recovery
Disposal

## Slide 11
Reduced Solvent: Sildenafil Citrate Production
Sildenafil citrate, commonly known as Viagra, is a selective inhibitor of phosphodiesterase 5 (PDE5). This new drug has immediately became a major seller, achieving sales of more than $1 billion during its first year on the market. With such a rapid sales take off it was critical that the environmental performance of the synthesis was good from the outset.
Average yield of last three steps = 97% yield.
Reduction of the ratio of solvent waste/kg product over 17 years from 1300 L/kg to only 7 L/kg by minimizing solvent use, increasing solvent recovery, improving solvent selection, and telescoping steps.
Only the solvents t-butanol, ethyl acetate, 2-butanone, and a trace of toluene still require disposal.
Comparison of organic and aqueous waste and vapor emissions for the sildenafil citrate process at three time points
Dunn, P.J et al Green Chem., 2004, 6, 43-48

## Slide 12
A one-pot, three step sequence.
Eliminates the need for several hazardous reagents such as ZnCl2, triphenylphosphine, and solvents such as dimethylformamide and dichloromethane.
E-factor improved by an order of magnitude.
Solvent consumption reduced by 95%, hazardous waste by 65%, preventing 1.5 million tons of hazardous waste per year.
Reduced Solvent: dNTPs
They are the building blocks of both DNA and RNA, which are chains of nucleotides made through the processes of DNA replication and transcription. Nucleoside triphosphates also serve as a source of energy for cellular reactions and are involved in signaling pathways. Nowadays they are synthesized and used in molecular biology.
Notes: dNTPs are essencial feedstock to perform Polymarase Chain Reaction (PCR)

## Slide 13
Reduced Solvent: Production of Ethylene Oxide
Ethylene oxide is used as an intermediate in the production of several industrial chemicals, the most notable of which is ethylene glycol. It is also used as a fumigant in certain agricultural products and as a sterilant for medical equipment and supplies.
Use of molecular oxygen removed the need for chlorine.
New process generated more than 16 times less waste than the original one, eliminating the formation of waste water.

## Slide 14: Utilizing Waste as a Feedstock
Some examples:
Waste cooking oil for biodiesel
Glycerol for lactic acid using catalyst
Red mud for bricks
Crustacean shell waste for chitosan based products

## Slide 15: Example: Used oils as biofuel source
Bio-diesel
Leung, D. Y. C., & Guo, Y. (2006). Transesterification of neat and used frying oil: optimization for biodiesel production. Fuel processing technology, 87(10), 883-890.
Used frying oil
Biodiesel from virgin vegetable oil is considered first generation biofuel because it competes with food
=> Turning to waste can offer a solution: frying oil can be used instead.

## Slide 16: Glycerol: a waste of biodiesel
2011 US bio-diesel production reached 967 million gallons.
  1 Olympic-size swimming = approximately 660,000 gallons.
  Almost 1460 Olympic-sized swimming pools of glycerol.
Current treatment:
  Dispose (sold for $240/ton!).
  Combust as fuel.
Chen, L.; Ren, S.; Ye, X. P., Fuel Processing Technology 2014, 120, 40-47.
T. Werpy, G. Petersen, Top value added chemicals from biomass, Pacific Northwest National Laboratory (PNNL), National Renewable Energy Laboratory (NREL), Office of Biomass Program (EERE), 2004.
Bio-diesel
“Waste”

## Slide 17: Glycerol: a waste of biodiesel
Polylactic acid
Valuable medicinal product
Sunless tanning product
Anti-freeze
Industrial chemical precursors
Skin exfoliating reagent
Notes: There are just a handful of examples of what we could do with glycerol so BURNING it is definitely not the most efficient way to use the limited resources nature offers.

## Slide 18: Production and Applications of Lactic Acid- Conventional process
90% of lactic acid comes from anaerobic fermentation of hexose sugar (e.g. corn starch).
Compete with food sources.
Slow and requires a lot of purifications.
Dusselier, M.; Van Wouwe, P.; Dewaele, A.; Makshina, E.; Sels, B. F., Energy & Environmental Science 2013, 6 (5), 1415-1442.
  Other applications of Lactic Acid:
  Food preservatives
  Edible pH modifier
  Textile industry
  Cosmetic and pharmaceutical industries

## Slide 19: Water Electrolysis with Earth Abundant Metal Catalyst
2H2O ---> O2 + 4H+ + 4e-
2H+ + 2e- ---> H2
Cathode
Anode
Power
Supply
e-
e-
e-
e-
e-
e-
e-
Cathode:
Any conductive materials
Anode:
Expansive platinum group metals
Cobalt 1,2‐bis(diphenylphosphino)ethane
(Co-DPPE)
Bloomfield, A. J.; Sheehan, S. W.; Collom, S. L.; Crabtree, R. H.; Anastas, P. T., A heterogeneous water oxidation catalyst from dicobalt octacarbonyl and 1,2-bis(diphenylphosphino)ethane. New J. Chem. 2014, 38 (4), 1540-1545.
Notes: Also, this catalyst works well in alkaline environment

## Slide 20: Electrocatalytic Oxidation of Glycerol
2H2O ---> O2 + 4H+ + 4e-
2H+ + 2e- ---> H2
Water-compatible
Atmospheric pressure
Rm temp. or above
Very low current / voltage
Cathode
Anode
Power
Supply
e-
e-
e-
e-
e-
e-
e-

## Slide 21: Example: Neutralization of Red Mud through generation of biofuels
The Bayer Process (Karl Bayer, 1887)
Element | Composition
Fe2O3 | 30-60wt%
Al2O3 | 10-20wt%
SiO2 | 3-50wt%
Na2O | 2-10wt%
CaO | 2-8wt%
TiO2 | trace-25wt%
K, Cr, V, Ni, Ba, Cu, Mn, Pb, Zn, Sc | Traces
NaOH, 170 – 180 °C
1 – 6 atm
Sodium aluminate
Na+ Al(OH)4-
Precipitation
Electrolytic Reduction
Red Mud
Alumina
Al2O3
(~2 tonne)
Aluminum
(~1 tonne)
Bauxites
(4 – 5 tonne)
Source: http://www.aluminiumleader.com/production/aluminum_production
Red mud
toxic sludge (highly basic pH=14)
byproduct of Bayer process
1 ton of Al2O3 => 1/3 to 2 tons of red mud.
Bayer Process: industrial process that refines bauxite, raw aluminum ore, into aluminum oxide, or alumina.
Notes: http://www.aluminiumleader.com/production/aluminum_production/

## Slide 22: Red Mud: Pollution and Accidents
Stade, Germany
Kolontar, Hungary
Noranda Alumina plant at Gramercy - located alongside the Mississippi River
Damandjodi, India
The red mud is kept in reservoirs
Oct. 4, 2010: A hungarian village, Kolontar, is flooded with toxic red mud.
one million cubic metres of red mud
Ten people died, and 150 people were injured
About 40 square kilometres (15 sq mi) of land affected
3 days later the spill reached the Danude
The base is strong enough to kill plant and animal life, and to cause burns and damage to airways if the fumes are breathed.
Notes: http://www.theguardian.com/environment/2014/jan/08/devecser-hungary-eco-town
http://www.theatlantic.com/photo/2011/09/a-flood-of-red-sludge-one-year-later/100158/
http://lacoastpost.com/blog/?p=13160
http://redmud.org/red-mud/disposal/

## Slide 23: Example: Neutralization of Red Mud through generation of biofuels
Pyrolysis of biomass
Pyrolysis of biomass (500°C) affords a mixture of solid, liquid and gas carbonaceous materials
See class on renewable feedstock
Gas (10-20 %)
→ Energy
CO/H2/CO2
Bio-coal (15-20 %)
→ Soil improvement
Bio-crude (60-75%)
→ Fuel
500°C
Further treatments are needed for fuel production => highly acidic (pH 2)
Notes: http://www.aluminiumleader.com/production/aluminum_production/

## Slide 24: Example: Neutralization of Red Mud through generation of biofuels
Prof. Marcel Schlaf, University of Guelph mixed the two waste streams
Neutralization takes place by mixing the waste streams together
Metals present in the red mud catalyze the reduction of the biofuels to obtain higher quality fuel
Bio-crude: biowaste
Red mud: industrial waste
Fuel
Karimi, E.; Gomez, A.; Kycia, S. W.; Schlaf, M. Energy & Fuels 2010, 24, 2747.
Neutral, magnetic powder could be used to make cement.
pH 2
pH 14
H2
C source
Source of metals for catalytic reduction

## Slide 25: Example: Extracting chitin with an ionic liquid
Robin Rogers and Mari Signum Mid-Atlantic, LLC, are commercializing a safe, environmentally friendly, low energy-demanding and overall less costly process to produce chitin from seafood waste. Chitin is used in a variety of applications, such as food processing, biodegradable plastics and biomedical applications. This zero-discharge process produces a very high-grade and pure chitin, making use of and monetizing this seafood processing waste.
Dr. Connelly (ACS), Robin Rogers, Julia Shamshina and John Keyes (awardees)
https://communities.acs.org/community/science/sustainability/green-chemistry-nexus-blog/blog/2018/10/18/american-chemical-society-announces-2018-green-chemistry-challenge-award-winners
chitin
Ionic liquid

## Slide 26: Biodegrade the Waste
Biodegradation - "A process by which microbial organisms transform or alter (through metabolic or enzymatic action) the structure of chemicals introduced into the environment." – US EPA, 2009
“Ready” biodegradability – remove 70% of dissolved organic carbon AND achieve 60% theoretical oxygen demand or CO2 production within a 10-day window in a 28-day test. – OECD
“Ultimate” biodegradability – 60-70% of organic carbon converted to CO2 within 28 days.

## Slide 27: Aerobic Versus Anaerobic Digestion
Difference in oxygen supply, organism types, and products formed.

## Slide 28: Aerobic Digestion
Bacteria consume organic matter.
Needs a constant supply of oxygen, pH adjustments, and mixing.
Byproducts: heat, CO2, and H2O.
Frequently used by water treatment plants or in composting.

## Slide 29: Anaerobic Digestion
Bacteria consume organic matter in the absence of oxygen.
Common in fermentation and landfill; produces biogas consisting of methane, ammonia, hydrogen sulfide.
Biogas is considered a renewable energy.

## Slide 30: Digestion versus Chemical Structure
Not all chemicals will biodegrade at the same rate (think plastic vs paper).
The rate of biodegradation depends on the microorganism, but also a chemical structure of the molecule.
Some parts of the molecule are known to be more biodegradable than the others.
There is a publically available software that analyses the chemical structure and predicts whether the molecule will degrade slower (days) or slower (months, years).

## Slide 31: Some chemical structures favor biodegradation
Favors biodegradation
OH
Linear chains
Cyclo
Esters
- Low molecular weight
Disfavors biodegradation
- High molecular weight
Halogens (F, Cl)
Tertiary carbon
Side chains and branching
Ethers
Poorly degraded
Readily degraded

## Slide 32: Predicting Biodegradation: EPA, EPISuite
EPI = Estimation Programs Interface http://www.epa.gov/oppt/exposure/pubs/episuitedl.htm

## Slide 33: BIOWIN Models Based on Molecular Fragment Contributions
Aerobic degradation models
Anaerobic degradation model
The program analyses the chemical structure of each molecule within the group, and assesses its biodegradation potential based on the molecule fragment and functional groups. The result is presented as a probability for degradation. If the number is greater or equal to 0.5, then the molecule will degrade faster. In contrast, values less than 0.5 indicate persistence and low biodegradation potential.

## Slide 34
Increasing number of rings & molecular weight
1.
2.
3.
4.
5.
1>2>4>3>5
Most biodegradable (aerobic)
Least biodegradable
Favors biodegradation
- OH
- Low molecular weight
Disfavors biodegradation
- High molecular weight
- Cl
4>1>2>3>5
Most biodegradable (anaerobic)
Least biodegradable
Ring structures
Notes: Increasing number of rings

## Slide 35
1.
2.
3.
4.
5.
6.
Bisphenol A derivatives: Halogenated and BPS
Poor biodegradation due to high MW
Disfavors biodegradation
- High molecular weight
Tertiary carbon
Halogens, but Cl better than F
Favors biodegradation
- Low molecular weight
1>6>3>4>2>5
Most biodegradable (aerobic)
Least biodegradable
6>2>4=5>3>1
Most biodegradable (anaerobic)
Least biodegradable
Bisphenol A derivatives

## Slide 36
1.
2.
3.
4.
5.
Different plasticizers
Linear and branched;
Two green plasticizers: Reduced ring to cyclo and isosorbide ring
Disfavors biodegradation
Side chains and branching
Ethers
arenes
Favors biodegradation
Linear chains
Saturated cyclo
Esters
1>4>2>3>5
Most biodegradable (aerobic)
Least biodegradable
1>5>2>4>3
Most biodegradable (anaerobic)
Least biodegradable
Plasticizers

## Slide 37
Explosives (TNT, nitroglycerine)
1.
2.
3.
4.
5.
Favors biodegradation
Small molecular weight
OH
Disfavors biodegradation
CH3
Large MW
NNO2CH3
Degrades faster due to small MW
4>5>1=2=3
Most biodegradable (aerobic)
Least biodegradable
4>5>2>1>3
Most biodegradable (anaerobic)
Least biodegradable
Explosives

## Slide 38
Design for Biodegradation?
Since we know the chemical moieties, functional groups, and types of bonds which make the molecule biodegradable, can we build-in biodegradability into chemical products?
YES!

## Slide 39
Example: Plasticizers
kills bacteria,
biodegradation halts
complete degradation to CO2 + H2O
Plasticizers are additives in plastic applications. Almost 90% of plasticizers are used in PVC, giving this material improved flexibility and durability.
Di-propylene glycol dibenzoate decomposes into a product which is toxic to bacteria, and therefore stops the biodegradation process.
With slightly changed structure, 1,5-pentanediol dibenzoate biodegrades into CO2 and H2O

## Slide 40
Example: Pesticides
DDT
DDT – Dichlorodiphenyltrichloroethane, which was used as agricultural pesticide, is persistent in the environment.
Not only does it bioaccumulates, but it undergoes a reaction to DDE which is even more toxic than DDT.
DDE
methoxychlor
Methoxychlor shares many insecticidal properties as DDT and it’s potency, but it is not persistent.
It degrades into methoxychlor phenol, which has also low toxicity and it is easily excreted.
Methoxychlor phenol
Slow degradation
Fast degradation

## Slide 41
Tetrapropylene alkylbenzene sulfonate (TPPS) was used as a surfactant for laundry detergents and accumulated into the water supply due to incomplete degradation.
Water tended to foam when coming out of the tap.
Example: Detergents
TPPS was replaced by linear alkylbenzene sulfonate (LAS).
Replacing the methyl branched chain of TPPS by a linear carbon chain reduces the biopersistence.
Low biodegradation
High biodegradation

## Slide 42
Triclosan is an antibacterial and antifungal agent found in some consumer products, including toothpaste, soaps, detergents, toys, and surgical cleaning treatments.
It persists in the environment.
Example: Antibacterial Products
Chlorophene is a bacteriocide and fungicide in cosmetics.
It is very biodegradable in the media and entirely removeable from the wastewater.
Low biodegradation
High biodegradation

## Slide 43
The Waste Treatment Pyramid
Reduced Solvent Use
Waste as a Feedstock
Biodegradation of Waste
Designing Processes to Include Biodegradation of Waste
Topics Covered

## Slide 44
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE