## Slide 1: Yale-UNIDO Train-the-Facilitator Workshop in Green Chemistry
Designing for Reduced Hazard
Image: Wikimedia Commons, Fume Hood , Author: U.S. National Institute for Occupational Safety and Health
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE

## Slide 2
Hazard and Risk – Past and Present
Toxicology
Assessing Hazards and Exposure
  What Happens When You’re Exposed?
Hazard Minimization Through Molecular Design
QSAR - Quantitative Structure Activity Relationship
Molecular Design Research Network (MoDRN)
Topics To Be Covered

## Slide 3
There are over 100,000 chemicals in global circulation.
700+ chemicals are introduced to the US Market each year.
85% of these chemicals lack experimental data.
There has been unintended biological activity which has led to increased hazard as well as toxic endpoints for humans and the environment.
The Challenge of Environmental Risk
Source: Wikimedia Commons

## Slide 4
The ability cause adverse consequence.
What types of chemical hazards are there?
  Global Hazards (global warming, acid rain, security threat, ozone depletion)
  Physical Hazards (explosivity, corrosivity, oxidizers/reducers)
  Toxicological
    Environmental (aquatic toxicity, avian toxicity, mammalian toxicity)
    Human (e.g., carcinogenicity, neurotoxicity, hepatotoxicity, dermal toxicity)
Hazard

## Slide 5
Risk = f(Hazard, Exposure)
Environmental risk is resulting from exposure to a potential environmental hazard
Risk can be reduced by in two ways:
If as hazard , exposure needs to be reduced to 0
If hazard = 0, exposure can be
Ultimate goal is to use BENIGN materials
Risk Equation

## Slide 6
Exposure becomes irrelevant
Less dependence on systems which can fail or be sabotaged
Competitive advantage – reduces costs associated with toxic materials
Why Use Benign Materials?

## Slide 7
Green chemistry focuses on reducing risk by reducing hazard.
If there is no hazard, exposure becomes irrelevant
The traditional approach to hazards focuses on reducing risk by minimizing exposure.
For example, wearing personal protective equipment or space ventilation if the chemical is volatile.
Mitigation of Risk through Design

## Slide 8: How have we dealt with chemicals and the environment in the past?

## Slide 9
Waste treatment, control, and disposal; pollutant monitoring; hazardous waste site cleanup.
Development of standards for emissions to air, releases to water, and disposal by land, as well as regulation of these standards.
“Command and Control”
Historical Approach to Environmental Problems

## Slide 10
In U.S., 3.93 billion lbs. of toxic chemicals were released directly to air, water, and land in 2011
Only 650 of toxic chemicals and toxic chemical categories out of 100,000 in commerce are tracked by Toxic Release Inventory
Mihelcic, J. R.; Zimmerman, J. B., Environmental engineering: Fundamentals, sustainability, design. Wiley Global Education: 2014.
Chemicals in the Environment

## Slide 11: Why should we care?

## Slide 12
One of Green Chemistry’s greatest strengths is the ability to design for reduced hazard.
148 xenobiotics in the body
Of the chemicals found:
  76 cause cancer in humans or animals,
  94 are toxic to the brain and nervous system, and
  79 cause birth defects or abnormal development.
The dangers of exposure to these chemicals in combination has never been studied.
Image Source: http://svtc.org/our-work/e-waste/
Body Burden

## Slide 13
The traditional definition of toxicology is "the science of poisons."
A more descriptive definition of toxicology is
"the study of the adverse effects of chemicals or physical agents on living organisms".
What is Toxicology

## Slide 14
What Counts as Toxic
Mihelcic, J. R.; Zimmerman, J. B., Environmental engineering: Fundamentals, sustainability, design. Wiley Global Education: 2014.

## Slide 15
Acute toxicity | Carcinogenicity | Bioconcentration
Subchronic & chronic toxicity | Neurotoxicity | Degradation & transport
Reproductive toxicity | Immunotoxicity | Aquatic toxicity
Developmental toxicity | Genotoxicity | Terrestrial organism toxicity
Molecular weight | Molecular volume | Dipole moment
Hydrophilic surface area | Hydrophobic surface area | Rotatable bonds
Hydrogen bonds | Ionization potential | Electron affinity
Partition coefficients | Acid/base properties | Polarizability
Relating Toxic Endpoints to Molecular Features & Properties

## Slide 16
A toxic agent is anything that can produce an adverse biological effect.
It may be chemical, physical, or biological in form.
For example, toxic agents may be
chemical (such as cyanide),
physical (such as radiation), and
biological (such as snake venom)
Definitions

## Slide 17: What is the most important factor in bringing about the adverse biological impact?

## Slide 18
Dose is the amount of a substance administered at given times.
For example:
  650 mg Tylenol as a single dose
  500 mg Penicillin every 8 hours for 10 days
Dose

## Slide 19
Highly toxic chemicals can be life saving when given in appropriate doses.
An apparently nontoxic chemical can be toxic at high doses. (Too much of a good thing can be bad)
Dose Makes the Poison
Source: Wikimedia Commons

## Slide 20
Source: Marczewski, A.E., and Kamrin, M. Toxicology for the citizen, Retrieved August 17, 2000: www.iet.msu.edu/toxconcepts/toxconcepts.htm.
Approximate Lethal Doses of Common Chemicals (Calculated for a 160 lb. human from data on rats)
Chemical Lethal Dose
Sugar (sucrose) 3 quarts
Alcohol (ethyl alcohol) 3 quarts
Salt (sodium chloride) 1 quart
Herbicide (2, 4-D) one half cup
Arsenic (arsenic acid) 1-2 teaspoons
Nicotine one half teaspoon
Food poison (botulism) microscopic
Lethal Doses

## Slide 21: How is toxicity testing done?

## Slide 22
The dose-response relationship is a fundamental and essential concept in toxicology. It correlates exposures and the spectrum of induced effects.
The dose-response relationship is based on observed data from experimental animal, human clinical, or cell studies.
Dose-Response

## Slide 23
Knowledge of the dose-response relationship:
  establishes causality that the chemical has in fact induced the observed effects
  establishes the lowest dose where an induced effect occurs - the threshold effect
  determines the rate at which injury builds up - the slope for the dose response.
Dose-Response

## Slide 24
LD 50- A common dose estimate for acute toxicity is the LD50 (Lethal Dose Response 50%).
This is a statistically derived dose at which 50% of the individuals will be expected to die.
NOAEL - No Observed Adverse Effect Level
Highest data point at which there was no adverse effect
LOAEL - Low Observed Adverse Effect Level
Lowest data point at which there was an adverse effect
LD 50
UF = Uncertainty factor (10-1000)
RfD – estimate of a daily oral exposure to the human population, that’s likely to be without risk of an effect
LD50, NOAEL, LOAEL, and RfD

## Slide 25
0
100
50
40
30
20
10
60
70
80
90
Inhaled Dose (ppm)
% Mortality
Solvent 99-7
Solvent 99-2
0 50 100 150 200 250 300 350
Plotted here are two theoretical curves for the toxicity of solvents used in the cleaning of silicon compounds. Both solvent 99-2 and 99-7 performed equally well against a variety of manufactured silicon compounds. The task at hand for you is to determine which solvent would you pick to be “safer” for use. As you can see from the accompanying data both compounds have an equivalent Lethal dose 50 value (LD50). These are based on average values during a 6 hour exposure period.
In-Class Discussion- Which Solvent Would You Use?

## Slide 26
Solvent 99-7 causes lethality at much lower levels than 99-2 (20ppm versus 100ppm respectively), and the response is much more predictable (i.e. less population heterogeneity). Solvent 99-2 because higher levels can be inhaled before any harmful effects should begin.
0
100
50
40
30
20
10
60
70
80
90
Inhaled Dose (ppm)
% Mortality
Solvent 99-7
Solvent 99-2
0 50 100 150 200 250 300 350
In-Class Discussion- Which Solvent Would You Use?

## Slide 27
Review and analysis of toxicology data and assessing if the substance causes toxic effects
Sources include animal and human studies and computational data
These studies have difficulty with showing causation (if a risk factor lead to disease)
Mihelcic, J. R.; Zimmerman, J. B., Environmental engineering: Fundamentals, sustainability, design. Wiley Global Education: 2014.
Hazard Assessment

## Slide 28
Determines the extent and frequency of human exposure to target chemicals.
Guidelines for residential, industrial and commercial sites
For engineers, the knowledge of risk and exposure provides information whether the site needs to be remediated.
Mihelcic, J. R.; Zimmerman, J. B., Environmental engineering: Fundamentals, sustainability, design. Wiley Global Education: 2014.
Exposure Assessment

## Slide 29: Hazard assessment, dose-response & exposure assessment
Risk Characterization

## Slide 30
ChemHAT - easy way to access summarized information on chemical hazards in the workplace
ChemSpider
Protox
Safer Choice - for consumers, businesses, and purchasers to find products that perform and are safer for human health and the environment.
toxicity assessment based on experimental or predicted LD 50
Tools For Hazard Characterization
Notes: Show tools

## Slide 31: What happens once you are exposed to a toxicant?

## Slide 32
ABSORBTION
DISTRIBUTION
METABOLISM
EXCRETION
ADME
http://blog.gyrosproteintechnologies.com/spinblog/adme-of-therapeutic-proteins

## Slide 33
Source: Wang and Skolnik, Chemistry and Biodiversity, 2009
Chemical Processes in ADME
Notes: More complex
ADME can be controlled by these parameters

## Slide 34
Dermal
Respiratory
Digestive
Skin is the first barrier to absorption for the chemical. The skin can keep chemicals out of the body, or it can let them in, depending on the physical and chemical properties of the chemical. Skin absorption depends on molecular weight, lipid solubility (log P), and physical state. These parameters determine if the chemical passes through the skin cell membranes into the body. Absorption of a chemical will result in the chemical circulating inside the body and perhaps causing adverse effects.
As chemicals are inhaled, they may reach the lungs. The lung surface is a poor barrier against the entry of many chemicals into the body, which means that absorption of chemicals into the lung can be rapid and efficient. Respiratory absorption depends on many factors such as molecular weight, log P and vapor pressure.
If chemicals are swallowed, either intentionally or unintentionally, they enter the gastrointestinal tract (GI). From there, they may either pass through the body or be absorbed into the body. GI absorption depends on many factors such as molecular weight, log P and physical state.
Absorption

## Slide 35
Dermal
Respiratory
Digestive
Absorption
Parameter | Preferred | Not Preferred
Physical state | solid | liquid
LogP | Less than 0 or greater than | Between 0 and 5
Molecular weight | More than 400 Da | Less than 400 Da
Parameter | Preferred | Not Preferred
Particle size [nm] | More than 5 | Less than 5
LogP | Less than 0 or greater than 5 | Between 0 and 5
Molecular weight [Da] | More than 400 | Less than 400
Vapor pressure [mmHg] | Less than 0.001 | More than 0.001
Parameter | Preferred | Not Preferred
Particle size [nm] | More than 100 | Less than 100
LogP | Less than 0 or greater than 5 | Between 0 and 5
Phase | solid | liquid
Molecular Weight [Da] | More than 500 | Less than 400

## Slide 36
Distribution is the movement of a chemical throughout the bloodstream and into other organs, such as the brain and the bones. Pharmaceuticals such as antibiotics and painkillers are designed to have high distribution rates so they can reach their target organs and have therapeutic effects. For chemicals such as detergents, distribution should be limited.
Distribution depends on many factors such as log P, polar surface area, acidic/basic properties, and molecular weight.
Distribution as opposed to absorption is more difficult to control.
Distribution
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor

## Slide 37
As a chemical is distributed through the body, it will most likely undergo metabolism. Metabolism is the body’s way of facilitating the excretion (removal) of the detergent through the kidneys. The rate at which a chemical is metabolized is usually dependent on its accessibility to enzymes.
Metabolism is more difficult to control than Absorption, and it can lead to detoxification or toxification of the organism.
Metabolism
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor

## Slide 38
After the chemical is absorbed, the body can eliminate it by a process called excretion which can occur through the kidneys, the skin, the GI tract, and the lungs. If the detergent is not eliminated from the body, it can accumulate, or stay in the blood, which can lead to disease.
Excretion as opposed to absorption is more difficult to control.
Elimination
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor

## Slide 39
Go to chemspider.com and put in following CAS number:
  Benzene 71-43-2
Using discussed parameters, predict respiratory, dermal and digestive absorption of compounds.
Benzene:
Colorless sweet smelling liquid; highly flammable
Used as precursor to many complex chemicals: polystyrenes, polycarbonates, epoxy resins, nylon
Toxic- known carcinogen
In-Class Exercise

## Slide 40
DERMAL | 
 | 71-43-2
LogP | 
Molecular weight [g/mol] | 
Phase | 
RESPIRATORY | 
 | 71-43-2
LogP | 
Molecular weight [g/mol] | 
Vapor pressure [mmHg] | 
DIGESTIVE | 
 | 71-43-2
LogP | 
Molecular weight [g/mol] | 
Phase | 

## Slide 41
DERMAL | 
 | 71-43-2-Benzene
LogP | 2.22
Molecular weight [g/mol] | 78.112
Phase | liquid
RESPIRATORY | 
 | 71-43-2-Benzene
LogP | 2.22
Molecular weight [g/mol] | 78.112
Vapor pressure [mmHg] | 100.9
DIGESTIVE | 
 | 71-43-2-Benzene
LogP | 2.22
Molecular weight [g/mol] | 78.112
Phase | liquid

## Slide 42
Benzene is volatile–it will absorb through the respiratory system
Once benzene is in the body, it has a moderate lipid and water solubility, therefore some of it will absorb in digestive track
Since it is a liquid, it will absorb easier than solid
Skin absorption is also probable
Conclusions

## Slide 43
Educational game based on ADME and scientific data for surfactants to make connection between physico-chemical properties and health.
http://gwiz.yale.edu
For Additional Practice: Safer Chemical Design Game
Courtesy of Molecular Design Research Network and Dr. Karolina Mellor

## Slide 44: Approaches to Hazard Minimization through Molecular Design

## Slide 45
Bioavailability Structure/Shape Activity Mechanism of Action
Molecular
Weight
Solubility
Electronic
Charge
Volatility
Reactive
Functional
Groups
Bioaccumulation/
Persistence
Particle
size
Receptor
binding
Key events
Shape/
Molar Volume
Toxicokinetics
Toxicodynamics
Chemists can control quite well
Not well understood and relatively complex
That’s what we want to target
Green Chemistry Molecular Design Pyramid

## Slide 46
Elimination of the molecular initiating event that activates pathway
Changing reactive functional groups
Reducing or eliminating bioavailability
Reduction of need for associated hazardous substances
Design for End-of-Useful product life
Approaches to Hazard Minimization Through Molecular Design

## Slide 47
Where the mechanistic pathway of action is known, molecular structures can be design such that the necessary reactions necessary are either impossible or highly disfavored resulting in significant toxicity reduction.
Elimination of the molecular initiating event that activates pathway

## Slide 48
In the absence of specific mechanistic information, chemists can modify structure such that certain reactive functional groups, e.g., cyano, electrophilic, etc, can be minimized or eliminated from the chemical structure where feasible.
B. Changing Reactive Functional Groups

## Slide 49
In order for a chemical to manifest its intrinsic hazard, it must be able to reach the toxicological target, human, animal, environmental or global. Through structural molecular design, properties such as solubility, log Kow, and volatility can adjusted to reduce hazard manifestation.
C. Reducing or Eliminating Bioavailability

## Slide 50
Many chemical substances, if not hazardous themselves, require the use of other hazardous substances e.g., paints with VOCs, surfaces requiring specific cleaners, plastics with various additives.
Through molecular design, these associated substances can be eliminated by making the desired properties integral to the product
D. Reduction of Need for Associated Hazardous Substances

## Slide 51
Persistence of chemical in the environment is a problem that can be designed out of molecular structure.
By creating products that degrade to innocuous by-products under designed conditions, e.g., heat, light, time one a can reduce or eliminate this hazard.
Design for utilization of waste as a feedstock is an important goal.
E. Design for End-of-Useful Product Life

## Slide 52: By Changing the Molecular Charge: Cephalosporins
Clinical nephrotoxicity was recognized early – damage to proximal tubular epithelia.
Mechanism: the drug is rapidly transported across basolateral membrane via the organic anion transporter, OAT1. Transport out of cell into lumen is less well characterized (involves other OAT, OAT4).
Cephalosporin has a very low affinity for OAT4 due to its zwitterionic character, resulting in considerable intracellular accumulation
Cephaloridine
Notes: Cephalosporins are a type of beta-lacatam antibiotic.
First generation:Cephaloridine

## Slide 53
In contrast, cephalothin, an anionic analog of the original zwitterionic drug, rapidly moves across the epithelia from blood into urine
Is thus not a neurotoxin
Cephalothin
Cephalothin
Notes: Kidney International (1999) 56, 2128–2136; doi:10.1046/j.1523-1755.1999.00789.x
http://www.nature.com/ki/journal/v56/n6/full/4491152a.html
Page 34

## Slide 54
Mechanism: After oral ingestion, a very small fraction is absorbed, but the blood levels remain constant for many hours as paraquat is not metabolized by the liver. Instead, it accumulates in the lung and is retained there even after blood concentrations decrease.
Paraquat was found to enter the lung via carrier-mediated transmembrane transport, specifically the polyamine transport system.
Diquat
Paraquat
By Manipulating Sterics: Paraquat and Diquat
Notes: Paraquat is s non-selective contact herbicide of the diphenyl class. It was introduced in the 1960s and became used worldwide.
However it was soon recognized that paraquat also cause selective pulmonary toxicity to humans (damage to alveolar cells type I and II, causing edema, inflammation and hermorrhage, lung fibrosis).

## Slide 55
Polyethoxylatednonylphenols
Emulsifiers, surfactants
When n = 14-19, intense myocardial necrosis at 40 mg/kg day in dogs and guinea pigs
When n<14>19, no myocardial effects
Glycidyl ethers
When n = 7-9, mutagenic, cause testicular lesions
When n = 11-13+, non-mutagenic
Through SAR Data: Nonylphenols and Glycidyl Ethers

## Slide 56
Acrylate is understood to be carcinogenic because it can readily undergo Michael addition reactions
The addition of a methyl group to form methacrylate decreases the electrophilicity of the b-carbon, and decreases tendency for Michael reactions.
While this does not reduce the commercial efficacy, but whereas acrylate causes cancer is experimental assays, methacrylate does not.
Acrylate
carcinogenic
Methacrylate
non-carcinogenic
By Manipulating Electrophilicity: Acrylates
Notes: Electr

## Slide 57
Benzene is known to cause hematoxicity and leukemia in humans
This is understood to be due to one of its metabolites, (E,E)-muconaldehyde.
Toluene is comparatively much less toxic, as the methyl group is oxidized more easily than the benzene ring to give benzoic acid
By Facilitating Detoxification: Benzene

## Slide 58
DDT is well known to be environmentally persistent
DDT analog with Silicon above was synthesized.
While less persistent, the analog turned out to be non-toxic to insects
This is due to the more readily oxidized (metabolized) Si-H bond compared to C-H and also the larger size of the molecule
DDT
(Toxic to insects)
Si-DDT Analog
(Non-toxic to insects)
By Isosteric Substitution: Carbon with Silicon

## Slide 59
Even if chemists design one chemical, it has to undergo tests
Designing New Molecules is Not a Trivial Task

## Slide 60
Assumes that similar chemicals behave similarly
Behavior of the chemical is derived from the structure
QSAR seeks for a relationship between chemical structure and activity
Identifies changes that lead to different activity (activity to avoid or keep)
QSAR-Quantitative Structure Activity Relantionship

## Slide 61
Not sufficient data on majority of chemicals
Not all chemicals will be tested
QSAR has been used for over 60 years
Better to predict than have nothing
When to use QSAR?

## Slide 62
They are associated with a specific endpoint [like LC50 or oxidative stress]
They ‘group’ chemicals based on activity like toxicity
Predict endpoints directly from chemical structure
QSAR Basics

## Slide 63
Lipinski rule of five
Number of rings
Number of rotatable bonds
Degree of branching
Connectivity
Overall shape
Predictors of function, toxicity, properties

## Slide 64
Prediction accuracy not higher than 65-70% for non-carcinogenic chemicals.
Lack of validation with up-to-date data
Application to a narrow range of chemical structures
Qualitative output
Current limitations
Examples of Popular Toxicity Prediction Tools

## Slide 65
As toxicology has increased its understanding of underlying biological processes leading to toxicity, computational chemistry can now describe the chemical transformations involved in these processes
Small molecules
Whole organisms
Polypeptide
DNA strands
Enzymes
Receptors
Genes
Organelles
Cells
Tissues
Organs
Technological and
Scientific Advances
System size
Toxicology
Computational chemistry
New Approach: Crossroads of Computational Chemistry & Toxicology
Notes: Jakub’s slide

## Slide 66
Pollution
Persistence
Depletion of resources
Flammability
Radioactivity
Risk of Explosion
Chemical Reactivity
Understanding Physicochemical Properties Associated with Reduced Hazard
Chemical and Physical Properties
pKa chain branching log P molecular refractivity mol. wt. hydrolyzable groups
EHOMO ELUMO electronegativity hardness dipole log D7.4 # H-bond accep/donor
DESIGN
DESIGN

## Slide 67
Absorption organs
GI tract
Skin
Lungs
Eyes
Acidic substance
pKa<7
Unionized at pH>pKa
Basic substance
pKa>7
Un-ionized at pH>pKa
Lipid soluble
Absorbed across intestine membrane intoblood
Chemical
Property-Based Guidelines for Bioavailability
Notes: Different absorption mechanisms - GI tract has largest SA, resp has largets blood flow & thinnest membrane, skin has variable thicknes; different requirements for water sol

## Slide 68
molecular size < 400 Da
log Pow 0 - 6
presence of solvents
Ionization (polar, ionized)
molecular size < 500 Da
log Pow 0 - 5
Non-ionization at GI pH
Particle size < 5um
molecular size < 400 Da
vapor pressure < 0.001 mmHg
water solubility molecular size
vapor pressure < 0.001 mmHg
Voutchkova, A.; Osimitz, T.; Anastas, T. Chem. Rev. 2010, 110, 5845
Property-Based Guidelines for Bioavailability
Absorption organs
GI tract
Skin
Lungs
Eyes

## Slide 69
Chemical
Properties
Receptor/Ligand
Interaction
DNA Binding
Protein Oxidation
Gene activation
Protein production
Altered signaling
Altered physiology
Disrupted homeostasis
Altered tissue development/ function
Lethality
Impaired
Development
Impaired
Reproduction
Toxicant
Cellular
Responses
Organ
Responses
Organism
Responses
Structure
Recruitment
Extinction
Population
Responses
Macro-Molecular
Interactions
Molecular
Cellular
Tissue
Organ
Organ System
Individual
Population
Ecosystem
Ankley et al. 2010 ET&C; Source: Gary Ankley & Dan Villeneuve, EPA
Adverse Outcome Pathways
Mechanistic understanding is critical for evaluating toxicity pathways
Design guidelines will be rationalized according to molecular initiation events

## Slide 70
Create a reliable tool for chemists which will not only predict the toxicity of existing chemicals but will allow a design of future molecules with reduced hazard

## Slide 71
Toxicology
Chemistry
Molecular Biology
Computational Chemistry
Molecular Design Research Network
Notes: MoDRN is the collaboration between 4 universities Baylor, GW, UWASH and Yale that uses advances in biology, toxicology, computational chemistry and engineering to develop a robust and well validated computer software that will not only predict toxicity of existing compounds but it will serve as a tool to redefine guidelines for the next generation molecules with reduced hazard. Our network will employ the newest strategies of computer modeling to build a computer software which will allow to understand what causes toxic endpoints and what can we do to avoid it. Our efforts will not only limit to research. To have the biggest possible impact we will engage educators and students on undergraduate and high school level to by including safer chemical design in students’ lesson plans and by developing interactive and hands-on teaching tools for undergraduate and high school students. Finally we plan to work with our colleagues across academia, colleagues across many industry sectors and policymakers on the government level to further inform and disseminate safe chemical concepts.

## Slide 72
EPA ToxCast
Tox21
Network lab assays
Where is Data Coming from?
High throughput assay
Low throughput assay

## Slide 73
Assay can test almost any biological effect
In vitro assay in cell
In vivo assay outcome in organism
Ideal assay is:
Reproducible: same result when repeated
Reliable: same result with different people repeat it
Sensitive: won’t miss an effect
Specific: won’t say there is an effect if there is not
Predictive of outcome of interest
What is an Assay?

## Slide 74
Set | Chemicals | Assays | Endpoints | Completion | Available
ToxCast Phase I | 293 | ~600 | ~700 | 2011 | Now
ToxCast Phase II | 767 | ~600 | ~700 | 03/2013 | 10/2013
ToxCast Phase IIIa | 1001 | ~100 | ~100 | Just starting | 2014
E1K (endocrine) | 880 | ~50 | ~120 | 03/2013 | 10/2013
Tox21 | 8,193 | ~25 | ~50 | Ongoing | Ongoing
Chemicals
Assays
~600
~8,200
0
Data from ToxCast
Notes: It’s important to note that this is not just a data collection exercise. ORD has assembled the infrastructure to house, QA, and analyze the tens of thousands of data points.
AND make all of this data publically available.

## Slide 75
ToxCast phase I: primarily pesticides
ToxCast phase II: industrial chemicals
ToxCast phase III: diverse chemical space; high production
Data from ToxCast

## Slide 76
Data Endpoints

## Slide 77
Hazard and Risk – Past and Present
Toxicology
Assessing Hazards and Exposure
  What Happens When You’re Exposed?
Hazard Minimization Through Molecular Design
QSAR - Quantitative Structure Activity Relationship
Molecular Design Research Network (MoDRN)
Topics Covered

## Slide 78
QUESTIONS?
Sponsored by Yale-UNIDO Initiative
CENTER for GREEN CHEMISTRY
and GREEN ENGINEERING at YALE